La-138

Reviewed by T. Nakagawa, JAERI, January 2004

1. Files

ENDF/B-VI:	No data are given.

JENDL-3.3 and JENDL-3.2:

The same data as JENDL-3.2 are given in JENDL-3.3. The evaluation was made by JNDC FPND working group [Ka92] for JENDL-3.1 in 1990. The data were taken over to JENDL-3.2 and JENDL-3.3.

JEFF-3.0 and JEF-2.2:

JEF-2.2 has no data for La-138. JEFF-3.0 adopted the data of JENDL-3.2.

CENDL-3:	No data are given.

BROND-2:	No data are given.

2. Thermal and resonance region

JENDL-3.3 and JENDL-3.2

Resolved resonance parameters were based on Mughabghab et al. [Mu81] A negative resonance was added to reproduce the thermal capture cross section of 57.2(5.7 [Mu81,Mi76].

In the unresolved resonance region from 330 eV to 100 keV, neutron strength functions were calculated with the optical model. Average level spacing was adjusted to the capture cross section calculated with the statistical model code CASTHY.

JEFF-3.0

The same as JENDL-3.3.

Recommendation/conclusion for the thermal and resonance region

JENDL-3.3 is recommended.

3. Fast neutron region

(1) Methodology

JENDL-3.3 and JENDL-3.2

The total, elastic and inelastic scattering, and capture cross sections were calculated with the spherical optical model and statistical model code CASTHY. The gamma-ray strength function was determined from the systematics of the radiation width (0.085 eV) and the level spacing (24.5 eV). Fifteen excited levels up to 0.836 MeV were adopted for the inelastic scattering cross section. The direct/semi-direct capture was calculated from a simple formula of Benzi and Reffo [Be69]

Other reaction cross sections were calculated with the preequilibrium and multi-step evaporation code PEGASUS. The (n,p) and (n,) reaction cross sections were normalized to 5.16 mb [Fo86], and 2.29 mb [Fo86] at 14.5 MeV. Sum of the threshold reaction cross sections were considered as a competing reaction cross sections in the CASTHY calculation.

Angular distributions of elastic and inelastic scattering were calculated with the CASTHY code. Isotropic distributions were assumed to the other reactions.

The energy distributions were calculated with the PEGASUS code.

JEFF-3.0 and JEF-2.2

Same as JENDL-3.3.

(2) Total cross section (MT=1)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/La138.htm#mt1

(3) Capture cross section (MT=102)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/La138.htm#mt102

(4) Elastic scattering cross section (MT=2)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/La138.htm#mt2

(5) Inelastic scattering cross section (MT=4, 51 – 91)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/La138.htm#mt4

Discrete levels considered in the evaluations are as follows:

JENDL-3.3, JEFF-3.0	15 levels up to 0.8360 MeV

The direct inelastic was not considered.

(6) (n,2n) reaction cross section (MT=16)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/La138.htm#mt16

(7) (n,p) reaction cross section (MT=103)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/La138.htm#mt103

(8) (n,) reaction cross section (MT=107)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/La138.htm#mt107

(9) Other reactions

The following reaction cross sections are given:

JENDL-3.3, JEFF-3.0	(n,3n), (n,n), (n,np), (n,nd), (n,nt), (n,d), (n,t), (n,3He)

Recommendation/conclusion for the fast energy region

JENDL-3.3 is recommended.

References

[Be69]	Benzi V. and Reffo G.: CCDN-NW/10 (1969).

[Fo86]	Forrest R.A.: AERE-R 12419 (1986).

[Ka92]	Kawai M. et al.: J. Nucl. Sci. Technol., 29, 195 (1992).

[Mi76]	Michael H., Neubert A., Wagner R. and Blair A.J.: Int. J. Appl. Radiat. Isotopes, 27, 533 (1976).

[Mu81]	Mughabghab S.F. et al.: Neutron Cross Sections, Vol. 1, part A, Academic press (1981).

[Mu03]	Mughabghab S.F.: “Thermal Neutron Capture Cross Sections Resonance Integrals and g-Factors,” INDC(NDS)-440 (2002)

Table 1  Summary for Resolved and Unresolved Resonance Region: La-138

-----------------------------------------------------------------------------------------------------------------

Library	RRP	URP	Remarks

-----------------------------------------------------------------------------------------------------------------

JENDL-3.3	330 eV, MLBW	0.33 – 100 keV

JEFF-3.0	330 eV, MLBW	0.33 – 100 keV	the same as JENDL-3.3

-----------------------------------------------------------------------------------------------------------------

Table 2. Thermal Cross Sections and Resonance Integral: La-138

Units: barns

-----------------------------------------------------------------------------------------------------------------

Library/Experiment	Total	Elastic	Capture	Res.Integ.

-----------------------------------------------------------------------------------------------------------------

JENDL-3.3	70.06	12.98	57.08	364

JEFF-3.0	70.06	12.98	57.08	364

Mughabghab et al. [Mu81]			57.2(5.7	409(90*1

Mughabghab et al. [Mu03]			57.2(5.7	362(25

Michael et al. [Mi76] 			57.2(5.7	384(90*2

-----------------------------------------------------------------------------------------------------------------

*1) Mughabghab et al. recommended Ic of 360(30 barns also.

*2) Resonance integral of non-1/v part. Total resonance integral is 410(90 barns.