Ce-138

Reviewed by T. Nakagawa, JAERI, January 2004

1. Files

ENDF/B-VI:	No data are given.

JENDL-3.3 and JENDL-3.2:

No data are given..

JEFF-3.0 and JEF-2.2:

No data are given.

CENDL-3:	Evaluation was made by Y.L.Han et al. in 2000.

BROND-2:	No data are given.

2. Thermal and resonance region

CENDL-3

No resonance parameters were given.

Cross sections below 100 keV were calculated with a formula of a+bE+C/sqrt(E).

Tables 2 and 3 compare the thermal cross sections and resonance integral with experimental data. The capture resonance integral of CENDL-3 seems to be too small.

Recommendation/conclusion for the thermal and resonance region

CENDL-3 is recommended.

3. Fast neutron region

(1) Methodology

CENDL-3

Theoretical calculation was performed using the NUNF code. The optical potential parameters were obtained by fitting to the total and non-elastic scattering cross sections and angular distributions of elastic scattering for natural Ce. Direct inelastic was calculated with DWUCK-4.

Emitted particle distributions are given in MF=6. Gamma-ray production data are also given.

(2) Total cross section (MT=1)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce138.htm#mt1

(3) Capture cross section (MT=102)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce138.htm#mt102

Maxwell averaged cross sections:

Average cross section (mb) at kT=25 keV

CENDL-3	48.3

Käppeler et al. [Ka96]	193(5

CENDL-3 is possibly too small.

(4) Elastic scattering cross section (MT=2)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce138.htm#mt2

(5) Inelastic scattering cross section (MT=4, 51 – 91)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce138.htm#mt4

Discrete levels considered in the evaluations are as follows:

CENDL-3	16 levels up to 2.4715 MeV

The direct inelastic was calculated with DWUCK4 code.

The data of continuum inelastic scattering is zero between threshold (2.49 MeV) and 5.0 MeV. Therefore, the total inelastic has a small dip at around 5 MeV and the capture, (n,p) and (n,) cross sections a peak at the same energy.

(6) (n,2n) reaction cross section (MT=16)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce138.htm#mt16

Experimental data [Qa74] are reproduced well.

(7) (n,p) reaction cross section (MT=103)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce138.htm#mt103

(8) (n,) reaction cross section (MT=107)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce138.htm#mt107

(9) Other reactions

The following reaction cross sections are given:

CENDL-3	(n,3n), (n,n), (n,np), (n,d), (n,t)

Recommendation/conclusion for the fast energy region

CENDL-3 is recommended.

References

[He78]	Heft R.E.: 78Mayag, p.495 (1978).

[Ka96]	Käppeler F. et al.: Phys. Rev., C53, 1397 (1996).

[Ke56]	Ketelle B.H. et al. : Phys. Rev., 103, 190 (1956).

[Mo50]	Moses A.J. and Martin D.S.: Phys. Rev., 79, 467 (1950).

[Mu81]	Mughabghab S.F. et al.: Neutron Cross Sections, Vol. 1, part A, Academic press (1981).

[Mu03]	Mughabghab S.F.: “Thermal Neutron Capture Cross Sections Resonance Integrals and g-Factors,” INDC(NDS)-440 (2002)

[Po52]	Pomerance H.: Phys. Rev., 88, 412 (1952).

[Qa74]	Qaim S.M.: Nucl. Phys., A224, 319 (1974).

[Se62]	Sehgal M.: Phys. Rev., 128, 761 (1962).

[Va74[	Van der Linden et al.: J. Radioanl. Chem., 23, 113 (1974).

Table 1  Summary for Resolved and Unresolved Resonance Region: Ce-138

-----------------------------------------------------------------------------------------------------------------

Library	RRP	URP	Remarks

-----------------------------------------------------------------------------------------------------------------

CENDL-3	not given 	not given

-----------------------------------------------------------------------------------------------------------------

Table 2. Thermal Cross Sections and Resonance Integral: Ce-138

Units: barns

-----------------------------------------------------------------------------------------------------------------

Library/Experiment	Total	Elastic	Capture	Res.Integ.

-----------------------------------------------------------------------------------------------------------------

CENDL-3	5.500	4.385	1.115	1.15

Mughabghab et al. [Mu81]			1.1(0.3

Mughabghab et al. [Mu03]			1.02(0.24

Pomeronce [Po52]			8.7(70%*1

Van der Linden et al. [Va74]				1.210.13*2

Heft [He78]			1.02(0.12*3	6.7(3.1

-----------------------------------------------------------------------------------------------------------------

*1	Measured in Maxwell spectrum.

*2	to a meta-stable state.

*3	Measured in a reactor.

Table 3. Thermal Capture Cross Sections: Ce-138

Units: barns

-----------------------------------------------------------------------------------------------------------------

Library/Experiment	ground	meta	ratio (M/G)	total

-----------------------------------------------------------------------------------------------------------------

CENDL-3				1.115

Mughabghab et al. [Mu81]	1.1 ( 0.3	0.015(0005	0.0136	1.1(0.3

Mughabghab et al. [Mu03]	1.02(0.24			1.02(0.24

Moses ad Martin [Mo50]	0.81*1

Pomeronce [Po52]				8.7(70%*2

Ketelle et al. [Ke56]	1.0*3	0.007*4

Sehgal [Se62]	1.26(0.20*5	0.018(0.005*2

Heft [He78]				1.02(0.12*6

-----------------------------------------------------------------------------------------------------------------

*1	Ratio of 138Ce(n,)/140Ce(n,) was measured in a reactor. The result of 1.4 was translated to the 138Ce(n,) cross section by assuming 140Ce(n,) of 0.58 barn [Mu03].

*2	Measured in Maxell spectrum.

*3	Measured in a reactor. 140Ce(n,) of 0.6 barn was assumed.

*4	Measured in a reactor. 136Ce(n,)137gCe of 2 barns was assumed.

*5	Measured in Maxell spectrum. 140Ce(n,) of 0.6 barn was assumed.

*6	Measured in a reactor.