NATIONAL HIGHWAY TRAFFIC SAFETY ADMINISTRATION

Office of Vehicle Safety Compliance

COMPLIANCE STATUS REPORT

REPORT DATE: OCTOBER 2005

The following definitions are essential to the interpretation of the report:

# INVESTIGATIONS —

CT (Compliance Test) — Investigations initiated based on the results of scheduled compliance test programs.

CI Number — OVSC Compliance Investigation Number (such as "CI-208-020320")

The CI number identifies FMVSS 208 with a test failure date of March 20, 2002.  A compliance investigation is established when there is a reasonable expectation that a noncompliance may exist.

PE Number — OVSC Preliminary Evaluation Number (such as "PE-214-020320")

The PE number identifies FMVSS 214 with a test failure date, inspection date, complaint date, etc., of March 20, 2002.  A preliminary evaluation action is taken to gather additional information in cases where there is only a possibility of a noncompliance.

The following types of investigations initiated as a result of information obtained from sources other than scheduled compliance test programs such as consumer complaints, industry disclosures, articles in the news media, etc:

IN (Inspection)		CP (Complaint)		MD (Manufacturer Defect)

ID (Part 574)		MI (Manufacturer Inquiry)

COMPLIANCE TESTING —

TEST PROGRAM — Tests conducted in accordance with scheduled compliance test programs

RETEST — Retesting of items that have initially failed during a scheduled compliance test program

RESPONSIVE — Not a part of a scheduled compliance test program but consists of special testing, consumer complaint testing, etc.

COMPLIANCE TESTING LEGEND —

The following identifiers are used:

STD - Federal Motor Vehicle Safety Standard (FMVSS) or Regulation (i.e., Part 575, Part 567)

LAB - Testing laboratory under contract to OVSC

GRP - Test report group number. The following identifiers are found in the last character of the GRP number for those tests other than SCHEDULED compliance tests:  R – Retest, T - Response test

SPECIAL CASES: FMVSS 109 - S=Test Program, R=Retest, C=Responsive

FMVSS 119 - A=Test Program, B=Retest, C=Responsive

US MFR/US DISTRIBUTOR - Manufacturer or distributor of motor vehicle or equipment item

MAKE - Make of motor vehicle or equipment item

MODEL - Information for motor vehicle or equipment item

STYLE/COMPONENT - Information for motor vehicle or equipment item

IDENTIFICATION NUMBER - Tire identification number

MY - Motor vehicle model year

HS NO. - Test report number used by the NHTSA Technical Information Services for identification purposes

RESULT - Test results (PASS or FAIL)

FAIL - P: performance failure

FAIL - I:  inspection failure

FAIL - L: labeling or instruction failure

| FEDERAL MOTOR VEHICLE SAFETY STANDARDS |
| --- |
| No. | STD | FMVSS TITLE | TYPE | MODE |
| 1 | 101 | Controls and Displays (Inspection) | Vehicle | Insp.-1 |
| 2 | 102 | Transmission Shift Lever Sequence, etc. (I) | Vehicle | Insp.-2 |
| 3 | 103 | Windshield Defrosting & Defogging Systems | Vehicle-1 | TEST |
| 4 | 104 | Windshield Wiping & Washing Systems | Vehicle-2 | TEST |
| 5 | 105 | Hydraulic Brake System | Vehicle-3 | TEST |
| 6 | 106 | Brake Hoses | Equip.-1 | TEST |
| 7 | 108 | Lamps, Reflective Devices, etc. | Equip.-2 | TEST |
| 8 | 109 | Passenger Car New Pneumatic Tires | Equip.-3 | TEST |
| 9 | 110 | Passenger Car Tire Selection & Rims | Vehicle-4 | TEST |
| 10 | 111 | Rearview Mirrors | Vehicle-5 | TEST |
| 11 | 113 | Hood Latch Systems (Inspection) | Vehicle | Insp.-3 |
| 12 | 114 | Theft Protection | Vehicle-6 | TEST |
| 13 | 116 | Hydraulic Brake Fluids | Equip.-4 | TEST |
| 14 | 117 | Retreaded Pneumatic Tires (Inspection) | Equipment | Insp.-4 |
| 15 | 118 | Power Operated Window Systems | Vehicle-7 | TEST |
| 16 | 119 | Truck/Bus New Pneumatic Tires | Equip.-5 | TEST |
| 17 | 120 | Truck/Bus Tire Selection & Rims | Vehicle-8 | TEST |
| 18 | 121 | Air Brake Systems | Vehicle-9 | TEST |
| 19 | 122 | Motorcycle Brake Systems | Vehicle-10 | TEST |
| 20 | 123 | Motorcycle Controls & Displays (Inspection) | Vehicle | Insp.-5 |
| 21 | 124 | Accelerator Control Systems | Vehicle-11 | TEST |
| 22 | 125 | Warning Devices | Equip.-6 | TEST |
| 23 | 129 | Passenger Car New Non-Pneumatic Tires | Equip.-7 | TEST |
| 24 | 131 | School Bus Pedestrian Safety Devices | Vehicle-12 | TEST |
| 25 | 135 | Passenger Car Brake Systems | Vehicle-13 | TEST |
| 26 | 201 | Occupant Protection in Interior Impact | Vehicle-14 | TEST |
| 27 | 202 | Head Restraints | Vehicle-15 | TEST |
| 28 | 203 | Impact Prot. for Driver from Strg. Control | Vehicle-16 | TEST |
| 29 | 204 | Steering Control Rearward Displacement | Vehicle-17 | TEST |
| 30 | 205 | Glazing Materials (Inspection) | Equipment | Insp.-6 |
| 31 | 206 | Door Locks & Door Retention Components | Equip.-8 | TEST |
| 32 | 207 | Seating Systems | Vehicle-18 | TEST |
| 33 | 208 | Occupant Crash Protection | Vehicle-19 | TEST |
| 34 | 209 | Seat Belt Assemblies | Equip.-9 | TEST |

| 35 | 210 | Seat Belt Assembly Anchorages | Vehicle-20 | TEST |
| --- | --- | --- | --- | --- |
| 36 | 212 | Windshield Mounting | Vehicle-21 | TEST |
| 37 | 213 | Child Restraint Systems | Equip.-10 | TEST |
| 38 | 214 | Side Impact Protection | Vehicle-22 | TEST |
| 39 | 216 | Roof Crush Resistance | Vehicle-23 | TEST |
| 40 | 217 | Bus Window Retention & Release | Vehicle-24 | TEST |
| 41 | 218 | Motorcycle Helmets | Equip.-11 | TEST |
| 42 | 219 | Windshield Zone Intrusion | Vehicle-25 | TEST |
| 43 | 220 | School Bus Rollover Protection | Vehicle-26 | TEST |
| 44 | 221 | School Bus Body Joint Strength | Vehicle-27 | TEST |
| 45 | 222 | School Bus Passenger Seating | Vehicle-28 | TEST |
| 46 | 223 | Rear Impact Guards | Equip.-12 | TEST |
| 47 | 224 | Rear Impact Protection (Inspection) | Vehicle | Insp.-7 |
| 48 | 225 | Child Restraint Anchorage Systems | Vehicle-29 | TEST |
| 49 | 301 | Fuel System Integrity | Vehicle-30 | TEST |
| 50 | 302 | Flammability of Interior Materials | Equip.-13 | TEST |
| 51 | 303 | Fuel System Integrity of CNG Vehicles | Vehicle-31 | TEST |
| 52 | 304 | CNG Fuel Container Integrity | Equip.-14 | TEST |
| 53 | 305 | Electric Vehicles | Vehicle-32 | TEST |
| 54 | 401 | Interior truck Release | Vehicle | TEST |
| 55 | 500 | Low Speed Vehicle Requirements | Vehicle-33 | TEST |
| SUMMARY: 34 vehicle standards, 14 equipment standards, 7 inspection standards |

REPORTS ACCEPTED DURING SEPTEMBER 2005 FOR FY 2005 TEST PROGRAM

A “FAIL” result is the first indication of a possible non-compliance issue that will undergo further analysis by NHTSA.  Consumers should continue to use a vehicle or equipment item unless notified by the manufacturer to stop.

| STD | LAB/ GRP | MFR/ DISTRIB | MY/MAKE/ MODEL/STYLE | RESULT/ HSNO. |
| --- | --- | --- | --- | --- |
| 201 | CAL 007 | KIA | 2005 KIA SPORTAGE MPV 4-DOOR | PASS 638017 |
| 201 | MGA 003 | TOYOTA | 2005 TOYOTA TACOMA PU TRUCK 4-DOOR | PASS 638016 |
| 218 | SRI 001 | AGV LAZER | 2005 AGV TI-TECH COMP. MOTORCYCLE HELMET | PASS 638014 |
| 218 | SRI 003 | HJC | 2005 HJC CL-21 PARTIAL MOTORCYCLE HELMET | PASS 638015 |
| 218 | SRI 006 | NOLAN | 2005 NOLAN X-1002 COMP. MOTORCYCLE HELMET | PASS 638013 |
| 218 | SRI 008 | SHOEI | 2005 SHOEI TZ-R COMP. MOTORCYCLE HELMET | PASS 638025 |
| 218 | SRI 010 | KIMPEX | 2005 KIMPEX CKX VX-11 COMP. MOTORCYCLE HELMET | FAIL-L 638011 |
| 218 | SRI 014 | SHANGHAI HEHUI | 2005 V CAN SPORTS MAX-603 COMP. MOTORCYCLE HELMET | PASS 638024 |
| 218 | SRI 015 | KYLIN | 2005 KYLIN KY-207 FULL MOTORCYCLE HELMET | FAIL-L 638021 |
| 218 | UST 015 | HJC | 2005 HJC CS-AIR COMP. MOTORCYCLE HELMET | PASS 638022 |
| 218 | UST 016 | SOAR | 2005 HCI 20C FULL MOTORCYCLE HELMET | FAIL-L 638026 |
| 218 | UST 017 | THH | 2005 CYBER US-94 COMP. FACIAL MOTORCYCLE HELMET | FAIL-L 638027 |
| 218 | UST 018 | RODIA | 2005 RODIA RHD200 PARTIAL MOTORCYCLE HELMET | FAIL-L 638028 |
| 218 | UST 019 | FULMER | 2005 FULMER AF-M MODUS COMP. MOTORCYCLE HELMET | FAIL-P 638023 |
| 218 | UST 020 | THH | 2005 THH T-796 COMP. MOTORCYCLE HELMET | FAIL-L 638029 |
| 218 | UST 021 | SIMPSON | 2005 SIMPSON HORIZON COMP. MOTORCYCLE HELMET | FAIL-L 638030 |
| 218 | UST 022 | SOAR | 2005 HCI 115 PARTIAL MOTORCYCLE HELMET | FAIL-L 638031 |

REPORTS ACCEPTED DURING SEPTEMBER 2005 FOR FY 2005 TEST PROGRAM

A “FAIL” result is the first indication of a possible non-compliance issue that will undergo further analysis by NHTSA.  Consumers should continue to use a vehicle or equipment item unless notified by the manufacturer to stop.

| STD | LAB/ GRP | MFR/ DISTRIB | MY/MAKE/ MODEL/STYLE | RESULT/ HSNO. |
| --- | --- | --- | --- | --- |
| 218 | UST 023 | CAPACETES M&S | 2005 CAPACETES CMS J3 FULL MOTORCYCLE HELMET | PASS 638032 |
| 218 | UST 024 | ZAMP | 2005 ZAMP FC-12 COMP. MOTORCYCLE HELMET | FAIL-L 638033 |
| 218 | UST 025 | KBC | 2005 KBC FFR MODULAR COMP. MOTORCYCLE HELMET | PASS 638034 |
| 218 | UST 026 | KBC | 2005 KBC O'NEAL 905 COMP. MOTORCYCLE HELMET | PASS 638035 |
| 222 | MGA 001 | CORBEIL | 2004 CORBEIL 30 PASSENGER SCHOOL BUS | FAIL-I 638010 |
| 225 | GTL 001 | DAIMLER/ CHRYSLER | 2005 CHRYSLER 300 4-DOOR SEDAN | PASS 638020 |
| 225 | GTL 002 | VOLVO | 2005 VOLVO S40 4-DOOR SEDAN | FAIL-I 638019 |
| 225 | MGA 010 | HONDA | 2005 ACURA TL 4-DOOR SEDAN | PASS 638018 |

FAILURE LEGEND:  P - PERFORMANCE; I - INSPECTION; L – LABELING

COMPLIANCE INVESTIGATIONS (CIs) IN PROGRESS THROUGH SEPTEMBER 2005

(CI NUMBER SYSTEM EXAMPLE: “CI-208-041220” FOR FMVSS 208 WITH A

TEST FAILURE DATE OF DECEMBER 20, 2004)

NONE

## CIs OPENED SINCE LAST REPORT

NONE

# CIs CLOSED SINCE LAST REPORT

###### NONE

CAUSE:

PE Petition

CT Compliance Test

IN Inspection

CP Complaint

ID Part 574

MI Mfgr. Inquiry

MD Mfgr. Defect

#### PRELIMINARY EVALUATION INVESTIGATIONS (PEs) IN PROGRESS THROUGH SEPTEMBER 2005

(PE NUMBER SYSTEM EXAMPLE: “PE-208-041220” FOR FMVSS 208 WITH A

TEST FAILURE DATE OF DECEMBER 20, 2004)

| PE NO. | MFR/MY/MAKE/MODEL/FAILURE | CAUSE |
| --- | --- | --- |
| PE-121-041101 | Indiana Phoenix Inc./2004 Air Brakes/Data request | MI |
| PE-201-041110 | Ford Motor Co./2005 Ford Escape/A-Pillar Hic > 1000 | CT |
| PE-201-050228 | Mazda North American Operations/2004 Mazda 6/Interior compartment door test | CT |
| PE-201-050325 | General Motors Corp./2005 Buick Lactosse/Upper roof rail target ( Ur2):1164 HIC<1000 HIC | CT |
| PE-208-050323 | Toyota Motor Co./2005 Toyota Corolla/Passenger neck compression | CT |
| PE-208-050405 | Mercedes Benz/2005 Mercedes C230/LRD test failure 5FHlll | CT |
| PE-221-050706 | Corbeil International/2005 Corbeil/30 passenger school bus/Joint tensil strength less than 60% | CT |
| PE-222-050525 | Blue Bird/2005 Blue Bird Vision/Barrier position and rear surface area | CT |

PEs OPENED SINCE LAST REPORT

| PE NO. | MFR/MY/MAKE/MODEL/FAILURE | CAUSE |
| --- | --- | --- |
| PE-120-050825 | US Bus Corp./2005 US Bus Universe/Data request | CT |
| PE-208-050603 | Hyundai/2005 Hyundai Santa Fe/Suppression test failure 6 Y0 Hlll | CT |
| PE-221-050705 | Collins Industries/2004 Collins Super Bantam/Joint tensil strength less than 60% | CT |

## PEs CLOSED SINCE LAST REPORT

| PE NO. | MFR/MY/MAKE/MODEL/FAILURE |
| --- | --- |
| PE-208-050603 | Hyundai/2005 Hyundai Santa Fe/Suppression test failure 6 Y0 Hlll/Manufacturer’s non compliance report 9/30/2005 |
| PE-221-050705 | Collins Industries/2004 Collins Super Bantam/Joint tensil strength less than 60%/ Technical investigation complete 8/12/2005 |

CAUSE:

PE Petition

CT Compliance Test

IN Inspection

CP Complaint

ID Part 574

MI Mfgr. Inquiry

MD Mfgr. Defect

# Footnotes

Labeling failures: No model designation, DOT symbol too small.

Labeling failures: No model designation, No date of manufacture, DOT symbol location too high.

Labeling failure: No model designation.

Labeling failure: Incomplete instructions to the purchaser.

Labeling failure: No model designation.

Penetration failure.

Labeling failure: Incomplete instructions to the purchaser.

Labeling failure: No model designation.

Labeling failure: No model designation.

Labeling failure: No date of manufacture.

Seat back height and surface area.

Owners manual doesn’t provide instructions for attaching a tether strap.