WPEC SG21: Assessment of Neutron Cross-Section Evaluations for the Bulk of Fission Products

59-Pr-142 Review

Pavel Oblozinsky, BNL, August 2003

### 1. General

### Properties: Unstable nucleus, half-life T1/2 = 19.12 h.

EXFOR data

Complete lack of experimental data.

### Evaluations

ENDF/B-VI	Year of origin 1974, by Schenter & Schmittroth (ORNL).

JEF-2	Year of origin 1982, taken from ENDF/B-V with some additions, charged particle production added from REAC-ECN-4 library, by Coordination Group.

BROND-2	None.

JENDL-3 	None.

CENDL-3	None.

### 2. Thermal and resonance region

For summary, see Table 1 and 2.

ENDF/B-VI

- No resonance parameters given (except of AP) due to complete lack of experimental data.

JEF-2

- As above.

Recommendation/Conclusion

ENDF/B-VI and JEF-2 are identical. ENDF/B-VI is recommended as original evaluation.

3. Fast neutron region

#### ENDF/B-VI methodology

- Dates back to 1974, evaluation taken over from ENDF/B-V.

- Simple statistical model, Moldauer OM parameterization.

##### JEF-2 methodology

- Taken over from ENDF/B-VI (1974 evaluation by Schenter & Schmittroth).

- Charged particle production from REAC-ECN-4 library.

Comparison of evaluations

- MT=1	 Complete lack of data, ENDF/B-VI has reasonable shape, JEF-2 is the same.

- MT= 4	 ENDF/B-VI looks somewhat unrealistic, but nothing better is available. JEF-2 is

the same.

- MT=16	 Not available.

- MT=102	 ENDF/B-VI has reasonable shape. JEF-2 is the same.

- MT=103	 Only JEF-2 available.

- MT=107	 Only JEF-2 available.

###### Recommendation/Conclusion

There is complete lack of experimental data. JEF-2 is more complete, though otherwise it is taken from ENDF/B-V. JEF-2 is recommended.

Table 1. Thermal cross sections, resonance integral and one-group capture values for Pr-142.

| Source | Total (barn) | Capture (barn) | Elastic (barn) | Resonance Capture Integral (barn) | One-group Capture (barn) [2] |
| --- | --- | --- | --- | --- | --- |
| ENDF/B-VI | 20.0 | 20.0 |  | 145.3 | 4.69E-1 |
| JEF-2 | 20.0 | 20.0 |  | 145.3 | 4.68E-1 |
| Mughabghab 2003 [1] |  | none |  |  |  |
| BNL-325 (1981) |  | 20 (3) |  |  |  |

Table 2. Summary of resolved and unresolved resonance region for Pr-142.

| Library | Year | First Author | RRR | URR | Remarks |
| --- | --- | --- | --- | --- | --- |
| ENDF/B-VI | 1974 | Schenter | None |  | No resonance parameters given. |
| JEF-2 | 1974 | Schenter | None |  | Taken from ENDF/B-V. |

#### References

- S.F. Mughabghab, Thermal neutron capture cross sections, resonance integrals and g-factors, Report INDC (NDS)-440 (IAEA, Vienna, February 2003).

- H. Gruppelaar et al, Status of pseudo-fission-product cross sections for fast reactors, Final Report of Subgroup 17, Report NEA/WPEC-17, ECN-R-98-014 (NEA, Paris, 1998). Recalculated systematically for all 211 FP and all 5 evaluated libraries by I. Sirakov (BNL, 2002), see http://www.nndc.bnl.gov/sg21/nucl/acs/accs.htm.