Ce-143

Reviewed by T. Nakagawa, JAERI, January 2003

1. Files

ENDF/B-VI:	Evaluation was made by Schenter et al. in 1974. Their data were carried over to ENDF/B-VI without any modifications.

JENDL-3.3:	No data are given.

JEFF-3.0: 	JEF-2.2 adopted the data of ENDF/B-V. The charged particle emission cross sections were included in 1989 adopting REAC-ECN-4. JEFF-3.0 is the same as JEF-2.2.

CENDL-3:	No data are given.

BROND-2:	No data are given.

2. Thermal and resonance region

The resonance parameters are summarized in Table 1.

ENDF/B-VI

No resonance parameters are given. The capture cross section at 0.0253 eV was taken from BNL-325 3rd edition [Mu73]. In the energy range up to 101.57 eV, the 1/v type cross section was assumed for the capture and a constant one for the elastic scattering.

JEFF-3.0

ENDF/B-V was adopted (same as ENDF/B-VI).

Thermal cross sections and resonance integral of capture cross section are listed in Table 2.

Recommendation/conclusion for the thermal and resonance region

ENDF/B-VI is recommended.

3. Fast neutron region

(1) Methodology

ENDF/B-VI

Theoretical calculation was performed using the optical potential parameters of Moldauer [Mo63]. Inelastic scattering cross sections were calculated with the COMNUC-3 code. No discrete levels were considered. The capture cross section was calculated with the NCAP code. No threshold reaction cross sections were given.

The angular distributions of all reactions were assumed to be isotropic in the laboratory system.

Evaporation spectra were given to the continuum inelastic scattering.

JEFF-3.0

Data were taken from ENDF/B-V. Charged particle emission cross sections were included from REAC-ECN-4 library.

(2) Total cross section (MT=1)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce143.htm#mt1

(3) Capture cross section (MT=102)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce143.htm#mt102

(4) Elastic scattering cross section (MT=2)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce143.htm#mt2

(5) Inelastic scattering cross section (MT=4, 51 – 91)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce143.htm#mt4

(6) (n,2n) reaction cross section (MT=16)

The cross section of (n,2n) reaction was not given in the both libraries.

(7) (n,p) reaction cross section (MT=103)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce143.htm#mt103

(8) (n,) reaction cross section (MT=107)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/Ce143.htm#mt107

(9) Other reactions

The following reaction cross sections are given:

ENDF/B-VI	no threshold reactions

JEFF-3.0	(n,d), (n,t), (n,3He), (n,2p)

Recommendation/conclusion for the fast energy region

JEFF-3.0 is recommended.

References

[Mo63]	Moldauer P.A.: Nucl. Phys., 47, 65 (1963).

[Mu73]	Mughabghab S.F. and Garber D.I.: BNL-325 3rd Edition (1973).

[Mu81]	Mughabghab S.F. et al.: Neutron Cross Sections, Vol. 1, Part A, Academic press (1981).

[Ro56]	Roy J.C. et al.: Can. J. Chem., 34, 1238 (1956).

Table 1  Summary for Resolved and Unresolved Resonance Region: Ce-143

-----------------------------------------------------------------------------------------------------------------

Library	RRP	URP	Remarks

-----------------------------------------------------------------------------------------------------------------

ENDF/B-VI	No RRP	No URP 	1/v region up to 101.57 eV

JEFF-3.0	No RRP	No URP

-----------------------------------------------------------------------------------------------------------------

Table 2  Thermal Cross Sections and Resonance Integral: Ce-143

Unit: barns

-----------------------------------------------------------------------------------------------------------------

Library/Experiment	Total	Elastic	Capture	Res.Integ.

-----------------------------------------------------------------------------------------------------------------

ENDF/B-VI	11.0	5.0	6.0	41.5

JEFF-3.0	11.0	5.0	6.0	41.5

Mughabghab et al. [Mu81]	--	--	6.0(0.7	--

Roy et al. [Ro56]			6.0(0.7*1

--------------------------------------------------------------------------------------------------------------

*1 average cross section in a reactor spectrum.