96E07/19/07

S156-96E.doc

Use on all projects

Section 156. - PUBLIC TRAFFIC

Construction Requirements

156.03  Accommodating Traffic During Work.  Delete the last two sentences of the first paragraph and substitute the following:

Submit situation-specific traffic control implementation drawings and alternate traffic control proposals according to Subsection 104.03 for acceptance at least 14 days before intended use.

156.04  Maintaining Roadways During Work.

(a) Add the following:

NOTE TO DESIGNER: Spell out exceptions here.

Do not construct detours outside of the clearing limits or use alternate route detours without the approval of the CO.

(c) Delete the text and substitute the following:

Snow removal to facilitate the work is the Contractor's responsibility.  Snow removal to provide public access is the responsibility of the maintaining agency and will be performed at the maintaining agency's discretion.  Allow the maintaining agency access to perform snow removal.

156.05  Maintaining Roadways During Non-Work Periods.  Delete the second sentence and substitute the following:

Snow removal to provide public access is the responsibility of the maintaining agency.

156.06  Limitations on Construction Operations.

NOTE TO DESIGNER: If long vehicles or tight curvature is anticipated, increase the minimum lane width for alternate one-way traffic control. If the existing roadway width is less than 22 feet, adjust minimums appropriately.

(d) Delete the first sentence and substitute the following:

For alternate one-way traffic control, provide a minimum lane width of 10 feet.  For two-way traffic, provide a minimum roadway width of 22 feet.

(j) Delete the text and substitute the following:

Limit construction-caused delays to public traffic to a maximum of 30 minutes per passage through the project except during the following times on Monday through Friday:

a.m. through           p.m.

p.m. through           p.m.

During the above times, allow traffic to pass through the construction without delay.

Add the following:

(k) Maintain existing guardrails and bridge railings until removal is necessary for construction.  Use a temporary barrier, or other appropriate shielding or warning devices, as directed by the CO, while the guardrails and bridge rails are absent.  Limit the length of area affected as directed by the CO.  Install new guardrails and bridge rails as soon as possible to minimize risk to the public.

On small jobs (i.e. ERFO, OMAD etc), check with the COE regarding the need for a traffic and safety supervisor that is separate from the Contractor’s Superintendent. If a separate traffic and safety supervisor is not needed, include the following paragraph:

156.08  Traffic and Safety Supervisor.

Delete the first paragraph and substitute the following:

Provide a traffic and safety supervisor who is certified by the State highway agency or other acceptable certification program.  Furnish the traffic safety supervisor’s name, address, and 24-hour telephone number(s) at the preconstruction conference.  At all times during the contract, including periods of suspensions and work stoppages, perform all of the following: