### ITEM F-161  WIRE FENCE WITH STEEL POSTS
(Classes C and D Fences)

DESCRIPTION

161-1.1  This item covers the requirements for furnishing materials and constructing new wire fences and gates with steel posts in accordance with the details included herein and as shown on the plans.  The class of fence to be erected shall be either Class C, woven wire fencing surmounted by two strands of barbed wire, or Class D, four strands of barbed wire, as indicated on the plans and in the bid proposal.

MATERIALS

161-2.1  WIRE.

a.  Woven Wire (Zinc-coated).  The woven wire fencing shall be 7-bar, 26-inch (66 cm) field fence with top and bottom wires No. 10 gauge, and filler and stay wires No. 12 1/2 gauge.  Stay wires shall be spaced 6 inches (150 mm) apart.  All wire shall be smooth galvanized steel wire conforming to ASTM A 121, Type B.  All wires shall be two-dip and spaced as shown on the plans.

b.  Barbed Wire (Zinc-coated).  Zinc-coated barbed wire shall be 2-strand twisted No. 12 1/2 gauge galvanized steel wire with 4-point barbs of No. 14 gauge galvanized steel wire.  All wire shall conform to ASTM A 121, Type A.  The barbs shall be spaced approximately 4 inches (100 mm) apart.

c.  Barbed Wire (Copper-covered).  Copper-covered steel barbed wire shall conform to ASTM A 121, Type A.

d.  Barbed Wire (Aluminum-coated).  Aluminum-coated steel barbed wire shall be 2-strand twisted No. 12 1/2 gauge.  The 4-point barbs of No. 14 gauge aluminum-coated steel wire shall be spaced approximately 5 inches (125 mm) apart.  The steel wire shall have a tensile strength of between 60,000 and 80,000 pounds per square inch (413 400 and 551 200 kPa) and the aluminum coating shall have a minimum weight of .30 ounce per square foot (0.07 kilogram per square meters) of wire surface on the No. 12 1/2 gauge line wire and .25 ounce per square foot (0.06 kg/square meter) of wire surface on the No. 14 gauge barbs.

e.  Bracing Wire (Zinc-coated).  Wire used for cable for bracing shall be No. 9 smooth galvanized soft wire.

161-2.2   FENCE POSTS, GATES, RAILS, BRACES, AND ACCESSORIES.  These items, when specified, shall conform to the requirements of Fed. Spec. RR-F-191 and shall be zinc-coated.

161-2.3  CONCRETE.  Concrete shall be of a commercial grade with a minimum 28-day compressive strength of 2500 psi.

CONSTRUCTION METHODS

161-3.1  GENERAL.  The fence shall be constructed in accordance with the details on the plans and as specified herein using new materials, and all work shall be performed in a workmanlike manner satisfactory to the Engineer.  Prior to the beginning of the work or upon the request of the Contractor, the Engineer shall locate the position of the work by establishing and marking the property line or fence line.  When directed, the Contractor shall span the opening below the fence with barbed wire fastened to stakes of the required length at locations of small natural or drainage ditches where it is not practical to conform the fence to the general contour of the ground surface.  The new fence shall be permanently tied to the terminals of existing fences whenever required by the Engineer.  The finished fence shall be plumb, taut, true to line and ground contour, and complete in every detail.  When directed, the Contractor shall stake down the woven wire fence at several points between posts.

When directed, in order to keep stock on adjoining property enclosed at all times, the Contractor shall arrange the work so that construction of the new fence will immediately follow the removal of existing fences.  The length of unfenced section at any time shall not exceed 300 feet (90 m) or such length that the stock can be kept in the proper field.  The work shall progress in this manner and at the close of the working day the newly constructed fence shall be tied to the existing fence.  Any openings in the fence shall be guarded when stock is using the adjoining property.

161-3.2  CLEARING FENCE LINE.  The site of the fence shall be sufficiently cleared of obstructions, and surface irregularities shall be graded so that the fence will conform to the general contour of the ground.  The fence line shall be cleared to a minimum width of 2 feet (60 cm) on each side of the centerline of the fence.  This clearing shall consist of the removal of all stumps, brush, rocks, trees, or other obstructions that will interfere with proper construction of the fence.  Stumps within the cleared area of the fence shall be placed a uniform distance above ground, as specified in the plans.  When shown on the plans or as directed by the Engineer, the existing fences which coincide with, or are in a position to interfere with, the new fence location shall be removed by the Contractor as a part of the construction work unless such removal is listed as a separate item in the bid schedule.  All holes remaining after post and stump removal shall be refilled with suitable soil, gravel, or other material acceptable to the Engineer and shall be compacted properly with tampers.

The work shall include the handling and disposal of all material cleared, excavated or removed, regardless of the type, character, composition, or condition of such material encountered.

161-3.3  INSTALLING POSTS.  All posts shall be spaced as shown on the plans.  Corner, brace, anchor, end, and gate posts shall be set in concrete bases as shown on the plans.  The top of the base shall be slightly above the ground surface, trowel finished, and sloped to drain.  Holes of full depth and size for the concrete bases for posts shall be provided even if blasting of rock or other obstructions is necessary.  All line posts may be either driven or set in dug holes to a penetration of 3 feet (90 cm).  All post setting shall be done carefully and to true alignment.  Dirt removed for placing posts, anchor bars, flanges, etc., shall be replaced, tamped, and leveled.  When posts are driven, care shall be exercised to prevent marring or buckling of the posts.  Damaged posts shall be replaced at the Contractor's expense.  No extra compensation will be made for rock excavation.  Rock excavation shall not be grounds for extension of time.

161-3.4  BRACING.  All corner, anchor, end, and gate posts shall be braced as shown on the plans.  Anchor posts shall be set at approximately 500-foot (150 meters) intervals and braced to the adjacent posts.

161-3.5  INSTALLING WIRE.  All barbed wire and woven wire shall be placed on the side of the post away from the airport, or as directed, at the height indicated on the plans.  The woven wire shall be carefully stretched and hung without sag and with true alignment.  Care shall be taken not to stretch the wire so tightly that it will break in cold weather or pull up corner and brace posts.  All horizontal wires shall be fastened securely to each post by fasteners or clips designed for use with the posts furnished.  The woven wire shall be wrapped around end, corner, and gate posts, and the ends of all horizontal wires shall be tied with snug, tight twists.  The wire shall be secured to prevent slipping up and down the post.  Barbed wire strands shall be stretched and each strand secured to each post to prevent slipping out of line or becoming loose.  At end, corner, and gate posts the barbed wire shall be securely wrapped and anchored once about the post from outside and secured against slipping by tying the ends with snug, tight twists.  However, on spans of less than 100 feet (30 m) both ends of the span need not be wrapped around the posts.  The bottom wire of the woven wire fencing shall clear the ground by not more than 4 inches (100 mm) or less than 1 inch (25 mm) at any place.

161-3.6  SPLICING WIRE.  Splices in barbed and woven wire will be permitted if made with an approved galvanized bolt-clamp splice or a wire splice made as follows:  The ends of each wire shall be carried 3 inches (75 mm) past the splice tool and wrapped around the other wire for at least six turns in opposite directions.  After the tool is removed, the space occupied by it shall be closed by pulling the ends together.  The unused ends of the wire shall be cut close to make a neat, workmanlike job.

161-3.7  INSTALLING GATES.  The gates shall be hung on gate fittings as shown on the plans.  They shall be attached in such a manner that the gate cannot be lifted off the hinges.  Gates shall be erected to swing in the direction indicated and shall be provided with gate stops, as specified or as shown on the plans.  Gates shall be erected at locations shown on the plans.

161-3.8  EXISTING FENCE CONNECTIONS.  Wherever the new fence joins an existing fence, either at a corner or at the intersection of straight fence lines, a corner or anchor post shall be set at the junction and braced and anchored the same as herein described for corner posts.

If the connection is made at other than the corner of the new fence, the last span of the old fence shall contain a brace span.

161-3.9  CLEANING UP.  The Contractor shall remove from the vicinity of the completed work all tools, buildings, equipment, etc., used during construction.

METHOD OF MEASUREMENT

161-4.1  Fences, Class C (Steel Posts), or Class D (Steel Posts), shall be measured in place from outside to outside of end posts or corner posts and shall be the length of fence actually constructed, except for the space occupied by the gates.

Driveway gates and walkway gates shall be measured in units for each gate installed and accepted.

BASIS OF PAYMENT

161-5.1  Payment shall be made at the contract unit price per linear foot (meter) for Class C or Class D wire fence.  This price shall be full compensation for furnishing all materials and for all preparation, erection, and installation of these materials, and for all labor, equipment, tools, and incidentals necessary to complete the item.

Payment will be made at the contract unit price per each for driveway or for walkway gates.  This price shall be full compensation for furnishing all materials and for all preparation, erection, and installation of these materials, and for all labor, equipment, tools, and incidentals necessary to complete the item.

Payment will be made under:

Item F-161-5.1	Fence, Class C—per linear foot (meter)

Item F-161-5.2	Fence, Class D—per linear foot (meter)

Item F-161-5.3	Driveway Gates—per each

Item F-161-5.4	Walkway Gates—per each

MATERIAL REQUIREMENTS

ASTM A 121	Standard Specification for Zinc Coated (Galvanized) Steel Barbed Wire

FED SPEC	Fencing, Wire, and Post, Metal

RR-F-191/Gen

END OF ITEM F-161

Intentionally Left Blank