WPEC SG 21: Assessment of Neutron Cross-Section Evaluations for the Bulk of Fission Products

Dy-161

Reviewed by Shen Qingbiao CIAE, February, 2003

1. Files

ENDF/B-VI: 	Evaluation was made in 1974 for ENDF/B-V. It was converted to ENDF/B-VI in 1990. The new/modified ENDF/B-VI evaluation was made in 1998 in which the resonance parameters and the smooth cross sections for MF=3, MT=1,2,102 were modified.

JEF-2.2:	ENDF/B-V was adopted. The resonance parameters were changed from SLBW to MLBW in 1988.. The data were compiled in 1992.

Figs: http://www.nndc.bnl.gov/~sirakov/fp/fp21/htm/Dy161.htm#mt1

2. Thermal and resonance region

(1) Resolved resonance parameters

ENDF/B-VI (1.0e-5 eV – 1.0 keV)

The number of resolved resonances is 254. The resonance parameters are taken from Mughabghab [Mu84].

JEF-2.2 (1.0e-5 eV – 0.067641 keV)

The multi level Breit-Wigner resonance parameters were used.

(2) Unresolved resonance parameters

ENDF/B-VI (1.0 – 10 keV)

The unresolved resonance parameters are based on Mughabghab [Mu84] and [RIPL98].

JEF-2.2

No unresolved resonance parameters are given.

(3) Recommendation/conclusion for resonance region

ENDF/B-VI is recommended.

3. Fast neutron region

(1) Methodology

ENDF/B-VI

Theoretical calculation was widely used. The optical potential of Moldauer was adopted.

Inelastic scattering was calculated with COMNUC-3 code, and the capture cross section with

NCAP code. No direct inelastic was considered. No threshold reaction cross sections are given.

Isotropic distributions were given to the elastic and inelastic scattering.

Evaporation spectra were given to the continuum inelastic scattering.

JEF-2.2

ENDF/B-V data were adopted.

(2) Total cross section (MT=1)

The total cross sections of ENDF/B-VI pass through the only experimental data at around 14 MeV. The shape of the total CS of JEF2.2 is not good compared with the experimental data of natural element (see 66-Dy 164 review).

(3) Capture cross section (MT=102)

The capture cross sections of both ENDF/B-VI and JEF2.2 are in good agreement with the experimental data.

(4) Elastic scattering cross section (MT=2)

This cross section was obtained as (total cross section) – (sum of partial cross sections) in the all

libraries.

(5) Inelastic scattering cross section (MT=4, 51 – 91)

Excited levels considered in the files.

ENDF/B-VI 	  7 levels up to 0.201 MeV

JEF-2.2 	 7 levels up to 0.201 MeV

No experimental data of total inelastic scattering cross section are available. Only ENDF/B-VI (JEF2.2) can be chosen. Its shape in high energy region is wrong since no (n,2n) cross sections are given..

(6) (n,2n) reaction cross section (MT=16)

No (n,2n) cross sections are given for ENDF/B-VI (JEF2.2).

(7) (n,p) reaction cross section (MT=103)

No (n,p) cross sections are given for ENDF/B-VI (JEF2.2).

(8) (n,() reaction cross section (MT=107)

No (n, () cross sections are given for ENDF/B-VI (JEF2.2).

(9) Other reactions

The following other reaction cross sections are given in the files.

JEF-2.2  no

ENDF/B-VI  no

(10) Recommendation/conclusions for fast neutron region

ENDF/B-VI is recommended. But it has no threshold reaction cross sections and some reaction cross sections are not good. It needs to be improved evidently. By the way the file of ENDF/B-VI lost the last line with ‘-1’.

References

[Da64] Danelyan L. S. et al., J, AE, 16(1), 56 (1964).

[Ho58] House L. et al., J, BAP, 3, 337(R6) (1958).

[Lu77] Lucas M. et al., C, 77Paris, 1, 431 (1977), IAEA-Publ., 475

[Mu84]	Mughabghab S.F. et al.: “Neutron Cross Sections, Vol.1, Part B,” Academic Press (1984)

[RIPL98]. ’Reference Input Parameter Library’, IAEA-TECDOC-1034, 1998.

[Sc66] Scoville J. J., J, NSE, 25, 12 (1966).

[Ve71] Vertebnyj V. P. et al., P, YFI-11, 59 (1971).

[Wa56] Walker W. H., T, Walker 1956

Table 1. Summary for Resolved and Unresolved Resonance Region: Dy-161-

-----------------------------------------------------------------------------------------------------------------

Library	RRP	URP	Remarks

-----------------------------------------------------------------------------------------------------------------

ENDF/B-VI	1.0 keV	10 keV

JEF-2.2	0.067641 keV	No URP

-----------------------------------------------------------------------------------------------------------------

Table 2. Thermal Cross Sections and Resonance Integral: Dy-161

-----------------------------------------------------------------------------------------------------------------

Library/Experiment 	Total 	Elastic 	Capture	Res.Integ.

-----------------------------------------------------------------------------------------------------------------

ENDF/B-VI 	616.849	16.5479	600.301 	1085.31

JEF-2.2 	608.845	23.7313	585.113 	1214.91

Mughabghab et al. [Mu84] 		16.51.5	6005	1200100

Scoville et al. [Sc66] 			58395*1 	1670167

Lucas et al. [Lu77] 			510	1150

Vertebnyj et al. [Ve71] 	67716	221	65516

House et al. [Ho58] 			58050*1

Walker [Wa56] 			59050*2

Danelyan et al. [Da64] 			61740

----------------------------------------------------------------------------------------------------------------

*1) Maxwellian averaged

*2) Spectrum averaged

Attachment 2

Figs: http://www.nndc.bnl.gov/~sirakov/fp/fp21/htm/Dy161.htm#mt1