WPEC SG 21: Assessment of Neutron Cross-Section Evaluations for the Bulk of Fission Products

Dy-162

Reviewed by Shen Qingbiao CIAE, February, 2003

1. Files

ENDF/B-VI: 	Evaluation was made in 1974 for ENDF/B-V. It was converted to ENDF/B-VI in 1990. The new/modified ENDF/B-VI evaluation was made in 1998 in which the resonance parameters and the smooth cross sections for MF=3, MT=1,2,102 were modified.

JEF-2.2:	ENDF/B-V was adopted. The resonance parameters were changed from SLBW to MLBW in 1988.. The data were compiled in 1992.

Figs: http://www.nndc.bnl.gov/~sirakov/fp/fp21/htm/Dy162.htm#mt1

2. Thermal and resonance region

(1) Resolved resonance parameters

ENDF/B-VI (1.0e-5 eV – 12.2 keV)

The number of resolved resonances is 142. The resonance parameters are taken from Mughabghab [Mu84].

JEF-2.2 (1.0e-5 eV – 0.43021 keV)

The multi level Breit-Wigner resonance parameters were used.

(2) Unresolved resonance parameters

ENDF/B-VI (12.2 – 50 keV)

The unresolved resonance parameters are based on Mughabghab [Mu84] and [RIPL98].

JEF-2.2

No unresolved resonance parameters are given.

(3) Recommendation/conclusion for resonance region

ENDF/B-VI or JEF-2.2 is recommended. The thermal scattering cross section of ENDF/B-VI is too small than the measured or evaluated value. And JEF-2.2 has no unresolved resonance parameters.

3. Fast neutron region

(1) Methodology

ENDF/B-VI

Theoretical calculation was widely used. The optical potential of Moldauer was adopted.

Inelastic scattering was calculated with COMNUC-3 code, and the capture cross section with

NCAP code. No direct inelastic was considered. No threshold reaction cross sections are given.

Isotropic distributions were given to the elastic and inelastic scattering.

Evaporation spectra were given to the continuum inelastic scattering.

JEF-2.2

ENDF/B-V data were adopted.

(2) Total cross section (MT=1)

The total cross sections of ENDF/B-VI pass through the only experimental data at around 14 MeV. The shape of the total CS of JEF2.2 is not good compared with the experimental data of natural element (see 66-Dy 164 review).

(3) Capture cross section (MT=102)

The values of ENDF/B-VI are in better agreement with the experimental data. The values of JEF2.2 are too high.

(4) Elastic scattering cross section (MT=2)

This cross section was obtained as (total cross section) – (sum of partial cross sections) in the all

libraries.

(5) Inelastic scattering cross section (MT=4, 51 – 91)

Excited levels considered in the files.

ENDF/B-VI 	  6 levels up to 1.5901 MeV

JEF-2.2 	 6 levels up to 1.5901 MeV

No experimental data of total inelastic scattering cross section are available. Only ENDF/B-VI (JEF2.2) can be chosen. Its shape in low energy region is not smooth and the shape in high energy region is wrong since no (n,2n) cross sections are given..

(6) (n,2n) reaction cross section (MT=16)

No (n,2n) cross sections are given for ENDF/B-VI (JEF2.2).

(7) (n,p) reaction cross section (MT=103)

No (n,p) cross sections are given for ENDF/B-VI (JEF2.2).

(8) (n,() reaction cross section (MT=107)

No (n, () cross sections are given for ENDF/B-VI (JEF2.2).

(9) Other reactions

The following other reaction cross sections are given in the files.

JEF-2.2  no

ENDF/B-VI  no

(10) Recommendation/conclusions for fast neutron region

ENDF/B-VI is recommended. But it has no threshold reaction cross sections and some reaction cross sections are not good. It needs to be improved evidently.

References

[Da64] Danelyan L. S. et al., J, AE, 16(1), 56 (1964).

[Ho58] House L. et al., J, BAP, 3, 337(R6) (1958).

[Lu77] Lucas M. et al., C, 77Paris, 1, 431 (1977), IAEA-Publ., 475

[Mu84]	Mughabghab S.F. et al.: “Neutron Cross Sections, Vol.1, Part B,” Academic Press (1984)

[RIPL98]. ’Reference Input Parameter Library’, IAEA-TECDOC-1034, 1998.

[Sc66] Scoville J. J., J, NSE, 25, 12 (1966).

[Ve71] Vertebnyj V. P. et al., P, YFI-11, 59 (1971).

[Wa56] Walker W. H., T, Walker 1956

Table 1. Summary for Resolved and Unresolved Resonance Region: Dy-162

-----------------------------------------------------------------------------------------------------------------

Library	RRP	URP	Remarks

-----------------------------------------------------------------------------------------------------------------

ENDF/B-VI	12.2 keV	50 keV

JEF-2.2	0.43021 keV	No URP

-----------------------------------------------------------------------------------------------------------------

Table 2. Thermal Cross Sections and Resonance Integral: Dy-162

-----------------------------------------------------------------------------------------------------------------

Library/Experiment 	Total 	Elastic 	Capture	Res.Integ.

-----------------------------------------------------------------------------------------------------------------

ENDF/B-VI 	193.794	0.0123477	193.782 	2745.35

JEF-2.2 	199.372	0.229401	199.142 	2777.65

Mughabghab et al. [Mu84] 		0.280.20	19410	2755270

Scoville et al. [Sc66] 			15227*1 	3325400

Lucas et al. [Lu77] 			245	2350

Vertebnyj et al. [Ve71] 	17211	2.50.8	17011

House et al. [Ho58] 			14040*1

Walker [Wa56] 			24020*2

Danelyan et al. [Da64] 			21516

----------------------------------------------------------------------------------------------------------------

*1) Maxwellian averaged

*2) Spectrum averaged

Attachment 2

Figs: http://www.nndc.bnl.gov/~sirakov/fp/fp21/htm/Dy162.htm#mt1