6.4

01-05

aj

aj - Ground Rod and Pipe Clamps

Station Installations (Indoors Only)

Manufacturer	Catalog Number

This conductor:	.162" (#6 AWG) Copper	.102" (#10 AWG) Copper	 .081" (#12 AWG) Copper

Connected to:	   Pipe Ground	  Pipe Ground	  Pipe Ground

(Copper or Steel)	(Copper or Steel)	(Copper or Steel)

5/8"-1-1/4" O.D. 	  5/8"-1-1/4" O.D. 	5/8"-1-1/4" O.D.

Electric Motion		EM5507		EM5507		EM5507

EM5517(3)		EM5517(3)		EM5517(3)

Reliable		13(1)		13(1)		13(1)

--		1(1)(2)		1(1)(2)

Notes:	(1)Smallest size pipe this clamp can be used on is 3/4".

(2)Can only be used on copper pipe.

(3)Can accommodate one #6 to #14 AWG and one #10 to #14 AWG copper conductor.

6.4.1

01-31-2008

aj

aj - Ground Rod and Pipe Clamps

Station Installations (Outdoors)

Manufacturer	Catalog Number

.081" (#12 AWG), .102" (#10 AWG) and .162" (#6 AWG) Copper

Ground Rod (Galvanized Steel)	Ground Rod (Copper-Covered Steel)

Connected to:	      1/2"    	      5/8"    	      1/2"    	      5/8"

H. L. Boggs	CR-1, M2009(1)	CR-1, M2012(4)	CR-1, 2009(1)	CR-1, M2012(4)

Burndy	GRC12(1)	        --	GRC12(1)	        --

Connector Castings(1)	        --	        --	G-4	G-5

Electric Motion	EM5507	EM5507	EM5507	EM5507

EM5517(3)	EM5517(3)	EM5517(3)	EM5517(3)

EM1DB	EM2DB	EM1DB	EM2DB

EM4DB(1)(8)	EM4DB(1)(8)	EM4DB(1)(8)	EM4DB(1)(8)

Erico, Inc	GR1-141G(1)(2)	GR1-161G(1)(2)	GR1-141G(1)(2)	GR1-161G(1)(2)

GR1-141A(1)(2)	GR1-161A(1)(2)	GR1-141A(1)(2)	GR1-161A(1)(2)

CP58	CP58	CP58	CP58

EHL58C1G(4)

Galvan	G4P(1)	G5P(1)	G4(1)	G5(1)

Joslyn	        --	        --	J8491	J8492(4)

Penn-Union	CEB-1-TN(4)	CEB-2-TN(4)	CEB-1(4)	CEB-2(4)

Thomas & Betts	        --	        --		--	DGC58-66(4)

Tyco Electronics	1-83017-1(5)	1-83017-3(5)	1-81713-1(5)	1-81713-3(6)

83017-5(4)	83017-2(4)		81713-5(4)	1-81713-2(7)

--	        --		--		81713-1(4)

81405-1		81406-1

Notes:

(1)Accepted only for use with 0.102" (#10 AWG) and 0.162" (#6 AWG) wire.

(2)Includes disposable mold.

(3)Can accommodate one #6 to #14 AWG and one #10 to #14 AWG copper conductor.

(4)Accepted only for use with .162" (#6 AWG) wire.

(5)Accepted only for use with 0.102" (#10 AWG) or 0.081" (#12 AWG) wire.

(6)Accepted only for use with 0.102" (#10 AWG) wire.

(7)Accepted only for use with 0.081" (#12 AWG) wire.

(8)Can be used on a ground that is already occupied by another ground rod clamp on top.