Solar Orbiter

Visible Imager / Magnetograph (VIM)

Optical Concept

Oskar von der Lühe1, Wolfgang Schmidt1, Achim Gandorfer2, and Valentin Martínez Pillet3

- Kiepenheuer-Institut für Sonnenphysik, Freiburg, Germany

- Institut für Astronomie, Eidgenössische Technische Hochschule, Zürich, Switzerland

- Instituto de Astrofísica de Canarias, La Laguna, Tenerife, Spain

June 2000

# Introduction

We describe the optical layout for the Visible Imager and Magnetograph (VIM) for the Solar Orbiter Mission, based on a filtergraph concept which includes a double Fabry-Pérot interferometer. The optics consists of three subsystems:

- 25 cm High Resolution Telescope (HRT)

- 5 cm Full Disk Telescope (FDT)

- Filtergraph Optics (FO)

The two telescopes, HRT and FDT, deliver an image of the sun at a common telescope focal plane. The FO produces a magnified image of the telescope focus on the instrument's only detector. While the HRT provides an image with a high resolution at its diffraction limit, the FDT adjusts its focal length such as to fill the detector with the solar disk. The filtergraph optics include a double Fabry-Pérot interferometer equipped with a narrow-band interference filter as a prefilter, tuned to the Fe I 630.2 nm line. This filtergraph is easily adjusted to the lineshifts which occur due to sun-spacecraft relative velocities up to 40 km s-1. We describe all components in the following sections.

# High Resolution Telescope

## General Decription

The HRT is a 250 mm diameter Gregorian reflector. It provides an image with a spatial resolution as high as 75 km on the solar surface during the near-Sun orbital phase. A polarisation modulator is foreseen in the optical path behind the main mirror in the F/17 beam and before the first oblique reflection.

Figure 1 shows an annotated perspective view of the HRT and FO. Table 1 presents the main characteristics of the HRT, Appendix A shows the surface design data. The results of a wavefront analysis of the design is shown in Appendix C.

## Thermal Control

The HRT will have to withstand the heat load during the near-Sun orbital phases. The primary mirror will be made from SiC and passively cooled to dispose off the approximately 170W of radiation which is absorbed in its reflective layer. SiC enjoys better static and dynamic thermal stability than other mirror blank materials.

We consider the following two concepts for disposing off the remaining heat load:

### Prefilter

A broad-band interference prefilter covers the entire telescope and reflects most of the incident sunlight, with the exception of the spectral range of interest. This makes a field stop at the primary focus unnecessary. A combination of decentering and tilt of the secondary mirror provides independent telescope pointing on the solar disk without affecting the image quality. Baffling at the focus and at intermediate pupils rejects remaining sunlight.

The prefilter must be of excellent optical quality. For reasons of weight savings, a pellicle filter should be preferred. The feasibility of such a filter needs further study.

### Primary Field Stop

The Gregorian design permits rejecting 96% of the incident radiation at its primary focus with a field stop. The field stop is an inclined mirror with a 2 mm central hole which transmits the observed field. The reflected light is directed out of the spacecraft.

The field stop will also absorb about 170 W which will require passive cooling.

A broadband interference filter will be included after M2 to reduce the amount of light in the filtergraph optics.

Figure 1: perspective view of the optical layout of high resolution telescope and filtergraph.

| Primary diameter [mm] | 250 |
| --- | --- |
| Primary focal length [mm] | 500 |
| Primary F ratio | F/2 |
| Solar image at primary focus [mm] at 1 AU at 0.7 AU at 0.22 AU | 4.7 6.7 21.1 |
| Secondary diameter [mm] | 80 |
| Secondary focal length [mm] | 134.2 |
| Secondary conic constant | -0.622684 |
| Secondary magnification | 8.5 |
| Secondary field diameter [mm] | 10.2 |
| Effective focal length [mm] | 4250 |
| Field of view [arcsec] | 500 |
| Image scale at secondary focus [Mm / mm] at 1 AU at 0.7 AU at 0.22 AU | 35672 24970 7848 |

Table 1: High Resolution Telescope characteristics.

# Full Disk Telescope

It is impractical to combine the functions of full-disk and high resolution viewing of the sun into a single telescope. Therefore, a separate telescope will provide a full disk image at the same position as the secondary image of the HRT. The filtergraph is therefore shared by both telescopes. A folding mirror which delivers the FDT image is movable and can be inserted into the optical path of the HRT. The mechanism will be such that the mirror will be removed from the optical beam in the case of a mechanism failure, the high resolution function will therefore have precedence.

The FDT consists of a refractor with a focal length which varies between 233 mm and 888 mm. The telescope provides a full-disk image of the Sun of constant diameter on the detector during all orbital phases between 0.22 and 0.9 AU. The zoom lens consists of a classical afocal PNP triplet followed by a fixed aperture stop and a camera lens which provides a focus at a fixed position. All lenses will be singlets as chromatic aberration is not a concern with the narrow-band filtergraph. A mechanism which drives the middle lens of the triplet and the camera lens provides the zoom function. The diameter of the entrance pupil varies between 20 mm and 50 mm as the focal length increases, resulting in a diffraction limited sampling of the detector at all distances from the sun. The optical design is diffraction limited for all settings of the focal length.

An interference filter at the entrance aperture reflects most of the incident sunlight so that the radiation load is not a problem for the FDT.

Figure 2 shows the annotated optical layout of the FDT from a similar point of view as the HRT in Figure 1. Note that the layout is "horizontal" (in the XZ plane) compared to the vertical (YZ plane) layout of the HRT proper. A separate modulator is necessary for the FDT in order to perform polarisation modulation within the centered optical path before the first oblique reflection. The surface design data of the FDT are given in Appendix A. The results of a wavefront analysis of the design is shown in Appendix C.

Figure 2: perspective view of the optical layout of one of seven configurations of the full disk telescope. Drawings of all configurations are shown in Appendix B.

| Entrance Pupil diameter [mm] | 20 ... 50 |
| --- | --- |
| Objective focal length [mm] | 233 ... 888 |
| Objective F ratio | F/11 ... F/18 |
| Solar image diameter at primary focus [mm] | 10 |
| Field of view [°] | 0.64 ... 2.46 |

Table 2: Full Disk Telescope characteristics.

Figure 3: arrangement of filtergraph optics.

# Filtergraph Optics

The FO consists of two singlet lenses which combine the functions of collimator and camera with a 1:2 magnification. A system of two off-axis ellipsoid and paraboloid mirrors provide a 1:1 pupil relay function and produce an F/66 telecentric intermediate image plane.

Two 50 mm diameter Fabry-Pérot etalons at the telecentric image plane provide the required spectral resolution of typically 5 pm. One etalon will provide the spectral resolution while the other blocks the secondary transmission maxima of the first. A separate interference filter with a 1 nm band blocks the secondary transmission maxima of the combined etalons.

We consider using two solid state etalons with fixed resonator widths which are mounted on a common rotating stage for fine tuning. About (1 degree of rotation angle is required for a shift of the passband of (100 pm, which is sufficient to cover both line width and sun-spacecraft velocity shifts.

As an alternative we consider variable gap width etalons which are electronically controlled to provide spectral scanning. This principle is the one which is used in the TESOS filtergraph which operates at the Vacuum Tower Telescope of the Kiepenheuer-Institut on Tenerife.

Figure 3 shows a plane view of the filtergraph optics. The position of the etalons in the telecentric beam is indicated. The design data are given in Appendix A and results of a wavefront analysis of the design is shown in Appendix C.

# Overall Configuration

The combination of all optical subsystems is shown in

Figure 4. The HRT is the large cylinder on top of the Y and Z views. The FDT is to the lower left of the Z view and near the bottom of the X view. The FO are to the lower left of the Z view and near the top of the X view.

The overall envelope of the optics is 250 mm x 400 mm x 1100 mm.

Figure 4: plan views (top left: Y, top right: Z, bottom: X) of the combined VIM. The HRT is arranged above the FDT and the FO, both of which are mounted on a common optical bench.

Appendix A: VIM optical Design Data

Solar Orbiter Magnetograph - High Resolution Telescope

SRF      RADIUS      THICKNESS   APERTURE RADIUS   GLASS  NOTE

OBJ       --        1.4900e+14    1.7944e+11         AIR  Solar Surface at 1 AU

AST       --        700.000000    125.000000         AIR  Entrance aperture

2   -1.0000e+03   -500.000000    125.842994        REFL  Main Mirror

3        --       -150.000000      0.602139         AIR  Primary Focus

4    268.422000    150.000000     38.029882        REFL  Secondary Mirror

5        --        500.000000     33.222977         AIR  Primary Focus on return beam

6        --        100.000000     20.732507         AIR  Primary Mirror on Return beam

7        --         50.000000     25.000000         BK7  Modulator

8        --         50.000000     25.000000         AIR

9        --            --         16.161891         AIR

10        --            --         16.161891        REFL  Folding Mirror 1

11        --       -200.000000     16.161891         AIR

12        --            --         11.165703         AIR

13        --            --         11.165703        REFL  Folding Mirror 2

14        --        242.078619     11.165703         AIR

15        --        100.000000      5.118352         AIR  Intermediate focus

CONIC AND POLYNOMIAL ASPHERIC DATA

SRF        CC          AD          AE          AF          AG

2      -1.000000      --          --          --          --

4      -0.622684      --          --          --          --

Solar Orbiter Magnetograph - Full Disk Telescope (Configuration 2)

SRF      RADIUS      THICKNESS   APERTURE RADIUS   GLASS   NOTE

OBJ       --        1.4900e+14    2.6320e+12         AIR   Solar Surface at 1 AU

1        --        400.000000     21.306463         AIR   Entrance aperture

2    442.581348      8.000000     40.000000         BK7   | Objective 1

3   -931.218609        --         40.000000         AIR   |

4        --         50.000000     14.059882         AIR   Variable space 1

5   -205.814311      5.000000     25.000000         BK7   | Zoom lens (movable)

6    194.505175        --         25.000000         AIR   |

7        --        250.000000     11.919031         AIR   Variable space 2

8    2.5108e+03      8.000000     25.000000         BK7   | Objective 2

9   -340.708620        --         25.000000         AIR   |

10        --         20.000000     16.874896         AIR

AST       --         61.711000     22.000000         AIR   Aperture stop

12    271.213023     10.000000     25.000000         BK7   | Imaging lens (movable)

13   -1.8478e+03        --         25.000000         AIR   |

14        --         88.289000     17.266174         AIR

15        --         20.000000     22.000000         BK7   Modulator

16        --         60.000000     22.000000         AIR

17        --            --         13.037993         AIR

18        --            --         13.037993        REFL   First folding mirror

19        --       -100.000000     13.037993         AIR

20        --            --         10.419743         AIR

21        --            --         10.419743        REFL   Second folding mirror

22        --        100.000000     10.419743         AIR

23        --        106.700000      7.801492         AIR   Image plane

IMS       --            --          5.007819

GROUP THICKNESSES AND AIR SPACES FOR ZOOMING SYSTEMS

Group 1 consists of surf  2 to  4   Thickness =    8.000000

Group 2 consists of surf  5 to  7   Thickness =    5.000000

Group 3 consists of surf  8 to 11   Thickness =   28.000000

Group 4 consists of surf 12 to 14   Thickness =   10.000000

CFG  OBJ<->GRP1  GRP1<->GRP2  GRP2<->GRP3  GRP3<->GRP4  GRP4<->GRP5

1     1.490e+14      10.0000     290.0000      80.0000      70.0000

2     1.490e+14      50.0000     250.0000      61.7110      88.2890

3     1.490e+14     100.0000     200.0000      37.5000     112.5000

4     1.490e+14     150.0000     150.0000      15.8000     134.2000

5     1.490e+14     200.0000     100.0000       7.8400     142.1600

6     1.490e+14     250.0000      50.0000      32.7210     117.2790

7     1.490e+14     290.0000      10.0000      87.3850      62.6150

MAGNIFICATION      CFG1       CFG2       CFG3       CFG4       CFG5       CFG6       CFG7

GRP1 -3.916e-12 -3.916e-12 -3.916e-12 -3.916e-12 -3.916e-12 -3.916e-12 -3.916e-12

GRP2    -0.5155    -0.5771    -0.6784    -0.8228    -1.0453    -1.4326    -2.0364

GRP3   -92.4215    26.7474    11.1628     7.8442     7.1690    10.3293   -28.7577

GRP4     0.0084    -0.0314    -0.0833    -0.1289    -0.1453    -0.0914     0.0260

POWER       EFL        FNP        SNP         FF         BF

GRP1     0.0017   583.4775     1.7043    -3.5860  -581.7731   579.8914

GRP2    -0.0052  -193.2866     1.6894    -1.5966   194.9760  -194.8831

GRP3     0.0017   582.8782     4.6535   -20.6315  -578.2247   562.2467

GRP4     0.0022   459.8018     0.8461    -5.7644  -458.9557   454.0374

IMAGE  EFFECTIVE   INFINITY      IMAGE      FIELD

CFG      EFL   DISTANCE        f/#        f/#     HEIGHT      ANGLE          MAG

1   233.2185   106.7000    11.6609    11.6609     4.9975     1.2282   -1.565e-12

2   283.0539   106.7000    14.1527    14.1527     4.9973     1.0120   -1.900e-12

3   367.8664   106.7000    12.2622    12.2622     5.0008     0.7787   -2.469e-12

4   485.4600   106.7000    12.1365    12.1365     5.0074     0.5901   -3.258e-12

5   635.1369   106.7000    14.4349    14.4349     5.0115     0.4510   -4.263e-12

6   788.9404   106.7000    16.4363    16.4363     5.0105     0.3631   -5.295e-12

7   887.8449   106.7000    17.7569    17.7569     5.0038     0.3227   -5.959e-12

Solar Orbiter Magnetograph - Filtergraph Optics

SRF      RADIUS      THICKNESS   APERTURE RADIUS   GLASS  NOTE

15        --        100.000000      4.973212         AIR  Intermediate focus

16    165.103614     5.000000     15.000000         BK7  | Collimator Lens

17    -77.429158    110.788664     15.000000         AIR

18        --        400.000000      3.022085         AIR  Pupil 1

19   -800.000000   -400.000000     22.433712        REFL  Off-axis paraboloid 1

20        --       -400.000000     19.411627         AIR  Telecentric image plane

21    800.000000        --         22.329705        REFL  Off-axis paraboloid 2

22        --        400.000000     22.329705         AIR

23        --        189.211336      3.022085         AIR

24    239.644089      5.000000     15.000000         BK7 | Camera Lens

25   -190.995523        --         15.000000         AIR |

26        --          1.931746     10.259100         AIR

26        --        204.705538     12.277548         AIR

IMS       --            --         10.023568             Detector surface

CONIC AND POLYNOMIAL ASPHERIC DATA

SRF        CC          AD          AE          AF          AG

2      -1.000000      --          --          --          --

4      -0.622684      --          --          --          --

19      -0.492733      --          --          --          --

21      -1.000000      --          --          --          --

Appendix B: Full Disk Telescope Configurations

Configuration 1

Configuration 2

Configuration 3

Configuration 4

Configuration 5

Configuration 6

Configuration 7

Appendix C: VIM Optical Performance

High Resolution Telescope Wavefront Analysis.

Wavefront Analysis of HRT and Filtergraph Optics combination.

Full disk Telescope Configuration 1 (longest focal length)

Full disk Telescope Configuration 3

Full disk Telescope Configuration 5

Full disk Telescope Configuration 7 (shortest focal length)

# Text boxes

Primary Mirror

Entrance Aperture

Modulator

Telescope Focus

FPI focus

Detector

Primary focus with field stop

Telescope focus

Movable folding mirror

Zoom lens arrangement

Modulator

Telescope focus

Detector focus

Off-axis ellipsoid

Off-axis paraboloid

FPI etalon position