Active Final Approach Spacing Tool (AFAST)

# Overview Description

January 31, 2002

# NAS2-98005

# Technical Research in Advanced Air Transportation Technologies

Final

Overview Description

Active Final Approach Spacing Tool (aFAST)

CDRL Item 5b

# Prepared under

# RTO – 62

# AATT Operational Concept for ATM – Year 2002 Update

#### January 31, 2002

#### Prepared For:  NASA Ames Research Center

#### Moffett Field, CA 94035-1000

#### Prepared By:  Titan Systems Corporation – SRC Division

#### Billerica, MA 01821-4134

ACKNOWLEDGEMENT

The majority of the descriptions presented in this document have been taken directly from NASA documents shown in the bibliography. Minor modifications have been made to the text to provide readability.  The aFAST Flow chart has however been independently developed for this description.   This approach to the development of this document was taken in order to remain faithful to the efforts that are presently being undertaken by the NASA AATT Project Office, the aFAST Tool Developers and the associated NASA AATT contractors.

Table of Contents

- Description	1

- Operational Concept	2

- Functional Flow	3

- Bibliography	5

# List of Figures

- aFAST System Overview	3

- aFAST Functional Flow	4

## AATT ACTIVE FINAL APPROACH SPACING TOOL (aFAST)

## OVERVIEW DESCRIPTION

1.  DESCRIPTION

Purpose

- Help terminal area controllers optimize traffic flow to runways to minimize delay and increase throughput.

- Compute an efficient landing sequence, approach spacing and runway assignment for arrival aircraft.

Users

- Terminal area air traffic controllers

- Terminal area traffic management coordinators (TMCs)

Operational Results

- In operational testing at DFW,  passive FAST increased landing rates by 9-13%.

- The FAA estimates that passive FAST saves airlines US$10 million per year at DFW.

- aFAST is not operational however benefits analysis indicates a potential savings of over $300 M/year for 10 major airports (see #35 Bibliography).

Overview

The Final Approach Spacing Tool (FAST) is a decision support tool for terminal area (TRACON) air traffic controllers. The TRACON typically encompasses the airspace within approximately 40 miles of a major airport. TRACON air traffic controllers manage arrival aircraft which enter their airspace from adjacent ATC facilities or internal airports. The controllers are responsible for assigning an appropriate runway and landing sequence to each aircraft and maintaining safe separation.

FAST assists air traffic controllers by providing its advisory information on the radar planview displays. Additionally, FAST assists traffic management coordinators by providing schedule information on auxiliary timeline displays.

In general, arrival aircraft are vectored from en-route airspace into terminal airspace over metering fixes. Aircraft are assigned to a default runway, which is typically the closest runway to their respective metering fix. A controller occasionally reassigns aircraft to alternate runways to reduce delay on a particular runway or to balance delay and aircraft among multiple runways. Ideally, a controller would prefer to finalize an aircraft's runway assignment as early as possible (i.e. near the metering fix), but uncertainties in the traffic situation often require later reassignments.

During each scheduling cycle, FAST builds a trajectory for each aircraft from its current position to the runway threshold. The FAST sequencing algorithm uses these trajectories to systematically order aircraft on common trajectory paths and to merge aircraft on different trajectory paths.  Using the relative sequences of aircraft on each trajectory path, FAST performs conflict prediction and resolution in order to achieve a conflict-free arrival plan.  When a conflict is predicted, it is resolved by adding delay to the aircraft's trajectories in the form of vectoring and speed control.

2.  OPERATIONAL CONCEPT

Active FAST is designed to deal with the complexities of inter-arrival spacing within the TRACON (particularly on the final approach path).  Active FAST generates “control instruction” level advisories whereby controllers issue specific speed and heading instructions based upon the advisories.  Advisories will be displayed to controllers via their standard terminal color displays.  Dedicated aFAST displays will be provided for TMCs in the ARTCC and TRACON.  These displays will be used for strategic planning.  Displays will also be available for ATCSs in the Tower.  The Tower displays will provide enhanced situational awareness.

As arrivals enter the TRACON, they are assigned a runway and sequence number.  Active FAST builds a plan for these arrivals based on aircraft performance characteristics, airspace constraints, and separation requirements.  A trajectory for each aircraft is created and adjusted based on real time radar updates.  These trajectory calculations include identification of when and where each aircraft should receive speed adjustments or headings.  These speeds and headings will eventually be able to be incorporated into future technologies such as Datalink.  However, in the near term operational environment, these advisories will be displayed in logical increments (e.g. speeds of 210 knots and 180 knots, headings in 10 degree increments) to the TRACON arrival controller so that they can be issued as control instructions.  Active FAST continues to monitor and update the plan based upon radar track updates.  The plan is modified when necessary, and ultimately leads to an optimized delivery of aircraft to the runway threshold.

The primary users of the aFAST advisories are the TRACON arrival controllers.  However, many other users can benefit from the information.  Other controllers within the TRACON can view the aFAST advisories to better understand the arrival controller’s plan (e.g. a departure controller may want to know whether or not an arrival may be instructed to slow down or turn).  TMCs in the TRACON can use the aFAST information to make dynamic runway changes for aircraft near the TRACON boundary.  The information displayed on the Planview Graphical User Interface (PGUI) can also help the TMCs in the TRACON and ARTCC better understand the traffic situation inside the TRACON.  Controllers in the ATCT can also benefit from the PGUI by observing where gaps will occur in the arrival stream (for runway crossings or departure slots).

As shown in Figure 1, the aFAST system uses aircraft flight plans and position data from FAA computers, inputs from TRACON arrival controllers and traffic managers, and current weather information, to produce advisories to assist controllers in managing and controlling arrival traffic. The weather information is provided either by the Rapid Update Cycle (RUC), or by the Integrated Terminal Weather System (ITWS).  RUC provides a weather forecast every 3 hours (80 km grid).  ITWS provides a weather forecast every 5 minutes (2 km grid).

Figure 1	aFAST System Overview

TRACON arrival controllers interact with aFAST, both receiving advisories and providing inputs, through standard FAA hardware. The aFAST advisories will be displayed to TRACON controllers on FAA TRACON display systems. Controller inputs will be made through message entry devices.  Traffic managers interact with aFAST through dedicated aFAST displays.  They provide inputs such as runway spacing requirements, airport configuration, and airport acceptance rates.  Traffic managers in both the ARTCC and TRACON may monitor aFAST timelines to gain a more accurate picture of the real-time operation in the TRACON.

- FUNCTIONAL FLOW

Figure 2 illustrates the detailed functional flow of  aFAST operating in the TRACON and depicts the functional interfaces with external data sources.  The input/output sources, appearing in double boxes, are shown in the figure.  The major functions within aFAST are:

- Data Acquisition and Processing

- Data Formatting  and Distribution

- Trajectory Generation

- Arrival Planning

- Advisory Generation

- Conflict Detection

- Display Message Processing

Figure 2  aFAST Functional Flow

The external interfaces required for aFAST include:

- Host Computer System - To receive flight data and radar tracks from the ARTCC's HCS via an interface device.

- Terminal Automation System – To receive flight data, radar tracks, and controller entries from the Terminal Automation System via an interface device.  This includes interfacing with the terminal color display hardware.

The additional external interfaces that are preferred for aFAST include:

- Integrated Terminal Weather System (ITWS) - To receive low altitude wind and storm motion data from ITWS via an interface device.

- Surface Decision Support Tools – To exchange information with surface decision support tools in order to optimize the queuing of departures.

- Other atmospheric data - To receive high altitude wind, temperature, and air pressure data as a function of position and altitude.

4.   BIBLIOGRAPHY

- National Aeronautics and Space Administration; Decision Support Tools of the Advanced Air Transportation Technologies Project; May 2000

- Federal Aviation Administration, US Department of Transportation, Washington DC; National Airspace System Architecture Version 4.0; January 1999

- National Aeronautics and Space Administration, Ames Research Center; CTAS - Final Approach Spacing Tool (FAST);  July 2000      http://ctas.arc.nasa.gov/project_description/fast.html

- National Aeronautics and Space Administration, Ames Research Center; Center TRACON Automation System – FAST Fact Sheet; April 2000

- Robinson III, J. E., D. R. Isaacson; A Concurrent Sequencing, and Deconfliction Algorithm for Terminal Area Air Traffic Control; AIAA Guidance, Navigation, and Control Conference, Denver, CO; August 2000

- Quinn, C., J. E. Robinson III; A Human Factors Evaluation of Active Final Approach Spacing Tool Concepts; 3rd USA/Europe Air Traffic Management R&D Seminar, Napoli, Italy; June 2000

- Mueller, K. T., J. E. Robinson III; Final Approach Spacing Tool (FAST) Velocity Accuracy Performance Analysis, AIAA Guidance, Navigation, and Control Conference, Boston, MA; August 1998

- Robinson III, J. E., T. J. Davis, and D. R. Isaacson; Fuzzy Reasoning-Based Sequencing of Arrival Aircraft in the Terminal Area; AIAA Guidance, Navigation and Control Conference, New Orleans, LA; August 1997

- Lee, K. K. and T. J. Davis; The Development of the Final Approach Spacing Tool(FAST): A Cooperative Controller-Engineer Design Approach; Journal of Control Engineering Practice, Vol. 4, No. 8, pp. 1161-1168; August 1996

- Lee, K. K., and T. J. Davis; The Development of the Final Approach Spacing Tool (FAST): A Cooperative Controller-Engineer Design Approach, NASA TM 110359; August 1995 and Proceedings the Fifth IFAC Symposium on Automated Systems Based on Human Skill; September 1995

- Krzeczowski, K. J., T. J. Davis, H. Erzberger, I. Lev-Ram, and C. P. Bergh; Knowledge-Based Scheduling of Arrival Aircraft in the Terminal Area; Proceedings of the AIAA Guidance, Navigation, and Control Conference, Paper No. AIAA-95-3366, Baltimore, MD; August 1995

- Slattery, R. A.; Terminal Area Trajectory Synthesis for Air Traffic Control Automation; submitted to the American Control Conference; June 1995

- Bergh, C. P., K. J. Krzeczowski, and T. J. Davis; TRACON Aircraft Arrival Planning and Optimization through Spatial Constraint Satisfaction; Air Traffic Control Quarterly, Vol. 3, No. 2; 1995

- Davis, T. J., K. J. Krzeczowski, and C. Bergh; The Final Approach Spacing Tool; IFAC Thirteenth Symposium on Automatic Control in Aerospace, Palo Alto, CA; September 1994

- Credeur, L., W. R. Capron, G.W. Lohr, D. J. Crawford, D. A. Tang, and W. G. Rodgers, Jr.; A Comparison of Final Approach Spacing Aids for Terminal ATC Automation; Air Traffic Control Quarterly, Vol. 1(2) 135-178; 1993

- Davis, T. J., H. Erzberger, S. M. Green, and W. Nedell; Design and Evaluation of an Air Traffic Control Final Approach Spacing Tool; Journal of Guidance, Control and Dynamics, Vol. 14, No. 4; July/August 1991

- NASA: Beyond Free Flight Phase 1 Tools; NASA Office of Aero-Space Technology

- Smith, Colin, National Air Traffic Services Ltd, England; FINAL APPROACH SPACING TOOL; December 1998

- Credeur, L., W.R. Capron, G.W. Lohr, D. J. Crawford, D. A. Tang, and W. G. Rodgers, Jr.; Final-Approach Spacing Aids (FASA) Evaluation for Terminal-Area, Time-Based Air Traffic Control; NASA Technical Paper 3399; December 1993

- Davis, T. J., H. Erzberger, and S. M. Green; Simulator Evaluation of the Final Approach Spacing Tool; American Control Conference; San Diego, CA; May 1990; NASA Technical Memorandum 102807; 1990

- Davis, T. J., H. Erzberger, and H. Bergeron; Design of a Final Approach Spacing Tool for TRACON Air Traffic Control; NASA Technical Memorandum 102229; Ames Research Center, 1989

- Erzberger, H., and Nedell, W., “Design of Automated System for Management of Arrival Traffic,” NASA TM-102201, June 1989.

- “Center TRACON Automation System Build 2 Operational Description Document,” MIT Lincoln Laboratory, July 1997.

- Swenson, H. N., Hoang, T., Engelland, S., Vincent, D., Sanders, T., Sanford, B., Heere, K., “Design and Operational Evaluation of the Traffic Management Advisor at the Fort Worth Air Route Traffic Control Center”, 1st USA/Europe Air Traffic Management Research & Development Seminar, Saclay, France, June 1997

- Davis, T. J., Erzberger, H., Green, S. M., Nedell, W., “Design and Evaluation of an Air Traffic Control Final Approach Spacing Tool”, Journal of Guidance, Control, and Dynamics, Vol. 14, No. 4, pp. 848-854.

- “Center-TRACON Automation System (CTAS) Build 2 Computer-Human Interface (CHI) Requirements Specification,” MIT Lincoln Laboratory, August 1998.

- Quinn, C., Zelenka, R. E., “ATC/Air Carrier Collaborative Arrival Planning”, 2nd USA/Europe Air Traffic Management Research & Development Seminar, Orlando, FL, December 1998.

- Davis, T. J., Isaacson, D. R., Robinson, J. E. III, den Braven, W., Lee, K. K., Sanford, B., “Operational Field Test Results of the Final Approach Spacing Tool”, Proceedings of the IFAC 8th Symposium on Transportation Systems, Chania, Greece, June 1997.

- Isaacson, D. R., Davis, T. J., Robinson J. E. III, “Knowledge-based Runway Assignment for Arrival Aircraft in the Terminal Area”, AIAA Guidance, Navigation, and Control Conference, New Orleans, LA, August 1997.

- Zelenka, R. E., Beatty, R., Engelland, S., “Preliminary Results of the Impact of CTAS Information on Airline Operational Control”, AIAA-98-4481.

- Slattery, R., “Examination of Possible Future Terminal Area Procedures”, AIAA Guidance, Navigation, and Control Conference, San Diego, CA, July 1996.

- Lee, K. K., Sanford, B., Slattery, R., “The Human Factors of FMS Usage in the Terminal Area”, AIAA Modeling and Simulation Technologies Conference, New Orleans, LA, August 1997.

- Hinton, D. A., “Aircraft Vortex Spacing System (AVOSS) Conceptual Design”, NASA TM 110184, August 1995.

- Clarke, J. B., Hansman, R. J.,  "Systems Analysis of Noise Abatement Procedures Enabled by Advanced Flight Guidance Technology," AIAA-97-0490, Presented at the 35th Aerospace Sciences Meeting, Reno, Nevada, January 6-9, 1997.

- Welsch, Jerry D.,  Andrews, John W., "An Examination of Prior aFAST Benefits Analysis Studies - Interim Report; MIT/LL 92PM-AATT-0002, December 1, 1999

- Welsch, Jerry D., Andrews, John W., "Final Approach Spacing Tool Benefits Final Report", MIT/LL 92PM-AATT-0009, September 15, 2000