December 3, 2002

Version 1.1

Disabling CFT Inputs to L1MUON

A problem with the CFT inputs might present itself in the following ways:

- And/Or terms 192 and 193 (the “beginning of turn” triggers) have values other than 47712 Hz.

- The central L1MUON crate (0x16) goes “Out of Synch” and doesn’t recover after the DAQ shifter issues an SCL init.

- The L3 input rate drops suddenly and stays low.

If the shifter sees a problem, he/she should:

- Check with the CFT shifter to see if there is a CFT-related problem.  If so, let them attempt to recover and, after the DAQ shifter issues an SCL init, check the above conditions again.

- If the problem persists, request that the run be paused and then disable the CFT inputs using the GUI (an illustrated guide is available in the L1MUON Documentation binder):

- mutest@d0ol46~> setup d0online

- mutest@d0ol46~>/projects/l1muo/vme_gui/l1muon_inputs.py&     (A GUI window will appear.)

- Click on the “CFT masks” tab (upper right).  (You will be taken to the notebook page for CFT Inputs.)

- Click on “kill all cft inputs” button.

- A new window will appear telling you to restore the MTCC crate.  Click on “ok I’ll do it” button.

- Click on “Crate Controls” tab (upper left) to return to the main page.

- In the row labeled MTCC, click on the “restore” button.

- If status button turns green, click on “exit no write” button.

- Ask the DAQ shifter to issue an SCL init. And/Or terms 192 and 193 on the DAQ Monitor should both be 47712 Hz.  If so, you're done!

Make a note in the logbook and send email to L1MUON experts (d0_l1mu@fnal.gov).

Disabling CFT Inputs to L1MUON:  Step by Step

- mutest@d0ol46~> setup d0online

- mutest@d0ol46~>/projects/l1muo/vme_gui/l1muon_inputs.py&

(A GUI window will appear)

Disabling CFT Inputs to L1MUON:  Step by Step

- Click on the “CFT masks” tab (upper right)

Disabling CFT Inputs to L1MUON:  Step by Step

- Click on “kill all cft inputs” button

Disabling CFT Inputs to L1MUON:  Step by Step

- A new window will appear telling you to restore the MTCC crate.  Click on “ok I’ll do it” button

Disabling CFT Inputs to L1MUON:  Step by Step

- Click on “Crate Controls” notebook tab (upper left)

Disabling CFT Inputs to L1MUON:  Step by Step

- In the row labeled MTCC, click on the “restore” button

Disabling CFT Inputs to L1MUON:  Step by Step

- If status button turns green, click on “exit no write” button.

Disabling CFT Inputs to L1MUON:  Step by Step

- Ask the DAQ shifter to issue an sclinit. And/Or terms 192 and 193 on the DAQ Monitor should both be 47712 Hz.  If so, you're done!

# Text boxes

Both rates should be

47712.xxx