|  | Fermilab |
| --- | --- |

Particle Physics Division

Mechanical Department Engineering Note

# Number:	MD-ENG- 079	         Date:  June 20, 2005

Project Internal Reference:

Project:  ILC

Title:	Vacuum Vessel Engineering Note for 1.3 GHz, β=1, Cryomodule

Author(s): Edward Chi

Reviewer(s):

Key Words:

Crymodule, Vacuum, Pressure, Operating Temperature, Vessel Shell,

Stiffening Rib, Reinforcement, Flange, Weldment, Up & Downstream

Abstract Summary:

The vacuum vessel of 1.3 GHz, β=1, Cryomodule has 38” O. D, ~ 448”

Length with multiple openings for different connections and

instrumentation. This engineering note is presented extensive

discussion, analysis and calculations for the vessel and nozzle shells,

stiffening rings, multiple openings and reinforcements, different

flanges, welds and others per Fermilab, ASME and other applicable

codes.

Applicable Codes:

ES&H Manual Chapter 5033, Fermilab.

“Boiler & Pressure Vessel Code” ASME VIII, Div.1

Addenda July 1, 2003

“Allowable Stress Design”, AISC, 9th edition

“Structural Welding Code-Steel”, AWS D1.1-90

CONTENTS

Section                                             Descriptions                                                        Pages

1.       Calculation for the Vacuum Vessel Cylindrical Shell Thickness                         4

2.       The Permissible Out of Roundness of the Vessel Cylindrical Shell                     6

3.       Analysis and Calculations for the Stiffening Rings

3.1  To Define the Stiffening Ring  for the Vessel Shell Under the                            7

External Pressure and the Calculations of the Weld

3.2  To Define the Downstream End Flange as the Stiffening Ring for the                10

Vessel Shell Under the External Pressure

3.3  To Define the Upstream End Flange as the Stiffening Ring for the                     12

Vessel Shell Under the External Pressure

4.       Calculations and Analysis for the Vessel Shell Openings

4.1.  Calculations for the Opening of Port Coldmass for the Reinforcement               13

and Weld Size

4.2.   Calculations for the Opening of  MC Port (#9) for the Reinforcement and        18

Weld Size

4.3    Calculations for the Opening of  Instrumentation Port for the                            22

Reinforcement and Weld Size

4.4    Calculations for the Opening of Port #16 for the Reinforcement and                 25

Weld Size

4.5    Calculations for the Opening of Port #22 for the Reinforcement and                 32

Weld Size

4.6    Calculations for the Opening of Port #24 for the Reinforcement and                 36

Weld Size

  - Analysis for the Opening Port #14 for the Reinforcement and                           40

Weld Size

  - Calculations for the Opening of Port #20 for the Reinforcement and                 44

Weld Size

5.        Calculations and Analysis for the Flanges, Bolts and Welds

5.1    Upstream End Flange, Sliding Flange and the Bellow Flange                            48

5.2    Downstream End Flange and the Bellow Flange                                                 58

5.3    Calculations for Flanges #8, #13, #15, #19, #21 and #23                                    61

6.        Calculations and Analysis for the Saddle Support                                               63

7.        Appendix                                                                                                              66

Figure i.1, An overall view of the vacuum vessel weldment of 1.3 MHz,

β=1,Cryomodulue

Reference drawing: ME – 443027

Overall length = 448.23 in

Wws = 7,745 lbs. the weight of the vessel shell weldment.

Assuming the vessel shell is operating under the room temperature.

Vessel shell material:  SA 516-60

Materials for flanges, ports and nozzles: see respective notes and drawings.

1.  Calculation for the Vacuum Vessel Cylindrical Shell Thickness

The Vacuum Vessel Cylindrical Shell:

Given:

P:   14.7 psi, the external design pressure,

Do:  38.00 in, outside diameter of the vessel shell

Di:  37.25 in, inside diameter of the vessel shell

tn:   The nominal vessel shell thickness.

Fa: 15,000 psi, the max. allowable stress of the shell material at the operating temp,

also know as Sv. (See Page 1-1).

Vessel shell material: SA 516-60, carbon steel, see dwg. #E-443054

Lv: Design length of the vessel between lines of the support.

M.A: Material corrosion and other misc. allowance, ~ 1/16”

Assuming:

Lv = 228.30 in (per drawing #E-443027-01)

Find out the required vessel shell thickness tn:

- Try tn = 0.375”

Lv/Do = 228.30” / 38.00” = 6.0079

Do/tn = 38.00” / 0.375” = 101.3333

Per section UG-28, also Fig. G and Fig. CS-2 in Subpart 3 of Section II, part D,

ASME VIII, Div. 1:

It is found out that:

A = 0.0002

B = 2850

Then:

Pa = (4B) / (3Do/tn)

= (4 x 2850) ÷ (3 x 101.3333)

= 37.50 psi

where:

Pa : The max. allowable external working pressure, psi

A:  Factor determined from Fig. G

B:  Factor determined from the applicable material chert in Fig. CS-2.

- Try tr2 = 0.25

Lv/Do = 6.053

Do/tr2 = 38”/0.25” = 152

Find:

A ≈ 0.000115

Since the value of A falling to the left of the applicable material/temperature

curve, so:

Pa2 = (2AE/3(Do/tr2)) = 15.13 psi

So, tr = 0.250”

So the vessel shell thickness is required 0.25”, using 3/8” as vessel shell thickness is above the shell thickness required and it is satisfactory.

2.  The Permissible Out of Roundness of the Vessel Cylindrical Shell

Given:

P:   14.7 psi, the external design pressure,

Do:  38.00 in, outside diameter of the vessel shell

Di:  37.25 in, inside diameter of the vessel shell

tn:   0.375”, the nominal vessel shell thickness.

Fa: 15,000 psi, the max. allowable stress of the shell material at the operating temp,

also know as Sv. (See Page 1-1).

Vessel shell material: SA 516-60, carbon steel, see dwg. #E-443054

Lv: ~230”, design length of the vessel between lines of the support.

The difference between the max. dia and the mini. dia. of the vessel shell at any cross

section shall not exceed:

  - x 38 in = 0.38 in

(per section UG-80 (b)(1) of ASME VIII, Div.1)

Per section UG-80(b)(2) and figure UG-80 of ASME VIII, Div.1,  it is found out that

the maximum plus or minus deviation from the true circular form, measured radially on

the outside or inside of the cylindrical vessel shall not exceed the maximum permissible

deviation e:

e ≈ 0.85t

= 0.85 x 0.375 in

= 0.319 in

where:

Do / t = 101

Lv / Do = 6.052

Per Figure UG-29.2, section UG-29 of ASME VIII, Div.1, it is found out that:

Arc length ≈ 0.36 Do

= 0.36 x 38 in

= 13.68 in

Chord length = 2 x Arc length

= 2 x 13.68 in

= 27.36 in

So, in a chord length of 27.36 in, the maximum plus or minus deviation from the true

circle form shall not exceed 0.32 in.

3.    Analysis and Calculation for the Stffening Rings

  - To Define the Stiffening Ring for the Vessel Shell Under the External Pressure

and the Calculations of the Weld

Reference drawings: ME-443027

Given:

E = 29 x 106 psi, Modules of elasticity of the stiffening materials

le = 1.1 (Dot)0.5 = 1.1 (38” x 0.375”)0.5

= 4.152”, the effective regional length of the vessel shell

Fy: 38 ksi, min. yield stress of the stiffening material SA516-70 under the operating

temperature.

To find the required moment of inertia of the combined stiffening ring – shell cross section about the neutral axis parallel to the axial of the shell, in4, Is’:

Is’ = [Do2Ls(t + As/Ls)A] / 10.9                     (eq. x-1)

(per UG-29, ASME VIII, Div.1)

Where:

As:  Cross-sectional area of the stiffening area, in2

= 1.50 in2, see figure 1.

Ls:  Distance between the stiffening ring and support,  ~230.0 in

( See drawing ME-443027)

B:  Factor determined from the applicable chart,

= 0.75 [PDo ÷ (t + As/Ls)]

= 0.75 [14.7 psi x 38 in ÷ (0.375 in + 1.50 in2/230 in)]

= 1098

Per figure CS-2 in Subpart 3 of section II, Part D,  where B = 1098 falling below the left end of the material/temperature curve, so:

A = 2B/E

= 2 x 1098 / (29 x 106)

= 0.0000757

(per step 5 of UG-29, ASME VIII, Div. 1)

Then the Eq. x-1 becomes:

Is’ = {[382 x 230 x (0.375 + 1.50/230) x 0.0000757] / 10.9}in4

=  0.88 in4

To find the combined moment of inertia of the cross section area of the stiffening ring and shell

Figure 3.1 is the cross-section view of the stiffening ring with the vessel shell, also refer to view S-S of drawing ME-443027, MC-443052

Figure 3.1, Cross-section view of the vessel shell with the stiffening rings

It is found that from the figure 3.1:

A1 = 4.152 in x 0.375 in = 1.557 in2

A2 = 0.5 in x 3.0 in = 1.500 in2

y1 = 0.1875 in

y2 = 1.8125 in

y = (A1y1 + A2y2) ÷ (A1 + A2)

= 0.9848 in

dy12 = (y – y1)2 = 0.6357 in2

dy22 = (y – y2)2 = 0.6851 in2

I1 = 0.0182 in4

I2 = 1.125 in4

I = ∑Ii + ∑Aidyi2

= 3.1507 in4 > I’= 0.88 in4

Since the requirement moment of inertia I’ is less than the value of I provided by the combined moment inertia of stiffening ring and vessel shell, so the stiffening ring design is satisfactory and it can be treated as a support of the vessel.

Calculations of the attachment welds of the stiffening ring:

Per UG-30(e), ASME VIII, Div. 1:

Radial pressure load PLs = 14.7 psi x 230 in

= 3381 lb/in

Radial shear load  V = 0.01 PLsDo = 0.01 x 14.7 psi x 230 in x 38 in

= 1,285 lb

Weld shear flow due to radial shear load: VQ/I

where Q is the first moment of area, per figure 3.1,

Q = 4.152 x 0.375 (0.9848 – 0.375/2)

= 1.24 in3

VQ/I = 1,285 lb x 1.24 in3/ 3.1507 in4

= 505.73 lb/in

The combined weld load (required)

Pr = (3,3812 + 5062)1/2 lb/in

= 3,419 lb/in

The calculated welding load from the ring welds:

The most weaker material is the shell:

Sv = 15 ksi (SA 516-60)

The allowable fillet weld stress:

Faf =  0.55Sv = 0.55 x 15,000 psi

=  8,250 psi (per UW-18(d), ASME VIII, Div.1)

The minimum fillet weld leg size is: 0.25” for the attachment.

(per UG-30(f), ASME VIII, Div.1)

Since there is weld on both sides of the ring (see view S-S, ME-443027)

The allowable load from the weld is:

Paw = 2 x 0.25 in x 8,250 psi

= 4,125 lb/in > Pr = 3,419 lb/in

So the min. fillet size of 0.25” is acceptable for the current stiffening ring design.

  - To Define the Downstream End Flange as the Stiffening Ring for the Vessel

Shell Under the External Pressure

Reference drawings: ME-443027, MD-443039

Givien:

E = 28 x 106 psi, Modules of elasticity of the flange materials

le = 1.1 (Dot)0.5 = 1.1 (38” x 0.375”)0.5

= 4.152”, the effective regional length of the vessel shell

Fy: 25 ksi, min. yield stress of the stiffening material A182-F304L under the

operating temperature.

Figure 3.2,  The cross-section view of the end flange with the vessel shell, also refer to

detail L of drawing ME-443027, and drawing MD-443039..

To find the required moment of inertia of the combined end flange – shell cross section about the neutral axis parallel to the axia of the shell, in4, Is’:

Is’ = [Do2Ls(t + As/Ls)A] / 10.9                     (eq. x-1)

(per UG-29, ASME VIII, Div.1)

Where:

Asd:  Cross-sectional area of the downstream end flange stiffening area, in2

= (1.18 x 2.26) in2 = 2.6668 in2,  see figure 3.2

Lsd:  Distance between the stiffening ring and downstream end flange,  ~230.0 in

( See drawing ME-443027)

B:  Factor determined from the applicable chart,

= 0.75 [PDo ÷ (t + As/Ls)]

= 0.75 [14.7 psi x 38 in ÷ (0.375 in + 2.6668 in2/230 in)]

= 1084

Per figure CS-2 in Subpart 3 of section II, Part D,  where B = 1084 falling below the left end of the material/temperature curve, so:

A = 2B/E

= 2 x 1084 / (28 x 106)

= 0.0000774

(per step 5 of UG-29, ASME VIII, Div. 1)

Then the Eq. x-1 becomes:

Is’ = {[382 x 230 x (0.375 + 2.6668/230) x 0.0000774] / 10.9}in4

= ((332,120 x 0.3866 x 0.0000723) /10.9) in4

=  0.912 in4

To find the combined moment of inertia of the cross section area of the stiffening ring and shell

It is found that from the figure 3.2:

A1 = 2.67 in x 0.375 in = 1.001 in2

A2 = 1.18 in x 2.26 in = 2.6668 in2

y1 = 0.1875 in

y2 = 1.505 in

y = (A1y1 + A2y2) ÷ (A1 + A2)

= 1.1454 in

dy12 = (y – y1)2 = 0.9176 in2

dy22 = (y – y2)2 = 0.1293 in2

I1 = 0.0117 in4

I2 = 1.1351 in4

I = ∑Ii + ∑Aidyi2

= (1.1468 + 1.2633) in4

= 2.4101 in4 > I’= 0.912 in4

Since the requirement moment of inertia I’ is less than the value of I provided by the combined moment inertia of the end flange(downstream) and vessel shell, so the downstream end flange is satisfactory and it can be treated as a support of the vessel.

  - To Define the Upstream End Flange as the Stiffening Ring for the Vessel Shell

Under the External Pressure

Reference drawings: Detail M of drawing ME-443027-2,

MD- 443040

Lsu:  Distance between the stiffening ring and upstream end flange,  ~ 45.0 in

(See figure 4-4.3 of Page 32)

Asu: ≈ 0.5 (45.67 - 38.12) x 1.57 in2 = 5.927 in2

Since Lsu < Lsd;  Asu > Asd

From the calculation steps of section x.x, we can conclude that the requirement moment of inertia I’ is less than the value of I provided by the combined moment inertia of the end flange(upstream) and vessel shell, so the upstream end flange is satisfactory and it can be treated as a support of the vessel.

4.         Calculations and Analysis for the Vessel Shell Openings

  - Calculations for the Opening of Coldmass Port for the Reinforcement and

Weld Size

The main vessel shell:

P:   14.7 psi, external design pressure

Do: 38.00 in, outside dia. Of the vessel shell.

Di: 37.25, inside dia. of the vessel shell.

t:   0.375 in, the nominal pipe wall thickness.

Fa: 15,000 psi, the max. allowable stress of the shell material at the operating temp,

also know as Sv. at the operating temp.,  -200  F to 1000 F (per Table 1A, part D,

Section II, ASME Boiler & Pressure Vessel Code 1995 edition).

Vessel shell material: SA 516, grade 60, carbon steel (see ME-443054)

Lv: Design length of the vessel section between lines of support (see Page UG-28(b)),

≈ 230”

Find out the required vessel shell thickness tr:

Try tr1 = 0.375”

Lv/Do = 230”/38” = 6.053

Do/tr = 38/0.375 = 101.333

From section UG-28, also Fig. G & Fig. CS-2 in Subpart 3 of section II, part D,

ASME VIII, Div I:

Find:

A = 0.0002

B = 2850

Pa1= (4B)/(3(Do/tr)) = 37.50 psi

where:

A:  Factor determined from Fig. G.

B:  Factor determined from applicable material chart in Fig. CS-2

Pa: Max. allowable external working pressure, psi

- Try tr2 = 0.25

Lv/Do = 6.053

Do/tr2 = 38”/0.25” = 152

Find:

A ≈ 0.000115

Since the value of A falling to the left of the applicable material/temperature

curve, so:

Pa2 = (2AE/3(Do/tr2)) = 15.13 psi

So, tr = 0.250”

The coldmass port:

do: 25.197”, outside dia. of the port.

Di:  15.512”, inside dia . of the port.

tn:  4.842”, wall thickness  of the port.

trn: required thickness of the port.

L:  length of projection defining the thickness portion of integral reinforcement of the

port beyond the outside surface of the vessel wall.

E:  28 x 106 psi, modulus of elasticity of the material at the opening temp.

Material: SA 182- 304L stainless steel pipe, Fa = Sn = 16,700 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

Reference drawings: MD-443049, MD-443050, ME-443027, and also as shown from

figure 4.1.

Figure 4.1, 3D view of the coldmass port and the vessel shell

Find out the thickness required:

- Assuming  L1 = 6.64 in, tr1 = 0.375 in, then:

L1/do = 6.64/25.197 = 0.2635

do/tr1 = 25.197/0.375 = 67

From Fig. G and Fig. HA-3 of subpart 3 of Sect. II, part D:

A = 0.013

B = 13300

Pa = (4B)/(3(do/tr1)) = (4 x 13300)/(3 x 67) = 264 psi > P

- Try: L2 = 6.64 in, tr2 = 0.0625 in

L2/do = 0.2635

do/tr2 = 403

get:

A = 0.00073

B = 8000

Pa = (4B)/(3(do/tr2)) = (4 x 8000)/(3 x 403) = 26.47 psi > P

- Try: L3 = 6.64 in, tr3 = 0.046 in

L3/do = 0.2635

do/tr3 = 25.197/0.046 = 548

get:

A = 0.000445

B = 6100

Pa = (4B)/(3(do/tr2)) = (4 x 6100)/(3 x 548) = 14.84 psi ≈ P

So: trn = tr3 = 0.046 in

Size of the weld required:

Per UG-37, UW-16 and Fig. UW-16.1(p) of ASME VIII, Div.1.

to:  the throat dimension of the outer attachment weld,  =0.5 tmin.

ti:   the throat dimension of the inside of the shell cutout,  ≥ 0.7tmin

to = 0.5 tmin = 0.5 x 0.375” = 0.1875”, so the fillet leg size is 0.27”

ti  = 0.7 tmin = 0.7 x 0.375” =0.26”, so the fillet leg size is 0.37”

Area of the reinforcement required Ar:

Per section UG-37(d)(1):

Ar = 0.5(dtrF + 2tntrF(1-fr1)

= 0.5 x (16.299” x 0.25” x 1.0 +2 x 4.842” x 0.25” x 1.0 x 0)

= 2.0374 in2

Where:

d:  Finished diameter of circle opening, see Fig. UG-37.1 of UG-37.

D = 16.299 in (per drawing ME-443054)

F: Correction factor

fr : Strength reduction factor, not greater than 1.0

fr1 =1.0 for nozzle wall abutting the vessel wall as shown in figure UG-40(j),

(k), (n) and (o).

fr2 = Sn / Sv

Area of reinforcement available Aa:

A1: Larger of the following calculated value: (area available in shell):

= d(E1t – Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 16.299” x  (1 x 0.375” – 1.0 x 0.25”) – 0

= 2.0374 in2

or      = 2(t + tn)(E1t –Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 2 (0.375” + 4.842”) x (1.0 x 0.375” – 1.0 x 0.25”) – 0

= 1.30425 in2

So pick A1 = 2.0374 in2

A2: Smaller of the following:

= 5 (tn-trn)tfr2

= 5 x (4.842 in – 0.046 in) x 0.375 in x 1.0

=  8.9925 in2

or     = 5 (tn-trn) fr2tn

= 5 x (4.842 in – 0.046 in) x 1.0 x 4.842 in

= 116.11 in2

So pick A2 = 8.9925 in2

A3:   Area available in inward nozzle, use the smallest value:

Since there is no inward nozzle

So pick A3 = 0.0 in2

A41: Outward nozzle weld

= leg2 fr2

= 0.272 in2 x 1.0

=0.0729 in2

A43: Inward nozzle weld

= leg2 fr2

= 0.372 in2 x 1.0

= 0.1369 in2

Then:

Aa = A1 + A2 + A3 + A41 + A43

= (2.0374 + 8.9925 + 0 + 0.0729 + 0.1369) in2

= 11.2397 in2 > Ar = 2.0374 in2

# Per Fig. UG-37.1, section UG-37, the opening is adequately reinforced under the current designated boundary conditions.

The analysis and conclusion should be also true for openings of #2 (have 2 openings @ both ends, see drawing ME-443027), this is because:  the value of Lv for #2 opening is equal or smaller than the value for #3 opening, the smaller value of Lv will lead to smaller value of tr, accordingly, it will lead to the smaller value of Ar.

4.2   Calculations for the Opening of  MC Port (#9) for the Reinforcement and

Weld Size

The main vessel shell:

From section 4.1, it is found that  tr = 0.250”

The MC port:

do: 11.339”, outside dia. of the port.

Di:  10.945”, inside dia . of the port.

tn:  0.197”, wall thickness  of the port.

trn: required thickness of the port.

L:  length of projection defining the thickness portion of integral reinforcement of the

port beyond the outside surface of the vessel wall.

E:  28 x 106 psi, modulus of elasticity of the material at the opening temp.

Material: SA 249-TP304L stainless steel pipe, Fa = Sn = 14,200 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

Reference drawings: ME-443027, and also as shown from figure 4.2.

Figure 4.2, The partial 2D and 3D views of the MC port from ME-443027

Find out the wall thickness required:

- Assuming  L1 = 8.54 in, tr1 = 0.125 in, then:

L1/do = 8.54/11.339 =0.7532

do/tr1 = 11.339/0.125 = 91

From Fig. G and Fig. HA-3 of subpart 3 of Sect. II, part D:

A = 0.00225

B = 10500

Pa = (4B)/(3(do/tr1)) = (4 x 10500)/(3 x 91) = 153 psi > P

- Try: L2 = 8.54 in, tr2 = 0.0625 in

L2/do = 0.7532

do/tr2 = 181

get:

A = 0.00075

B = 8050

Pa = (4B)/(3(do/tr2)) = (4 x 8050)/(3 x 181) = 59.3 psi > P

Try: L3 = 8.54 in, tr3 = 0.033 in

L2/do = 0.7532

do/tr3 = 344

get:

A = 0.000280

B = 3950

Pa = (4B)/(3(do/tr2)) = (4 x 3950)/(3 x 344) = 15.31 psi ≈ P

So: trn = tr3 = 0.033 in

Size of the weld required:

Per UG-37, UW-16 and Fig. UW-16.1© of ASME VIII, Div.1.

tmin:   0.197”

tc:     ≥ 0.7tmin = 0.138”, so the fillet leg size is 0.195”

Full penetration weld plus the fillet weld tc.

Area of the reinforcement required Ar:

Per section UG-37(d)(1):

Ar = 0.5(dtrF + 2tntrF(1-fr1)

= 0.5 x (11.339” x 0.25” x 1.0 +2 x 0.197” x 0.25” x 1.0 x 0.053)

= 1.4226 in2

Where:

d:  Finished diameter of circle opening, see Fig. UG-37.1 of UG-37.

D = 11.339 in (per drawing ME-443054)

F: Correction factor

fr : Strength reduction factor, not greater than 1.0

fr1 = Sn / Sv  for nozzle wall inserted through the vessel wall

fr2 = Sn / Sv = 14.2 / 15 =0.947

Area of reinforcement available Aa:

A1: Larger of the following calculated value: (area available in shell):

= d(E1t – Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 11.339” x  (1 x 0.375” – 1.0 x 0.25”) – 2 x 0.197 (1.0 x 0.375 – 1.0 x 0.25) x

0.053

= (1.4174 – 0.0026) in2

= 1.4148 in2

or      = 2(t + tn)(E1t –Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 2 (0.375” + 0.197”) x (1.0 x 0.375” – 1.0 x 0.25”) – 2 x 0.197 (1.0 x 0.375 – 1.0 x

0.25) x 0.053

= (0.143 – 0.0026) in2

= 0.1405 in2

So pick A1 = 1.4148 in2

A2: Smaller of the following:

= 5 (tn-trn)tfr2

= 5 x (0.197 in – 0.033 in) x 0.375 in x 0.947

=  0.2912 in2

or     = 5 (tn-trn) fr2tn

= 5 x (0.197 in – 0.033 in) x 0.947 x 0.197 in

= 0.153 in2

So pick A2 = 0.153 in2

A3:   Area available in inward nozzle, use the smallest value:

Since there is no inward nozzle

So pick A3 = 0.0 in2

A41: Outward nozzle weld

= leg2 fr2

= 0.1952 in2 x 0.947

=0.036 in2

A43: Inward nozzle weld

= leg2 fr2

= 0.02 in2 x 1.0

= 0.0 in2

Then:

Aa = A1 + A2 + A3 + A41 + A43

= (1.4148 + 0.153 + 0 + 0.036 + 0.0) in2

= 1.6038 in2 > Ar = 1.4226 in2

# Per Fig. UG-37.1, section UG-37, the opening is adequately reinforced under the current designated boundary conditions.

The analysis and conclusion should be true for all 8 openings (#9 openings, see drawing ME-443027 & ME-443054). Any issue related the multiple openings will discuss in different section.

4.3      Calculations for the Opening of  Instrumentation Port (#10 opening)

for the Reinforcement and Weld Size

The main shell (Tube #9)

From section 4.2, it is found that:  tr = 0.033 in

The instrumentation port:

do: 3.50”, outside dia. of the port.

Di:  3.334”, inside dia . of the port.

tn:  0.083”, wall thickness of the port.

trn: required thickness of the port.

L:  length of projection defining the thickness portion of integral reinforcement of the

port beyond the outside surface of the vessel wall.

E:  28 x 106 psi, modulus of elasticity of the material at the opening temp.

Material: SA 249-TP304L stainless steel pipe, Fa = Sn = 14,200 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

Reference drawings: section G-G, ME-443027, and also as shown from figure 4.2.

Find out the wall thickness requires:

Assuming  L1 = 2.0075 in, tr1 = 0.083 in, then:

where: L1 = 7.48 – (11.339/2 – 0.197) = 2.0075”

L1/do = 2.0075/3.50 =0.5736

do/tr1 = 3.50/0.083 = 42

From Fig. G and Fig. HA-3 of subpart 3 of Sect. II, part D:

A = 0.009

B = 13200

Pa = (4B)/(3(do/tr1)) = (4 x 13200)/(3 x 42) = 419 psi > P

Try: L2 = 2.0075 in, tr2 = 0.015625 in

L2/do = 0.5736

do/tr2 = 224

get:

A = 0.0007

B = 8000

Pa = (4B)/(3(do/tr2)) = (4 x 8000)/(3 x 224) = 47.62 psi > P

Try: L3 = 2.0075 in, tr3 = 0.0094 in

L3/do = 0.5732

do/tr3 = 372

get:

A = 0.0003

B = 4250

Pa = (4B)/(3(do/tr2)) = (4 x 4250)/(3 x 372) = 15.23 psi ≈ P

So: trn = tr3 = 0.0094 in

Size of the weld required:

Per UG-37, UW-16 and Fig. UW-16.1© of ASME VIII, Div.1.

tmin:   0.083”

tc:       ≥ 0.7tmin = 0.056”, so the fillet leg size is 0.08”

Full penetration weld plus the fillet weld tc.

Area of the reinforcement required Ar:

Per section UG-37(d)(1):

Ar = 0.5(dtrF + 2tntrF(1-fr1)

= 0.5 x (3.5” x 0.033” x 1.0 + 2 x 0.083” x 0.033” x 1.0 x 0)

= 0.0578 in2

Where:

d:  Finished diameter of circle opening, see Fig. UG-37.1 of UG-37.

D = 11.339 in (per drawing ME-443054)

F: Correction factor

fr : Strength reduction factor, not greater than 1.0

fr1 = Sn / Sv  for nozzle wall inserted through the vessel wall

fr2 = Sn / Sv = 14.2 / 14.2 = 1.0

Area of reinforcement available Aa:

A1: Larger of the following calculated value: (area available in shell):

= d(E1t – Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 3.50” x  (1 x 0.197” – 1.0 x 0.033”) – 2 x 0.083 (1.0 x 0.197 – 1.0 x 0.033) x 0

= 0.574 in2

or      = 2(t + tn)(E1t –Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 2 (0.197” + 0.083”) x (1.0 x 0.197” – 1.0 x 0.033”) – 2 x 0.197 (1.0 x 0.375 – 1.0

x 0.25) x 0.0

=  (2 x 0.28 x 0.164) in2

= 0.0918 in2

So pick A1 = 0.574 in2

Since A1 = 0.574 in2

Also: Aa = A1 + A2 + A3 + A41 + A43

That leads to:

Aa > Ar = 0.0578 in2

# Per Fig. UG-37.1, section UG-37, the opening is adequately reinforced under the current designated boundary conditions.

The analysis and conclusion should be true for all 8 instrumentation ports (#10 openings, see section G-G, drawing ME-443027).

  - Calculations for the Opening of Port #16 for the Reinforcement and

Weld Size

The main vessel shell:

From section 4.1, it is found that  tr = 0.250”

The port #16:

do: 11.811”, outside dia. of the port.

Di:  11.417”, inside dia . of the port.

tn:  0.197”, wall thickness  of the port.

trn: required thickness of the port.

L:  length of projection defining the thickness portion of integral reinforcement of the

port beyond the outside surface of the vessel wall.

E:  30 x 106 psi, modulus of elasticity of the material at the opening temp.

Material: SA 249-TP304L stainless steel pipe, Fa = Sn = 14,200 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

Reference drawings: Section H-H of ME-443027, and also as shown

from figure 4-4.1 and figure 4-4.2..

Figure 4-4.1   Multiple openings of the upstream end of the vessel

Figure 4-4.2, The 2D view of the port #16 from drawing ME-443027

Find out the wall thickness required:

Assuming  L1 = (23.62 – 18.625) in = 5.00 in, tr1 = 0.035 in, then:

L1/do = 5.00/11.811 = 0.4233

do/tr1 = 11.811/0.035 = 337

From Fig. G and Fig. HA-3 of subpart 3 of Sect. II, part D:

A = 0.00057

B = 7700

Pa = (4B)/(3(do/tr1)) = (4 x 7700)/(3 x 337) = 30.46 psi > P

- Try: L2 = 5.00in, tr2 = 0.025 in

L2/do = 0.4233

do/tr2 = 472

get:

A = 0.00033

B = 4650

Pa = (4B)/(3(do/tr2)) = (4 x 4650)/(3 x 472) = 13.13 psi < P

Try: L3 = 5.00 in, tr3 = 0.026in

L2/do = 0.4233

do/tr3 = 454

get:

A = 0.00035

B = 5000

Pa = (4B)/(3(do/tr2)) = (4 x 5000)/(3 x 454) = 14.68 psi > ≈ P

So: trn = tr3 = 0.026 in

Size of the weld required:

Per UG-37, UW-16 (d.1) and Fig. UW-16.1(k) of ASME VIII, Div.1.

to:  the throat dimension of the outer attachment weld,  ≥ 0.7tmin.

ti:   the throat dimension of the inside of the shell cutout,  ≥ 0.7tmin

to =  0.7 tmin = 0.7 x 0.197” =0.138”, so the fillet leg size is 0.19”

ti  = 0.7 tmin = 0.7 x 0.197” =0.138”, so the fillet leg size is 0.19”

to + ti = 0.138” + 0.138” = 0.276” ≥ 1.25 tmin =0.246”

Area of the reinforcement required Ar:

Per section UG-37(d)(1):

Ar = 0.5(dtrF + 2tntrF(1-fr1))

= 0.5 x (11.417” x 0.25” x 1.0 + 2 x 0.197” x 0.25” x 1.0 x 0.053)

= (1.4271 + 0.0026) in2

= 1.4297 in2

Where:

d:  Finished diameter of circle opening, see Fig. UG-37.1 of UG-37.

D = 11.417 in (per drawing ME-443054)

F: Correction factor

fr : Strength reduction factor, not greater than 1.0

fr1 = Sn / Sv  for nozzle wall inserted through the vessel wall

fr2 = Sn / Sv = 14.2 / 15 =0.947

Area of reinforcement available Aa:

A1: Larger of the following calculated value: (area available in shell):

= d16(E1t – Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 4.90” x  (1 x 0.375” – 1.0 x 0.25”) – 2 x 0.197” x 1.0 x .125” x 0.053

= (0.6125 – 0.0026) in2

= 0.6099 in2

or      = 2(t + tn)(E1t –Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 2 (0.375” + 0.197”) x (1.0 x 0.375” – 1.0 x 0.25”) – 2 x 0.197” x 1.0 x .125” x

0.053

= (0.143 – 0.0026) in2

= 0.1404 in2

So pick A1 = 0.6099 in2

where:

d16 ≈ 2 x 51% x [(Π do x 13.3o) ÷ 360o + 2dn] = 4.90”,  per UG-42 (a)(1) and section

C-C of drawing ME-443054. 51% is the portion of the cross section can be

considered between two openings (#16 & #9) by the ratio of the diameters.

A2: Smaller of the following:

= 5 (tn-trn)tfr2

= 5 x (0.197 in – 0.026 in) x 0.375 in x 0.947

=  0.3036 in2

or     = 5 (tn-trn) fr2tn

= 5 x (0.197 in – 0.026 in) x 0.947 x 0.197 in

= 0.1595 in2

So pick A2 = 0.1595 in2

A3:   Area available in inward nozzle, use the smallest value:

Since there is no inward nozzle

So pick A3 = 0.0 in2

A41: Outward nozzle weld

= leg2 fr2

= 0.192 in2 x 1.0

=0.036 in2

A43: Inward nozzle weld

= leg2 fr2

= 0.192 in2 x 1.0

= 0.036in2

Then:

Aa = A1 + A2 + A3 + A41 + A43

= (0.6099 + 0.1595 + 0 + 0.036 + 0.036) in2

= 0.8414 in2 < Ar = 1.4297 in2

The opening is not adequate, either to reduce the tr value or adding reinforcing element.

Assuming to add a stiffening rib like #26 of drawing ME-443027 at the location as shown in figure 4-4.3

Figure 4-4.3,  New version upstream end of the vessel with new stiffening rib.

If going through the similar procedures as shown on section 4.1, it was found that:

tr ≈ 0.13” when Lv = 45”

then:

Area of the reinforcement required Ar:

Per section UG-37(d)(1):

Ar = 0.5(dtrF + 2tntrF(1-fr1))

= 0.5 x (11.417” x 0.13” x 1.0 + 2 x 0.197” x 0.13” x 1.0 x 0.053)

= (0.7421 + 0.0014) in2

= 0.7435 in2

Area of reinforcement available Aa:

A1: Larger of the following calculated value: (area available in shell):

= d16(E1t – Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 4.90” x  (1 x 0.375” – 1.0 x 0.13”) – 2 x 0.197” x 1.0 x .245” x 0.053

= (1.2005 – 0.0051) in2

= 1.1954 in2

or      = 2(t + tn)(E1t –Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 2 (0.375” + 0.197”) x (1.0 x 0.375” – 1.0 x 0.13”) – 2 x 0.197” x 1.0 x .245” x

0.053

= (0.2803 – 0.0051) in2

= 0.2752 in2

So pick A1 = 1.1954 in2

where:

d16 ≈ 2 x 51% x [(Π do x 13.3o) ÷ 360o + 2dn] = 4.90”,  per UG-42 (a)(1) and section

C-C of drawing ME-443054. 51% is the portion of the cross section can be

considered between two openings (#16 & #9) by the ratio of the diameters.

A2: Smaller of the following:

= 5 (tn-trn)tfr2

= 5 x (0.197 in – 0.026 in) x 0.375 in x 0.947

=  0.3036 in2

or     = 5 (tn-trn) fr2tn

= 5 x (0.197 in – 0.026 in) x 0.947 x 0.197 in

= 0.1595 in2

So pick A2 = 0.1595 in2

A3:   Area available in inward nozzle, use the smallest value:

Since there is no inward nozzle

So pick A3 = 0.0 in2

A41: Outward nozzle weld

= leg2 fr2

= 0.192 in2 x 1.0

=0.036 in2

A43: Inward nozzle weld

= leg2 fr2

= 0.192 in2 x 1.0

= 0.036in2

Then:

Aa = A1 + A2 + A3 + A41 + A43

= (1.1954 + 0.1595 + 0 + 0.036 + 0.036) in2

= 1.4269 in2 > Ar = 0.7435 in2

# Per Fig. UG-37.1, section UG-37, the opening is adequately reinforced under the modified boundary conditions.

Applying the similar approach, it also will find out that the opening #9 at the upstream end is adequately reinforced under the modified boundary condition.

  - Calculations for the Opening of Port #22 for the Reinforcement and

Weld Size

The main vessel shell:

From section 4.4, it is found that  tr = 0.13”

The port #22:

do: 8.780”, outside dia. of the port.

Di:  8.386”, inside dia . of the port.

tn:  0.197”, wall thickness  of the port.

trn: required thickness of the port.

L:  length of projection defining the thickness portion of integral reinforcement of the

port beyond the outside surface of the vessel wall.

E:  28 x 106 psi, modulus of elasticity of the material at the opening temp.

Material: SA 249-TP304L stainless steel pipe, Fa = Sn = 14,200 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

Reference drawings: Section K-K and detail L of ME-443027, and also as shown

from figure 4-5.1

Find out the wall thickness required:

- Assuming  L1 = 14.533 in, tr1 = 0.0625 in, then:

L1/do = 14.533/8.780 =1.6552

do/tr1 = 8.780/0.0.0625 = 140

From Fig. G and Fig. HA-3 of subpart 3 of Sect. II, part D:

A = 0.00053

B = 7400

Pa = (4B)/(3(do/tr1)) = (4 x 7400)/(3 x 140) = 70.48 psi > P

- Try: L2 = 14.533 in, tr2 = 0.03125 in

L2/do = 1.6552

do/tr2 = 281

get:

A = 0.00017

B = 2300

Pa= (4B)/(3(do/tr2)) = (4 x 2300)/(3 x 281)

= 10.91 psi < P

Figure 4-5.1,  The 2D view of the ports of #22, #24 & #14

Try: L3 = 14.533 in, tr3 = 0.035 in

L2/do = 1.6552

do/tr3 = 251

get:

A = 0.00021

B = 2800

Pa = (4B)/(3(do/tr2)) = (4 x 2800)/(3 x 251) = 14.87 psi ≈ P

So: trn = tr3 = 0.035 in

Size of the weld required:

Per UG-37, UW-16 (d.1) and Fig. UW-16.1(k) of ASME VIII, Div.1.

to:  the throat dimension of the outer attachment weld,  =0.5 tmin.

ti:   the throat dimension of the inside of the shell cutout,  ≥ 0.7tmin

to =  0.7 tmin = 0.7 x 0.197” =0.138”, so the fillet leg size is 0.19”

ti  = 0.7 tmin = 0.7 x 0.197” =0.138”, so the fillet leg size is 0.19”

to + ti = 0.138” + 0.138” = 0.276” ≥ 1.25 tmin =0.246”

Area of the reinforcement required Ar:

Per section UG-37(d)(1):

Ar = 0.5(dtrF + 2tntrF(1-fr1))

= 0.5 x (8.386” x 0.13” x 1.0 +2 x 0.197” x 0.13” x 1.0 x 0.053)

= 0.5 x (1.0902 + 0.0027)

= 0.5465 in2

Where:

d:  Finished diameter of circle opening, see Fig. UG-37.1 of UG-37.

D = 8.386 in (per drawing ME-443054)

F: Correction factor

fr : Strength reduction factor, not greater than 1.0

fr1 = Sn / Sv  for nozzle wall inserted through the vessel wall

fr2 = Sn / Sv = 14.2 / 15 =0.947

Area of reinforcement available Aa:

A1: Larger of the following calculated value: (area available in shell):

= d22(E1t – Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 3.243”x (1 x 0.375” – 1.0 x 0.13”) – 2 x 0.197 x (1.0 x 0.375”-1.0 x 0.13) x

0.053

= (0.7945 – 0.0051) in2

= 0.7894 in2

or      = 2(t + tn)(E1t –Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 2 (0.375” + 0.197”) x (1.0 x 0.375” – 1.0 x 0.13”) – 2 x 0.197 x (1.0 x 0.375”-1.0

x 0.13) x 0.053

= 0.28 – 0.0051

= 0.2749 in2

So pick A1 = 0.7894 in2

where:

d22 ≈ 2 x 77% x [(Π do x 5.4o) ÷ 360o + dn22 + dn24 ] = 3.243”,  per UG-42 (a)(1) and

section  C-C of drawing ME-443054. 51% is the portion of the cross section can

be considered between two openings (#22 & #24) by the ratio of the diameters.

A2: Smaller of the following:

= 5 (tn-trn)tfr2

= 5 x (0.197 in – 0.035 in) x 0.375 in x 0.947

=  0.2877 in2

or     = 5 (tn-trn) fr2tn

= 5 x (0.197 in – 0.046 in) x 0.947 x 0.197 in

= 0.1408 in2

So pick A2 = 0.1408 in2

A3:   Area available in inward nozzle, use the smallest value:

Since there is no inward nozzle

So pick A3 = 0.0 in2

A41: Outward nozzle weld

= leg2 fr2

= 0.192 in2 x 1.0

=0.0361 in2

A43: Inward nozzle weld

= leg2 fr2

= 0.192 in2 x 1.0

= 0.0361in2

Then:

Aa = A1 + A2 + A3 + A41 + A43

= (0.7894 + 0.1408 + 0 + 0.0361 + 0.0361) in2

= 0.9979 in2 > Ar = 0.5465 in2

# Per Fig. UG-37.1, section UG-37, the opening is adequately reinforced under the current designated boundary conditions.

The analysis and conclusion should be also true for openings of #2 (have 2 openings @ both ends, see drawing ME-443027), this is because:  the value of Lv for #2 opening is equal or smaller than the value for #3 opening, the smaller value of Lv will lead to smaller value of tr, accordingly, it will lead to the smaller value of Ar.

4.6      Calculations for the Opening of Port #24 for the Reinforcement and

Weld Size

The main vessel shell:

From section 4.4, it is found that  tr = 0.130”

The port #24:

do: 2.756”, outside dia. of the port.

di:  2.52”, inside dia . of the port.

tn:  0.118”, wall thickness  of the port.

trn: required thickness of the port.

L:  length of projection defining the thickness portion of integral reinforcement of the

port beyond the outside surface of the vessel wall.

E:  28 x 106 psi, modulus of elasticity of the material at the opening temp.

Material: SA 249-TP304L stainless steel pipe, Fa = Sn = 14,200 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

Reference drawings: Section K-K and detail L of ME-443027, and also as shown

from figure 4-4.3 and figure 4-5.1.

Find out the wall thickness required:

1.   Assuming  L1 = (22.44 – 18.625) in = 3.815 in, tr1 = 0.0625 in, then:

L1/do = 3.815/2.756 =1.3843

do/tr1 = 2.756/0.0.0625 = 44

From Fig. G and Fig. HA-3 of subpart 3 of Sect. II, part D:

A = 0.0035

B = 11500

Pa = (4B)/(3(do/tr1)) = (4 x 11500)/(3 x 44) = 348 psi > P

- Try: L2 = 3.815 in, tr2 = 0.03125 in

L2/do = 1.3843

do/tr2 = 88

get:

A = 0.0012

B = 8950

Pa = (4B)/(3(do/tr2)) = (4 x 8950)/(3 x 88) = 135.6 psi > P

3.   Try: L3 = 3.815 in, tr3 = 0.013 in

L2/do = 1.3843

do/tr3 = 212

get:

A = 0.00033

B = 4550

Pa = (4B)/(3(do/tr2)) = (4 x 2800)/(3 x 251) = 28.62 psi > P

4.   Try: L3 = 3.815 in, tr3 = 0.011 in

L2/do = 1.3843

do/tr3 = 251

get:

A = 0.000215

B = 2900

Pa = (4B)/(3(do/tr2)) = (4 x 2900)/(3 x 251) = 15.41 psi ≈ P

So: trn = tr3 = 0.011 in

Size of the weld required:

Per UG-37, UW-16 (d.1) and Fig. UW-16.1(k) of ASME VIII, Div.1.

to:  the throat dimension of the outer attachment weld,  =0.5 tmin.

ti:   the throat dimension of the inside of the shell cutout,  ≥ 0.7tmin

to =  0.7 tmin = 0.7 x 0.118” =0.0826”, so the fillet leg size is 0.117”

ti  = 0.7 tmin = 0.7 x 0.197” =0.0826”, so the fillet leg size is 0.117”

to + ti = 0.0826” + 0.0826” = 0.165” ≥ 1.25 tmin =0.148”

Area of the reinforcement required Ar:

Per section UG-37(d)(1):

Ar = 0.5(dtrF + 2tntrF(1-fr1))

= 0.5 x (2.52” x 0.13” x 1.0 + 2 x 0.118” x 0.13” x 1.0 x 0.053)

= 0.5 x (0.3276 + 0.0016) in2

= 0.1646 in2

Where:

d:  Finished diameter of circle opening, see Fig. UG-37.1 of UG-37.

d = 2.52 in (per drawing ME-443054)

F: Correction factor

fr : Strength reduction factor, not greater than 1.0

fr1 = Sn / Sv  for nozzle wall inserted through the vessel wall

fr2 = Sn / Sv = 14.2 / 15 =0.947

Area of reinforcement available Aa:

A1: Larger of the following calculated value: (area available in shell):

= d24(E1t – Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 0.9686” x  (1 x 0.375” – 1.0 x 0.13”) – 2 x 0.118” x 1.0 x .245” x 0.053

= (0.237 - 0.0031) in2

= 0.2339 in2

or      = 2(t + tn)(E1t –Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 2 (0.375” + 0.118”) x (1.0 x 0.375” – 1.0 x 0.13”) – 2 x 0.118” x 1.0 x .245” x

0.053

= (0.1208 – 0.0031) in2

= 0.1177 in2

So pick A1 = 0.2339 in2

where:

d24 ≈ 2 x 23% x [(Π do x 5.4o) ÷ 360o + dn22 + dn24 ] = 0.9686”,  per UG-42 (a)(1)

and section  C-C of drawing ME-443054. 51% is the portion of the cross section

can be considered between two openings (#22 & #24) by the ratio of the

diameters.

A2: Smaller of the following:

= 5 (tn-trn)tfr2

= 5 x (0.118 in – 0.011 in) x 0.375 in x 0.947

=  0.190 in2

or     = 5 (tn-trn) fr2tn

= 5 x (0.118 in – 0.011 in) x 0.947 x 0.118 in

= 0.0598 in2

So pick A2 = 0.0598 in2

A3:   Area available in inward nozzle, use the smallest value:

Since there is no inward nozzle

So pick A3 = 0.0 in2

A41: Outward nozzle weld

= leg2 fr2

= 0.112 in2 x 1.0

=0.012 in2

A43: Inward nozzle weld

= leg2 fr2

= 0.112 in2 x 1.0

= 0.012in2

Then:

Aa = A1 + A2 + A3 + A41 + A43

= (0.2339 + 0.0598 + 0 + 0.0121 + 0.0121) in2

= 0.3179 in2 > Ar = 0.1646 in2

# Per Fig. UG-37.1, section UG-37, the opening is adequately reinforced under the current designated boundary conditions.

4.7  Analysis for the Opening of Port #14 for the Reinforcement and Weld Size

The main vessel shell:

From section 4.1, it is found that  tr = 0.250”

The port #14:

do: 6.625”, outside dia. of the port.

di:  6.187”, inside dia . of the port.

tn:  0.219”, wall thickness  of the port.

trn: required thickness of the port.

L:  length of projection defining the thickness portion of integral reinforcement of the

port beyond the outside surface of the vessel wall.

L = 22.44”- 18.625 = 3.815”

E:  28 x 106 psi, modulus of elasticity of the material at the opening temp.

Material: SA 249-TP304L stainless steel pipe, Fa = Sn = 14,200 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

Reference drawings: Section K-K and detail L of ME-443027, and also as shown

from figure 4-4.3 and figure 4-5.1.

Find out the wall thickness required:

1.   Assuming  L1 = (22.44 – 18.625) in = 3.815 in, tr1 = 0.0625 in, then:

L1/do = 3.815/6.625 =0.5758

do/tr1 = 6.625/0.0625 = 106

From Fig. G and Fig. HA-3 of subpart 3 of Sect. II, part D:

A = 0.0023

B = 10500

Pa = (4B)/(3(do/tr1)) = (4 x 10500)/(3 x 106) = 132 psi > P

- Try: L2 = 3.815 in, tr2 = 0.02 in

L2/do = 0.5758

do/tr2 = 331

get:

A = 0.0004

B = 7000

Pa = (4B)/(3(do/tr2)) = (4 x 7000)/(3 x 331) = 28.2 psi > P

3.   Try: L3 = 3.815 in, tr3 = 0.0170 in

L3/do = 0.5758

do/tr3 = 390

get:

A = 0.00031

B = 4350

Pa = (4B)/(3(do/tr2)) = (4 x 4350)/(3 x 390) = 14.87 psi ≈ P

So: trn = tr3 = 0.017 in

Size of the weld required:

Per UG-37, UW-16 (d.1) and Fig. UW-16.1(k) of ASME VIII, Div.1.

to:  the throat dimension of the outer attachment weld,  =0.5 tmin.

ti:   the throat dimension of the inside of the shell cutout,  ≥ 0.7tmin

to =  0.7 tmin = 0.7 x 0.219” =0.153”, so the fillet leg size is 0.216”

ti  = 0.7 tmin = 0.7 x 0.219” =0.153”, so the fillet leg size is 0.216”

to + ti = 0.153” + 0.153” = 0.306” ≥ 1.25 tmin =0.274”

ti22 = to22 = 0.19” < ti14 = to14 = 0.21”

Area of the reinforcement required Ar:

Per section UG-37(d)(1):

Ar = 0.5(dtrF + 2tntrF(1-fr1))

= 0.5 x (6.187” x 0.25” x 1.0 + 2 x 0.219” x 0.25” x 1.0 x 0.053)

= (0.7734 + 0.0058) in2

= 0.7792 in2

Where:

d:  Finished diameter of circle opening, see Fig. UG-37.1 of UG-37.

d = 6.187 in (per drawing ME-443054)

F: Correction factor

fr : Strength reduction factor, not greater than 1.0

fr1 = Sn / Sv  for nozzle wall inserted through the vessel wall

fr2 = Sn / Sv = 14.2 / 15 =0.947

Area of reinforcement available Aa:

A1: Larger of the following calculated value: (area available in shell):

= d14(E1t – Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 5” x  (1 x 0.375” – 1.0 x 0.25”) – 2 x 0.219” x 1.0 x .125” x 0.053

= (0.625 - 0.0058) in2

= 0.6192 in2

or      = 2(t + tn)(E1t –Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 2 (0.375” + 0.219”) x (1.0 x 0.375” – 1.0 x 0.25”) – 2 x 0.219” x 1.0 x .125” x

0.053

= (0.1485 – 0.0058) in2

= 0.1427 in2

So pick A1 = 0.6192 in2

where:

d14 ≈ 2 x 71% x (Π do x 10.9o) ÷ 360o = 5.08”,  per UG-42 (a)(1) and section C-C of

drawing ME-443054. 71% is the portion of the cross section can be considered

between two openings (#24 & #14) by the ratio of the diameters.

A2: Smaller of the following:

= 5 (tn-trn)tfr2

= 5 x (0.219in – 0.017 in) x 0.375 in x 0.947

=  0.3587in2

or     = 5 (tn-trn) fr2tn

= 5 x (0.219 in – 0.017 in) x 0.947 x 0.219 in

= 0.2095 in2

So pick A2 = 0.2095 in2

A3:   Area available in inward nozzle, use the smallest value:

Since there is no inward nozzle

So pick A3 = 0.0 in2

A41: Outward nozzle weld

= leg2 fr2

= 0.212 in2 x 1.0

=0.044 in2

A43: Inward nozzle weld

= leg2 fr2

= 0.212 in2 x 1.0

= 0.044in2

Then:

Aa = A1 + A2 + A3 + A41 + A43

= (0.6192 + 0.2095 + 0 + 0.044 + 0.044) in2

= 0.9167 in2 > Ar = 0.7792 in2

Per Fig. UG-37.1, section UG-37 and UG-42, the opening is adequately reinforced under the boundary conditions.

Notes:

- The actual tr = 0.13” in the upstream end area after adding the stiffening rib as

shown in figure x.1, that leads even smaller value of Ar and larger value of Aa,

so the additional reinforcing element is not necessary.

- The analysis of the above is based on the opening in the upstream end of the

Vessel. Per sections A-A and C-C of drawing ME-443054, sections A-A and K-K of drawing ME-443027, #14 opening in the downstream end of the vessel has

larger space distance to its neighboring opening, to this end, we conclude that #14 opening at the downstream end is adequately reinforced under the current design configuration.

4.8     Calculations for the Opening of Port #20 for the Reinforcement and Weld Size

The main vessel shell:

From section x.x, it is found that  tr = 0.130”

The port #20:

do: 4.50”, outside dia. of the port.

di:  4.26”, inside dia . of the port.

tn:  0.120”, wall thickness  of the port.

trn: required thickness of the port.

L:  length of projection defining the thickness portion of integral reinforcement of the

port beyond the outside surface of the vessel wall.

E:  28 x 106 psi, modulus of elasticity of the material at the opening temp.

Material: SA 249-TP304L stainless steel pipe, Fa = Sn = 14,200 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

Reference drawings: Section J-J of ME-443027, and also as shown

from figure 4-4.3 and figure 4-8.1..

Figure 4-8.1, The 2D view of the port #20 from  drawing ME-443027-2

Find out the wall thickness required:

1.   Assuming  L1 = 2.771 in, tr1 = 0.035 in, then:

L1/do = 2.771/4.50 = 0.6158

do/tr1 = 4.50/0.035 = 129

From Fig. G and Fig. HA-3 of subpart 3 of Sect. II, part D:

A = 0.0015

B = 9500

Pa = (4B)/(3(do/tr1)) = (4 x 9500)/(3 x 129) = 98 psi > P

- Try: L2 = 2.771 in, tr2 = 0.025 in

L2/do = 0.6158

do/tr2 = 180

get:

A = 0.00089

B = 8400

Pa = (4B)/(3(do/tr2)) = (4 x 8400)/(3 x 180) = 62.2 psi > P

3.   Try: L3 = 2.771 in, tr3 = 0.013 in

L2/do = 0.6158

do/tr3 = 375

get:

A = 0.00032

B = 4400

Pa = (4B)/(3(do/tr2)) = (4 x 4400)/(3 x 375) = 15.64 psi > ≈ P

So: trn = tr3 = 0.013 in

Size of the weld required:

Per UG-37, UW-16 (d.1) and Fig. UW-16.1(k) of ASME VIII, Div.1.

to:  the throat dimension of the outer attachment weld,  ≥ 0.7tmin.

ti:   the throat dimension of the inside of the shell cutout,  ≥ 0.7tmin

to =  0.7 tmin = 0.7 x 0.120” =0.084”, so the fillet leg size is 0.119”

ti  = 0.7 tmin = 0.7 x 0.120” =0.084”, so the fillet leg size is 0.119”

to + ti = 0.084” + 0.084” = 0.168” ≥ 1.25 tmin =0.15”

Area of the reinforcement required Ar:

Per section UG-37(d)(1):

Ar = 0.5(dtrF + 2tntrF(1-fr1))

= 0.5 x (4.26” x 0.13” x 1.0 + 2 x 0.120” x 0.13” x 1.0 x 0.053)

= 0.5 x (0.5538 + 0.0017) in2

= 0.2778 in2

Where:

d:  Finished diameter of circle opening, see Fig. UG-37.1 of UG-37.

d = 4.26 in (per drawing ME-443054)

F: Correction factor

fr : Strength reduction factor, not greater than 1.0

fr1 = Sn / Sv  for nozzle wall inserted through the vessel wall

fr2 = Sn / Sv = 14.2 / 15 =0.947

Area of reinforcement available Aa:

A1: Larger of the following calculated value: (area available in shell):

= d20(E1t – Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 3.346” x  (1 x 0.375” – 1.0 x 0.13”) – 2 x 0.120” x 1.0 x .245” x 0.053

= (0.8198 - 0.0031) in2

= 0.8167 in2

or      = 2(t + tn)(E1t –Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 2 (0.375” + 0.120”) x (1.0 x 0.375” – 1.0 x 0.13”) – 2 x 0.120” x 1.0 x .245” x

0.053

= (0.2426 – 0.0031) in2

= 0.2395 in2

So pick A1 = 0.8167 in2

Where:    d20 ≈ 2 x 27% x 6.1975 = 3.346”,  per UG-42 (a)(1) and front view of drawing

ME-443054. 27% is the portion of the cross section can be considered between

two openings (#16 & #20) by the ratio of the diameters.

6.1975” = 14.036” (ctr. to ctr. distance of the openings #20 & #16) – 0.5 x

15.677”

A2: Smaller of the following:

= 5 (tn-trn)tfr2

= 5 x (0.120 in – 0.013 in) x 0.375 in x 0.947

=  0.190 in2

or     = 5 (tn-trn) fr2tn

= 5 x (0.120 in – 0.013 in) x 0.947 x 0.120 in

= 0.0608 in2

So pick A2 = 0.0608 in2

A3:   Area available in inward nozzle, use the smallest value:

Since there is no inward nozzle

So pick A3 = 0.0 in2

A41: Outward nozzle weld

= leg2 fr2

= 0.122 in2 x 1.0

=0.014 in2

A43: Inward nozzle weld

= leg2 fr2

= 0.122 in2 x 1.0

= 0.014in2

Then:

Aa = A1 + A2 + A3 + A41 + A43

= (0.8167 + 0.0608 + 0 + 0.014 + 0.014) in2

= 0.9055 in2 > Ar = 0.2778 in2

# Per Fig. UG-37.1, section UG-37, the opening is adequately reinforced under the designated boundary conditions.

5.  Analysis and Calculations for the Flanges,Their Bolts and Welds

5.1  Upstream End Flange, Sliding Flange and Bellow Flange

References: ME-443027-1, MD-443039, MD-443038,

TTF-CRY3-01.01.00, TTF-CRY3-01.03.00,

and Figure 5.1

Figure 5.1, Upstream end flanges with the below flange

Figure x.x.1 is the assembly configuration of the upstream flange connecting with the below flange, where the upstream flange is assumed as the combination of the flange MD-443038 and MD-443039.

It was found that:

A = 45.669” (dia.)

B1 = 42.677” (dia.)

B2 = 37.25” (dia.)

C = 44.488” (dia.)

G = 43.15” (41.85) (dia.)*

T1 = 1.654”

T2 = 1.181”

P = 14.7 psi

n = 24

E1 = E2 = 2.8 x 107 psi

*: There are 2 o’ring grooves, conservatively pick the larger one.

Material: SA 182-F304L stainless steel, Fa = Sf= 16,700 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

assuming bolt spec: ½ - 13 UNC

Ab = 24 x  0.1257 in2 = 3.0168 in2

The cross-sectional area of the bolts using the root  dia. (0.4001”) of the

thread in sq. in.

Per section Y-5.1, Y-5.2, figure Y-5.1.2 of Appendix Y,

Section 2-4, figure 2-4 of Appendix 2 of ASME VIII:

B1 > ½ C,

So it is defined as: Class 2, Category 3 flange

Flange Analysis:

The moment due to the pressure M’p:

M’p = HD’hD’ + HT’hT’ (per Y-6.2(3), Appendix Y, ASME VIII)

HD’= 0.785 B22 P

= 0.785 x 37.252 in2 x 14.7 psi

= 16,012 lbs.

HT’= 0.785P (B12 –B22)

= 0.785 x 14.7 psi (42.6772 – 37.252) in2

=  5,006 lbs.

hD’ = (B1 – B2) ÷ 2

= (42.677 – 37.25) in ÷ 2

= 2.7135 in

hT’ = (B1 – B2) ÷ 4

= (42.677 – 37.25) in ÷ 4

= 1.3568 in

So:    M’p = (16,012 x 2.7135) lbs-in + (5,006 x 1.3568) lbs-in

= 50,241 lbs-in

= C5

(per section Y-6.2(4)(a), Appendix Y, ASME VIII, Div.1)

Let:    C6 = 0.829 / log(B1/B2)

= 0.829 ÷ 0.059

= 14.051

(per section Y-6.2(4)(b), Appendix Y, ASME VIII, Div.1)

C1 = [1 – 2.095Js log(A/B1)] ÷ (- C6 – 1.738 Js)

(per section Y-6.2(4)(c), Appendix Y, ASME VIII, Div.1)

Where:

Js = (1/B1) [2hD/β + hC/α] + π ґB

hD = (C – B) / 2

=  (44.488 – 42.677) / 2 in

= 0.9055 in

hC =  (A – C) / 2

= (45.669 – 44.488) / 2 in

= 0.5905 in

β = ( C + B)/ 2B

= (44.488 + 42.677) / (2 x 42.677)

= 1.021

α = ( A + C)/ 2B

= (45.669 + 44.488) / (2 x 42.677)

= 1.056

ґB = (1/n)[4/(1 – ()2)1/2tan-1((1+ )/(1 - ))1/2 – π -2]

where:

= nD/ πC

= (24 x 0.551”) / π 44.488”

= 0.0946

D: the bolt hole diameter

ґB = (1/24)[4/(1 – (0.0946)2)1/2tan-1((1+ 0.0946)/(1 – 0.0946))1/2 – π –

2 x 0.0946]

= 0.041667 x (4.018 x 47.7141- π – 0.1892)

= 7.849

Js = (1/42.677”) [2 x 0.9055/1.021 + 0.5905/1.056] + π x 7.849

= 0.0234 x (1.774 + 0.559) + 24.658

= 24.713

So:

C1 = [1 – 2.095 x 24.713 x log(45.669/42.677)] ÷ ( - 14.051 – 1.738 x 24.713)

= ( 1 – 1.5236 ) ÷ (-57.0022)

= 0.0091

C2 = (1.738JpMp – C5C6) ÷ (- C6 – 1.738 Js)

(per section Y-6.2(4)(d), Appendix Y, ASME VIII, Div.1)

where:

Jp = (1/B1) [hD/β + hC/α] + π ґB

= (1/42.677”) [0.9055/1.021 + 0.5905/1.056] + π x 7.849

= 0.0234 x (0.8869 + 0.559) + 24.658

= 24.692

Mp = HDhD + HThT + HGhG (per sectionY-3, Appendix Y, ASME VIII)

HD = 0.785 B12 P

= 0.785 x 42.6772 in2 x 14.7 psi

= 21,017 lbs.

H   = 0.785G2P

= 0.785 x 43.152 in2 x 14.7 psi

= 21,486 lbs.

HT = H - HD

= 21,486 – 21,017

=  469 lbs.

hG  = (C – G)/2

= (44.488 – 43.15) in / 2

= 0.669 in

hD = 0.9055 in

hT = (hD  + hG) / 2

= 0.7873 in

HG = W – H, gasket load

(per section 2-3, appendix 2, ASME VIII)

W = H + Hp,

flange design load for the operating condition

(per section 2-5(c)(1), appendix 2, ASME VIII)

which leads to:

HG = W – H

=  H + Hp – H

=  Hp

= 2b x 3.14GmP

= 2 x 0.315 in x 3.14 x 43.15 in x 6.00 x 14.7 psi

=  7,529 lbs.

Mp = HDhD + HThT + HGhG

= (21,017 x  0.9055 + 489 x 0.7873 + 7,529 x 0.669)  lbs-in

= (19,031 + 385 + 5,037) lbs-in

= 24,453 lbs-in

C2 = (1.738JpMp – C5C6) ÷ (- C6 – 1.738 Js)

= (1.738 x 24.692 x 24,453 – 14.051 x 52,041) lbs-in ÷ (-14.051 – 1.738 x

24.713)

= 318,165 lbs-in / (- 57.002)

= - 5,582 lbs-in

For the rigid body rotation of the flange times E*:

E1* θrbi = X(C4 – C2) ÷ (1.206 log(A/B1) –XC3 – (1 – X)C1)

where:

C3 = - (0.575 – 1.206 Js log(A/B1)) ÷ (Js + t13/F1’)

F1’= 0 (per section Y-3(6c), Appendix Y, ASME VIII, Div.1)

C3 = - (0.575 – 1.206 Js log(A/B1)) ÷ (Js)

= - (0.575 – 1.206 x 24.713 x 0.0294) / 24.713

= 0.0122

C4 = - (JpMp) ÷ (Js + t13/F1’)

= - (24.692 x 24,453 lbs-in) / 24.713

= - 24,432 lbs-in

X = E1* / (E1* + E2*)

E1* = E1 t13

E2* = E2 t23

E1 = E2

X = E1 t13 / (E1 t13  + E2 t23 )

= t13 / (t13 + t23 )

= 4.525 / (4.525 + 1.647)

= 0.733

E1* θrbi = 0.733(-24,432 – (-5,582)) ÷ [(1.206 x 0.0294) –(0.733 x 0.0122) – (1 –

0.733) x 0.00919)]

= 0.733 x (-18,850) lbs-in ÷ (0.0355 – 0.0089 – 0.00245)

= - 13,817 lbs-in ÷ 0.02415

= - 572,133 lbs-in

E2* θrbii = - E1* θrbi (E2* / (E1*)

= - (-572,133 x 0.3635) lbs-in

= 207,970 lbs-in

Total Flange Moment at Diameter B1:

Ms1 = C3 (E1* θrbi) + C4

= 0.0122 x  (- 572,133 lbs-in) + (- 24,432 lbs-in)

=  - 31,412 lbs-in

Ms2 = C1 (E2* θrbii) + C2

= 0.00919 x 207,970 lbs-in + (- 5,582 lbs-in)

= - 3,671 lbs-in

Unbalanced Flange Moment at Diameter B1:

Mu1 = 1.206 (E1* θrbi) log(A/B1)

= 1.206 x (- 572,133 lbs-in) x 0.0294

=  - 20,286 lbs-in

Mu2 = 1.206 (E2* θrbii) log(A/B1)

= 1.206 x (207,970 lbs-in) x 0.0294

=  7,374 lbs-in

Balanced Flange Moment at Diameter B1:

Mb1 =  Ms1 - Mu1

= - 31,412 lbs-in - (- 20,286 lbs-in)

= - 11,126 lbs-in

Mb2 =  Ms2 - Mu2

= - 3,671 lbs-in – 7,374 lbs-in

= - 11,045 lbs-in

Slope of Flange at Diameter B1 times E:

E1 θBi = (5.46/π t13) (JsMb1 + JpMp) + E1* θrbi / t13

= 0.384 in-3 x (24.713 x (– 11,126 lbs-in) + 24.692 x 24,453 lbs-in) + (-

572,133 lbs-in / 4.525 in3)

= (126,273 + (-126,438)) psi

= -165 psi

E2 θBii = (5.46/π t23) (JsMb2 + JpMp) + E2* θrbii / t23

(per section Y-6.2(e), Appendix Y, ASME VIII, Div.1)

= [1.055 x (24.713 x (-11,045) + 24.692 x 24,453) + 207,970 / 1.647] psi

= (349,035 + 126,272) psi

= 475,307 psi

Contact Force between Flange at hc:

Hc = (Mp + Mb1) / hc

= (24,453 +(- 11,126)) lbs-in / 0.5905 in

= 22,569 lbs.

Bolt Load at Operating Conditions:

Wm1 = H + HG  + HC

=( 21,486 + 7,529 + 22,569) lbs

= 51,584 lbs.

Operating Bolt Stress fb:

fb  = Wm1 /Ab1

= 51,584 lbs / 3.0168 in2 (See page 52, section 5.1 of the note)

= 17,099 psi

Design Pre-stress in Bolts:

Si = fb – 1.159 hc2 (Mp + Mb1) / (2(1 – X)a t13 l re1B1)

where:

re1: ≈ 1.0, elasticity factor, the ratio between Eflange and Ebolt

a = (A + C) / 2B1

= (45.669 + 44.488) in / 2 x 42.677 in

= 1.056  (shape factor)

l: = t1 + t2 + 0.5db (calculated strain length of the bolt)

= (1.654 + 1.181 + 0.25) in

= 3.085 in

Si = 17,099 psi– 1.159 x 0.59052 in2 x (24,453 – 11,126)lbs-in / (2(1 – 0.733) x

1.056 x 1.6543 in3  x 3.085 in x 1.0 x 42.677 in)

= 17,099 psi – 5,386 lbs-in3 / 336 in5

= 17,083 psi

Redial Stress in Flange I @ Bolt Circle:

SR1 = 6(Mp + MS1) / t12(πC –nD)

= 6 x ( 24,453 -31,412) lbs-in / 1.6542 in2  x (π 44.488 in – 24 x 0.551 in)

= - 41,754 lbs-in / 346.175 in3

= | -121 | psi < Sn = 16,700 psi

Tangential Stress in Flange I @ Inside Diameter:

St1 = t1 E1 θBi / B1

= 1.654 in x -165 psi / 42.677 in

= |-6.39 | psi < Sn = 16,700 psi

Tangential Flange Stress Adjacent to Central Nozzle:

St2n = Y(M’p + MS2) / t22 B2

where:

Y = (1/(K-1))[0.66845 + 5.71690 K2log10K/(K2 -1)]

(per figure 2-7.1, Appendix 2, ASME VIII, Div. 1)

K = A/B

= 45.669 / 37.25

= 1.226

Y = (1/(1.226-1))[0.66845 + 5.71690 x 1.5031 x log10K/(K2 -1)]

= 4.4248 x (0.6685 + 5.7169 x 0.2643)

= 9.6437

St2 = 9.6437 x (50,241 – 3,671) lbs-in / (1.1812 x 37.25) in3

= 8,644 psi < Sn = 16,700 psi

Longitudinal Hub Stress in Flange 1:

Sh1 = 0

(per equation (34c), section Y-6.3, appendix Y, ASME VIII, Div.1)

Radial Stress in Flange 2 @ bolt circle:

Sr2b = 6(Mp + MS2) / t22(πC –nD)

= 6 x ( 24,453 – 3,671) lbs-in / 1,1812 in2  x (π 44.488 in – 24 x 0.551 in)

= 124,692 lbs-in / 176.492 in3

= 707 psi < Sn = 16,700 psi

Radial Stress in Flange 2 @ Diameter B1:

Sr2B1 = 6 MS2 / t22 πB1

= 6 x (-3,671) lbs-in / 1.1812 in2  x π 42.677 in

= |- 118 | psi < Sn = 16,700 psi

Tangential Stress in Flange 2 @ Diameter B1:

St2B1 =  t2 E2 θBii / B1 – 1.8 MS2 / t22 πB1

= (1.181 in x 475,307 psi / 42.677 in) – (1.8 x (– 3,671 lbs-in)) / 1.1812 in2

π 42.677 in

= 13,153 psi + 35 psi

=  13,188 psi < Sn = 16,700 psi

Radial and Tangential Stress at Center of Flange 2:

Sr2 = St2 = (0.3094 PB12 / t22) – (6 MS2 / πB1 t22)

= (0.3094 x 14.7 psi x 42.6772 in2 / 1.1812 in2 )

- ( 6 x (-3,671 lbs-in) / π 42.677 in x 1,1812 in2 )

= 5,939 psi + 118 psi

= 6,057 psi < Sn = 16,700 psi

Welds Analysis and Calculations:

See UW-13 (e)(2), Fig. UW-13.2, section 2-3 and  Fig. 2-4(4a), Appendix 2 of

ASME VIII, Div.1. for the related codes and the physical representation of the

nomenclatures.

Per above codes, it is required that the throat of the fillet  c = 0.7tmin. = 0.26”,

So the fillet leg size is ~ 0.37”.

However, per the assembly configuration of the upstream flange connecting with

the below flange (see drawing TTF-CRY3-01.01.00 & TTF-CRY3-01.03.00), it is

found that there only has ~0.19 clearance between flange MD-443038 and

MD-443039, so it is suggested to use 0.37” bevel groove instead of 0.37” fillet weld to

meet the related code required and to avoid the parts interference.

It is found that:

tp= 0.32” > 0.25”

where is the smallest of tn, tx and 0.25” is 0.25”

c = tn = 0.375” = leg of the fillet or bevel groove

b = 0.16” + 2 x tan 15o x 0.43”

= 0.39”

a = 0.43” + 0.37”- 0.06”

= 0.74”

a + b = 1.13” ≥ 3tn = 1.125”

The weld design for the end flange is ok.

Also run a weld strength calculation for the noted location as the 2nd analysis

approach:

Radial pressure load Frp:

Frp = P Lsd

= 14.7 psi x 230 in

= 3,381 lbs/in

Shear flow due to radial shear load Fsr:

Fsr = VQ/I

where:

Radial shear load V:

V = 0.01 P Lsd Do

= 0.01 x 14.7 psi x 230 in x 38,0 in

= 1,285 lbs.

The 1st moment of area Q:

Q = 2.67 in x 0.375 in x (1.1454 – 0.1875) in

= 0.959 in3

I = 2.4101 in4

Fsr = VQ/I

= 1,285 lbs. x 0.959 in3 / 2.4101 in4

=  511 lbs/in

The required resultant weld load Frw:

Frw = ( 3,3812 + 5112)1/2 lbs/in

=  3,419 lbs/in

The welds for connecting the flange and the vessel shell is single groove weld inside

and intermittent fillet outside, the lowest allowable weld stress Faw:

Faw = 0.60 Sn = 0.60 x 16.7 ksi

= 10.02 ksi

The requires calculated minimum weld size Cm:

Cm  =  Frw / Faw

= 3,419 / 10,020 (in)

= 0.341 in < 0.43 in (designated single groove weld)

If adding the value of the outside intermittent bevel groove weld (0.0.37”), the weld

size even can go further smaller size.

So, the design of the weld for the upstream end flange is satisfactory.

Per the above calculationsand analysis, the upstream end flange and the bellow flange have met the codes of ASME VIII, Div.1.

5.2.        Downstream End Flange and Bellow Flange

References: ME-443027-1, MC - 443040,

TTF-CRY3-01.01.00, TTF-CRY3-01.03.00

Since there some information are missing at this moment, so it is to make the best assumption as followings:

1. The downstream end flange MC-443040 connect to the upstream end flange of the

bellow (see drawing TTF-CRY3-01.03.00).

2. The above two flanges are connected by the clamps, the center line of the clamp

C = 43.78” + (45.47 – 43.78”) / 2 = 44.625”.

3.  A = 45.669”, G = 44.488”, T1 = 1.57”, T2 = 1.57”, B1 = 42.677”, B2 = 37.37.25”.

4. n = 12,  D = 0.55”

Material: SA 182-F304L stainless steel, Fa = Sf= 16,700 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

Per section Y-5.1, Y-5.2, figure Y-5.1.2 of Appendix Y,

Section 2-4, figure 2-4 of Appendix 2 of ASME VIII:

B1 > ½ C,

So it is defined as: Class 2, Category 3 flange

In order to reduce the amount of work required as shown on section 5.1, per section Y-9, of Appendix Y, ASME VIII, Div.1, we apply the method of estimating flange thickness and bolting for the downstream flanges.

ta = 2.45 [Mp / ((πC –nD)Sf)]1/2

(per eq. 39 of Y-9, appendix Y, ASME VIII, Div.1)

where:

Mp = HDhD + HThT + HGhG (per sectionY-3, Appendix Y, ASME VIII)

HD = 0.785 B12 P

= 0.785 x 42.6772 in2 x 14.7 psi

= 21,017 lbs.

H   = 0.785G2P

= 0.785 x 44.4882 in2 x 14.7 psi

= 22,839 lbs.

HT = H - HD

= 22,839 – 21,017

=  1,822 lbs.

hG  = (C – G)/2

= (44.625 – 44.488)in / 2

= 0.0685 in

hD = (C – B) / 2

= ( 44.625 – 42.677) / 2

= 0.974 in

hT = (hD  + hG) / 2

= 0.5213 in

HG = W – H, gasket load

(per section 2-3, appendix 2, ASME VIII)

W = H + Hp,

flange design load for the operating condition

(per section 2-5(c)(1), appendix 2, ASME VIII)

which leads to:

HG = W – H

=  H + Hp – H

=  Hp

= 2b x 3.14GmP

= 2 x 0.315 in x 3.14 x 44.488 in x 6.00 x 14.7 psi

=  7,766 lbs.

Mp = HDhD + HThT + HGhG

= (21,017 x  0.974 + 1,822 x 0.5213 + 7,766 x 0.0685)  lbs-in

= (20,471 + 950 + 532) lbs-in

= 21,953 lbs-in

ta = 2.45 [Mp / ((πC –nD)Sf)]1/2

= 2.45 x [ 21,953 lbs-in / ((π 44.625 in – 24 x 0.551 in) x 16,700 psi)]1/2

= 2.45 x 0.102 in

= 0.250 in

tb = 0.56 B1 (P/Sf)1/2

= 0.56 x 42.677 in x (14.7 psi / 16,700 psi)1/2

= 0.56 x 42.677 in x 0.0297

= 0.71 in

Since tc is the greater of ta or tb, so:

tc = tb = 0.71”

Per equation 42 of A-7, Appendix Y, ASME VIII, Div. 1:

A’b = (H + 2 Mp / (A – C)) ÷ Sb

= (22,839 lbs + 2 x 21,953 lbs-in / (45.669 – 44.625) in ) ÷ 20,000 psi

= (22,839 lbs + 42,056 lbs) / 20,000 psi

= 3.245 in2

Per Table Y-9.1, Appendix Y, ASME VIII, Div.1, it is found:

t1 = 1.1ta = 0.275” < T1 = 1.57”

t2 = 1.1tc = 0.781” < T2 = 1.57”

So the thickness of the flanges are ok for the downstream end flanges.

Welds Analysis and Calculations:

The weld configurations are the same as the upstream flange, it designed per section UW-13 (e)(2), Fig. UW-13.2, section 2-3 and Fig. 2-4(4a), Appendix 2 of ASME VIII, Div.1

Also, since the valus of Lsd for downstream end flange is ~45” (~230” for upstream end flange), I value for downstream end flange is large than the upstream flange, all these lead to a smaller values of Frw and Cm than the upstream end flange requires, however, the designated welds of the downstream end flange are the same as the upstream end flange, so the welds design are satisfactory.

Per the above calculations, the upstream end flange and the bellow flange have met the codes of ASME VIII, Div.1.

5.3.            Flanges #8, #11, #13, #15, #19, #21 & #23

In order to reduce the amount of work required as shown on section 5.1, per section Y-9, of Appendix Y, ASME VIII, Div.1, we apply the method of estimating flange thickness and bolting for the above flanges.

Since the information of the most mating flanges are not available at this moment, I made some engineering judgments per the best of my logic knowledge.

Table 5.3,  Estimated Calculated Flange thickness and bolting VS. the designated data

|  |  | Flanges (see drawing ME-443027) |
| --- | --- | --- |
| nomenclature | unit | #8 | #11 | #13 | #15 | #19 | #21 | #23 |
|  |  | MC-443037 | MC-443034 | MC-443036 | MC-443031 | MC-443033 | MC-443035 | MC-443032 |
| P | psi | 14.7 | 14.7 | 14.7 | 14.7 | 14.7 | 14.7 | 14.7 |
| Sf | psi | 18,800 | 18,800 | 18,800 | 18,800 | 18,800 | 18,800 | 18,800 |
| A | in | 10.945 | 5.512 | 8.67 | 13.78 | 6.535 | 11.22 | 4.472 |
| B1 | in | 8.386 | 3.334 | 6.194 | 11.418 | 4.26 | 8.386 | 2.522 |
| B2 | in | 3.75 | 3.334 | 0 | 0 | 0 | 0 | 0 |
| C | in | 9.646 | 4.882 | 7.874 | 12.99 | 5.748 | 10.236 | 3.628 |
| G | in | 8.793 | 4.012 | 7.034 | 12.204 | 5.004 | 9.311 | 3.024 |
| Classification | 3 | 1 | 3 | 3 | 3 | 3 | 3 |
| Categorization | 3 | 3 | 3 | 3 | 3 | 3 | 3 |
| n |  | 24 | 4 | 8 | 8 | 6 | 12 | 8 |
| D | in | 0.3125 | 0.394 | 0.394 | 0.394 | 0.394 | 0.335 | 0.335 |
| m |  | 6 | 6 | 6 | 6 | 6 | 6 | 6 |
| b |  | 0.21 | 0.21 | 0.21 | 0.21 | 0.21 | 0.21 | 0.21 |
| HD | lbs | 812 | 128 | 443 | 1504 | 209 | 812 | 73 |
| H | lbs | 892 | 186 | 571 | 1719 | 289 | 1000 | 106 |
| HT | lbs | 81 | 57 | 128 | 214 | 80 | 189 | 32 |
| hG | in | 0.4265 | 0.435 | 0.42 | 0.393 | 0.372 | 0.4625 | 0.302 |
| hD | in | 0.63 | 0.774 | 0.84 | 0.786 | 0.744 | 0.925 | 0.553 |
| hT | in | 0.5283 | 0.6045 | 0.6300 | 0.5895 | 0.5580 | 0.6938 | 0.4275 |
| HG | lbs | 1023 | 467 | 818 | 1420 | 582 | 1083 | 352 |
| MP | lbs-in | 990 | 337 | 796 | 1867 | 417 | 1383 | 161 |
| ta | in | 0.1178 | 0.0885 | 0.1086 | 0.1258 | 0.0921 | 0.1253 | 0.0767 |
| tb | in | 0.1313 | 0.0522 | 0.0970 | 0.1788 | 0.0667 | 0.1313 | 0.0395 |
| tc | in | 0.1313 | 0.0885 | 0.1086 | 0.1788 | 0.0921 | 0.1313 | 0.0767 |
| A'b | in^2 | 0.1285 | 0.0668 | 0.1368 | 0.3428 | 0.0717 | 0.2027 | 0.0258 |
| t1 | in | 0.1296 | 0.0885 | 0.1194 | 0.1384 | 0.1013 | 0.1378 | 0.0844 |
| t2 | in | 0.1444 | 0.0885 | 0.1194 | 0.1967 | 0.1013 | 0.1444 | 0.0844 |
| Ab | in^2 | 0.1350 | 0.0668 | 0.1436 | 0.3599 | 0.0753 | 0.2128 | 0.0271 |
| t1d | in | 0.787 | 0.512 | 0.709 | 0.79 | 0.51 | 0.984 | 0.68 |
| t2d | in | N/A | 0.512 | N/A | N/A | N/A | N/A | N/A |
| Abd | in^2 | 1.088 | 0.271 | 0.542 | 0.542 | 0.4065 | TBA | TBA |

The most representation of nomenclature of the Table can be found from section 5.1 of this note, also from the appendix 2 and appendix Y of ASME VIII, Div.1, except:

t1,  Estimated calculated flange 1 thickness

t2,  Estimated calculated flange 2 thickness

Ab, Estimated calculated root diameter area of the bolts.

t1d,  Designated flange 1 thickness

t2d,  Dersignated flange 2 thickness

Abd, Designated root diameter area of the bolts.

Per table 5.3, it is found that all t1 > t1d; t2 > t2d and Ab > Abd for all respective flanges, so the flange design are satisfactory.

Per figure UW-13.2, section UW-13, appendix 2 of ASME VIII, Div. 1 and drawing ME-443027, it is found that all flange welds are designed per the related codes.

6.    Calculation and Analysis of the Saddle support

Reference drawing:     ME-443027

Figure: 6.1 and Figure 6.2

Per drawing ME-443027 and figure x.x.1, it is found that:

Lc = 163.50 x 2 = 327 in (the ctr. distance between 2 saddle support.)

Wws = 7,745 lbs. the weight of the vessel shell weldment.

Wother = 8,846 lbs.,

the weight of coldmass shields & pipe, 8 cavity string w/mech. turners,

individual dressed cavity w/turner, main coupler.

Wtot = 1.05 (Wws + Wtot ) ≈ 17,421 lbs

(Total weight including 5% mice. parts weight applying to two saddle supports)

Figure 6.1, The weight and the location of the ctr. of gravity of the vessel shell assembly.

The force distribution diagram on figure x.x.2 is created conservatively based on the information from figure x.x.1 and drawing ME- 443027.

It is found that:

Q1 + Q2 = 17,421 lbs = Wtot

Q2 = (Wtot x 148.13) / 327

the reaction force on the downstream saddle support.

= 7,892 lbs

Q1 = 9,529 lbs.

the reaction force on the upstream saddle support.

A = 76.854 in

the distance from the end of the upstream end to the ctr, of the 1st saddle support.

Ltot ≈ 448 in

Θ = 120o, the value of the assuming contact angle of the saddle support.

Figure 6.2, The force distribution diagram of the vacuum vessel.

To find the longitudinal stress on the saddle support 1:

f1s = QA [ 1 – (1 – A/L + (R2 – H2) / 2AL) / (1 + 4H/3L)] / KR2ts

where H = 0,

R = 19.0”

K = constant, from page 88 of Pressure Vessel Handbook,  7th edition,

by E. Megyesy

f1s = 9,529 lbs x 76.854” x [1 - (1 – 76.854 / 448 + (192 / 2 x 76.854 x 448))

÷ (1 + 0)] / (0.335 x 192 x 0.375 in3)

= 732,342 lbs-in x [ 1- (1 – 0.1715 + 0.0052)] ÷ 45.351 in3

= 2,686 psi

To find the longitudinal stress on the middle of the span:

f1m = (QL/4) [(1 + 2 (R2 – H2) /L2)) / (1 + 4H/3L) – 4A/L] / KR2ts

= 1,067,248 lbs-in x ( 1.0036 – 0.6862) ÷ 45.351 in3

= 7,469 psi

Stress due to the pressure:

fp = PR / 2ts

= 14.7 psi x 19.0 in / 2 x 0.375 in

= 373 psi

So, the total longitudinal stress at the middle span of the vessel:

fbm =  f1m + fp = 7,469 psi + 373 psi

= 7,842 psi < 0.80 Fa = 12 ksi

where:

Fa: allowable stree, see page x.

0.80, joint efficiency, see Table UW-12, section UW-12, ASME VIII, Div.1.

To find the tangential stress on the vessel shell:

f2t = (K2Q / Rts )( L -2A) / (L + 1.333H)

= ((1.1712 x 9,529 lbs./ 19 in x 0.375 in)  x (448 – 2 x 76.854) in) ÷ 448 in

= 1,834 psi x 294.29 in / 448 in

= 1,197 psi < 0.80 Fa = 12 ksi

To find the circumferential stress on the vessel shell:

f4c =  (Q / (4ts(b + 1.56(Rts)1/2) – 3K6Q / 2ts2

where:  b, the width of the saddle support, assuming 3/4 inch, so:

f4c  = [9,529 lbs / 4 x 0.375 in x (0.75 + 1.56 x (19 x 0.375)1/2 in] – (3 x 0.053 x 9,529

lbs / (2 x 0.3752 in2))

= -1,293 psi – 5,387 psi

= |- 6,680| psi < 1.50 Fa = 22.5 ksi

So, all the stresses are less than the allowable stress respectively, so the saddle support design is satisfactory (Since the design hasn’t finished yet, the calculation and analysis is

based on the assumption of: the saddle support has al least 120o degree contact angle with 3/8 in thick wear plate).

- Appendix

  - The Lists of the Design Drawings of 1.3 MHz, β = 1, Cryomodule Vacuum

Vessel (Fermilab)

1.  Vacuum Vessel Weldment Assy.                  ME – 443027 – 1 (2)

2.  Vessel Shell                                                   ME – 443054

3.  Port End Coldmass                                        MD – 443050

4.  Port Middle Coldmass                                   MD – 443049

5.  Pick Point Weldment                                     MC – 443028

6.  Pad Weld Upper                                             MC – 443043

7.  Vessel Support Weldment                              MC – 443029

8.  Pad Weld Lower                                             MC – 443042

9.  Flange MC Port                                              MC – 443037

10. Instrumentation Flange                                   MC – 443034

11. Flange Side Rib                                               MB - 443051

12. Flange – K1, K3                                              MC – 443036

13. Flange D                                                          MC – 443031

14. MC Bracket Weldment – LH                          MC – 443058

15. MC Bracket Weldment – RH                          MC – 443059

16. Flange E.O.D. 166                                           MC – 443033

17. Flange G.O.D. 285                                           MC – 443035

18. Flange DN 63 DF                                             MC – 443032

19. Ring Flange Stop                                              MC – 443053

20. Stiffening Rib                                                   MC – 443052

21. Pipe Support Plate                                            MC – 443047

22. Plate Welded Outrigger                                    MC – 443048

23. Gusset Welded Outrigger                                 MC – 443041

24. Flange, Fixed Downstream                               MC – 443040

25. Flange, Fixed Upstream                                    MC – 443039

26. Flange, Bellow Sliding                                      MD – 443038

27. Flange Weld Ring                                              MC – 443060

  - The Lists of the Design Drawings of 1.3 MHz, β = 1, Cryomodule Vacuum

Vessel (ARES - TTF)

1. Vacuum Vessel Shell Assy.                                 TTF – CRY3 – 01.01.00

2. Support Post Cover                                              TTF – CRY3 – 01.01.01

3. Vacuum Vessel Shell Details                               TTF – CRY3 – 01.01.02

4. Adjustable Support Assy.                                     TTF – CRY3 - 01.02.00

5. Adjustable Support Details                                   TTF – CRY3 – 01.02.01

6. Universal Expansion Joint                                    TTF – CRY3 – 01.03.00

# Text boxes

148.132

Q2

Q1

327.0

W

A

L