Mr. John Giusti

Acting Chief of the International Bureau

Federal Communications Commission

445 12th Street SW

Washington, D.C. 20554

Dear Mr. Giusti:

The National Telecommunications and Information Administration (NTIA), on behalf of the Executive Branch Agencies, has approved the release of an additional draft Executive Branch proposal for WRC-07.  This proposal considers the federal agency inputs toward the development of U.S. Proposals for WRC-07.

The enclosed draft proposal for Agenda Item 1.6 (Res. 415) is a clean-up item promised by NTIA in the Executive Branch comments to the FCC FNPRM on Part 87 of the Commission's rules concerning the aviation radio service, WT Docket Number 01-289.  NTIA filed comments with the FCC on September 13, 2004 indicating that the allocation for AMS(R)S under RR 5.198 can be deleted from the International Radio Regulations, and consequently from the U.S. allocation table and that NTIA would undertake to make this proposal during WRC-07 proposal preparation.

This proposal is forwarded for your consideration and review by your WRC-07 Advisory Committee.  Jim Vorhies of my staff is the primary contact for NTIA.

Sincerely,

(Original Signed December 11, 2006)

Fredrick R. Wentland

Associate Administrator

Office of Spectrum Management

Enclosure

United States of America

## DRAFT PROPOSAL FOR THE WORK OF THE CONFERENCE

Agenda Item 1.6 (Res. 415): to consider additional allocations for the aeronautical mobile (R) service in parts of the bands between 108 MHz and 6 GHz, in accordance with Resolution 414 (WRC-03) and, to study current satellite frequency allocations, that will support the modernization of civil aviation telecommunication systems, taking into account Resolution 415 (WRC-03)

Background Information:  This proposal considers the suppression of the secondary allocation to the aeronautical mobile-satellite (R) service (AMS(R)S) in the 117.975 – 136 MHz band.

Existing aeronautical mobile (R) service bands are nearing saturation in high traffic areas.  In addition, new applications and concepts in air traffic management put further pressure on existing aeronautical mobile bands.  In particular, the 117.975 - 136 MHz band is extremely congested due to increased aeronautical mobile use in the band.  For the aforementioned reasons, and since there are no operational or planned AMS(R)S systems in this band, the secondary allocation to AMS(R)S in RR No. 5.198 should be suppressed.

Proposal:

USA/  / 1	MOD

75.2-137.175 MHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| .... |
| 117.975-137 AERONAUTICAL MOBILE (R) 5.111 SUP 5.199 5.200 5.201 5.202 5.203 5.203A 5.203B |
| .... |

Reasons:  The modification of the table is due to the suppression of 5.198.

USA/  / 2	SUP

5.198	Additional allocation:  the band 117.975-136 MHz is also allocated to the aeronautical mobile-satellite (R) service on a secondary basis, subject to agreement obtained under No. 9.21.     (WRC-97)

Reason:  The secondary allocation by footnote to AMS(R)S is no longer needed.

# Footnotes

This proposal is an additional proposal to previous proposals made under this agenda item.