MSFC PRACA : 2003-02-12 08:41

MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A15408 | In-Flight Anomaly Number -- | Contractor Report Number E-151 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title ELECTRICAL CONNECTOR FAILED A DIELECTRIC WITHSTAND VOLTAGE TEST AT MAF |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1 |
| HCRIT -- | Sys_Lvl -- | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE ELECTRICAL CONNECTOR | PART# NB SERIES (18-32 INS | SER/LOT# N/A | MANUFACTURER ITT CANNON |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EL - SHORT | Cause MA - MFG-ASY |
| System ELECTRICAL | Defect CN - CONTAM | Material F - INSUL | Work Contact JOHN ADAMS | Fail Date 02/19/1993 |
| Received at MSFC 05/19/1993 | Date Isolated 02/19/1993 | FMEA Reference 3.1.4.1 & 3.1.5.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom EL - SHORT | Time Cycle -- |
| Effectivity Text -- |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 09/03/1993 | CN RSLV SBMT 08/12/1993 | Defer Date 06/11/1993 | Add Date 05/19/1993 | R/C Codes 2 - MFG -- -- |
| Assignee |
| Design R. MOYE | Chief Engineer R.A. MOYE | S & MA R. JACKSON | Project -- | Project MGR P. COUNTS |
| Approval |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR P. COUNTS |
| PAC Assignee B. HURST | PAC Review Complete BH | MSFC Closure Date 08/25/1993 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID T-127033 |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description AN NB SERIES ELECTRICAL CONNECTOR FAILED A DIELECTRIC WITHSTAND VOLTAGE TEST (DWV) AT MAF. FAILURE ANALYSIS OF THE CONNECTOR FOUND THE CAUSE TO BE A FOREIGN PARTICLE, QUARTZ, IN THE CONNECTOR INSERT. THE VENDOR OF THE CONNECTOR REVIEWED THE FAILURES REPORTED TO THEM BY OTHER USERS AND FOUND A NEARLY IDENTICAL FAILURE. THIS SECOND FAILURE OCCURED IN A CONNECTOR PRODUCED USING AN INSERT FROM THE SAME PRODUCTION RUN AS THAT WHICH FAILED AT MAF. NOTIFICATION OF THE SECOND FAILURE WAS RECEIVED FROM ITT CANNON ON MAY 13, 1993. AT THAT TIME THE FAILURE WAS DETERMINED TO MEET THE PROBLEM REPORTING REQUIREMENTS CRITICALITY: THE ORIGINAL FAILURE WAS A DWV FAILURE BETWEEN PINS "Y" AND "Z" OF CONNECTOR 314W02J2. THESE CONTACTS ARE PART OF LOX LEVEL SENSOR CIRCUITS FOR 326A09 AND 326A11. THESE CIRCUITS ARE CRIT. 3, FMEA ITEM CODES 3.1.4.1 AND 3.1.5.1, "FAILS WITH FALSE WET SIGNAL." HOWEVER, THE 18-32 INSERTS ARE USED IN OTHER APPLICATIONS ON THE ET WHICH ARE CRIT. 1 *REVISION "B"--UPDATES AND CLOSES ALL TASKS. (SEE ASTERISKS) |
| Contractor Investigation/Resolution GENERAL: WIRE HARNESS 314W02 ON ET-68 FAILED A DIELECTRIC WITHSTAND VOLTAGE TEST (DWV) DURING WORK IN THE FINAL ASSEMBLY AREA. THE HARNESS HAD A RESISTANCE LESS THAN THE MINIMUM ACCEPTABLE VALUE OF 3 MEGOHMS AT 1500 VOLTS REQUIRED BY TEST PROCEDURE-6R101-FA. THE FAILURE OCCURRED BETWEEN CONTACTS "Y" AND "Z" OF CONNECTOR JACK 2 (J2). TROUBLESHOOTING OF THE HARNESS ISOLATED THE FAILURE TO THE CONNECTOR INSERT OF J2 THE TEST PROCEDURE WAS BEING PERFORMED IN FINAL ASSEMBLY DUE TO TEST ERRORS DURING THE ORIGINAL ACCEPTANCE TESTS IN THE HARNESS FABRICATION SHOP. THE TEST ERRORS WERE ADDRESSED IN CAPS E-148 THE DEFECTIVE CONNECTOR WAS AN NB7E18-32PWR ASSEMBLED BY TIME ELECTRONICS FROM COMPONENTS MANUFACTURED BY ITT CANNON. THE CONNECTOR HAD THE TIME ELECTRONICS LOT CODE 8517-71. THE LOT CODE INDICATES THAT THE CONNECTOR WAS ASSEMBLED IN THE SEVENTEENTH WEEK OF 1985 AND WAS THE SEVENTY-FIRST LOT OF THAT WEEK. FAILURE ANALYSIS T-127033 TRACED THE CAUSE OF THE DWV FAILURE TO A QUARTZ PARTICLE INCLUSION IN THE MOLDED PHENOLIC INSULATION MANUFACTURED BY CANNON ITT CANNON HAD A VIRTUALLY IDENTICAL FAILURE REPORTED TO THEM IN MAY OF 1990 BY ANOTHER CUSTOMER. THE OTHER FAILURE OCCURRED IN AN NB6GE18-32PNT3 CONNECTOR ASSEMBLED BY TIME ELECTRONICS. THAT CONNECTOR HAD A LOT CODE 8513-84. BOTH CONNECTORS HAD INSERTS FROM THE SAME ITT CANNON PRODUCTION RUN TASK I. FAILURE INVESTIGATION *A.ITT CANNON IS INVESTIGATING THE PRODUCTION HISTORY OF THE TWO FAILED CONNECTORS. THE GOAL IS TO IDENTIFY ALL CONNECTORS ASSOCIATED WITH THE INSERT PRODUCTION RUN USED IN THE TWO FAILED CONNECTORS RESPONSIBILITY: D. HUDSON/3830 -- M.COMBS/3830 J. ADAMS/3741 -- D. WESTPHAL/3740 COMPLETE: JULY 26, 1993 CLOSURE STATEMENT ITT CANNON WAS UNABLE TO IDENTIFY THE SPECIFIC CONNECTOR PART NUMBERS AND LOT CODES THAT MAY BE AFFECTED. PROBLEMS AROSE DUE TO THE LENGTH OF TIME WHICH ELAPSED SINCE MANUFACTURE OF THE CONNECTORS AND THE COORDINATION WITH THE ASSEMBLY FIRM, TIME ELECTRONICS. THE RELATED PARTS MAY BE ANY NON-HERMETIC CONNECTOR OF THE 18-32 INSERT CONFIGURATION, PIN OR SOCKET CONTACT TYPE, MADE BETWEEN JANUARY 1984 AND DECEMBER 1985 *B.RELIABILITY ASSURANCE IS RECOVERING THE TRACEABILITY RECORDS FOR ALL TIME ELECTRONICS AND ITT CANNON CONNECTORS, OF THE 18-32 CONFIGURATION, USED ON THE ET. THE SEARCH IS LIMITED TO THE 1984 THROUGH 1986 TIME FRAME RESPONSIBILITY: J. ADAMS/3741 -- D. WESTPHAL/3740 COMPLETE: JULY 1, 1993 CLOSURE STATEMENT OVER 170 CONNECTORS WERE IDENTIFIED AS HAVING BEEN RECEIVED FROM ITT CANNON OR TIME. THE FAILED CONNECTOR WAS THE ONE RECEIVED WITH THAT PART NUMBER AND LOT CODE TASK CLOSED TASK II. CORRECTIVE ACTION *A.GOVERNMENT-INDUSTRY DATA EXCHANGE PROGRAM (GIDEP) ALERT 9Q-A-93-02 ISSUED AGAINST ITT CANNON CONNECTORS WITH THE 18-32 INSERT CONFIGURATION AND WITH LOT CODES 8401-## THROUGH 8552-## RESPONSIBILITY: B. CORNAY/3742 D. WESTPHAL/3740 COMPLETE: JULY 26, 1993 *B.SUPPLIER CORRECTIVE ACTION REQUEST (SCAR) 93-076 WAS ISSUED TO ITT CANNON FOR THE FAILED CONNECTOR. IN RESPONSE, CANNON CITED IMPROVED MANUFACTURING CONTROLS, IMPLEMENTED IN THE EIGHT YEARS SINCE THE FAILED PART WAS PRODUCED, WHICH REDUCE THE LIKELIHOOD OF A RECURRENCE RESPONSIBILITY: T. PASTORET/3742--D. WESTPHAL/3740 COMPLETE: JULY 13,1993 TASK CLOSED TASK III. CLEARANCE OF EFFECTIVITIES ALL ET'S CLEARED. THE CONNECTOR FAILED DURING ACCEPTANCE TESTING AND ALL DELIVERED ETS HAVE PASSED THE ACCEPTANCE TESTS. THE FAILURE OCCURRED AT 1500 VOLTS; NO SERVICE VOLTAGE ON THE ET EXCEEDS 100 VOLTS. NO CRITICALITY 1 CIRCUIT HAS A SERVICE VOLTAGE EXCEEDING 32 VOLTS DC NOTE: THIS IS ALSO THE DEFERRAL RATIONALE TASK CLOSED CAUSE: VENDOR ERROR; THE CONNECTOR FAILED AS THE RESULT OF CONTAMINATION IN THE PHENOLIC INSULATION TASK IV. CAPS CLOSURE SUMMARY A SINGLE CONNECTOR FAILED A 1500 VOLTS TEST. NO SERVICE VOLTAGE OF A CRITICALITY 1 CIRCUIT ON THE ET EXCEEDS 32 VOLTS DC. ITT CANNON HAS IMPROVED THE MANUFACTURING CONTROLS FOR THE CONNECTORS. THE EXISTING PERFORMANCE TESTS IN THE ET BUILD CYCLE ARE SUFFICIENT TO ASSURE PERFORMANCE TASK CLOSED THIS CAPS IS CLOSED. NO FURTHUR ACTION IS REQUIRED |
| MSFC Response/Concurrence 6/2/93 - DEFERRAL RATIONALE: BASED ON THE DEFERRAL RATIONALE IN "TASK III. CLEARANCE OF EFFECTIVITIES"(ABOVE), THIS REPORT HAS BEEN DEFERRED FOR THE NEXT SIX MONTHS PER NSTS 07700, VOLUME XI, PARAGRAPH 3.4.1, ITEM C AND NSTS 08126 REV. E PARAGRAPH 3.3.10.1, ITEM D WHICH STATES "THE PROBLEM CONDITION IS CLEARLY SCREENED BY PREFLIGHT CHECKOUT OR SPECIAL TEST." THE DEFERRAL STATUS HAS BEEN APPROVED BY THE EXTERNAL TANK PROJECT MANAGER, MR. PARKER V. COUNTS _____________PARKER V. COUNTS (SIGNED), 6/11/93_____________________ |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A15408 | IFA# -- | Contractor RPT# E-151 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# NB 18-32 INSERT | Asmnt Part Name ELECTRICAL CONNECTOR | Asmnt Serial/Lot# N/A |
| HCRIT CD -- | FCRIT CD 1 | CAUSE CD MA - MFG-ASY | FAIL MODE EL - SHORT |
| Asmnt FMEA 3.1.4.1 | Asmnt FM 1 | FMEA CSE N/A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |