US Forest Service Flight Training and Standardization

08/05/2006

DC3-TP67

GENERAL

- Dimensions

1. Wing Span                            95 Ft.  8 In.

2.  Height                                  17 Ft.  10 In.

3.  Length                                  67 Ft.  1 In.

- Engines

Pratt & Whitney PT6A-67R turbine engines

Emergency Power			    1424 SHP

Max Takeoff                                       1281 SHP

Max Continuous                                 1220 SHP

- Propellers

Hartzell HC-B5MA-3M/M11691NS, five-bladed, 118.7” diameter, all-metal full- feathering, reversible.

- Fuel

Jet A, Jet A-1, Jet A-2, Jet B

JP-4, JP-5, JP-8,  Avgas not approved.

Standard System (lbs)

Total capacity                                     5146 lbs

Total Usable                                       5042 lbs

- Oil

Total capacity                                     2.5 Gallons

Usable quantity                                   1.5 Gallons

- Maximum Weights

Max Takeoff                                              28,750 lbs

Max Landing                                             28,750 lbs

Max Zero Fuel                                           28,750 lbs

1

US Forest Service Flight Training and Standardization

08/05/2006

DC3-TP67

OPERATING LIMITATIONS

- Airspeed Limitations

Max Operating, Vmo					170 KIAS

Max Maneuvering, Va				107 KIAS

Max Flap Extension, Vfe 1/4				133 KIAS

Max Flap Extension, Vfe ½				  97 KIAS

Max Flap Extension, Vfe ¾ to Full			  95 KIAS

Max Ldg Gear Extend and Operating, Vle and Vlo	141 KIAS

Min Control-Air, Vmca				  67 KIAS

Min Control-Ground, Vmcg				  56 KIAS

Min Control-Air, Vmca, Emergency Power                 71 KIAS

Min Control-Ground, Vmcg, Emergency Power          60 KIAS

B. Power Plant Limitations

Max Torque, Emergency Power			111%

Max Torque                             			100%

Max Continuous Torque				  95%

Max Transient Torque, 20 seconds			129%

Max Torque, Prop feathered				50.5%

Max Torque, Oil pressure 60 psi			50%

Max Torque, Oil pressure 85 psi                                75%

Max ITT, Emergency Power                                      855( C

Max ITT, Takeoff					825( C

Max Continuous ITT					840( C

Starting ITT, 5 seconds				1000( C

Transient ITT 20 seconds				870( C

Max Reverse ITT					765( C

Oil Pressure						90-135 psi

Min Oil pressure idle					60 psi

Transient Oil Pressure					40 to 200 psi

Oil Temperature, Takeoff				10( to 110( C

Oil Temperature, Continuous				10( to 105( C

Oil Temperature, Transient				-40( to 110( C

Oil Temperature, Reverse				10( to 99( C

Min Oil Temperature					-40( C

Max Propeller rpm					1700 rpm

Max Gas Generator rpm				104 rpm

- Propeller Ground Limitations

Stabilized engine ground operations is prohibited between the following propeller rpm’s:

400 to 900 rpm

Above 1600 rpm unless headed into wind.

2

- Fuel Pressure

Max Pressure						50 psi

Normal						5 to 50 psi

- Generator Ammeter

Max in flight						300 amps

Normal						0 to 300 amps

Max on ground					250 amps

- Minimum Flight Crew

A minimum flight crew of one pilot and one copilot for all operation.

- Takeoff and Landing

Takeoffs and landings are limited to pressure altitudes between –1000 feet and 10,000 feet and temperatures between –40( C minimum to ISA +35(C maximum.

- Maximum Operating Altitude and Enroute Temperature Limit

The maximum operating pressure altitude is 25,000 feet.  Enroute temperature limits are –40( C minimum to ISA +35( C maximum.

- Engine Ice Protection

Engine inlet and propeller icing protection must be on whenever the outside air temperature is at or below +5( C and visible moisture is present.

- Maneuvering Flight Loads

Flaps up						+2.5 G

Flaps down						+2.0 G

Negative						-1.0 G

- Crosswind

The maximum demonstrated crosswind at 50-foot height is 24 knots.  This is not limiting.

- Reverse Thrust Limitation

Reverse thrust is limited to ground operations only.  Prior to lowering the tail wheel to the ground, caution should be exercised as directional control may be reduced during reverse thrust operations.

Positioning of power levers below flight idle is prohibited while airplane is in flight.

Note:  Do not attempt to move power levers into reverse unless associated engine is running.

3

- Starter Limitations

30 seconds on followed by 1 minute off for a maximum of three consecutive start cycles.  After the third start attempt a period of 30 minutes off minimum must be allowed before a fourth start is attempted.

- Alternate Static Source

Use of alternate static source for takeoff is prohibited.

- Fuel Quantity Indication

The fuel quantity gauges shall be used to determine fuel quantity and not the fuel flow/totalizer.

- Approved Fuel Anti-Icing Additives

Anti-icing additive is required.

4