03E03/29/06

S204-03E.doc

Use on all projects with earthwork.

Section 204. - EXCAVATION AND EMBANKMENT

Construction Requirements

204.05  Conserved Topsoil.  Delete the first sentence and substitute the following:

Conserve topsoil from the roadway excavation and from embankment foundation areas to the extent and depth determined by the CO.

Use Subsection 204.06 on projects with potential rock excavation, even when no rock excavation pay item is included. Check with Geotech on the necessity of controlled blasting. Edit the [use/do not use] text accordingly.

204.06  Roadway Excavation.

(b) Rock cuts.  Add the following:

When blasting rock, [use/do not use] controlled blasting methods according to Subsection 205.08(c).

Use the following on all projects.

204.14  Disposal of Unsuitable or Excess Material.  Add the following:

Secure environmental clearances according to Subsection 107.10.

Measurement

204.16

(a) Roadway Excavation.

(1) Include the following volumes in roadway excavation:

(e) Delete the text and substitute the following:

Conserved topsoil stripped from cuts.

(h) Delete the text and substitute the following:

Conserved material taken from stockpiles and used in Section 204 work except topsoil measured under Section 624.  Only materials required to be conserved by the CO are eligible for measurement under this item.

(2) Do not include the following in roadway excavation:  Add the following:

(m) Conserved topsoil stripped from fills.

Payment

204.17  Add the following:

Payment for Item 20401 is limited to ten percent of the plan quantity of excavation in the cut until the slope rounding in that cut is completed.