South Corridor I-205 / Portland Mall LRT

Portland, Oregon

(November 2004)

The Tri-County Metropolitan Transportation District (TriMet) and Portland Metro, the region’s metropolitan planning organization, are proposing to construct 8.3 miles of new light rail transit (LRT) guideway consisting of two segments connecting to the existing “MAX” LRT system along I-84 (Banfield Expressway).  Long-range regional forecasts point toward increasing traffic congestion along the I-205 corridor, for trips both originating and terminating in the southeastern metropolitan Portland area.  The intent of the South Corridor I-205/Portland Mall LRT project is to address increased travel demand in this rapidly growing corridor; to provide additional fixed guideway access between regional activity centers; and to help the Portland region achieve its land use, development, and growth management goals and objectives.

The first segment of the proposed project is a 6.5-mile double-track line that runs north/south and parallel to I-205, connecting the Clackamas Regional Center in southeast Portland with the Gateway Transit Center east of downtown on TriMet’s existing LRT system.  The I-205 line will also include eight new stations with approximately 2,100 park-and-ride spaces which are intended to draw commuters from throughout the southeastern metropolitan Portland area to downtown and other major employment centers located along the regional MAX system.  The second segment of the project is a 1.8-mile LRT spur which would begin at the existing Rose Quarter Transit Center and terminate at Portland State University (PSU) in south downtown Portland.  This new LRT alignment, which would run along the existing downtown bus mall on 5th and 6th Avenues, is needed because TriMet’s existing downtown LRT line (to the region’s west side) does not have the capacity to carry the additional eight trains per peak hour into the central business district (CBD) that will result from the I-205 extension.

| Summary Description |
| --- |
| Proposed Project: | Light Rail Transit |
|  | 8.3 Miles 15 Stations |
| Total Capital Cost ($YOE): | $502.1 Million (includes $8.7 million in finance charges) |
| Section 5309 New Starts Share ($YOE): | $296.2 Million (59.0%) |
| Annual Forecast Year Operating Cost: | $27.9 Million |
| Ridership Forecast (2025): | 46,500 Average Weekday Boardings |
|  | 9,400 Daily New Riders |
| Opening Year Ridership Forecast (2009): | 25,300 Average Weekday Boardings |
| FY 2006 Finance Rating: | Medium |
| FY 2006 Project Justification Rating: | Medium-High |
| FY 2006 Overall Project Rating: | Recommended |

Project Development History and Current Status

The South/North Major Investment Study covering the travel shed connecting the cities of Oregon City and Milwaukie, the Clackamas Regional Center area, downtown, north, and southeast Portland, and the city of Vancouver, Washington, was initiated in 1993 and completed in 1995.  In 1998, Metro issued a Draft Environmental Impact Statement (EIS) and adopted LRT as the locally preferred alternative (LPA).  The failure of a November 1998 ballot measure that would have provided local funding for the LPA triggered the need to re-evaluate the potential improvements, including a separate analysis of the I-205 corridor within the southern portion of the MIS study area.  A Supplemental Draft EIS that focused on transportation alternatives in the I-205 corridor was completed in December 2002.  In October 2003, TriMet completed an Amendment to the Supplemental Draft EIS that examined the potential impacts of a downtown LRT spur, an improvement that had not been included in the previous environmental work.  A revised LPA that included the downtown spur alignment was approved by FTA into preliminary engineering in March 2004.  The Final EIS is expected to be complete in late 2004, with a NEPA Record of Decision anticipated in early 2005 and final design approval anticipated in Summer 2005.

Significant Changes Since Last Evaluation (March 2004)

TriMet and Metro have updated the travel forecasts for the project to reflect a 2025 design year.  The project scope was refined to eliminate approximately 400 park-and-ride spaces and reduce total vehicle requirements.  In August 2004, the TriMet Board approved an increase in the regional payroll tax, which will increase revenues for the operation of the regional transit system, including the proposed South Corridor I-205/Portland Mall LRT project.

Project Justification Rating: Medium-High

The project is rated Medium-High based on a Medium rating for cost effectiveness and a Medium-High rating for transit-supportive land use.

Cost Effectiveness Rating: Medium

The Medium cost effectiveness rating reflects a good level of travel-time benefits (7,700 hours each weekday) relative to the project’s annualized costs. The estimate of both costs and benefits of the project at this stage of development is considered reliable.

| Cost Effectiveness |
| --- |
| Cost per Hour of Transportation System User Benefit Incremental Cost per Incremental Trip | New Start vs. Baseline $14.88* $9.86 |

* Indicates that measure is a component of Cost Effectiveness rating.

The implementation of fixed guideway transit in a congested regional transportation corridor is expected to improve travel times between the southeastern metropolitan Portland area and downtown Portland.  Eighty-three percent of total project boardings and 60 percent of travel-time benefits will result from trips with at least one end in the I-205 corridor.  Downtown Portland is the primary destination for trips originating in the corridor.  The second downtown LRT alignment will penetrate areas in the southern part of the CBD not presently served by MAX and will provide over 30 percent of the project’s travel-time benefits.  Less than six percent of travel-time benefits are attributable to increased service frequencies along the existing I-84 MAX alignment resulting from the South Corridor I-205/Portland Mall LRT project.

The South Corridor I-205 / Portland Mall LRT project’s cost estimate is comparable to those of other LRT at-grade projects in the New Starts pipeline.  TriMet has an excellent track record of constructing LRT projects on schedule and within budget.

Transit-Supportive Land Use Rating: Medium-High

The Medium-High rating reflects the Medium-High ratings assigned to transit-supportive plans and policies and their performance and impacts, and the Medium rating for existing land use in the project corridor.

Existing Land Use: Medium

- The I-205 South segment of the corridor currently is characterized by auto-oriented development in the form of detached, single-family homes and low-density commercial and light industrial development.  Population density is low to moderate, averaging 4,200 persons per square mile.

- The proposed new downtown segment serves a high-density, mixed-use, pedestrian-friendly environment, and proposed station areas contain over 150,000 jobs.

- There is little vacant land available for development, so most transit-oriented development will require developers to assemble parcels as they become available.

- Portland encourages alternatives to auto trips to its downtown by limiting the supply of surface parking lots; however, ample parking for auto-oriented uses exists along the I-205 segment.  Including monthly discounts, the average daily rate for parking in the central city is $7.43.

Transit-Supportive Plans and Policies: Medium-High

- Oregon’s comprehensive planning system has been in place for more than 25 years, and the Portland urban growth boundary has effectively constrained development to designated areas.  Metro (the regional government) has unparalleled authority to establish and enforce land use policy.  Its Urban Growth Management Functional Plan identifies growth centers and requires that local jurisdictions require minimum densities in these centers as well as policies that support pedestrian and transit access.

- Numerous State, regional, and local plans and policies strongly emphasize corridor and station area development.  Two stations in the I-205 segment of the corridor serve designated local or regional centers, where a mix of land uses and high-density, transit-oriented development is specified in planning documents.  Other stations largely include established single-family neighborhoods.

- Regional policies require local jurisdictions to adopt transit-supportive zoning ordinances.  Minimum and maximum parking requirements in South Corridor station areas are lower than those generally found in suburban areas, and include allowances for reduced parking based on proximity to transit.

- Metro’s Transit-Oriented Development Program provides technical and financial assistance to support transit-oriented development activities throughout the region.  Two proposed stations on the I-205 segment and all proposed stations along the downtown segment would be located within areas targeted for pedestrian improvements in regional and local plans.

Performance and Impacts of Policies: Medium-High

- Portland’s urban growth boundary has helped protect open space from rapid, low-density development, while a variety of infill projects and new transit-oriented developments have occurred in existing LRT station areas.  Specific projects have not yet been demonstrated in proposed station areas in the I-205 South corridor.

- The light rail expansion project is expected to help promote more mixed-use, transit-oriented development in the station areas over time and may spur redevelopment in both Clackamas Regional Center and Lents Town Center.  The amount of vacant land available for new development is minimal in most station areas, though, so the project’s impact on regional land use may be modest.

Other Project Justification Criteria

| Mobility Improvements Rating: Medium |
| --- |
| Within ½-mile radius of boarding areas: Existing Employment Projected Employment (2025) Low Income Households (% of total HH) Average Per Station: Employment Low Income Households Transportation System User Benefit Per Project Passenger Mile (Minutes) | 150,400 221,500 3,800 (21%) 10,026* 253* New Start vs. Baseline 1.97* |
| Environmental Benefits Rating: Medium |
| Criteria Pollutant (Reduction in tons) Carbon Monoxide (CO) Nitrogen Oxide (NOx) Volatile Organic Compounds (VOC) Particulate Matter (PM10) Carbon Dioxide (CO2) Criteria Pollutant Status Carbon Monoxide 1-Hour Ozone (O3) Annual Energy Savings (million British Thermal Units) | New Start vs. Baseline 195 6 6 N/A 7,898 EPA Designation Maintenance Area* Maintenance Area* 91,669 |
| Operating Efficiencies Rating: Medium |
| System Operating Cost per Passenger Mile (current year dollars) | Baseline $0.354* | New Start $0.347* |

* Indicates that measure is a component of rating for each criterion.

N/A indicates information was not available for this entry.

# Local Financial Commitment Rating: Medium

The Medium rating is based on the Medium rating for the capital finance plan.

Section 5309 New Starts Share of Total Project Costs: 59%

Rating: Medium

TriMet is requesting a 59 percent New Starts share of total project costs, which results in a Medium rating for this measure.

| Locally Proposed Financial Plan |
| --- |
| Source of Funds | Total Funds ($million) | Percent of Total |
| Federal: Section 5309 New Starts Flexible Funds (STP-Regional) Flexible Funds (STP-Oregon DOT) FTA Section 5309 Bus Discretionary | $296.2 $48.5 $23.0 $2.9 | 59.0% 9.7% 4.6% 0.6% |
| Local: TriMet General Fund Clackamas County City of Portland Portland Development Comm. | $28.8 $36.3 $46.3 $20.0 | 5.7% 7.2% 9.2% 4.0% |
| Total: | $502.1 | 100.0 % |

NOTE:  The financial plan reflected in this table has been developed by the project sponsor and does not reflect a commitment by DOT or FTA.  The sum of the figures may differ from the total as listed due to rounding.

# Capital Finance Plan Rating: Medium

The capital finance plan is rated Medium, based upon the average of the ratings assigned to each of the subfactors listed below.  The commitment of funds subfactor received a High rating; plan completeness received a Medium-High rating; capital funding capacity received a Medium-Low rating while the remaining subfactors received Medium ratings.

#### Agency Capital Condition: Medium

- TriMet’s bus fleet has an average age of 7.5 years, which is in line with the industry average.

- The agency’s good bond ratings, issued in January 2003, are as follows: Moody’s Aa3 and Standard & Poor’s AA.

#### Completeness of Capital Plan: Medium-High

- The capital plan was complete and included a detailed 20-year cash flow statement, levels of commitment of project funds and supporting evidence, fleet management plans, financial statements, and more than 20 years of historical information.  It also included a limited sensitivity analysis.

#### Commitment of Capital Funds: High

- Eighty-eight percent of non-New Starts funding is committed, which is outstanding for a project at this stage of development.  Committed funds deriving from existing sources include federal flexible funds, Clackamas County urban renewal funds, TriMet general funds from payroll taxes, City of Portland funds, and Portland Development Commission urban development funds.

#### Capital Funding Capacity: Medium-Low

- The project’s financial plan shows projected cash balances, reserve accounts, and/or access to credit that would allow TriMet to cover cost increases or funding shortfalls equal to approximately 19 percent of project costs.

#### Capital Cost Estimate and Planning Assumptions: Medium

### All material assumptions affecting the capital plan are consistent with past trends.

- The capital cost estimate includes a contingency of just under 10 percent of project costs, which is slightly lower than the norm for a project in preliminary engineering.

#### Operating Finance Plan Rating: Medium-High

The operating finance plan is rated Medium-High, based upon the average of the ratings of the five subfactors listed below.  The operating funding capacity and operating cost estimates and planning assumptions subfactors received Medium ratings, while all other subfactors received High ratings.

#### Agency Operating Condition: High

- TriMet is in excellent financial condition.  Trimet had expanded transit service steadily until the past fiscal year, when service was stabilized due to a stagnant economy.  There have been no service cutbacks or unfunded operating deficits in recent years.

- TriMet’s current ratio of assets to liabilities as reported in its most recent audited financial statement is 2.0, which is excellent.

#### Completeness of Operating Plan: High

### The operating plan submission was thorough and complete.  It included an identification of all sources and uses of funds; evidence of commitment of operating funds for the project; detailed assumptions on which the operating plan was based; historical data on service levels, operating costs, and revenues dating to the early 1980s; and a sensitivity analysis.

#### Commitment of Operating Funds: High

- All operating funding is committed.  The principal sources of operating and maintenance funds include TriMet payroll tax revenue, passenger fares, and FTA Section 5307 formula funds.

#### Operating Funding Capacity: Medium

- The project’s financial plan shows projected cash balances, reserve accounts, and/or access to credit exceeding 12 percent of annual operating expenses.

#### Operating Cost Estimates and Planning Assumptions: Medium

- Operating cost growth assumptions are conservative with respect to historical experience, while operating revenue assumptions are in line with historical experience.

Map