REPORT ON EMWIN TESTING AT WALLOPS CDAS

February 22 to 24 2005

Prepared by

Peter Woolner

Mitretek Systems

SUMMARY

Following a successful but short test performed on February 2, 2005 at Avtec’s facility at Chantilly VA, additional tests were made at the Wallops CDA Station on February 22 to 24, 2005.  These tests were performed using the revised Avtec receive software and IF Adapter designed for operation at 19.2 kbps user data rate.  The EMWIN signal was Offset Quadrature Phase Shift Keyed (OQPSK) modulated and used a pulse shaping filter.  The same Forward Error Correction (FEC) coding that was used in the previous 9.6 kbps implementation was also applied to this signal at double the data rate.

The tests were made with the Avtec transmit and receive equipment connected back-to-back on the bench, but with the real GOES East receive signals added to prove the receiver could tolerate that level of interference.  This was a close approximation of the level of interference that is expected from the GOES N/P satellites.

The test results show the prototype EMWIN receive system met the required performance criterion of one frame missing or one frame with errors in 10,000, when the receive EB/N0 (roughly equivalent to the signal to noise ratio) is between 3.0 and 4.5 dB.  This is considered an excellent result.  It shows that any existing EMWIN user, i.e. one receiving the current EMWIN signal at 9.6 kbps, will probably not need to upgrade the figure of merit (G/T) of the receive system when they change to the new EMWIN signal which is to be broadcast through the GOES N/P series of satellites.

The new EMWIN signal format, using OQPSK and a pulse shaping filter, has not yet been tested through its allocated transponder on a GOES N/P series satellite.  Therefore the amount of degradation caused by non-linearities or other imperfections in that transponder is still unknown.  The tests results shown in this report indicate that satellite degradation of up to 4.7 dB can be tolerated without requiring the receive G/T be better than the NOAA standard that was recommended for the existing EMWIN links on the GOES I/M series of satellites.  This writer believes it is unlikely the satellite degradation will exceed this amount, but tests are scheduled to measure that degradation as soon as a satellite is available.

TEST DESCRIPTION

All tests were performed with the equipment configured as shown figure 1.

Figure 1.  Block Diagram of Test Configuration

All the FER tests were made using OQPSK modulation at 19.2 kbps user data rate, but with the start and stop bits removed and the Attached Sync Marker and frame header bits added.  The FEC coding used was a rate ½ Convolutional inner code concatenated with a RS (255,223) outer code.  The level of the EMWIN signal into the receiver was set at -55 dBm.  The signal received from GOES East was combined with the test signal out of the EMWIN modulator so that the level of the LRIT and EMWIN-I signals from GOES East were 7 dB stronger than the EMWIN signal.  The noise generator output level was then adjusted as necessary to provide the desired EB/N0 value.

For all tests, the frame sync parameters were set to Search Threshold = 0, Lock Threshold = 6, Check Frames = 0, and Flywheel frames = 4.

Prior to the start of the Frame Error Rate (FER) tests, the power out of the modulator when modulated, was compared to its output power when unmodulated.  In each condition, the modulator output was fed to the Boonton wattmeter.  The power when modulated was found to be 1.0 dB greater than when not modulated.  That 1.0 dB correction has been applied to all measurements recorded herein.

At the start of each test the C/N0 was measured for an unmodulated carrier using a spectrum analyzer with internal averaging set at 100.  The offset for the N0 part of the measurement was chosen at the frequency that produced the lowest noise.  The C/N0 was also measured at the end of each FER test and averaged with the start value to provide the reference for that test.  The EB/N0 values were then calculated as:

EB/N0 = C/N0 + 1.0 – 10*LOG(15400) = C/N0 – 40.9 dB/Hz

In each FER test, the carrier was modulated with a recorded EMWIN data set, then the receiver was locked and allowed to run for a pre-determined period of time.  The numbers of frames transmitted and received were recorded, plus the numbers of frames that are uncorrectable by the RS code, Viterbi sync errors, frames missing, and data frame sequence errors.  This last item was used as a way to measure of how many separate error events had occurred.

The count of missing frames included the uncorrectable frames, as well as those frames that were missed because the Attached Sync Marker could not be correctly identified.  Since either event will result in a frame that is omitted from the data passed to the user, it was the total number of missing frames that was recorded and used to derive the FER.  The FER was calculated by dividing the total number of missing frames by the total number of transmitted frames.  Frames transmitted count was derived from the receiver monitor values by subtracting from the received frames count the number of fill frames (if any) then adding the total number of missing frames minus the uncorrectable frames.

The timing of the start of each test was controlled by manually setting the receive monitor parameters to zero, after the system had shown it was in lock.  Each test was ended by taking a screen shot of the receiver monitor parameters at the pre-determined time.  The values shown for each parameter were used in the subsequent calculations.

TEST RESULTS

The following table shows the results of these tests, arranged in order of increasing EB/N0.

| Test Nbr | EB/N0 dB/Hz | Total Frames Transmitted | No. of Events | Missing or Error Frames | FER | Errors per Event |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 2.3 | 3160 | 31 | 58 | 1.8E-02 | 1.87 |
| 1 | 2.6 | 904 | 48 | 75 | 8.3E-02 | 1.56 |
| 9 | 2.8 | 24042 | 54 | 113 | 4.7E-03 | 2.09 |
| 4 | 2.9 | 115504 | 82 | 645 | 5.6E-03 | 7.87 |
| 2 | 3.0 | 10000 | 15 | 15 | 1.5E-03 | 1.00 |
| 8 | 3.1 | 23554 | 2 | 2 | 8.5E-05 | 1.00 |
| 5 | 3.95 | 23237 | 6 | 34 | 1.5E-03 | 5.67 |
| 7 | 4.25 | 116023 | 1 | 79 | 6.8E-04 | 79.00 |
| 6 | 4.3 | 24104 | 0 | 1 | 4.1E-05 | 0.00 |
| 10 | 5.0 | 120012 | 0 | 1 | 8.3E-06 | 0.00 |

The following chart is a plot of these results for EB/N0 versus FER, with some additional annotations that are discussed in the following section.

Chart 1.  Back-to-Back Frame Error Rate Test Results

DISCUSSION OF TEST RESULTS

- The two points shown with red circles actually experienced no errors or missing frames during that test period.  One error was artificially added to the result for each of these tests in order to produce the points plotted on the chart.  The actual error rates for these points are unknown.  It is probable, but not certain, that they lie some unknown distance below these plotted points.

- Test 7 (the point third from the right in the chart) was significantly different from all other test results.  There was one error event in which 13 frames were uncorrectable and 66 were missing, giving a total of 79 frame errors in that single event.  This is an order of magnitude worse than the next closest errors per event.  It seems reasonable to consider this an anomaly.  (The event occurred during an overnight test and had no witnesses.)

- Even if this point is eliminated, the fourth point from the right in the chart will remain, producing a curve that does not follow the normal “waterfall” shape.  No explanation was found for this unusual effect.  The only way this could be resolved was to make many more measurements with EB/NO values between 3.0 and 4.0 dB/Hz and determine which point is supported by the additional tests.  No time was available to perform such a check, so these results create a degree of extra uncertainty in the actual performance of the system.

- Two dashed lines were added to the chart to signify the boundaries within which this writer believes the true FER curve would lie if a sufficiently long test time had been available to collect enough measurement points to determine that curve with accuracy and at a high degree of confidence.

- These two dashed lines cross the FER value of 10-4 (the pass/fail criterion) at EB/N0 values of 3.0 and 4.5 dB/Hz.  All the test results obtained are consistent with receiver performance within this range.  However, even if the worst case value of 4.5 dB/Hz was the correct one, the system would be considered acceptable.

Using this worst case value, the minimum EIRP expected from the GOES N series satellites of 44.8 dBmi, an EMWIN terminal G/T of -0.3 dB/K, and the actual transmitted user data rate before FEC codes are added of 15.4 kbps, the worst case available EB/N0 is calculated at 11.2 dB/Hz.  (See Appendix A for the full link calculations.)  Then:

Margin 	= Available EB/N0 – Back-to-back EB/N0 – Satellite degradation

= 11.2 – 4.5 – 2.0  (If the satellite degradation is 2 dB.)

= 4.7 dB

The 4.7 dB margin is 2.7 dB over the minimum recommended operating margin for this link, 2 dB, and is therefore available as an additional contingency if future tests should show the actual satellite degradation is more than the 2 dB estimated above.  If the actual receiver performance is better than the worst case as explained above, even more satellite degradation could occur and an acceptable link performance would still be provided.

Since the satellite transponder was not designed to carry a signal with the modulation and using a pulse shaping root raised cosine filter as is used on the EMWIN signal, more than usual degradation due to the satellite transponder is expected to occur.  However, as long as that degradation does not exceed 4.7 dB, the EMWIN link as currently designed will provide acceptable performance.  It is considered unlikely that the satellite degradation will exceed 4.7 dB, but this cannot be known for sure until the link is tested through an actual GOES N series satellite.

APPENDIX A.  REFERENCE LINK BUDGET

| EMWIN LINK CALCULATIONS FOR 19200 bps NOMINAL RATE |
| --- |
|  | Parameter | Units | Value |
|  | Data Rate (before framing and coding) | bps | 15514 |
|  | Modulation Type |  | OQPSK |
|  | FEC Coding Type |  | Conv+RS |
|  | FEC Coding Rate |  | 0.437 |
| Ground Uplink Transmitter |  |  |
|  | Uplink Frequency | MHz | 2034.70 |
| Transmit EIRP | dBmi | 76.7 |
| Antenna Pointing Loss | dB | 0.5 |
| Earth - To - Space |  |  |
|  | Path Distance (for 5 deg elevation) | km | 41127 |
| Free Space Loss | dB | 190.9 |
| Atmospheric Attenuation | dB | 0.4 |
| S/C Receive Performance |  |  |
| Polarization Loss | dB | 0.2 |
| U/L Incident Power | dBmi | -115.3 |
|  | Antenna Gain (from 5 deg elevation) | dBi | 14.8 |
| G/T (incl cable losses) | dB/K | -14.2 |
| Boltzmann constant | dBm/Hz/K | -198.6 |
| Uplink Thermal C/No | dB/Hz | 69.1 |
| S/C Transmit Performance |  |  |
|  | Downlink Frequency | MHz | 1692.70 |
| Transmit EIRP (to 5 deg elevation) | dBmi | 44.8 |
| Space - To - Earth |  |  |
|  | Path Distance (for 5 deg elevation) | km | 41127 |
| Free Space Loss | dB | 189.3 |
| Atmospheric Attenuation | dB | 0.4 |
| Ground Downlink Receiver |  |  |
| Downlink Incident Power | dBmi | -144.9 |
|  | Pwr Flux Density Rqmt (EOC in 4 kHz) | dBW/m2 | -154 |
|  | Power Flux Density (EOC in 4 kHz) | dBW/m2 | -159.0 |
| E/S G/T | dB/K | -0.3 |
| Polarization Loss | dB | 0.2 |
| Boltzmann constant | dBm/Hz/K | -198.6 |
| Downlink Thermal C/No | dB/Hz | 53.2 |
| Eb/No Overall Calculation |  |  |
| Overall Composite C/No | dB/Hz | 53.1 |
| Data Rate in dB | dB-Hz | 41.9 |
| Eb/No Calculated | dB | 11.2 |

| Required Eb/No Adjustments |  |  |
| --- | --- | --- |
|  | Required BER |  | 1E-06 |
| Theoretical Eb/No with no coding | dB | 10.6 |
| Theoretical coding gain | dB | 8.0 |
| Theoretical Eb/No with FEC coding | dB | 2.6 |
| Ground Segment Implementation Loss | dB | 1.9 |
| Satellite Segment Degradations | dB | 4.7 |
| Required Eb/No | dB | 9.2 |
| Eb/No MARGIN | dB | 2.0 |

# Text boxes

ZERO

errors

recorded