# INTELLIGENT TRANSPORTATION SYSTEM (ITS) PROJECTS

PREQUALIFICATION CRITERIA

WORK CLASSIFICATION P1: Camera Monitoring Systems (CCTV)

DESCRIPTION:	Furnishing and installation of a complete, fully operational, closed circuit television (CCTV) system, which includes roadside camera assemblies able to accommodate the varying light conditions to be encountered, all weather camera enclosures, lightning protection, and outdoor control cabinet assemblies, as well as necessary central equipment.

EXPERIENCE REQUIREMENTS:

- Experience in having successfully installed, within the last 5 years, at least two CCTV systems, with at least one being ITS oriented.

WORK CLASSIFICATION P2: Highway Advisory Radio Systems (HAR)

DESCRIPTION:	Furnishing and installation of a complete, fully operational, highway advisory radio (HAR) system, which includes a vertical whip antenna, FCC licensed transmitter, radial or triad grounding system on either a dial up or fiber-optic connection, and all necessary documentation and permits.

EXPERIENCE REQUIREMENTS:

- Have a minimum of 2 years of experience in the installation of HAR systems.

- Experience with FCC and FAA frequency coordination, clearance, and licensing.

- Experience in radio coverage analyses and propagation.

- Experience in having successfully installed, within the last 5 years, at least two HAR systems.

WORK CLASSIFICATION P3: Dynamic Message Signs (DMS)

DESCRIPTION:	Furnishing and installation of a complete, fully operational, dynamic message sign (DMS) system.

EXPERIENCE REQUIREMENTS:

- Have a minimum of 3 years of experience in the installation of DMS systems.

- Experience in having successfully installed, within the last 5 years, at least two DMS systems.

WORK CLASSIFICATION P4: Integrated Communication Systems

DESCRIPTION:	Furnishing and installation of a complete, fully operational, communication system, which allows for the transfer of surveillance data and control commands between field devices and the control center through use of land line (i.e. fiber-optic, coaxial, twisted pair) and wireless (i.e. area-wide network, terrestrial microwave links, spread spectrum radio, satellite) transmission, as well as developing and installing network management software for monitoring network performance and the reliability of communication equipment.

EXPERIENCE REQUIREMENTS:

- Have a minimum of 3 years of experience in the installation of fiber-optic cables, including the splicing, terminating, and testing of single mode fiber.

- Experience in having successfully installed, within the last 5 years, at least two ITS-related, land line and/or wireless communication systems.

WORK CLASSIFICATION P5: Level 1 System Integrators (Hardware)

DESCRIPTION:	Furnishing, installation, and testing of complete field subsystems for the hardware integration of Closed Circuit Television (CCTV), Incident Management, Variable Message Sign (VMS), and Highway Advisory Radio (HAR) systems that combine products and equipment, including but not limited to sensors, detectors, video cameras, controllers, communications equipment, software and firmware, from diverse vendors.  Also, designing, developing, and installing voice, data, and video communication drivers to enable hardware integration consistent with TCP/IP standards, the requirements of the central software, and the National ITS Architecture and its associated dictionaries and standards to include those of the National Transportation Communications for ITS Protocols (NTCIP).

EXPERIENCE REQUIREMENTS:

- Have a minimum of 3 years of experience in the integration of ITS projects having hardware integration as part of the scope of work.

- Experience in providing complete documentation of the process, protocols, and data flows associated with software and firmware design and development.

- Experience in developing, executing, and documenting subsystem acceptance test programs.

- Experience in providing training in the operation and maintenance of all field equipment encompassed by the subsystem.

- Experience in having successfully integrated, within the last 5 years, at least two ITS projects.

WORK CLASSIFICATION P6: Level 2 System Integrators (Software)

DESCRIPTION:	Developing, installation, documentation, and testing of complete, integrated, application software packages for transportation management and traveler information systems operating in a client/server environment using centralized or decentralized processing; incorporating, as appropriate, National ITS Architecture and its associated data dictionaries and standards, and ensuring documentation and software development procedures are consistent with System Engineering Institute best practices.

EXPERIENCE REQUIREMENTS:

- Have a minimum of 3 years of experience in the integration of ITS projects having software integration as part of the scope of work.

- Experience in developing software on an open architecture using commercially available operating system and industry standard tools and documentation procedures to ensure software will support real-time control and information systems.

- Experience in integrating diverse application software packages and commercially available off the shelf (COTS) software using common databases updated on a real-time basis.

- Experience in conducting all software test procedures for final acceptance of the system.

- Experience in having successfully integrated, within the last 5 years, at least two ITS projects.

WORK CLASSIFICATION P7: Level 3 System Integrator (Hardware & Software)

DESCRIPTION:	Developing, installation, documentation, and testing of complete, integrated systems encompassing field equipment and subsystems with central integrated application software.

EXPERIENCE REQUIREMENTS:

- Have a minimum of 3 years of experience in the integration of ITS projects having hardware and software integration as part of the scope of work.

- Experience in developing, installing, documenting, and testing network and microprocessor-based systems, including software, hardware, communications, and real-time control and diagnostics.

- Experience in developing complete integrated systems based on industry standards to include NTCIP and TCP/IP.

- Experience in documenting the development process, including preliminary, critical, and final design documentation, following the Software Engineering Institute’s recommended practices, including, but not limited to, an implementation of TCP/IP that is capable of supporting the following:

- DoD Internet Protocol (IP)

- Transmission Control Protocol (TCP)

- User Datagram Protocol (UDP)

- Internet Control Message Protocol (ICMP)

- Routing Information Protocol (RIP)

- Open Shortest Path First Protocol (OSPF)

- Address Resolution Protocol (ARP WINS, DHCP)

- Reversed Address Resolution Protocol (RARP)

- Remote logins (TELNET and RLOGIN)

- File transfer (FTP and RCP)

- Electronic Mail (SMTP, POP3, MAPI)

- Name service (DNS)

- Management (SNMP)

- File systems (NTFS, FAT)

- Remote procedure calls (RPC)

- Experience in having successfully integrated, within the last 5 years, at least two ITS projects.