NUMERICALL CONTROLLED WIRE ELECTRIC DISCHARE MACHINE

SOLICITATION # 552-76877-912

Technical questions:

Q.  Travel: Do you require the travel of the programmable Z to be 10 inches. If not , how many inches of programmable Z are required?

A.  The complete travel must be programmable.

Q.  Accuracy: What testing verification of accuracy is required?

A.  Ref. VDI 3441 standards: Reversal error U; Repeatability Ps; Positional deviation Pa.

Q.  What cutting performance tests are required to support above measured

specifications?

A.  Ref. ISO 230-4 Circularity Test U.S. standards NMTBA or ASME B5.54-92 are preferred, but other standards such as VDI 3441 or ISO 230 will be considered.

Q.  Position Measurement: If Closed Loop Operation and Absolute Position

Detection is required on X and Y axes would you also prefer it on U, V, and Z?

A.  Closed loop operation and absolute position sensing  on U, V, and Z axes

would be preferred but not required.

Q.  Tapering: Do you require 30 degree taper cutting capability through the maximum part height?

A.  The 30 degree taper capability is required for a 3 inch thickness only.

Q.  Submerged Operation: Do you require the part to be fully submerged up to the maximum cutting thickness?

A.  Yes.

Q.  Ozone Generator: What is the ozone generator and what is its function on a wire EDM machine?

A.  This keeps algae from growing in the dielectric fluid.

Q.  Wire Threading: Is it required that the automatic wire feeder reliably thread all types of wire? i.e. Coated wires from .004î to.012î.

A.  Yes.  For example, brass coated steel wire.

Q.  Will "Installation" require rigging, offloading and setting in place?

A.  No.  Goddard will perform these operations.