Before the

Federal Communications Commission

Washington, D.C. 20554

| In the Matter of Amendment of the Commission’s Rules Concerning Maritime Communications Petition for Rule Making filed by Regionet Wireless License, LLC | ) ) ) ) ) ) ) | PR Docket No. 92-257 RM-9664 |
| --- | --- | --- |

ERRATUM

Released:  June 4, 2004

By the Chief, Public Safety and Critical Infrastructure Division, Wireless Telecommunications Bureau:

1.	On April 8, 2002, the Commission released a Second Memorandum Opinion and Order and Fifth Report and Order (Fifth Report and Order) in the above-captioned proceeding.  In the Fifth Report and Order, the Commission determined that unassigned Automated Maritime Telecommunications System (AMTS) spectrum would be made available for licensing throughout the United States by ten Automated Maritime Telecommunications System Areas (AMTSAs).  Each AMTSA consists of one or more of the 174 Economic Areas (EAs) or EA-like areas in International Telecommunication Region 2—i.e., the 172 EAs specified by the Department of Commerce and the Commission-created EA-like areas for Puerto Rico and the United States Virgin Islands (EA 174) and the Gulf of Mexico (EA 176).  However, neither the text of the Fifth Report and Order nor Section 80.385(a)(3) of the Commission’s Rules, as set forth in Appendix C of the Fifth Report and Order, included a reference to the perimeter of EA 176.

2.	In view of the foregoing, Section 80.385(a)(3) of the Commission’s Rules, as set forth in Appendix C of the Fifth Report and Order is hereby corrected to read as follows to conform to the Commission’s intention.  We also take this opportunity to correct a typographical error in the table in Section 80.385(a)(2) of the Commission’s Rules that occurred when the Fifth Report and Order was published in the Federal Register:

§ 80.385  Frequencies for automated systems.

* * * * *

(a)  * * *

(1)  * * *

(2)  The following carrier frequencies are available for assignment to public coast stations for public correspondence communications with ship stations and units on land.  AMTS operations must not cause harmful interference to the U.S. Navy SPASUR system which operates in the band 216.880-217.080 MHz.

| Channel No. | Carrier frequency (MHz) |
| --- | --- |
|  | Ship transmit1, 3 | Coast transmit2 | Group |
| 101................... 102................... 103................... 104................... 105................... 106................... 107................... 108................... 109................... 110................... 111................... 112................... 113................... 114................... 115................... 116................... 117................... 118................... 119................... 120................... 121................... 122................... 123................... 124................... 125................... 126................... 127................... 128................... 129................... 130................... 131................... 132................... 133................... 134................... 135................... 136................... 137................... 138................... 139................... 140................... 141................... 142................... 143................... 144................... 145................... 146................... 147................... 148................... 149................ | .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... .................... 219.0125 219.0375 219.0625 219.0875 219.1125 219.1375 219.1625 219.1875 219.2125 | 216.0125 216.0375 216.0625 216.0875 216.1125 216.1375 216.1625 216.1875 216.2125 216.2375 216.2625 216.2875 216.3125 216.3375 216.3625 216.3875 216.4125 216.4375 216.4625 216.4875 216.5125 216.5375 216.5625 216.5875 216.6125 216.6375 216.6625 216.6875 216.7125 216.7375 216.7625 216.7875 216.8125 216.8375 216.8625 216.8875 216.9125 216.9375 216.9625 216.9875 217.0125 217.0375 217.0625 217.0875 217.1125 217.1375 217.1625 217.1875 217.2125 | D C B |
| 150................... 151................... 152................... 153................... 154................... 155................... 156................... 157................... 158................... 159................... 160................... 161................... 162................... 163................... 164................... 165................... 166................... 167................... 168................... 169................... 170................... 171................... 172................... 173................... 174................... 175................... 176................... 177................... 178................... 179................... 180................... | 219.2375 219.2625 219.2875 219.3125 219.3375 219.3625 219.3875 219.4125 219.4375 219.4625 219.4875 219.5125 219.5375 219.5625 219.5875 219.6125 219.6375 219.6625 219.6875 219.7125 219.7375 219.7625 219.7875 219.8125 219.8375 219.8625 219.8875 219.9125 219.9375 219.9625 219.9875 | 217.2375 217.2625 217.2875 217.3125 217.3375 217.3625 217.3875 217.4125 217.4375 217.4625 217.4875 217.5125 217.5375 217.5625 217.5875 217.6125 217.6375 217.6625 217.6875 217.7125 217.7375 217.7625 217.7875 217.8125 217.8375 217.8625 217.8875 217.9125 217.9375 217.9625 217.9875 | A |

1 Ship transmit frequencies in Groups C and D are not authorized for AMTS use.

2 Coast station operation on frequencies in Groups C and D are not currently assignable and are shared on a secondary basis with the Low Power Radio Service in part 95 of this chapter. Frequencies in the band 216.750-217.000 MHz band are available for low power point-to-point network control communications by AMTS coast stations under the Low Power Radio Service (LPRS). LPRS operations are subject to the conditions that no harmful interference is caused to the United States Navy's SPASUR radar system (216.88-217.08 MHz) or to TV reception within the Grade B contour of any TV channel 13 station or within the 68 dBu predicted contour of any low power TV or TV translator station operating on channel 13.

3 Ship transmit frequencies in Groups A and B are permitted to provide mobile-to-mobile communications where the written consent of all affected licensees is obtained.

* * *

(3) As listed in the table in this paragraph, AMTS Areas (AMTSAs) are based on, and composed of one or more of, the U.S Department of Commerce's 172 Economic Areas (EAs).  See 60 FR 13114 (March 10, 1995).  In addition, the Commission shall treat Puerto Rico, the United States Virgin Islands, and the Gulf of Mexico as EA-like areas.  The Gulf of Mexico EA extends from 12 nautical miles off the United States Gulf coast outward into the Gulf.  See Section 27.6(a)(2) of this chapter and 62 FR 9636.  Maps of the EAs and AMTSAs are available for public inspection and copying at the Federal Communications Commission, Reference Center, 445 12th Street, S.W., Room CY-A257, Washington, D.C.  20554.  These maps and data are also available on the FCC website at www.fcc.gov/oet/info/maps/areas/.  The Group A and B frequency pairs listed in the table in paragraph (a)(2) of this section are available for assignment to a single licensee in each of the AMTSAs listed in the table in this paragraph.  In addition to the listed EAs listed in the table in this paragraph, each AMTSA also includes the adjacent waters under the jurisdiction of the United States.

AMTS areas (AMTSAs)

| AMTSAs | EAs |
| --- | --- |
| (Northern Atlantic) (Mid-Atlantic) (Southern Atlantic) (Mississippi River) (Great Lakes) (Southern Pacific) (Northern Pacific) (Hawaii) (Alaska) (Mountain) | 1-5, 10 9, 11-23, 25, 42, 46 24, 26-34, 37, 38, 40, 41, 174 35, 36, 39, 43-45, 47-53, 67-107, 113, 116-120, 122-125, 127, 130-134, 176 6-8, 54-66, 108, 109 160-165 147, 166-170 172 171 110-112, 114-115, 121, 126, 128, 129, 135-146, 148-159 |

* * * * *

3.  Accordingly, IT IS ORDERED that this Erratum is issued under delegated authority pursuant to Section 0.331 of the Commission’s Rules, 47 C.F.R. § 0.331.

FEDERAL COMMUNICATIONS COMMISSION

D’wana R. Terry

Chief, Public Safety and Critical Infrastructure Division

Wireless Telecommunications Bureau

# Footnotes

See Amendment of the Commission’s Rules Concerning Maritime Communications, Second Memorandum Opinion and Order and Fifth Report and Order, PR Docket No. 92-257, 17 FCC Rcd 6685 (2002), recon. granted in part and denied in part, Third Memorandum Opinion and Order, 18 FCC Rcd 24391 (2003).

Id. at 6698 ¶ 28; see also 47 C.F.R. § 80.385(a)(3).