Notice of Proposed Rule Making

Docket Number: FAA-2007-29281

Notice Number: 08-06

Comments By:

Harold F. Phillips

Introduction

In this paper I will discuss the Notice of Proposed Rule Making over the use of polishing frost and how if passed will do away with this procedure and the terminology in FAR 91. 527, 125.221, and 135.227. I will also give my comments over the proposal.

Summary

This Notice to Proposed Rulemaking is stating that the ability for pilots and aircraft owners to “polish frost” off the wings is politically incorrect and not a safe practice to follow. FAR 91.527, FAR 125.221, and FAR 135.227 are the focus of this notice.

FAR 91.527 reads no pilot may take off an airplane that has – (1) frost, snow, or ice adhering to any propeller, windshield, or power plant installation or to an airspeed, altimeter, rate of climb, or flight attitude instrument system, (2) snow or ice adhering to the wings or stabilizing or control surfaces; or (3) any frost adhering to the wings or stabilizing or control surfaces, unless that frost has been polished to make it smooth.

FAR 125.221 and FAR 135.227 state no pilot may take off an airplane that has frost, ice, or snow adhering to any propeller, windshield, wing, stabilizing or control surface, to a power plant installation, or to an airspeed, altimeter, rate of climb, or flight attitude instrument system, except that takeoffs may be made with frost adhering to the wings, or stabilizing or control surfaces, if the frost has been polished to make it smooth.

In part 91.527 the phrase “unless that frost has been polished to make it smooth.” will be omitted. Parts 125.221 and 135.227, the phrase “except that takeoffs may be made with frost adhering to the wings, or stabilizing or control surfaces, if the frost has been polished to make it smooth.” will also be omitted.

The research provided demonstrate that the risk of having any frost on the wing will cause the wing to produce less lift and be a hazard to the operation of the aircraft in question, and the safety of the crew and passengers. Research has shown that the maximum lift of the aircraft in question may decrease as much as thirty percent, the angle of attack for maximum lift may be reduced by several degrees, increased parasitic drag will be created, and the handling and performance of the aircraft may change unexpectedly from that of an uncontaminated aircraft.

Research on the economically impact was also conducted and found that the benefits will out way the cost severely. All companies that are abiding under the described FARs above will have no problem financially to prevent or remove frost form the wings of their aircraft.

Comments

I am in favor of this Notice of Proposed Rule Making. There is no reason, in my opinion, to not change FARs 91.527, 125.221, and 135.227. The research provided proves that frost is a hazardous to flight and that to fix this problem will not be a financial burden to anyone.

There is no safe way to fly an airplane with frost on the wings. I am an aviator myself and the thought of knowing that aircraft can depart an airport with frost of any kind on the wings is a scary one. The performance of that aircraft in an emergency will not be as good as it needs to be. In slow flight the aircraft is closer to a stall than if the crew had deiced the wings and incase of a missed approach to land this could be detrimental if they needed to hit their best angle of climb to miss an obstacle.

The plan to prevent and remove the frost will not be a financial burden according to the research within the NPRM. The estimated costs for all who are affected will not affect them in a major way due to the fact their profits are much higher than the cost.

Conclusion

I have reviewed this NPRM and found myself in favor of removing the terminology of departing with “Polished Frost” and banning any such procedure to be used within the United States. The use of such a procedure would be a breach in the duty of a safe flight to any passenger flying on any aircraft that didn’t remove the frost completely or to the specification of the FAR.

Reference

(nd), DOT and FAA, Notice of Proposed Rule Making. Docket Number: FAA-2007-29281, Notice Number: 08-06, RIN 2120-AJ09