United States of America

DRAFT PROPOSAL FOR THE WORK OF THE CONFERENCE

## WRC-03 Agenda Item 1.12a:  to consider allocations and regulatory issues related to the space science services in accordance with Resolution 723 (Rev. WRC-2000);

Background Information:  ITU-R Recommendation SA.363-5 recommends that frequencies below 1 GHz are technically suitable for telecommand of satellites in the space science services operating below an altitude of 2000 km.  A deficiency in telecommand (uplink) frequency allocations has been previously identified, compared to the available telemetry (downlink) allocations in the 100 MHz to 1 GHz range.  The deficiency was first noted in Resolution 712 (WARC-92), repeated in Resolution 712 (Rev. WRC-95), and again in Resolution 723 (WRC-97).

This item was originally placed on the WRC-97 agenda.  WRC-97 determined that insufficient study had been completed to take action on this agenda item.

Since WRC-2000, additional studies have been undertaken in the ITU-R.  The study results show that show that separation distances for aeronautical mobile stations must be over 400 km and for MSS approximately 100 km.  These required coordination distances make use of RR 9.17/17a and Appendix 7 impractical and will result in large geographical regions where existing Aeronautical Mobile, MS, FS, and MSS services are unusable.

Proposal:

USA/ /1	NOC

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
|  | 220-225 |  |
| 223-230 BROADCASTING Fixed Mobile | AMATEUR FIXED MOBILE Radiolocation 5.241 | 223-230 FIXED MOBILE BROADCASTING |
|  | 225-235 FIXED MOBILE | AERONAUTICAL RADIONAVIGATION Radiolocation |
| 5.243 5.246 5.247 |  | 5.250 |
| 230-235 FIXED MOBILE |  | 230-235 FIXED MOBILE AERONAUTICAL RADIONAVIGATION |
| 5.247 5.251 5.252 |  | 5.250 |
| 235-267 FIXED MOBILE 5.111 5.199 5.252 5.254 5.256 |
| 267-272 FIXED MOBILE Space operation (space-to-Earth) 5.254 5.257 |
| 272-273 SPACE OPERATION (space-to-Earth) FIXED MOBILE 5.254 |
| 273-312 FIXED MOBILE 5.254 |
| 312-315 FIXED MOBILE Mobile-satellite (Earth-to-space) 5.254 5.255 |
| 315-322 FIXED MOBILE 5.254 |
| 322-328.6 FIXED MOBILE RADIO ASTRONOMY 5.149 |
| 328.6-335.4 AERONAUTICAL RADIONAVIGATION 5.258 5.259 |
| 335.4-387 FIXED MOBILE 5.254 |
| 387-390 FIXED MOBILE Mobile-satellite (space-to-Earth) 5.208A 5.254 5.255 |
| 390-399.9 FIXED MOBILE 5.254 |
| 399.9-400.05 MOBILE-SATELLITE (Earth-to-space) 5.209 5.224A RADIONAVIGATION-SATELLITE 5.222 5.224B 5.260 5.220 |

Reasons:  ITU-R studies have shown that sharing between telecommand and existing services in the 225 – 400 MHz band results in impractical coordination requirements with existing services.