Norfolk LRT

Norfolk, Virginia

(November 2004)

Hampton Roads Transit (HRT) is proposing to construct and operate an 11-station, 7.4-mile light rail transit (LRT) line within the city of Norfolk that is intended to serve as the initial segment of a regional rapid transit system.  The project alignment would begin at the Eastern Virginia Medical Center, move eastward as a dedicated in-street guideway through downtown Norfolk to Norfolk State University, and continue along an existing Norfolk Southern Railroad right-of-way (ROW) parallel to Interstate-264

(I-264), to the eastern terminus at Newtown Road.  Park-and-ride access to the system would be provided by the construction of new facilities at Newtown Road, Military Highway, and Ballantine Boulevard, as well as shared use of existing parking facilities at the Harbor Park baseball stadium on the southeastern fringe of downtown, where a station is planned.  The project scope also includes LRT maintenance facilities and the purchase of nine vehicles.  Service would operate at 7.5-minute frequencies during peak periods.

Travel forecasts indicate worsened congestion on I-264 and major arterials (Brambleton Avenue, Virginia Beach Boulevard, Tidewater Drive) within the project corridor through 2025.  Options for improving mobility within the area are limited by geographic constraints (numerous waterways) and the absence of transportation rights-of-way.  The Norfolk LRT project takes advantage of an existing rail ROW and is intended to help meet future travel demand to downtown Norfolk and throughout the corridor, provide improved mobility for transit-dependent populations, and achieve local land use goals.  The project is further intended to provide a rapid transit connection from Harbor Park and other fringe park-and-ride facilities to destinations within the downtown area.

| Summary Description |
| --- |
| Proposed Project: | Light Rail Transit |
|  | 7.4 Miles 11 Stations |
| Total Capital Cost ($YOE): | $203.5 Million (includes $4.9 million in finance charges) |
| Section 5309 New Starts Share ($YOE): | $100.7 Million (49.5%) |
| Annual Forecast Year Operating Cost: | $6.8 Million |
| Ridership Forecast (2025): | Not Available |
| Opening Year Ridership Forecast: | Not Available |
| FY 2006 Finance Rating: | Medium |
| FY 2006 Project Justification Rating: | Not Rated |
| FY 2006 Overall Project Rating: | Not Rated |

The project is Not Rated based on the information available at this time.  While HRT has demonstrated progress in improving its travel forecasting procedures, its estimate of project travel-time benefits is based upon an unsubstantiated assumption regarding future parking deficits in downtown Norfolk.  In addition, uncertainty regarding the cost of acquiring Norfolk Southern Railroad ROW for the project and the need for updated costs reflecting more advanced design may result in changes to the project cost estimate, which could affect cost effectiveness calculations.  Prior to advancing the project into final design, HRT must update its cost estimate and schedules, provide evidence of the implementation of parking policies and ordinances intended to constrain future downtown parking supply, and develop an acceptable cost effectiveness rating.  FTA will assist HRT in meeting these objectives.

Project Development History and Current Status

In 1997, FTA approved into preliminary engineering (PE) an 18-mile LRT system extending between the cities of Norfolk and Virginia Beach.  The Draft Environmental Impact Statement (EIS) for the project was completed in April 1999.  In November 1999, Virginia Beach voters failed to approve a local funding measure for the project, resulting in the truncation of the project at Kempsville Road within the city limits of Norfolk.  FTA approved the abridged project into PE in October 2002.  A Supplemental Draft EIS was completed in January 2003.  Since that time, HRT has undertaken additional scope and cost reductions that have resulted in the current 7.4-mile alignment.  HRT anticipates completion of the project’s Final EIS and receipt of a Record of Decision in Spring 2005, with final design approval assumed shortly thereafter.  Revenue operations are anticipated to begin in Summer 2008.

Significant Changes Since Last Evaluation (November 2003)

Based on FTA comments, HRT has improved its travel forecasting procedures and generated revised estimates of the project’s ridership and travel-time benefits.  These revised forecasts reflect the Hampton Roads region’s adopted 2025 population and employment assumptions, as well as an assumed (though unsubstantiated) parking deficit in downtown Norfolk.  Since last year, the project implementation schedule has been extended a year, resulting in a modest cost increase reflecting inflation.

###### Project Justification Rating: Not Rated

The project is Not Rated for project justification based on the absence of defensible information on the cost effectiveness of the project.  The project is rated Medium for transit-supportive land use.

Cost Effectiveness Rating: Not Rated

HRT’s submission of project benefits indicates that the Norfolk LRT project will predominantly benefit downtown-bound commuters.  HRT’s travel forecasts assume the existence of a significant parking deficit in downtown Norfolk by 2025.  This parking deficit would be relieved, in part, by the connection of the proposed LRT system to parking facilities located on the fringe of the central business district (CBD).   Seventy-five percent of projected user benefits are consequently attributable to this park-and-ride market.  However, there is insufficient evidence that local parking policies under consideration would result in the parking deficit that is assumed in the travel forecasting model.

The project’s current cost estimate represents an escalation (based on inflation) of a 2002 preliminary engineering estimate.  The per-mile cost appears to be low for a light rail project, especially one with multiple grade conditions.  As noted, HRT must fully update its cost estimate and schedule prior to advancing the project into final design.

Transit-Supportive Land Use Rating: Medium

The Medium land use rating is based upon the Medium-High rating assigned to transit-supportive plans and policies and performance and impacts of policies, and the Medium-Low rating for existing land uses in the project corridor.

Existing Land Use: Medium-Low

- Employment and population levels in the area served by the project are modest.  Station area employment is estimated at approximately 53,800 employees.  Total CBD employment is 42,000, and population densities average 4,200 persons per square mile in station areas.

- Pedestrian access in the CBD and redeveloping waterfront neighborhoods has improved considerably within the past few years.  Elsewhere, neighborhoods are generally walkable, but some developments at each end of the alignment have considerable surface parking.

- Downtown Norfolk generally maintains a more than adequate parking supply, although some areas suffer from parking shortages.  Parking costs in the CBD range from $4 to $14 per day.

Transit-Supportive Plans and Policies: Medium-High

- Jurisdictions in the Hampton Roads area have adopted and applied various tools for growth management, primarily oriented toward the preservation of natural areas.

- The city of Norfolk has adopted and implemented redevelopment plans for the downtown area that focus on creating a mixed-use, pedestrian-scaled environment that builds on historic architecture and amenities such as the waterfront.

- Residential densities in corridor neighborhoods typically range from six to 15 units per acre but are much higher for some newer downtown developments.  Redevelopment plans are also being implemented to rebuild residential neighborhoods in the corridor.

- Pedestrian-oriented design guidelines have been adopted for a number of areas in the corridor, especially near downtown, and are being enforced.

- Some downtown and adjacent districts do not require off-street parking and allow provisions for shared parking.

- The city is considering the adoption of a transit overlay district that could be applied to station areas to restrict uses, establish design standards, and restrict parking.

- The city of Norfolk has been a strong leader in planning initiatives to redevelop downtown and many residential neighborhoods of the city.  City agencies have a number of financial and regulatory incentives at their disposal and have aided with land acquisition and assembly in redevelopment areas.

Performance and Impacts of Policies: Medium-High

- Significant redevelopment activities have occurred in downtown Norfolk in recent years, and these developments have been consistent with pedestrian-oriented design principles.

- Vacant and underutilized properties are being transformed into mixed-use, urban-scale developments with residential, retail, and office uses.

- Development in the easternmost station areas continues to be auto-oriented.

- There is a moderate amount of redevelopment potential in transit station areas.  A market for both new commercial and residential development in the downtown area has been demonstrated and is likely to continue.

- HRT’s estimates of station area development potential suggest that approximately 12,000 new residents and 25,000 jobs could be accommodated if currently vacant or underutilized parcels were built out, which is more development than assumed in regional land use forecasts for the corridor.

Other Project Justification Criteria

| Mobility Improvements Rating: Not Rated |
| --- |
| Within ½-mile radius of boarding areas: Existing Employment Projected Employment (2025) Low Income Households (% of total HH) Average Per Station: Employment Low Income Households Transportation System User Benefit Per Project Passenger Mile (Minutes) | 53,800 62,200 1,800 (24%) 4,890* 164* New Start vs. Baseline N/A* |
| Environmental Benefits Rating: Not Rated |
| Criteria Pollutant (Reduction in tons) Carbon Monoxide (CO) Nitrogen Oxide (NOx) Volatile Organic Compounds (VOC) Particulate Matter (PM10) Carbon Dioxide (CO2) Criteria Pollutant Status 1-Hour Ozone (O3) 8-Hour Ozone Annual Energy Savings (million British Thermal Units) | New Start vs. Baseline N/A N/A N/A N/A N/A EPA Designation Maintenance Area* Marginal Non-Attainment Area* N/A |
| Operating Efficiencies Rating: Not Rated |
| System Operating Cost per Passenger Mile (current year dollars) | Baseline N/A* | New Start N/A* |

* Indicates that measure is a component of rating for each criterion.

N/A indicates information was not available for this entry.

Other Factors

Based on an alternative land use forecast developed by HRT, which reflects anticipated development generated by the project beyond the region’s adopted land use forecast, HRT is estimating that the Norfolk LRT project will generate approximately 2,800 hours of travel-time benefits each weekday.  This would result in a cost effectiveness of $16.21 per hour of user benefits.  This estimate is based upon optimistic parking and land use development assumptions, as well as an early PE-level cost estimate, and consequently carries some risk.  However, it does provide some indication of the potential of the project should these assumptions prove achievable.

# Local Financial Commitment Rating: Medium

The Medium rating for local financial commitment was determined by the Medium ratings for the New Starts share, as well as both the capital and operating plans.

Section 5309 New Starts Share of Total Project Costs: 50%

Rating: Medium

HRT is requesting slightly under 50 percent in New Starts funding to cover total project costs, which results in a Medium rating for this measure.

| Locally Proposed Financial Plan |
| --- |
| Source of Funds | Total Funds ($million) | Percent of Total |
| Federal: Section 5309 New Starts Flexible Funds (STP) FHWA FY 2003 Earmark | $100.7 $33.6 $1.0 | 49.5% 16.5% 0.5% |
| State: General Assembly Appropriations Virginia Mass Transit Fund Virginia Transportation Trust Fund | $9.3 $21.4 $3.6 | 4.6% 10.5% 1.8% |
| Local: City of Norfolk Bonds | $33.9 | 16.7% |
| Total: | $203.5 | 100.0% |

NOTE:  The financial plan reflected in this table has been developed by the project sponsor and does not reflect a commitment by DOT or FTA.  The sum of the figures may differ from the total as listed due to rounding.

# Capital Finance Plan Rating: Medium

The capital finance plan is rated Medium, based upon the average of the ratings assigned to each of the subfactors listed below.  The project received a High score on completeness, a Medium-High score on capital funding capacity, and a Medium-Low score on capital condition.  The remaining subfactors received Medium ratings.

#### Agency Capital Condition: Medium-Low

- The average age of HRT’s bus fleet is 8.2 years, which is older than the industry average.

- HRT does not have bond ratings.

#### Completeness of Capital Plan: High

- HRT submitted a very thorough plan that included a 20-year cash flow statement, identification of all key assumptions, a fleet management plan, more than five years of historical data, and an extensive sensitivity analysis.

#### Commitment of Capital Funds: Medium

- Approximately 24 percent of non-New Starts funding is committed and 43 percent is budgeted.  Local funding is expected to come from bonds issued by the city of Norfolk, Federal flexible funds, and State capital grants.

#### Capital Funding Capacity Medium-High

- The city of Norfolk (which is responsible for the local share of the project capital cost) can cover cost increases or funding shortfalls through additional bonding equal to more than twice the project cost.  However, the city will undoubtedly have other demands on this debt capacity, aside from the transit system.

#### Capital Cost Estimate and Planning Assumptions: Medium

### Assumptions in the capital financial plan are consistent with historical experience.

- Capital cost estimates, contingency, and project schedule reflect an early PE-level of design and need to be updated.

#### Operating Finance Plan Rating: Medium

The operating finance plan is rated Medium, based upon the average of the ratings of the five subfactors listed below.  Completeness was rated High, commitment of operating funds was rated Medium-High, and Medium ratings were assigned to the operating condition and operating funding capacity subfactors.  A Medium-Low rating was assigned to the operating cost estimates and planning assumptions subfactor.

#### Agency Operating Condition: Medium

- HRT is in average operating condition, with service cutbacks in FY 2002 that eliminated some demonstration services and reduced service in Chesapeake, Portsmouth, and Virginia Beach.

- HRT’s current ratio of assets to liabilities as reported in its most recent audited financial statement (FY 2003) is 1.31.

#### Completeness of Operating Plan: High

- HRT submitted a very thorough plan that contained all required elements including a 20-year cash flow statement, identification of all key assumptions with an extensive level of detail, more than five years of historical data, and an extensive sensitivity analysis.

#### Commitment of Operating Funds: Medium-High

- Over 55 percent of operating funding is committed.  The city of Norfolk will fund project operating and maintenance costs that are not covered by fare revenues and State operating assistance.

#### Operating Funding Capacity: Medium

- The project’s financial plan shows projected cash balances, reserve accounts, and/or access to credit exceeding 20 percent of annual operating expenses.

#### Operating Cost Estimates and Planning Assumptions: Medium-Low

### Ridership and fare revenue assumptions are optimistic compared to historical experience.

### Revenue projections for other operating sources and operating cost projections are in line with historical experience.

Map