United States of America

DRAFT PROPOSAL FOR THE WORK OF THE CONFERENCE

Agenda Item 1.31:  to consider the additional allocations to the mobile-satellite service in the 1-3 GHz band, in accordance with Resolutions 226 (WRC-2000) and 227 (WRC-2000);

Background Information:  WRC-2000 considered proposals for worldwide allocation of the band 1 683-1 690 MHz to the mobile-satellite service (MSS) (Earth-to-space) in response to Resolution 213 (WRC-95).  The frequency band 1 675-1 710 MHz is allocated to the MSS (Earth-to-space) in Region 2 on a co-primary basis. However, the 1 683-1 690 MHz portion is used mainly by the meteorological-satellite (MetSat) and meteorological aids (MetAids) services.  While there are only a limited number of MetSat earth stations operating in this band in Region 1, there are a large number of MetSat earth stations operating in Regions 2 and 3, and the locations of many of these stations are not identified.  Sharing between MetSat and MSS in the band 1 675-1 690 MHz is feasible only if appropriate separation distances are maintained.

Sharing between MetSat and MSS may not be feasible in those countries where a large number of MetSat stations are deployed.  Recommendation ITU-R SA.1158-2 indicates that additional studies are required in order to determine the criteria for coordination between MSS and the MetSat service for GVAR/S-VISSR stations operated in the band 1 683-1 690 MHz in Regions 2 and 3.

Other spectrum identified in Resolution 213 included 1 690-1 710 MHz.  However, the ITU-R has concluded that co-channel sharing between MSS and MetAids is not feasible and that co-frequency sharing between MetAids and MetSat services is not feasible.  Therefore, the World Meteorological Organization (WMO) has identified future spectrum requirements for MetAids operations as limited to the 1 675-1 683 MHz portion of the 1 675-1 700 MHz band, but some administrations will continue to require spectrum in the range 1 683-1 690 MHz for MetAids operations.   Resolution 227 observed that no further study is required on sharing in the 1 675-1 683 MHz and 1 690-1 710 MHz bands, due to incompatibility between MSS and existing services in these bands.

The existing Region 2 allocation includes the provision that MSS operation should not constrain current and future development of the MetSat service, as specified in No. 5.377.  No MSS services have been implemented under the Region 2 allocation in this band.

Proposal:

USA/  /1	MOD

1 675-1 710 MHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 1 675-1 690 METEOROLOGICAL AIDS FIXED METEOROLOGICAL- SATELLITE (space-to-Earth) MOBILE except aeronautical mobile | 1 675-1 690 METEOROLOGICAL AIDS FIXED METEOROLOGICAL- SATELLITE (space-to-Earth) MOBILE except aeronautical mobile | 1 675-1 690 METEOROLOGICAL AIDS FIXED METEOROLOGICAL- SATELLITE (space-to-Earth) MOBILE except aeronautical mobile |
| 5.341 | 5.341 | 5.341 |
| 1 690-1 700 METEOROLOGICAL AIDS METEOROLOGICAL- SATELLITE (space-to-Earth) Fixed Mobile except aeronautical mobile | 1 690-1 700 METEOROLOGICAL AIDS METEOROLOGICAL- SATELLITE (space-to-Earth) | 1 690-1 700 METEOROLOGICAL AIDS METEOROLOGICAL- SATELLITE (space-to-Earth) |
| 5.289 5.341 5.382 | 5.289 5.341 5.381 | 5.289 5.341 5.381 |
| 1 700-1 710 FIXED METEOROLOGICAL-SATELLITE (space-to-Earth) MOBILE except aeronautical mobile | 1 700-1 710 FIXED METEOROLOGICAL- SATELLITE (space-to-Earth) MOBILE except aeronautical mobile | 1 700-1 710 FIXED METEOROLOGICAL- SATELLITE (space-to-Earth) MOBILE except aeronautical mobile |
| 5.289 5.341 | 5.289 5.341 | 5.289 5.341 5.384 |

Reasons:  There are no MSS systems operating in this band, and none are currently planned, due to the incompatibility of MSS and the Metaids and MetSat services.

USA/  /2	SUP

5.377

Reasons:  Consequential to the deletion of the allocation for MSS.

# Footnotes

This is a revised version of the original draft U.S. proposal on this agenda item. (06/26/02)