Hazard Analysis

Work Plan Title:	Calibration Room Improvements	Date: 	4-16-2008

Prepared By:	C. Bradford, E. Dijak, R. Wyatt

Reviewed By:(optional)

Approved By (Supervisor/Task Manager):

Description of work:

- Removal  and relocation of equipment for new layout.

- Drilling and grinding and use of general hand tools.

- Removal and installation of floor tiles.

Personal Protective Equipment:  (Check protective equipment required for the job.)

X Safety glasses     □ Side shields	□ Chemical splash goggles

X Hearing Protection	□ Hard Hats

□ 3.0 Braising goggles	□ Impact goggles

□ Face shield	□ Rubber apron

X Leather gloves	□ Hot/Cold thermal protective gloves

□ Chemical resistant gloves (specify type):	□ Respirators

Other required PPE (specify): 	□ Fall protection equipment (specify):

X Dust mask

Equipment required for the job:  (List the tools needed to perform the job),

- TE55 Hilti drill, grinder, 2 pound hammer,vacuum.

- Equipment necessary for tile installation.

Work Plan History Information:  (List any lessons learned accidents from this job, tips from previous jobs)

# HAZARD ANALYSIS

| Step | Description | Hazards | Precautions / Safety Procedures |
| --- | --- | --- | --- |
| 1 | Removal of tooling bars And post, relocate to new Positions. Bar must be removed from stands. | Back strain | Remove tooling bars from support posts. Two people can Remove bar off posts and relocate elsewhere. Stand can be relocated by sliding on floor. |
| 2 | Grinding existing studs and anchors to floor level. | Trip hazard, Hot Metal shavings and sparks from grinding. | Safety glasses, dust mask, leather gloves, Direct grindings away from equipment in room. |
| 3 | Drilling holes for anchors. | Dust and concrete chips from drilling. | Safety glasses, dust mask, leather gloves Vacuum for containing dust And debris. |
| 4 | Removing floor tiles. | Tile chipping. | Wear safety glasses and gloves while prying tile up from floor with hand tools. |
| 5 | Laying tile. | Fumes | Ventilate as necessary |
| 6 |  |  |  |
| 7 |  |  |  |
| 8 |  |  |  |
| 9 |  |  |  |
| 10 |  |  |  |

(Use additional pages as needed.)

My supervisor has reviewed this hazard analysis with me and I understand the hazards and required precautionary actions.  I will follow the requirements of this hazard analysis or notify my supervisor if I am unable to do so.  I understand that there are Environmental, Safety and Health Professionals on staff if I need further assistance or clarification.

| Name and ID (please print) | Signature | Date |
| --- | --- | --- |