# DIKE

## PRACTICE INTRODUCTION

USDA, Natural Resources Conservation Service—Practice Code 356

### DIKE

A dike is an embankment constructed of earthen or other suitable material to protect land against overflow or to regulate water.

### PRACTICE INFORMATION

Dikes or levees are used where the control of water level is desired. They are used to prevent or reduce flood damage to people and property, for flow control in conjunction with floodways, to impound or regulate water for fish and wildlife management, or to manage water for production of seasonally flooded crops such as rice and cranberries.

Dikes for cropland water management include perimeter and interior dikes to temporarily impound water for harvesting, trash removal, pest control, seasonal flooding, or other management purposes. These dikes usually have small interior drainage areas in relation to the surface area of the regulated water level.

Considerations for locating a dike include  the foundation soils; property lines; setbacks from property lines; exposure to open water; distance to streambanks; availability of outlets by gravity or pumping; buried utilities; cultural resources; and natural resources such as wetlands, natural areas, and fish and wildlife habitat.

### COMMON ASSOCIATED PRACTICES

Dike is commonly used in a Conservation Management System with practices such as:

Structure for Water Control (587)

Land Smoothing (466)

Irrigation Water Management (449)

Nutrient Management (590)

Pest Management (595)

Wetland Wildlife Habitat Management (644)

For further information, refer to the practice standard in the local Field Office Technical Guide and associated specifications and job sheets.

# Text boxes

Associated practice

(+) increase; (-) decrease

Pathway

C.  Cumulative effect

I.  Indirect effect

D.  Direct effect

D.5 (-) River-floodplain/
tide-marsh interactions

C.2 (+/-) Biodiversity

D.3 (-) Fish passage;       (+) habitat fragmentation

Notes:

Effects are qualified with a plus (+) or minus (-). These symbols indicate only an increase (+) or a decrease (-) in the effect upon the resource, not whether the effect is beneficial or adverse.

The scope of the practice implementation and resulting effects are limited to those described in the “initial setting.” Construction of dikes for other purposes, in floodplains, marshes, estuaries, or other sensitive areas or where a hazard class of I or II applies may need to be evaluated in a site-specific EA.

I.4 (+/-) Wetland wildlife populations (species specific)

D.2 (-) Floodplain, fresh/saltwater wetland, and/or estuarine habitats

D.8 (+) Cost of installation, operation and maintenance (O&M)

#.  Created by practice

I.13 (+) Crop vigor and production (target crop)

I.2 (-) Crop production

I.14 (+) Potential income

I.6 (+) Habitat for shoreline, wading and shallow water wildlife species (non-fisheries)

D.1 (-) Acres of cropland and/or wetland (dike footprint)

D.7 (+) Water use efficiency

I.5 (-) Freshwater and estuarine fish populations

I.16 (+) Water conservation

Structure for Water Control (587)

2. Closed agricultural water use system

I.3 (-) Wetland wildlife habitat

1. Earthen embankment, vegetated

Start

Dike                                                  12/2008

LEGEND

I.15 (+/-) Net return

D.4 (+) Water depth (seasonal)

I.8 (+) Flooding (extent, duration, damages)

Initial setting: Cropland on which retention and management of water is needed and construction of small, hazard class III dike(s) will achieve the following purposes: (1) production of crops requiring seasonal flooding; or (2) creation of small moist soil units to benefit wildlife

I.1 (-) Cropland and wetland benefits

I.11 (+/-) Quality of receiving waters

I.10 (+) Bank erosion

C.1 (+/-) Income and income stability (individuals and community)

D.6 (+) Water retention (seasonal)

Dike (356)

I.7 (-) Habitat complexity

I.12 (-) Contaminants to downstream discharge

I.9 (+) O&M activities (individuals and community)