| NRCS Natural Resources Conservation Service | WASTE TREATMENT LAGOON Conservation Practice Job Sheet 359 |
| --- | --- |
| New Mexico February 2005 |
| Client: |  | Tract: |  | Farm No. |  | Field No.: |  |
| Farm/Ranch Location: |  | County: |  | Acre(s): |  | Date: |  |
| Program: |  | Contract No: |  | Planned Installation Date: |  |
| Drawing No.: |  | Item No.: |  |  |
| Definition: |

A waste treatment impoundment made by constructing an embankment and/or excavating a pit or dugout.

Purpose:

To biologically treat waste, such as manure and wastewater, and thereby reduce pollution potential by serving as a treatment component of a waste management system.

Requirements:

- CONSTRUCTION SHALL NOT COMMENCE PRIOR TO THE ISSUANCE OF A DESIGN ACCEPTANCE LETTER ISSUED BY THE NRCS.  (See §NM521.01 of the National Engineering Manual.)

- It shall be the responsibility of the owner / lessee to obtain all necessary permits and/or rights, and to comply with all ordinances and laws pertaining to this installation.

- On Federal, State, or Tribal lands, or when federal funding is involved on private land, the landowner / lessee must have archaeological clearance and approval / permit from the responsible permitting agency prior to any construction.  If during installation, any cultural resources, historical resources, threatened or endangered species are found, the landowner / lessee must cease operations and obtain archaeological clearance and approval / permit from the responsible permitting agency prior to continuing construction.

- Installation shall be in accordance with the drawings, specifications, and special requirements.

- The following additional data, as applicable to the type of structure, is required: Computations for size, length, width, and depth; inlet, outlet, vent, and safety feature details.  The National Engineering Handbook, Part 651, Agricultural Waste Management Field Handbook, shall be used as needed.

- NM-ENG-121, NM-ENG-127, and NM-ENG-242 may be used to assist in design.

Practice Classification and Approval (NEM Section 501):

The highest Job Class identified for all applicable practices shall be used to identify the Job Class of the project.

| Job Class |
| --- |
| Aerobic Surface Area |  | Acres |  |
| Anaerobic Volume |  | Thousand Cubic Feet |  |
| Effective Dam Height |  | Feet |  |

Engineer Certification:

A registered professional engineer shall certify that the design has been prepared in accordance with Practice Standard 359, the Statement of Work for Practice Standard 359, and any other applicable practice standards necessary to complete the design.

For designs prepared by NRCS personnel:

Design Approved by SCE: 					  New Mexico PE License No.:  				  Date:

For designs prepared by other than NRCS personnel:

Designed by:  								  New Mexico PE License No.: 				  Date:

Accepted by SCE for NRCS: 							  Date:

Landowner/Operator Acknowledgement and Acceptance:

The landowner/operator acknowledges that:

- They have received a copy of the construction drawings and specifications, and understands the contents and requirements and,

- Maintenance of the installed work is necessary for proper performance for the life of the practice.  All federal cost shared practices must be maintained to these specifications for the expected life of the practice.

Accepted by: ____________________________________ Date: _____________________

Signature of Landowner/Operator

Practice Completion:

I have made an on-site inspection (or I am accepting owner/contractor documentation located in the case file), and have determined that the job, as installed, conforms to the drawings and specifications.

Accepted by: _____________________________ Job Title: ___________________ Date: ____________

Authorized NRCS Representative