(IWM – 3) Soils Data Interpretation Table for IWM Planning

| Soil Texture | % Sand | % Silt | % Clay | CEC Range (meq/100g) | Bulk Density (g/cm3) | Soil weight (Million lbs. per ac-ft) | Soil Solids | Unavail-able Water | Available Water | Soil Porosity at FC |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | % Vol. | in/ft | % Vol. | in/ft | % Vol. | in/ft | % Vol. | in/ft |
| Sands | 86 - 98 | 2 - 14 | 2 - 8 | 2 – 6 3 – 8 7 – 15 10 –19 15 - 30 | 1.65 | 4.48 | 62.3 | 7.47 | 2.5 | 0.3 | 4.17 | 0.5 | 31.1 | 3.73 |
| Loamy Sands | 72 - 88 | 2 - 28 | 2 - 14 |  | 1.6 | 4.35 | 60.4 | 7.25 | 7.0 | 0.84 | 8.33 | 1.0 | 24.3 | 2.91 |
| Fine Sands V. F. Sands Loamy F. Sands Loamy V. F. Sands | 86 - 98 | 2 - 14 | 2 - 8 |  | 1.65 | 4.48 | 61.5 | 7.38 | 10.2 | 1.22 | 10.4 | 1.25 | 17.9 | 2.15 |
|  | 86 - 98 | 2 - 14 | 2 - 8 |  | 1.65 | 4.48 |  |  |  |  |  |  |  |  |
|  | 72 - 88 | 2 - 28 | 2 - 14 |  | 1.6 | 4.35 |  |  |  |  |  |  |  |  |
|  | 72 - 88 | 2 - 28 | 2 - 14 |  | 1.6 | 4.35 |  |  |  |  |  |  |  |  |
| Sandy Loam Fine Sandy Loam | 46 - 84 | 2 - 48 | 2- 18 |  | 1.56 | 4.24 | 58.8 | 7.06 | 12.3 | 1.48 | 12.5 | 1.5 | 16.3 | 1.96 |
|  | 46 - 84 | 2 - 48 | 2 - 18 |  | 1.56 | 4.24 |  |  |  |  |  |  |  |  |
| V. F. Sandy Loam Loam Silt Loam Silt | 46 - 84 | 2 - 48 | 2 - 18 |  | 1.53 | 4.16 | 55.4 | 6.65 | 16.2 | 1.94 | 16.7 | 2.0 | 11.8 | 1.41 |
|  | 26 - 50 | 30 - 48 | 10 - 26 |  | 1.42 | 3.86 |  |  |  |  |  |  |  |  |
|  | 2 - 48 | 52 - 78 | 2 - 26 |  | 1.46 | 3.97 |  |  |  |  |  |  |  |  |
|  | 2 - 18 | 82 - 98 | 2 - 10 |  | 1.47 | 3.99 |  |  |  |  |  |  |  |  |
| Sandy Clay Loam Silty Clay Loam Clay Loam | 46 - 78 | 2 - 26 | 22 - 36 |  | 1.4 | 3.8 | 50.2 | 6.02 | 20.0 | 2.4 | 18.3 | 2.2 | 11.5 | 1.38 |
|  | 2 - 18 | 42 - 70 | 28 - 38 |  | 1.27 | 3.45 |  |  |  |  |  |  |  |  |
|  | 22- 44 | 18 - 50 | 28 - 38 |  | 1.32 | 3.59 |  |  |  |  |  |  |  |  |
| Sandy Clay Silty Clay Clay | 46 - 62 | 2 - 16 | 38 - 54 |  | 1.33 | 3.61 | 47.9 | 5.75 | 21.5 | 2.58 | 16.7 | 2.0 | 13.9 | 1.67 |
|  | 2 - 18 | 42 - 58 | 42 - 58 |  | 1.23 | 3.34 |  |  |  |  |  |  |  |  |
|  | 2 - 44 | 2 - 38 | 42 - 98 |  | 1.25 | 3.4 |  |  |  |  |  |  |  |  |
| V = Very & F = Fine Particle diameter (mm) for Sand, Silt & Clay: Very Coarse Sand (2.0 -1.0), Coarse Sand (1.0 - 0.5), Med. Sand (0.5 - 0.25), Fine Sand (0.25 -0.1), Very Fine Sand (0.1 - 0.05), Silt (0.05 - 0.002) and Clay (< 0.002) Cation Exchange Capacity (CEC) taken from the Western Fertilizer Handbook, 2nd ED., 1995 | Bulk Density (Ref. bulk density calculator @ Pedosphere.com) Unavailable Water (Ref. Figure 1-9 of the National Engineering Handbook; Section 15 – Irrigation) Available Water (Ref. NRCS Salinity Management for Soil & Water; Table 5.1, page 5.10 ) FC = Field Capacity. |
| NOTE: Soil structure is evaluated for its effect on downward movement of water: Single grain (rapid), Granular (rapid), Blocky (moderate), Prismatic (moderate), Platy (slow) and Massive (slow). The Soil Intake Family (typically 0.1 thru 2.0) is used in IWM field evaluations and irrigation system design. Irrigation Water Quality (i.e., Electrical Conductivity of irrigation water (ECiw ) in dS/m & Sodium Adsorption Ratio (SAR)) is evaluated for its potential detrimental effects on plant moisture availability and water infiltration. rudy garcia 2008 |