# FEDERAL AVIATION ADMINISTRATION

# AIRWORTHINESS DIRECTIVES

# SMALL AIRCRAFT, ROTORCRAFT, GLIDERS,

# BALLOONS, & AIRSHIPS

# BIWEEKLY 2002-17

# This electronic copy may be printed and used in lieu of the FAA biweekly paper copy.

# U.S. Department of Transportation

Federal Aviation Administration

Regulatory Support Division

Delegation and Airworthiness Programs Branch, AIR-140

P. O. Box 26460

Oklahoma City, OK  73125-0460

FAX  405-954-4104

Biweekly 2002-01

| 2001-26-13 |  | Pilatus Aircraft | PC-7 |
| --- | --- | --- | --- |
| 2001-26-25 |  | Grob-Werke | Sailplane: G102 Club Astir III, G102 Club Astir IIIb, and G102 Standard Astir III |
| 2002-01-02 |  | Turbomeca S.A. | Engine: Arrius 1A |

Biweekly 2002-02

| 2000-20-19 | C, S 86-15-10R2 | Eurocopter France | Rotorcraft: AS-350B, BA, B1, B2, B3, C, D, and D1, and AS-355E, F, F1, F2 and N |
| --- | --- | --- | --- |
| 2001-25-51 | FR | MD Helicopters | Rotorcraft: MD900 |
| 2001-26-52 | FR | Eurocopter Deutschland | Rotorcraft: EC135 |
| 2001-26-53 | FR | Eurocopter France | Rotorcraft: AS350B, B1, B2, B3, BA, D, and AS355E |
| 2002-01-05 |  | British Aerospace | HP.137 Jetstream Mk.1, Jetstream Series 200, Jetstream Series 3101, and Jetstream Model 3201 |
| 2002-01-06 |  | Eurocopter France | Rotorcraft: AS332L2 |
| 2002-01-07 |  | Bell Helicopter Textron Canada | Rotorcraft: 430 |
| 2002-01-09 |  | Pilatus Aircraft | PC-7, PC-12, and PC-12/45 |
| 2002-01-10 |  | Raytheon Aircraft | 65-90, 65-A90, B90, C90, C90A, 65-A90-1, 65-A90-4, E90, and H-90 |
| 2002-01-11 |  | Pilatus Britten-Norman | BN-2, BN-2A, BN-2A-2, BN-2A-3, BN-2A-6, BN-2A-8, BN-2A-9, BN-2A-20, BN-2A-21, BN-2A-26, BN-2A-27, BN-2B-20, BN-2B-21, BN-2B-26, BN-2B-27, BN-2T, BN-2T-4R, BN2A MK. III, BN2A MK. III-2, and BN2A MK. III-3 |

Biweekly 2002-03

| 2001-25-04 |  | Honeywell International | Engine: LTS101-600A-2, LTS101-600A-3, LTP101-600A-1A, LTP101-700A-1A Turboprop |
| --- | --- | --- | --- |
| 2001-26-54 | FR | Eurocopter France | Rotorcraft: EC 155B |
| 2002-01-16 | S 86-24-11 & 86-25-04 | Fairchild Aircraft | SA26-AT, SA226-AT, SA226-T, SA226-T(B), SA226-TC, SA227-AC, SA227-AT, SA227-TT |
| 2002-01-30 |  | Eurocopter France | Rotorcraft: SE 3130, SE 313B, SA 315B, SE 3160, SA 316B, SA 316C, SA 3180, SA 318B, SA 318C, and SA 319B |
| 2002-01-31 | S 2000-22-51 | Bell Helicopter | Rotorcraft: HH-1K, TH-1F, TH-1L, UH-1A, UH-1B, UH-1E, UH-1F, UH-1H, UH-1L, and UH-1P, SW204, SW204HP, SW205, and SW205A-1 |
| 2002-02-01 |  | Eagle Aircraft PTY | 150B |
| 2002-02-51 | E | Eurocopter France | Rotorcraft: AS350B, AS350BA, AS350B1, AS350B2, AS350B3, AS350C, AS350D, AS350D1, AS355E, AS355F, AS355F1, AS355F2, AS355N, and EC130 B4 |
| 2002-03-52 | E, S 2002-02-51 | Eurocopter France | Rotorcraft: AS350B, AS350BA, AS350B1, AS350B2, AS350B3, AS350C, AS350D, AS350D1, AS355E, AS355F, AS355F1, AS355F2, AS335N, and EC130 B4 |

Biweekly 2002-04

| 2001-26-55 | FR | Eurocopter France | Rotorcraft: AS350B, AS350B1, AS350B2, AS350BA, AS350B3, AS350C, AS350D, AS350D1, AS355E, AS355F, AS355F1, AS355F2, and AS355N |
| --- | --- | --- | --- |
| 2002-02-10 |  | Pilatus Britten Norman | BN-2, BN-2A, BN-2A-2, BN-2A-3, BN-2A-6, BN-2A-8, BN-2A-9, BN-2A-20, BN-2A-21, BN-2A-26, BN-2A-27, BN-2B-20, BN-2B-21, BN-2B-26, BN-2B-27, BN-2T, and BN-2T-4R |
| 2002-02-11 |  | Pilatus Britten Norman | BN-2, BN-2A, BN-2A-2, BN-2A-3, BN-2A-6, BN-2A-8, BN-2A-9, BN-2A-20, BN-2A-21, BN-2A-26, BN-2A-27, BN-2B-20, BN-2B-21, BN-2B-26, BN-2B-27, BN-2T, BN-2T-4R, BN2A MK.III, BN2A MK.III-2, and BN2A MK.III-3 |
| 2002-03-01 |  | Honeywell International | Engine: T5311A, T5311B, T5313B, T5317A, T5317B, and former military T53-L-11, T53-L-11A, T53-L-11B, T53-L-11C, T53-L-11D, T53-L-11A S/SA, T53-L-13B, T53-L-13B S/SA, T53-L-13B S/SB, and T53-L-703 Turboshaft |
| 2002-03-02 | S 98-13-03 | British Aerospace | HP.137 Jetstream Mk.1, Jetstream Series 200, Jetstream Series 3101 |

Biweekly 2002-04 continued

| 2002-03-03 |  | Socata-Groupe Aerospatiale | TBM 700 |
| --- | --- | --- | --- |
| 2002-03-04 |  | Pilatus Britten Norman | BN-2, BN-2A, BN-2A-2, BN-2A-3, BN-2A-6, BN-2A-8, BN-2A-9, BN-2A-20, BN-2A-21, BN-2A-26, BN-2A-27, BN-2B-20, BN-2B-21, BN-2B-26, BN-2B-27, BN-2T, BN-2T-4R, BN2A MK.III, BN2A MK.III-2, and BN2A MK.III-3 |
| 2002-03-09 |  | Honeywell International | Engine: LTS101 Series Turboshaft and LTP101 Series Turboprop |
| 2002-03-16 | S 2000-18-52 | Bell Helicopters (See AD) | OH-13E, OH-13H, and OH-13S |
| 2002-04-51 | E | Textron Lycoming | Engine: LTIO-540 and TIO-540 (See AD) |

Biweekly 2002-05

| 2002-04-07 |  | Eurocopter France | Rotorcraft: AS350BA and B2 |
| --- | --- | --- | --- |

Biweekly 2002-06

| 2002-03-09 | R1 | Honeywell International | Engine: LTS101 Series Turboshaft and LTP101 Series Turboprop |
| --- | --- | --- | --- |
| 2002-03-52 | FR, S 2002-02-51 | Eurocopter France | Rotorcraft: AS350B, AS350BA, AS350B1, AS350B2, AS350B3, AS350C, AS350D, AS350D1, AS355E, AS355F, AS355F1, AS355F2, AS355N, and EC130 B4 |
| 2002-05-04 | S 77-15-06 | Socata-Groupe Aerospatiale | MS 892A-150, MS 892E-150, MS 893A, MS 893E, MS 894A, MS 894E, Rallye 150T, and Rallye 150ST |
| 2002-05-05 |  | Cirrus Design Corporation | SR20 and SR22 |
| 2002-05-06 | COR, S 86-09-11 | Sikorsky Aircraft Corporation | Rotorcraft: S-76A |
| 2002-06-04 |  | Eurocopter France | Rotorcraft: AS350B, AS350B1, AS350B2, AS350B3, AS350BA, AS350C, AS350D, AS350D1, AS355E, AS355F, AS355F1, AS355F2, and AS355N |
| 2002-06-05 |  | Transport Category Airplanes Rockwell Collins | Appliance: Mode C 621A-3 Air Traffic Control (ATC) Transponder(s) |
| 2002-06-08 |  | Rolls-Royce Corp. | Engine: 250-C28, -C28B, and -C28C |
| 2002-06-52 | E, S 2000-02-12 | Bell Helicopter Textron Canada | Rotorcraft: 407 |

Biweekly 2002-07

| 2002-06-06 |  | Rockwell Collins, Inc. | Appliance: TDR-94 and TDR-94D Mode S Transponders |
| --- | --- | --- | --- |
| 2002-06-10 |  | Pilatus Aircraft | PC-12 and PC-12/45 |
| 2002-07-01 |  | Cessna | P206C, TP206C, P206D, TP206D, P206E, TP206E, U206C, TU206C, U206D, TU206D, U206E, TU206E, U206F, TU206F, U206G, TU206G, 207, T207, 207A, T207A, 210G, 210H, 210J, 210K, T210K, 210L, T210L, 210M, T210M, 210N, T210N, P210N, T210G, T210H, T210J |

Biweekly 2002-08

| 2001-24-51 | FR | MD Helicopters, Inc. | Rotorcraft: 600N |
| --- | --- | --- | --- |
| 2002-06-52 | FR, S 2000-02-12 | Bell Helicopter Textron Canada | Rotorcraft: 407 |
| 2002-08-01 |  | Fairchild Aircraft, Inc. | SA226-AT, SA226-T, SA226-T(B), SA226-TC, SA227-AC, SA227-AT, and SA227-TT |
| 2002-08-02 | S 2001-20-14 | Fairchild Aircraft, Inc. | SA226-AT, SA226-T, SA226-T(B), SA226-TC, SA227-AC, SA227-AT, SA227-TT, and SA227-TT(300) |
| 2002-08-03 | S 2001-22-01 | Enstrom Helicopter Corp. | Rotorcraft: F-28, F-28A, F-28C, F-28F, 280, 280C, 280F and 280FX |

Biweekly 2002-09

| 2001-25-52 | FR, S 76-18-01 | Schweizer Aircraft Corp. | Rotorcraft: 269A, 269A-1, 269B, 269C, and TH-55A |
| --- | --- | --- | --- |
| 2002-03-52 | FR, COR, S 2002-02-51 | Eurocopter France | Rotorcraft: AS350B, AS350BA, AS350B1, AS350B2, AS350B3, AS350C, AS350D, AS350D1, AS355E, AS355F, AS355F1, AS355F2, AS355N, and EC130 B4 |
| 2002-08-02 | COR, S 2001-20-14 | Fairchild Aircraft, Inc. | SA226-AT, SA226-T, SA226-T(B), SA226-TC, SA227-AC, SA227-AT, SA227-TT, and SA227-TT(300) |
| 2002-08-04 |  | Piaggio Aero Industries S.p.A. | P-180 |
| 2002-08-16 | S 2001-19-51 | Eurocopter France | Rotorcraft: SA341G, SA342J, and SA-360C |
| 2002-08-53 | E | Bell Helicopter Textron, Inc. | Rotorcraft: 205A, A-1 and B |
| 2002-08-54 | E | Bell Helicopter Textron Canada | Rotorcraft: 222, 222B, 222U, and 230 |
| 2002-09-03 |  | Eurocopter France | Rotorcraft: AS332L2 |
| 2002-09-04 |  | Bell Helicopter Textron, Inc. | 205A, 205A-1, 205B, 212, 412, 412EP, and 412CF |
| Biweekly 2002-10 |  |  |
| 2002-09-08 | S 77-12-06 R2 | Hartzell Propellers | Propellers: ( )HC-( )( )Y( )-( )( )( ) Compact Series |
| 2002-09-09 |  | Honeywell International | Engine: T53 Series |
| 2002-09-11 | COR, S 2001-05-03 | SOCATA | TBM 700 |
| 2002-09-12 | COR | Raytheon | C90A |
| 2002-09-13 |  | Cessna | 441 |
| 2002-09-51 | E, S 2002-08-53 | Bell Helicopters | Rotorcraft: 204B, 205A, A-1, and B |
| 2002-10-05 | S 2001-07-09 | MD Helicopters | Rotorcraft: MD-900 |

| Biweekly 2002-11 |  |  |
| --- | --- | --- |
| 2002-10-13 |  | Raytheon Aircraft Company | 58P, 60, A60, B60, and 65-88 |
| 2002-10-14 |  | Bombardier-Rotax GmbH | Engine: 914 F Series |
| 2002-11-01 |  | Eurocopter Deutschland | Rotorcraft: EC135 |
| 2002-11-02 |  | Raytheon Aircraft Company | 390 |
| 2002-11-05 |  | Air Tractor, Inc. | AT-400, AT-401, AT-401B, AT-402, AT-402A, AT-402B, AT-501, AT-802, and AT-802A |

Biweekly 2002-12

| 2002-11-03 |  | Air Tractor, Inc. | AT-502, AT-502A, AT-502B, AT-503A |
| --- | --- | --- | --- |
| 2002-11-07 |  | Raytheon Aircraft | E55, E55A, A56TC, 58, 58A, 58P, 58PA, 58TC, and 58TCA |
| 2002-11-09 |  | Bell Helicopter | Rotorcraft: 407 |
| 2002-11-10 | S 2001-25-08 | Sikorsky | Rotorcraft: S-70A, S-70C |
| 2002-12-02 |  | Eurocopter France | Rotorcraft: AS332L2 |
| 2002-12-03 |  | Eurocopter France | Rotorcraft: AS332L2 |

Biweekly 2002-13

| 2002-11-03 | COR | Air Tractor, Inc. | AT-502, AT-502A, AT-502B, AT-503A |
| --- | --- | --- | --- |
| 2002-12-07 | S 2000-18-53 | Textron Lycoming | Engine: O–320–H1AD, –H1BD, –H2AD, –H2BD, –H3AD, -H3BD, (L)O–360,–A1AD, –A1F6D, –A1G6D, –A1LD, –A3AD, –A4AD, –A5AD, –E1A6D, IO–360–A1B6D, –A1D6D, –A3B6D, –A3D6D, –C1E6D, –J1AD, –J1A6D, (L)TO–360,–A1A6D, -C1A6D, –E1A6D, –F1A6D, TIO–360–C1A6D, (L)HIO-360-E1AD, –E1BD, –F1AD, O–540–H1A5D, –H1B5D, -H2A5D, –H2B5D, –J1A5D, –J1B5D, –J1C5D, –J1D5D, -J2A5D, –J2B5D, –J2C5D, –J2D5D, –J3A5D, –J3C5D, –L3C5D, IO-540-C4D5D, –K1A5D, –K1B5D, –K1E5D, –K1F5D, -K1G5D, –K1J5D, –L1A5D, -L1B5D, –M1A5D, –M1B5D, –M2A5D, -T4A5D, –T4B5D, –T4C5D, –U1A5D, -U1B5D, –V4A5D, -W1A5D, –W3A5D, (L)TIO–540–K1AD, –S1AD, –AA1AD, -AB1AD, –AB1BD, –F2BD, –J2BD, –N2BD, -R2AD, –T2AD, -V2AD, AEIO–540–L1B5D, TIO–541–E Series, TIGO–541–D1A, –D1B, –E1A, IO–720–A1BD, –B1BD, –C1BD, –D1BD, –D1CD |
| 2002-12-09 |  | Honeywell International | Engine: TPE331-11U, -12B, -12JR, -12UA, -12UAR, and -12UHR Series Turboprop |
| 2002-12-14 | S 99-23-07 | Eurocopter France | Rotorcraft: SA330F, G, SA330J, AS332C, L, and L1 |
| 2002-13-04 | S 2000-11-51 | Teledyne Continental | Engine: C-125, C145, O-300, IO-360, TSIO-360, and LTSIO-520-AE Series Reciprocating |
| 2002-13-05 |  | MD Helicopters | Rotorcraft: 369D, 369E, 369F, and 369FF |
| 2002-13-06 |  | Eurocopter Deutschland | Rotorcraft: BO-105A, BO-105C, BO-105 C-2, BO-105 CB-2, BO-105 CB-4, BO-105S, BO-105 CS-2, BO-105 CBS-2, BO-105 CBS-4, and BO-105LS A-1 |
| 2002-13-51 | E | Bell Helicopters | Rotorcraft: HH-1K, TH-1F, TH-1L, UH-1A, UH-1B, UH-1E, UH-1F, UH-1H, UH-1L, UH-1P; SW204, SW204HP, SW205, and SW205A-1 |

Biweekly 2002-14

| 2002-13-02 |  | Air Tractor | AT-300, AT-301, AT-302, and AT-400A |
| --- | --- | --- | --- |
| 2002-13-07 |  | Honeywell, Inc. | Appliance: Inertial Reference Unit |
| 2002-13-08 |  | de Havilland | DHC-2 Mk.I, DHC-2 Mk. II, and DHC-2 Mk. III |
| 2002-13-11 |  | Eurocopter France | Rotorcraft: EC120B |
| 2002-14-01 |  | Eurocopter France | Rotorcraft: AS332L and AS332L1 |
| 2002-14-17 | S 99-12-01 | Eurocopter Deutschland | Rotorcraft: EC135 |
| 2002-14-18 |  | Glaser-Dirks Flugzeugbau | Sailplane: DG-400 and DG-800A |
| 2002-14-51 | E | Agusta S.p.A | Rotorcraft: A109E and A119 |

Biweekly 2002-15

| 2002-13-04 | COR S 2000-11-51 | Teledyne Continental | Engine: C-125, C145, O-300, IO-360, TSIO-360, and LTSIO-520-AE Series Reciprocating |
| --- | --- | --- | --- |
| 2002-14-19 |  | Rockwell Collins | Appliance: Air Data Computers (ADC) |
| 2002-14-22 | COR | Pilatus Aircraft | PC-12 and PC-12/45 |
| 2002-14-26 |  | Turbomeca S.A. | Engine: Arriel Models 1A, 1A1, 1B, 1D, and 1D1 Turboshaft |
| 2002-14-28 |  | de Havilland | DHC-2, Mk. I, DHC-2 Mk. II, and DHC-2 Mk. III |
| 2002-15-01 |  | Diamond Aircraft | Sailplane: H-36 ''Dimona'', HK 36 R ''Super Dimona'', HK 36 TC, HK 36 TS, HK 36 TTC, HK 36 TTC-ECO, HK 36 TTC-ECO (Restricted Category), and HK 36 TTS |
| 2002-15-02 |  | Hamilton Sundstrand Power Sys. | Appliance: Auxiliary Power Units (APU's) |
| 2002-15-51 | E | Sikorsky | Rotorcraft: S76A, B, and C |

Biweekly 2002-16

| 2002-08-54 | FR | Bell Helicopter | Rotorcraft: 222, 222B, 222U, 230 |
| --- | --- | --- | --- |
| 2002-09-51 | FR, S 2002-08-53 | Bell Helicopter | Rotorcraft: 204B, 205A, A-1, and B |
| 2002-13-51 | FR | Bell Helicopter, (See AD) | Rotorcraft: HH-1K, TH-1F, TH-1L, UH-1A, UH-1B, UH-1E, UH-1F, UH-1H, UH-1L, and UH-1P; SW204, SW204HP, SW205, and SW205A-1 |
| 2002-15-04 |  | Honeywell International | Engine: T5313B, T5317 Series, and former military T53 Series Turboshaft |
| 2002-15-05 |  | Turbomeca | Engine: Makila 1 A, 1 A1, and 1 A2 Turboshaft |
| 2002-15-06 |  | Air Tractor | AT-802 and AT-802A |
| 2002-15-07 |  | MD Helicopters | Rotorcraft: MD900 |
| 2002-15-08 |  | Eurocopter France | Rotorcraft: EC120B, EC155B, SA330F, SA330G, SA330J, AS332C, AS332L, AS332L1, AS332L2, AS350B, AS350BA, AS350B1, AS350B2, AS350B3, AS350D, AS355E, AS355F, AS355F1, AS355F2, AS355N, AS-365N2, AS 365 N3, SA-365N, and SA-365N1 |

Biweekly 2002-17

| 2002-08-54 | COR | Bell Helicopter | Rotorcraft: 222, 222B, 222U, 230 |
| --- | --- | --- | --- |
| 2002-16-04 | S 46-38-03, 86-22-09 | Univair Aircraft | (ERCO) 415-C, 415-CD, 415-D, 415-E, 415-G, (Forney) F-1, and F-1A |
| 2002-16-07 |  | Bombardier-Rotax GmbH | Engine: 912 F, 912 S, and 914 F Series Reciprocating |
| 2002-16-17 |  | Barry Aviation | Sailplane: Model PZL-Krosno KR-03A ''Peregrine'' (Puchatek) |
| 2002-16-25 |  | Turbomeca S.A. | Engine: Arriel 2S1, 2B and 2 C Turboshaft |
| 2002-16-26 | COR | Bombardier-Rotax GmbH | Engine: 912 F series and 914 F series reciprocating |
| 2002-17-51 | E, S 02-14-51 | Agusta S.p.A. | Rotorcraft: A109E |
| 2002-17-52 | E, S 02-14-51 | Agusta S.p.A. | Rotorcraft: A119 |
| 2002-17-53 | E | Textron Lycoming | Engine: LTIO-540 and TIO-540 |

BW 2002-17

BELL HELICOPTER TEXTRON CANADA

AIRWORTHINESS DIRECTIVE

SMALL AIRCRAFT, ROTORCRAFT, GLIDERS, BALLOONS, & AIRSHIPS

EDITORIAL CORRECTION [Federal Register: August 21, 2002 (Volume 67, Number 162); Page 54259; www.access.gpo.gov/su_docs/aces/aces140.html]

2002-08-54  Bell Helicopter Textron Canada: Amendment 39-12835, Docket No. 2002-SW-22-AD.

Applicability: The following model helicopters with the listed part number (P/N) installed, certificated in any category:

| Model | With hub assembly P/N | With grip assembly P/N | With pitch horn assembly P/N |
| --- | --- | --- | --- |
| (1) 222 or 222B | 222–011–101–103, -105, -107, or -109 | 222–010–104–105 | 222–011–104–101 |
|  | 222–012–101–103, or -107 | 222–012–104–101 | 222–012–102–101 |
| (2) 222U | 222–011–101–105, -107, or -109 | 222–010–104–105 | 222–011–104–101 |
|  | 222–012–101–103, OR -107 | 222–012–104–101 | 222–012–102–101 |
| (3) 230 | 222–012–101–105, or -109 | 222–012–104–101 | 222–012–102–101 |

Note 1: This AD applies to each helicopter identified in the preceding applicability provision, regardless of whether it has been otherwise modified, altered, or repaired in the area subject to the requirements of this AD. For helicopters that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (d) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance: Required as indicated, unless accomplished previously.

To prevent failure of the grip or pitch horn and subsequent loss of control of the helicopter, if either the grip or pitch horn has accumulated 1250 or more hours time-in-service (TIS) since initial installation on any helicopter, accomplish the following:

(a) Before further flight and thereafter at intervals not to exceed 8 hours TIS:

(1) Wipe clean the main rotor grip and pitch horn surfaces to remove grease and dirt in the check area as shown in Figure 1 of this AD:

(2) Visually check both main rotor grips for a crack, paying particular attention to the inboard and outboard tangs/portions of the grip, which are in direct contact with the pitch horns and the main rotor blades. Check the area to at least 3 inches beyond the grip/pitch and grip/blade contact areas as shown in Figure 2 of this AD:

(3) Visually check all visible portions of each pitch horn for a crack. Pay particular attention to the attachment lugs of the pitch horns, which are in direct contact with the inboard tangs of the main rotor grips, as shown in Figure 3 of this AD, and the four large bolt cutouts, as shown in Figure 4 of this AD:

(4) An owner/operator (pilot) may perform the visual check required by this AD. The pilot must enter compliance with paragraph (a) of this AD into the helicopter maintenance records in accordance with 14 CFR 43.11 and 91.417(a)(2)(v)). A pilot may perform this check because it involves only a visual check for a crack in the grip or pitch horn and can be performed equally well by a pilot or a mechanic.

(b) Within 7 days or 10 hours TIS, whichever occurs first, and thereafter at intervals not to exceed 25 hours TIS, using a 10-power or higher magnifying glass, visually inspect each grip and pitch horn for a crack in accordance with the Accomplishment Instructions, Part II, paragraphs 1 and 2, of Bell Helicopter Textron Alert Service Bulletin Nos. 222U-02-64, 222-02-93, and 230-02-26, all dated April 1, 2002, as applicable.

(c) If a crack is found, replace the unairworthy grip or pitch horn with an airworthy part before further flight.

(d) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Regulations Group, FAA. Operators shall submit their requests through an FAA Principal Maintenance Inspector, who may concur or comment and then send it to the Manager, Regulations Group.

Note 2: Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Regulations Group.

(e) Special flight permits may be issued in accordance with 14 CFR 21.197 and 21.199 to operate the helicopter to a location where the inspection requirements of paragraph (b) of this AD can be accomplished.

(f) The inspection shall be done in accordance with the Accomplishment Instructions, Part II, paragraphs 1 and 2, of Bell Helicopter Textron Alert Service Bulletin Nos. 222U-02-64, 222-02-93, and 230-02-26, all dated April 1, 2002, as applicable. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Bell Helicopter Textron Canada, 12,800 Rue de l'Avenir, Mirabel, Quebec J7J1R4, telephone (450) 437-2862 or (800) 363-8023, fax (450) 433-0272. Copies may be inspected at the FAA, Office of the Regional Counsel, Southwest Region, 2601 Meacham Blvd., Room 663, Fort Worth, Texas; or at the Office of the Federal Register, 800 North Capitol Street, NE., suite 700, Washington, DC.

(g) This amendment becomes effective on August 21, 2002, to all persons except those persons to whom it was made immediately effective by Emergency AD 2002-08-54, issued May 2, 2002, which contained the requirements of this amendment.

Note 3: The subject of this AD is addressed in Transport Canada (Canada) AD CF-2002-23, dated April 2, 2002.

Issued in Fort Worth, Texas, on July 25, 2002.

Eric Bries,

Acting Manager, Rotorcraft Directorate, Aircraft Certification Service.

[FR Doc. 02-19486 Filed 8-5-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-17

UNIVAIR AIRCRAFT CORPORATION

AIRWORTHINESS DIRECTIVE

SMALL AIRCRAFT, ROTORCRAFT, GLIDERS, BALLOONS, & AIRSHIPS

2002-16-04 Univair Aircraft Corporation: Amendment 39-12843; Docket No. 2000-CE-79-AD; Supersedes AD 46-38-03 and AD 86-22-09, Amendment 39-5457.

(a) What airplanes are affected by this AD? This AD affects all serial numbers of Models (ERCO) 415-C, (ERCO) 415-CD, (ERCO) 415-D, (ERCO) 415-E, (ERCO) 415-G, (Forney) F-1, and (Forney) F-1A airplanes that:

(1) are certificated in any category; and

(2) have the gascolator connected to the side of the carburetor. This AD does not affect those airplanes with the gascolator mounted on the firewall.

(b) Who must comply with this AD? Anyone who wishes to operate any of the airplanes identified in paragraph (a) of this AD must comply with this AD.

(c) What problem does this AD address? The actions specified by this AD are intended to prevent failure of the fuel line fittings or the gascolator because of the current airplane design configuration (aluminum fuel line nipples, aluminum fuel line elbows, and/or no double support tubes on the gascolator). Such failure could result in a lack of fuel to the engine with consequent loss of control of the airplane.

(d) What actions must I accomplish to address this problem? To address this problem, you must accomplish the following:

| Actions | Compliance | Procedures |
| --- | --- | --- |
| (1) Visually inspect the fuel line nipple and elbow located between the carburetor and gascolator for cracks or misalignment, and replace as necessary. | Inspect within the next 25 ours time-in-service (TIS) after September 13, 2002 (the effective date of this AD) and replace prior to further flight after the inspection. You must inspect even if you have inspected previously. | In accordance with Univair Service Bulletin No. 24B, dated January 29, 2002. |
| (2) Replace any aluminum fuel line nipple with one made of brass or steel. | Within the next 25 TIS after September 13, 2002 (the effective date of this AD), unless already accomplished (compliance with AD 86–22–09 and/or Univair Service Bulletin No. 24A, dated August 22, 1986). | In accordance with Univair Service Bulletin No. 24B, dated January 29, 2002. |
| (3) Replace any aluminum fuel elbow fitting with one made of brass or steel. Manufacturer replacement parts numbers are referenced in the service information. | Within the next 25 hours TIS after September 13, 2002 (the effective date of this AD), unless already accomplished (compliance with AD 46–38–03). | In accordance with Univair Service Bulletin No. 24B, dated January 29, 2002. |

| (4) Inspect for the existence of double support tubes on the gascolator and install these tubes if they do not exist, as follows: (i) For all affected airplanes except for (Forney) F–1 and (Forney) F–1A airplanes, install part numbers 48076 and 48096 (or FAA-approved equivalent part numbers) double support tubes; and (ii) For all affected (Forney) F–1 and (Forney) F1–A airplanes, install part numbers 48098 and 48099 (or FAA-approved equivalent part numbers) double support tubes. | Inspect within the next 25 hours TIS after September 13, 2002 (the effective date of this AD) and install the double support tubes prior to further flight after the inspection, unless already accomplished (compliance with Univair Service Bulletin No. 24A, dated August 22, 1986). | In accordance with Univair Service Bulletin No. 24B, dated January 29, 2002. |
| --- | --- | --- |
| (5) Do not install, on any affected airplane, an aluminum fuel line nipple or aluminum elbow. | As of September 13, 2002 (the effective date of this AD). | Not Applicable. |
| (6) Do not install a gascolator on the side of the carburetor on any affected airplane, unless the double support tubes specified in paragraph (d)(4)(i) or (d)(4)(ii) of this AD are installed. | As of September 13, 2002 (the effective date of this AD). | Not Applicable. |

(e) Can I comply with this AD in any other way?

(1) You may use an alternative method of compliance or adjust the compliance time if:

(i) Your alternative method of compliance provides an equivalent level of safety; and

(ii) The Manager, Denver Aircraft Certification Office (ACO), approves your alternative. Submit your request through an FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Denver ACO.

(2) Alternative methods of compliance approved in accordance with AD 46-38-03 and/or AD 86-22-09, which are superseded by this AD, are not approved as alternative methods of compliance with this AD.

Note: This AD applies to each airplane identified in paragraph (a) of this AD, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For airplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (e) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if you have not eliminated the unsafe condition, specific actions you propose to address it.

(f) Where can I get information about any already-approved alternative methods of compliance? Contact Elizabeth Bumann, Aerospace Engineer, FAA, Denver Aircraft Certification Office, 26805 East 68th Avenue, Room 214, Denver, Colorado 80249; telephone: (303) 342-1083; facsimile: (303) 342-1088.

(g) What if I need to fly the airplane to another location to comply with this AD? The FAA can issue a special flight permit under Secs. 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate your airplane to a location where you can accomplish the requirements of this AD.

(h) Are any service bulletins incorporated into this AD by reference? Actions required by this AD must be done in accordance with Univair Service Bulletin No. 24B, dated January 29, 2002. The Director of the Federal Register approved this incorporation by reference under 5 U.S.C. 552(a) and 1 CFR part 51. You can get copies from Univair Aircraft Corporation, 2500 Himalaya Road, Aurora, Colorado 80011. You can look at copies at the FAA, Central Region, Office of the Regional Counsel, 901 Locust, Room 506, Kansas City, Missouri, or at the Office of the Federal Register, 800 North Capitol Street, NW., Suite 700, Washington, DC.

(i) Does this AD action affect any existing AD actions? This amendment supersedes AD 46-38-03 and AD 86-22-09, Amendment 39-5457.

(j) When does this amendment become effective? This amendment becomes effective on September 13, 2002.

Issued in Kansas City, Missouri, on July 30, 2002.

Michael Gallagher,

Manager, Small Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-19874 Filed 8-9-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-17

BOMBARDIER-ROTAX GMBH

AIRWORTHINESS DIRECTIVE

ENGINE

SMALL AIRCRAFT, ROTORCRAFT, GLIDERS, BALLOONS, & AIRSHIPS

2002-16-07  Bombardier-Rotax GmbH: Amendment 39-12846. Docket No. 2002-NE-17-AD.

Applicability

This airworthiness directive (AD) is applicable to Bombardier-Rotax GmbH type 912 F, 912 S, and 914 F series reciprocating engines with the serial numbers (SN's) in Table 1 of this AD, and all engines that have been converted to a single valve spring arrangement at engine repair or general overhaul. Table 1 follows:

| TABLE 1.—ENGINE SERIES BY SN |
| --- |
| Engine model | Engine SN |
| 912 F | 4,412.757 to 4,412.794 |
|  | 4,412.796 to 4,412.807 |
| 912 S | 4,922.501 to 4,922.534 |
|  | 4,922.536 to 4,922.552 |
|  | 4,922.554 to 4,922.577 |
|  | 4,922.579 to 4,922.636 |
| 914 F | 4,420.039 to 4,420.048 |
|  | 4,420.050 to 4,420.067 |
|  | 4,420.069 to 4,420.082 |
|  | 4,420.084 to 4,420.097 |
|  | 4,420.099 to 4,420.114 |
|  | 4,420.116 to 4,420.155 |
|  | 4,420.157 to 4,420.253 |

These engines are installed on, but not limited to, Diamond Aircraft Industries, DA20-A1, Diamond Aircraft Industries GmbH Model HK 36 TTS, Model HK 36TTC, and Model HK 36 TTC-ECO, Iniziative Industriali Italiane S.p.A. Sky Arrow 650 TC and Sky Arrow 650 TCN, Aeromot-Industria Mecanico Metalurgica ltda., Models AMT-300 and AMT-200S, and Stemme S10-VT aircraft.

Note 1: This AD applies to each engine identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For engines that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (c) of this AD. The request should include an

assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance

Compliance with this AD is required as indicated, unless already done.

To prevent cracking of the valve spring retainers resulting in possible engine failure while in-flight, do the following:

Replacement Procedure

(a) Replace valve spring retainers part number (P/N) 854.182, of single valve spring configuration, with valve spring retainers P/N 854.184, in accordance with 3.1.1 of the Accomplishment Instructions of Mandatory Service Bulletin (MSB) SB-912-022/SB-914-011, dated March, 2001, using the compliance times in the following Table 2:

| TABLE 2.—COMPLIANCE SCHEDULE |
| --- |
| Engine flight hours (FH) on the effective date of this AD | Replace |
| (1) 0 FH (new engine) | Before installing on aircraft. |
| (2) 10 hours or less .. | Within 10 FH after the effective date of this AD. |
| (3) More than 10 but less than or equal to 25 FH. | Within 25 FH after the effective date of this AD. |
| (4) More than 25 FH | Before exceeding 100 FH. |

(b) For engines that have had the oil system accessed during repair or maintenance, replace the valve spring retainers in accordance with 3.1.1 of the Accomplishment Instructions of Mandatory Service Bulletin (MSB) SB-912-022/SB-914-011, dated March, 2001, within 10 FH after the effective date of this AD.

Alternative Methods of Compliance

(c) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Engine Certification Office (ECO). Operators must submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, ECO.

Note 2: Information concerning the existence of approved alternative methods of compliance with this airworthiness directive, if any, may be obtained from the ECO.

Special Flight Permits

(d) Special flight permits may be issued in accordance with Secs. 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the aircraft to a location where the requirements of this AD can be done.

Documents That Have Been Incorporated by Reference

(e) The replacements must be done in accordance with Bombardier-Rotax GmbH Mandatory Service Bulletin (MSB) SB-912-022/SB-914-011, dated March, 2001. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Bombardier-Rotax GmbH, Welser Strasse 32, A-4623 Gunskirchen, Austria; telephone 7246-601-232; fax 7246-601-370. Copies may be inspected at the FAA, New England Region, Office of the Regional Counsel, 12 New England Executive Park, Burlington, MA; or at the Office of the Federal Register, 800 North Capitol Street, NW, suite 700, Washington, DC.

Note 3: The subject of this AD is addressed in Austro Control airworthiness directive No. 108.

Effective Date

(f) This amendment becomes effective on September 3, 2002.

Issued in Burlington, Massachusetts, on August 2, 2002.

Jay J. Pardee,

Manager, Engine and Propeller Directorate, Aircraft Certification Service.

[FR Doc. 02-20266 Filed 8-15-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-17

BARRY AVIATION, LLC

AIRWORTHINESS DIRECTIVE

SMALL AIRCRAFT, ROTORCRAFT, GLIDERS, BALLOONS, & AIRSHIPS

2002-16-17  Barry Aviation, LLC: Amendment 39-12856; Docket No. 2002-CE-30-AD.

(a) What sailplanes are affected by this AD? This AD applies to Model PZL-Krosno KR-03A ''Peregrine'' (Puchatek) sailplanes, serial numbers 03-01 through 03-24 and 04-01 through 04-20, that are certificated in any category.

Note 1: PZL-Krosno previously held the type certificate for these sailplanes.

(b) Who must comply with this AD? Anyone who wishes to operate any of the sailplanes identified in paragraph (a) of this AD must comply with this AD.

(c) What problem does this AD address? The actions specified by this AD are intended to prevent cracking in the horizontal stabilizer attachment fittings, which could result in the horizontal stabilizer separating from the sailplane with consequent loss of control of the sailplane.

(d) What must I do to address this problem? To address this problem, you must accomplish the following actions:

| Actions | Compliance | Procedures |
| --- | --- | --- |
| (1) Inspect the horizontal stabilizer attachment fittings to ensure that the correct fittings are installed:. (i) If part number (P/N) NS–03/08/93–01L/P attachment fittings (or FAA-approved equivalent part numbers) are installed, no further action is required by this paragraph. (ii) If the attachment fittings are P/Ns other than NS–03/08/93–01L/P (or FAA-approved equivalent part numbers), replace the fittings with the P/N NS–03/08/93–01L/P attachment fittings (or FAA-approved equivalent part numbers). | Inspect within 10 hours time-in-service (TIS) after August 30, 2002 (the effective date of this AD). Replace prior to further flight after the inspection. | Inspect in accordance with Barry Aviation ‘‘KROSNO KR–03A Glider’’ Service Bulletin No. 1–02, dated June 10, 2002. Replace in accordance with WSK ‘‘PZL–KROSNO’’ Service Bulletin No. BE–29/KR–03A/93, dated November 16, 1993. |
| (2) Incorporate a ‘‘NO LIFT’’ placard to the vertical stabilizer. | Within 10 hours TIS after August 30, 2002 (the effective date of this AD). | Use paint or a permanent placard and add the words ‘‘NO LIFT’’ to both sides of the vertical stabilizer near the top and leading edge. Use letters that are at least .5 inch and a color that contrasts with the color of the airplane, e.g., use red on a blue airplane. |

(e) Can I comply with this AD in any other way? You may use an alternative method of compliance or adjust the compliance time if:

(1) Your alternative method of compliance provides an equivalent level of safety; and

(2) The Manager, Atlanta Aircraft Certification Office (ACO), approves your alternative. Submit your request through an FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, Atlanta ACO.

Note 2: This AD applies to each sailplane identified in paragraph (a) of this AD, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For sailplanes that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (e) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if you have not eliminated the unsafe condition, specific actions you propose to address it.

(f) Where can I get information about any already-approved alternative methods of compliance? Contact William O. Herderich, Aerospace Engineer, FAA, Atlanta Aircraft Certification Office, 1895 Phoenix Boulevard, suite 450, Atlanta, Georgia 30349; telephone: (770) 703-6082; facsimile: (770) 703-6097; e-mail: william.o.herderich@faa.gov.

(g) Are any service bulletins incorporated into this AD by reference? Actions required by this AD must be done in accordance with WSK ''PZL-KROSNO'' Service Bulletin No. BE-29/KR-03A/93, dated November 16, 1993; and Barry Aviation ''KROSNO KR-03A Glider'' Service Bulletin No. 1-02, dated June 10, 2002. The Director of the Federal Register approved this incorporation by reference under 5 U.S.C. 552(a) and 1 CFR part 51. You may get copies from Barry Aviation, LLC, 11600 Aviation Boulevard, suite 16, West Palm Beach, Florida 33412. You may view this information at FAA, Central Region, Office of the Regional Counsel, 901 Locust, Room 506, Kansas City, Missouri, or at the Office of the Federal Register, 800 North Capitol Street, NW., suite 700, Washington, DC.

(h) When does this amendment become effective? This amendment becomes effective on August 30, 2002.

Issued in Kansas City, Missouri, on August 6, 2002.

Michael Gallagher,

Manager, Small Airplane Directorate, Aircraft Certification Service.

[FR Doc. 02-20400 Filed 8-15-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-17

TURBOMECA S.A.

AIRWORTHINESS DIRECTIVE

ENGINE

SMALL AIRCRAFT, ROTORCRAFT, GLIDERS, BALLOONS, & AIRSHIPS

2002-16-25  Turbomeca S.A.: Amendment 39-12864. Docket No. 2001-NE-10-AD.

Applicability

This airworthiness directive (AD) is applicable to Turbomeca S.A. Arriel models 2 S1, 2 B, and 2 C turboshaft engines. These engines are installed on, but not limited to Sikorsky S76, Eurocopter France ''Ecureuil'' AS 350 B3, and Eurocopter France ''Dauphin'' AS 365 N3 helicopters.

Note 1: This AD applies to each engine identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For engines that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (e) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance

Compliance with this AD is required as indicated, unless already done.

To prevent fuel leakage, which may cause engine fires that could lead to an in-flight engine shutdown, damage to the helicopter, and forced landing, do the following:

Inspections and Actions

(a) For the fuel metering high pressure/low pressure (HP/LP) pump assemblies listed by serial number (SN) in Appendix 1 of Turbomeca Service Bulletin (SB) No. 292 73 2803, dated July 2, 1999, do the following:

(1) After the last flight of each day, within five minutes of engine shutdown, perform a visual inspection of the floor of the helicopter engine bay for fuel leaks.

(2) If evidence of a fuel leak is observed, inspect the fuel metering HP/LP pump assembly for leakage and if leakage is observed, replace with a serviceable pump assembly before further flight.

(3) If visual inspection of the floor of the helicopter engine bay for fuel leaks reveals no leaks, do either of the following:

(i) Continue repetitive visual inspections of the floor of the helicopter engine bay for fuel leaks in accordance with paragraph (a)(1) of this AD, and perform repetitive visual inspections of the fuel metering HP/LP pump assembly for fuel leaks at intervals not to exceed 50 hours of operation. If evidence of fuel leaking is observed, replace the pump assembly with a serviceable pump assembly before further flight, in accordance with Turbomeca SB No. 292 73 2803, dated July 2, 1999; or

(ii) Remove the pump assembly and inspect to determine if pump body material wall thickness is below the minimum material thickness, in accordance with Section 2 of Turbomeca SB No. 292 73 2803, dated July 2, 1999. If pump body material wall thickness is at or above the minimum material thickness, mark the pump assembly by adding a letter ''x'' to the end of the SN.

(b) Replace the fuel metering HP/LP pump assembly if listed by SN in Appendix 1 of Turbomeca Service Bulletin (SB) No. 292 73 2803, dated July 2, 1999, with a serviceable pump assembly by December 31, 2006.

Definition

(c) For the purposes of this AD, a serviceable pump assembly is a fuel metering HP/LP pump assembly not listed by SN in Appendix 1 of Turbomeca SB No. 292 73 2803, dated July 2, 1999, or a fuel metering HP/LP pump assembly listed by SN in Appendix 1 whose pump body material wall thickness has been determined by inspection to be at or above the minimum material thickness, and marked in accordance with paragraph (a)(3)(ii) of this AD.

Terminating Action

(d) Replacement, or verification of correct wall thickness of a fuel metering HP/LP pump assembly that is listed in Appendix 1 of Turbomeca SB No. 292 73 2803, dated July 2, 1999, with a serviceable pump assembly as defined in paragraph (c) of this AD, is considered terminating action for the inspection requirements specified in paragraph (a) of this AD.

Alternative Methods of Compliance

(e) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Engine Certification Office (ECO). Operators must submit their request through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, ECO.

Note 2: Information concerning the existence of approved alternative methods of compliance with this airworthiness directive, if any, may be obtained from the ECO.

Special Flight Permits

(f) Special flight permits may be issued in accordance with Secs. 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the aircraft to a location where the requirements of this AD can be done.

Documents That Have Been Incorporated by Reference

(g) The inspections and removals must be done in accordance with Turbomeca SB No. 292 73 2803, dated July 2, 1999. This incorporation by reference was approved by the Director of the Federal Register in accordance with 5 U.S.C. 552(a) and 1 CFR part 51. Copies may be obtained from Turbomeca, 40220 Tarnos, France; telephone (33) 05 59 64 40 00; fax (33) 05 59 64 60 80. Copies may be inspected at the FAA, New England Region, Office of the Regional Counsel, 12 New England Executive Park, Burlington, MA; or at the Office of the Federal Register, 800 North Capitol Street, NW., Suite 700, Washington, DC.

Note 3: The subject of this AD is addressed in Direction Generale de L'Aviation Civile (DGAC) Airworthiness Directive AD 99-285(A), dated July 13, 1999.

Effective Date

(h) This amendment becomes effective on September 26, 2002.

Issued in Burlington, Massachusetts, on August 14, 2002.

Mark C. Fulmer,

Acting Manager, Engine and Propeller Directorate, Aircraft Certification Service.

[FR Doc. 02-21355 Filed 8-21-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-17

BOMBARDIER-ROTAX GMBH

AIRWORTHINESS DIRECTIVE

ENGINE

SMALL AIRCRAFT, ROTORCRAFT, GLIDERS, BALLOONS, & AIRSHIPS

EDITORIAL CORRECTION:  The effective date of the preamble in this AD which published in the Federal Register today is incorrect.  The correct effective date should be August 30, 2002.  The FAA will issue a correction.  We have corrected this copy.

2002-16-26  Bombardier-Rotax GmbH: Amendment 39-12865. Docket No. 2002-NE-08-AD.

Applicability

This airworthiness directive (AD) is applicable to Bombardier-Rotax GmbH type 912 F series reciprocating engines serial number (SN) 4,412.796, or lower, and 914 F series reciprocating engines SN 4,420.313, or lower. These engines are installed on, but not limited to, Aeromot-Industria Mecanico Metalurgica Itda. model AMT-300, Diamond Aircraft Industries DA20-A1, Diamond Aircraft Industries GmbH Model HK 36 TTS, Iniziative Industriali Italiane S.p.A. Sky Arrow 650 series, and Stemme S10-VT aircraft.

Note 1: Examples of lower SN's are 4,412.795, 4,412.794, and 4,412.793, and 4,420.312, 4,420.311, and 4,420.310.

Note 2: This AD applies to each engine identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For engines that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (c) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance

Compliance with this AD is required as indicated, unless already done.

To prevent oil loss caused by cracks in the engine crankcase, which could lead to in-flight failure of the engine and forced landing, do the following:

Initial Inspection

(a) Within 50 hours time-in-service (TIS) from the effective date of this AD, perform a visual inspection as follows:

(1) Inspect the engine crankcase (item 1, Figure 1 of this AD) for cracks especially in the area of cylinder 1 upper side (item 2), between cylinder 1 and 3 upper side (item 3), and cylinder 4 lower side (item 4).

(2) Cracks in crankcases of engines with a ROTAX cooling air baffle may not be easily visible, and oil leaks may be an indication of cracks. Visually inspect for oil leaks in areas of (item 2) and (item 3).

(3) If oil leaks are found, determine the source by either using a borescope or removing the object blocking the view such as the air baffle or accessory, and perform the inspection.

(4) If the engine crankcase is cracked, replace engine before further flight. Repair oil leaks from any other cause.

Note 3: Information concerning this inspection can be found in Bombardier-Rotax mandatory service bulletins No's. SB-912-029, dated May 2001/SB-914-018, Revision 1, dated December 2001.

Repetitive Inspections

(b) Visually inspect the engine crankcase (item 1, Figure 1 of this AD) for cracks at each 100-hour, annual, or progressive inspection, or within 110 hours TIS since last inspection, whichever occurs first, in accordance with paragraph (a) of this AD.

Alternative Methods of Compliance

(c) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Engine Certification Office (ECO). Operators must submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, ECO.

Note 4: Information concerning the existence of approved alternative methods of compliance with this airworthiness directive, if any, may be obtained from the ECO.

Special Flight Permits

(d) Special flight permits may be issued in accordance with Secs. 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the aircraft to a location where the requirements of this AD can be done.

Note 5: The subject of this AD is addressed in Austro Control airworthiness directive No. 107 R1, dated December 1, 2001.

Effective Date

(e) This amendment becomes effective on August 30, 2002.

Issued in Burlington, Massachusetts, on August 7, 2002.

Jay J. Pardee,

Manager, Engine and Propeller Directorate, Aircraft Certification Service.

[FR Doc. 02-20679 Filed 8-14-02; 8:45 am]

BILLING CODE 4910-13-P

BW 2002-17

AGUSTA S.p.A.

AIRWORTHINESS DIRECTIVE

EMERGENCY

SMALL AIRCRAFT, ROTORCRAFT, GLIDERS, BALLOONS, & AIRSHIPS

2002-17-51  AGUSTA S.p.A.:  Docket No. 2002-SW-42-AD.  Supersedes Emergency AD 2002-14-51, Docket No. 2002-SW-35-AD.

Applicability:  Model A109E helicopters, with tail rotor blade, part number 109-8132-01-111, installed, certificated in any category.

Note 1:  This AD applies to each helicopter identified in the preceding applicability provision, regardless of whether it has been otherwise modified, altered, or repaired in the area subject to the requirements of this AD.  For helicopters that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (e) of this AD.  The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance:  Required as indicated, unless accomplished previously.

To prevent failure of the tail rotor blade and subsequent loss of control of the helicopter, accomplish the following:

(a)  Before further flight, install a placard in the helicopter and mark the airspeed indicator at 140 knots indicated airspeed (KIAS) to indicate a reduction in the helicopter never exceed speed (Vne) of 28 KIAS in accordance with the Compliance Instructions, Part I, of Agusta Alert Bollettino Tecnico No. 109EP-30, Revision A, dated July 25, 2002 (BT).

(b)  Before each start of the helicopter engines, visually check both sides of each tail rotor blade for a crack in the area depicted in Figure 1 of this AD.  An owner/operator (pilot) holding at least a private pilot certificate may perform this visual check and must enter compliance with this paragraph into the aircraft maintenance records in accordance with 14 CFR 43.11 and 91.417(a)(2)(v).  See Figure 1:

Note 2:  Paint irregularities on the tail rotor blade may be due to a crack.

(c)  Within 25 hours time-in-service (TIS), and thereafter at intervals not to exceed 25 hours TIS, and anytime there is an increase in vibration levels, using a 5x or higher magnifying glass, visually inspect each tail rotor blade for a crack before further flight in accordance with the Compliance Instructions, Part III, paragraphs 1. through 5., of the BT.  Reporting to Agusta Service Engineering is not required.  If you are unable to determine by the visual inspection whether there is a crack, dye penetrant inspect the tail rotor blade for a crack in accordance with the Compliance Instructions, Part III, paragraph 6., of the BT.

(d) Replace any cracked tail rotor blade with an airworthy blade before further flight.

(e)  An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Regulations Group, Rotorcraft Directorate, FAA.  Operators shall submit their requests through an FAA Principal Maintenance Inspector, who may concur or comment and then send it to the Manager, Regulations Group.

Note 3:  Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Regulations Group.

(f)  Special flight permits will not be issued.

(g)  Copies of the applicable service information may be obtained from Agusta, 21017 Cascina Costa di Samarate (VA) Italy, Via Giovanni Agusta 520, telephone 39 (0331) 229111, fax 39 (0331) 229605-222595.

(h)  Emergency AD 2002-17-51, issued August 19, 2002, becomes effective upon receipt.

Note 4:  The subject of this AD is addressed in Ente Nazionale per l’Aviazione Civile (Italy) AD No. 2002-384, dated July 29, 2002.

FOR FURTHER INFORMATION CONTACT:  Jim Grigg, Aviation Safety Engineer, FAA, Rotorcraft Directorate, Rotorcraft Standards Staff, Fort Worth, Texas 76193-0110, telephone (817) 222-5490, fax (817) 222-5961.

Issued in Fort Worth, Texas, on August 19, 2002.

David A. Downey,

Manager, Rotorcraft Directorate,

Aircraft Certification Service.

BW 2002-17

AGUSTA S.p.A.

AIRWORTHINESS DIRECTIVE

EMERGENCY

SMALL AIRCRAFT, ROTORCRAFT, GLIDERS, BALLOONS, & AIRSHIPS

2002-17-52  AGUSTA S.p.A.:  Docket No. 2002-SW-43-AD.  Supersedes Emergency AD 2002-14-51, Docket No. 2002-SW-35-AD.

Applicability:  Model A119 helicopters, with hub and tail rotor blades assembly, part number (P/N) 109-8131-02-149, or tail rotor blades, P/N 109-8132-01-111, installed, certificated in any category.

Note 1:  This AD applies to each helicopter identified in the preceding applicability provision, regardless of whether it has been otherwise modified, altered, or repaired in the area subject to the requirements of this AD.  For helicopters that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (i) of this AD.  The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

Compliance:  Required as indicated, unless accomplished previously.

To prevent failure of the tail rotor blade and subsequent loss of control of the helicopter, accomplish the following:

(a)  Before further flight, install a placard in the helicopter and mark the airspeed indicator at 132 knots indicated airspeed (KIAS) to indicate a reduction in the helicopter never exceed speed (Vne) by 30 KIAS.  Make and install the placard in accordance with the Compliance Instructions, Part I, of Agusta Alert Bollettino Tecnico No. 119-6, Revision A, dated July 12, 2002 (BT).  On the glass of the airspeed indicator, apply a red mark over the value of 132 KIAS.

(b)  Before each start of the helicopter engine, visually check both sides of each tail rotor blade for a crack in the area depicted in Figure 1 of this AD.  An owner/operator (pilot) holding at least a private pilot certificate may perform this visual check and must enter compliance with this paragraph into the aircraft maintenance records in accordance with 14 CFR 43.11 and 91.417(a)(2)(v).  See Figure 1:

Note 2:  Paint irregularities on the tail rotor blade may be due to a crack.

(c)  Within 25 hours time-in-service (TIS), and thereafter at intervals not to exceed 25 hours TIS, and any time an increase in vibration levels occur, using a 5x or higher magnifying glass, visually inspect each tail rotor blade for a crack in accordance with the Compliance Instructions, Part III, paragraphs 1. through 5., of the BT.  Reporting to Agusta Service Engineering is not required.  If you are unable to determine by the visual inspection whether there is a crack, dye penetrant inspect the tail rotor blade for a crack in accordance with the Compliance Instructions, Part III, paragraph 6., of the BT.

(d)  Replace any cracked tail rotor blade with an airworthy blade before further flight.

(e)  Not later than October 30, 2002, in accordance with the Compliance Instructions, Part IV, and Figure 2 of the BT:

(1)  Install a new grip and bushing assembly, P/N 109-8131-02-147, into tail rotor hub and blade assembly, P/N 109-8131-02-149;

(2)  Reidentify the modified tail rotor hub and grips assembly, P/N 109-8131-02-141, as P/N 109-8132-01-153; and

(3)  Reidentify the modified tail rotor hub and blade assembly, P/N 109-8131-02-149, as P/N 109-8131-02-155.

Returning the grips to the manufacturer is not required by this AD.

(f)  After completing the actions required by paragraph (e) of this AD, remove the Vne placard and the airspeed indicator marking at 132 KIAS that were installed in accordance with paragraph (a) of this AD.   Modifying and reidentifying the parts as required by paragraph (e) of this AD is terminating actions for the requirements of paragraph (a) of this AD and restores the original Vne.

(g)  After completing the actions required by paragraph (e) of this AD, establish a retirement life of 1,000 hours TIS for tail rotor control rod, P/N 109-0135-02-101.

(h)  After completing the actions required by paragraph (e) of this AD, revise the helicopter Airworthiness Limitations Section of the Agusta Model A119 helicopter maintenance manual by inserting a 1,000 hour TIS retirement life for each tail rotor control rod, P/N 109-0135-02-101.

(i)  An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, Regulations Group, Rotorcraft Directorate, FAA.  Operators shall submit their requests through an FAA Principal Maintenance Inspector, who may concur or comment and then send it to the Manager, Regulations Group.

Note 3:  Information concerning the existence of approved alternative methods of compliance with this AD, if any, may be obtained from the Regulations Group.

(j)  Special flight permits will not be issued.

(k)  Copies of the applicable service information may be obtained from Agusta, 21017 Cascina Costa di Samarate (VA) Italy, Via Giovanni Agusta 520, telephone 39 (0331) 229111, fax 39 (0331) 229605-222595.

(l)  Emergency AD 2002-17-52, issued August 21, 2002, becomes effective upon receipt.

Note 4:  The subject of this AD is addressed in Ente Nazionale per l’Aviazione Civile (Italy) AD No. 2002-367, dated July 16, 2002.

FOR FURTHER INFORMATION CONTACT:  Richard Monschke, Aviation Safety Engineer, FAA, Rotorcraft Directorate, Rotorcraft Standards Staff, Fort Worth, Texas 76193-0110, telephone (817) 222-5116, fax (817) 222-5961.

Issued in Fort Worth, Texas, on August 21, 2002.

David A. Downey,

Manager, Rotorcraft Directorate,

Aircraft Certification Service.

BW 2002-17

TEXTRON LYCOMING

AIRWORTHINESS DIRECTIVE

ENGINE

EMERGENCY

SMALL AIRCRAFT, ROTORCRAFT, GLIDERS, BALLOONS, & AIRSHIPS

2002-17-53 Textron Lycoming: Docket No. 20002-NE-03-AD. Supersedes Emergency AD 2002-04-51.

## Applicability

This AD is applicable to all Textron Lycoming LTIO-540 and TIO-540 engines, rated at 300 HP or greater.

Note 1:  This AD applies to each engine identified in the preceding applicability provision, regardless of whether it has been modified, altered, or repaired in the area subject to the requirements of this AD. For engines that have been modified, altered, or repaired so that the performance of the requirements of this AD is affected, the owner/operator must request approval for an alternative method of compliance in accordance with paragraph (e) of this AD. The request should include an assessment of the effect of the modification, alteration, or repair on the unsafe condition addressed by this AD; and, if the unsafe condition has not been eliminated, the request should include specific proposed actions to address it.

## Compliance

Compliance with this AD is required before further flight.

To prevent crankshaft failure, which could result in total engine power loss, in-flight engine failure and possible forced landing, do the following:

(a) For any engine listed in Table 1 of this AD, replace the crankshaft before further flight with a crankshaft that is not listed by SN in Table 2 of this AD. Tables 1 and 2 follow:

Table 1 List of Engine SN’s

| MODEL | ENGINE S/N | MODEL | ENGINE S/N | MODEL | ENGINE S/N |
| --- | --- | --- | --- | --- | --- |
| LTIO-540-F2BD | 1144-68A | LTIO-540-J2B | 2641-68A | LTIO-540-J2BD | 1885-68A |
| LTIO-540-F2BD | 1272-68A | LTIO-540-J2B | 2650-68A | LTIO-540-J2BD | 1908-68A |
| LTIO-540-F2BD | 1465-68A | LTIO-540-J2B | 2694-68A | LTIO-540-J2BD | 1940-68A |
| LTIO-540-F2BD | 1871-68A | LTIO-540-J2B | 2807-68A | LTIO-540-J2BD | 1941-68A |
| LTIO-540-F2BD | 1874-68A | LTIO-540-J2B | 2865-68A | LTIO-540-J2BD | 1994-68A |
| LTIO-540-F2BD | 2103-68A | LTIO-540-J2B | 2888-68A | LTIO-540-J2BD | 2111-68A |
| LTIO-540-F2BD | 2645-68A | LTIO-540-J2B | 2968-68A | LTIO-540-J2BD | 2286-68A |
| LTIO-540-F2BD | 2988-68A | LTIO-540-J2B | 2991-68A | LTIO-540-J2BD | 2330-68A |
| LTIO-540-J2B | 345-68A | LTIO-540-J2B | 2994-68A | LTIO-540-J2BD | 2419-68A |
| LTIO-540-J2B | 376-68A | LTIO-540-J2BD | 149-68A | LTIO-540-J2BD | 2450-68A |
| LTIO-540-J2B | 701-68A | LTIO-540-J2BD | 172-68A | LTIO-540-J2BD | 2485-68A |
| LTIO-540-J2B | 703-68A | LTIO-540-J2BD | 186-68A | LTIO-540-J2BD | 2500-68A |

| LTIO-540-J2B | 788-68A | LTIO-540-J2BD | 217-68A | LTIO-540-J2BD | 2667-68A |
| --- | --- | --- | --- | --- | --- |
| LTIO-540-J2B | 877-68A | LTIO-540-J2BD | 297-68A | LTIO-540-J2BD | 2813-68A |
| LTIO-540-J2B | 1017-68A | LTIO-540-J2BD | 355-68A | LTIO-540-J2BD | 2823-68A |
| LTIO-540-J2B | 1127-68A | LTIO-540-J2BD | 530-68A | LTIO-540-J2BD | 2844-68A |
| LTIO-540-J2B | 1159-68A | LTIO-540-J2BD | 648-68A | LTIO-540-J2BD | 2846-68A |
| LTIO-540-J2B | 1206-68A | LTIO-540-J2BD | 732-68A | LTIO-540-J2BD | 2856-68A |
| LTIO-540-J2B | 1252-68A | LTIO-540-J2BD | 741-68A | LTIO-540-J2BD | 2900-68A |
| LTIO-540-J2B | 1282-68A | LTIO-540-J2BD | 752-68A | LTIO-540-J2BD | 2912-68A |
| LTIO-540-J2B | 1333-68A | LTIO-540-J2BD | 839-68A | LTIO-540-J2BD | 2932-68A |
| LTIO-540-J2B | 1401-68A | LTIO-540-J2BD | 979-68A | LTIO-540-J2BD | 2942-68A |
| LTIO-540-J2B | 1426-68A | LTIO-540-J2BD | 980-68A | LTIO-540-J2BD | 2986-68A |
| LTIO-540-J2B | 1488-68A | LTIO-540-J2BD | 999-68A | LTIO-540-J2BD | 2990-68A |
| LTIO-540-J2B | 1566-68A | LTIO-540-J2BD | 1027-68A | LTIO-540-J2BD | 2992-68A |
| LTIO-540-J2B | 1928-68A | LTIO-540-J2BD | 1048-68A | LTIO-540-J2BD | 2993-68A |
| LTIO-540-J2B | 1984-68A | LTIO-540-J2BD | 1058-68A | LTIO-540-J2BD | 3001-68A |
| LTIO-540-J2B | 2018-68A | LTIO-540-J2BD | 1186-68A | TIO-540-A2B | 2169-61A |
| LTIO-540-J2B | 2079-68A | LTIO-540-J2BD | 1249-68A | TIO-540-A2B | 4732-61A |
| LTIO-540-J2B | 2094-68A | LTIO-540-J2BD | 1271-68A | TIO-540-A2B | 5911-61A |
| LTIO-540-J2B | 2108-68A | LTIO-540-J2BD | 1331-68A | TIO-540-A2B | 6274-61A |
| LTIO-540-J2B | 2164-68A | LTIO-540-J2BD | 1344-68A | TIO-540-A2B | 6468-61A |
| LTIO-540-J2B | 2168-68A | LTIO-540-J2BD | 1395-68A | TIO-540-A2B | 6629-61A |
| LTIO-540-J2B | 2317-68A | LTIO-540-J2BD | 1517-68A | TIO-540-A2B | 7277-61A |
| LTIO-540-J2B | 2331-68A | LTIO-540-J2BD | 1563-68A | TIO-540-A2B | 7931-61A |
| LTIO-540-J2B | 2455-68A | LTIO-540-J2BD | 1598-68A | TIO-540-A2B | 10119-61A |
| LTIO-540-J2B | 2572-68A | LTIO-540-J2BD | 1716-68A | TIO-540-A2B | 10292-61A |
| LTIO-540-J2B | 2622-68A | LTIO-540-J2BD | 1775-68A | TIO-540-A2B | 10453-61A |
| LTIO-540-J2B | 2636-68A | LTIO-540-J2BD | 1868-68A | TIO-540-A2B | 10742-61A |
| TIO-540-A2B | 11111-61A | TIO-540-AE2A | 6955-61A | TIO-540-AE2A | 10537-61A |
| TIO-540-A2C | 1678-61A | TIO-540-AE2A | 6959-61A | TIO-540-AE2A | 10540-61A |
| TIO-540-A2C | 3038-61A | TIO-540-AE2A | 7738-61A | TIO-540-AE2A | 10545-61A |
| TIO-540-A2C | 3280-61A | TIO-540-AE2A | 7825-61A | TIO-540-AE2A | 10547-61A |
| TIO-540-A2C | 3558-61A | TIO-540-AE2A | 8254-61A | TIO-540-AE2A | 10552-61A |
| TIO-540-A2C | 3654-61A | TIO-540-AE2A | 9647-61A | TIO-540-AE2A | 10559-61A |
| TIO-540-A2C | 4067-61A | TIO-540-AE2A | 9761-61A | TIO-540-AE2A | 10560-61A |
| TIO-540-A2C | 4141-61A | TIO-540-AE2A | 9777-61A | TIO-540-AE2A | 10569-61A |
| TIO-540-A2C | 4281-61A | TIO-540-AE2A | 9804-61A | TIO-540-AE2A | 10572-61A |
| TIO-540-A2C | 4611-61A | TIO-540-AE2A | 9822-61A | TIO-540-AE2A | 10578-61A |
| TIO-540-A2C | 4824-61A | TIO-540-AE2A | 9838-61A | TIO-540-AE2A | 10591-61A |

| TIO-540-A2C | 5324-61A | TIO-540-AE2A | 9849-61A | TIO-540-AE2A | 10593-61A |
| --- | --- | --- | --- | --- | --- |
| TIO-540-A2C | 5937-61A | TIO-540-AE2A | 9853-61A | TIO-540-AE2A | 10594-61A |
| TIO-540-A2C | 6618-61A | TIO-540-AE2A | 9952-61A | TIO-540-AE2A | 10595-61A |
| TIO-540-A2C | 7264-61A | TIO-540-AE2A | 10027-61A | TIO-540-AE2A | 10603-61A |
| TIO-540-A2C | 7401-61A | TIO-540-AE2A | 10072-61A | TIO-540-AE2A | 10608-61A |
| TIO-540-A2C | 7516-61A | TIO-540-AE2A | 10168-61A | TIO-540-AE2A | 10620-61A |
| TIO-540-A2C | 7763-61A | TIO-540-AE2A | 10173-61A | TIO-540-AE2A | 10622-61A |
| TIO-540-A2C | 7961-61A | TIO-540-AE2A | 10338-61A | TIO-540-AE2A | 10645-61A |
| TIO-540-A2C | 7965-61A | TIO-540-AE2A | 10382-61A | TIO-540-AE2A | 10646-61A |
| TIO-540-A2C | 8309-61A | TIO-540-AE2A | 10387-61A | TIO-540-AE2A | 10647-61A |
| TIO-540-A2C | 8810-61A | TIO-540-AE2A | 10393-61A | TIO-540-AE2A | 10648-61A |
| TIO-540-A2C | 8855-61A | TIO-540-AE2A | 10405-61A | TIO-540-AE2A | 10650-61A |
| TIO-540-A2C | 8965-61A | TIO-540-AE2A | 10408-61A | TIO-540-AE2A | 10756-61A |
| TIO-540-A2C | 9134-61A | TIO-540-AE2A | 10427-61A | TIO-540-AE2A | 10758-61A |
| TIO-540-A2C | 9410-61A | TIO-540-AE2A | 10436-61A | TIO-540-AE2A | 10759-61A |
| TIO-540-A2C | 9440-61A | TIO-540-AE2A | 10448-61A | TIO-540-AE2A | 10760-61A |
| TIO-540-A2C | 9833-61A | TIO-540-AE2A | 10449-61A | TIO-540-AE2A | 10762-61A |
| TIO-540-A2C | 9863-61A | TIO-540-AE2A | 10451-61A | TIO-540-AE2A | 10766-61A |
| TIO-540-A2C | 9895-61A | TIO-540-AE2A | 10455-61A | TIO-540-AE2A | 10781-61A |
| TIO-540-A2C | 9988-61A | TIO-540-AE2A | 10459-61A | TIO-540-AE2A | 10785-61A |
| TIO-540-A2C | 10401-61A | TIO-540-AE2A | 10462-61A | TIO-540-AE2A | 10793-61A |
| TIO-540-A2C | 11147-61A | TIO-540-AE2A | 10463-61A | TIO-540-AE2A | 10979-61A |
| TIO-540-AE2A | 2543-61A | TIO-540-AE2A | 10466-61A | TIO-540-AE2A | 10989-61A |
| TIO-540-AE2A | 2650-61A | TIO-540-AE2A | 10471-61A | TIO-540-AE2A | 11001-61A |
| TIO-540-AE2A | 4777-61A | TIO-540-AE2A | 10479-61A | TIO-540-AE2A | 11012-61A |
| TIO-540-AE2A | 5068-61A | TIO-540-AE2A | 10489-61A | TIO-540-AE2A | 11013-61A |
| TIO-540-AE2A | 5110-61A | TIO-540-AE2A | 10495-61A | TIO-540-AE2A | 11015-61A |
| TIO-540-AE2A | 5468-61A | TIO-540-AE2A | 10499-61A | TIO-540-AE2A | 11016-61A |
| TIO-540-AE2A | 6038-61A | TIO-540-AE2A | 10510-61A | TIO-540-AE2A | 11017-61A |
| TIO-540-AE2A | 6575-61A | TIO-540-AE2A | 10535-61A | TIO-540-AE2A | 11035-61A |
| TIO-540-AE2A | 11053-61A | TIO-540-AH1A | 10458-61A | TIO-540-AH1A | 10702-61A |
| TIO-540-AE2A | 11057-61A | TIO-540-AH1A | 10472-61A | TIO-540-AH1A | 10703-61A |
| TIO-540-AE2A | 11058-61A | TIO-540-AH1A | 10481-61A | TIO-540-AH1A | 10707-61A |
| TIO-540-AE2A | 11065-61A | TIO-540-AH1A | 10486-61A | TIO-540-AH1A | 10714-61A |
| TIO-540-AE2A | 11066-61A | TIO-540-AH1A | 10492-61A | TIO-540-AH1A | 10719-61A |
| TIO-540-AE2A | 11087-61A | TIO-540-AH1A | 10500-61A | TIO-540-AH1A | 10722-61A |
| TIO-540-AE2A | 11093-61A | TIO-540-AH1A | 10501-61A | TIO-540-AH1A | 10723-61A |
| TIO-540-AE2A | 11108-61A | TIO-540-AH1A | 10508-61A | TIO-540-AH1A | 10725-61A |

| TIO-540-AE2A | 11112-61A | TIO-540-AH1A | 10519-61A | TIO-540-AH1A | 10734-61A |
| --- | --- | --- | --- | --- | --- |
| TIO-540-AE2A | 11119-61A | TIO-540-AH1A | 10524-61A | TIO-540-AH1A | 10748-61A |
| TIO-540-AE2A | 11133-61A | TIO-540-AH1A | 10530-61A | TIO-540-AH1A | 10749-61A |
| TIO-540-AE2A | 11137-61A | TIO-540-AH1A | 10533-61A | TIO-540-AH1A | 10750-61A |
| TIO-540-AE2A | 11142-61A | TIO-540-AH1A | 10567-61A | TIO-540-AH1A | 10755-61A |
| TIO-540-AE2A | 11159-61A | TIO-540-AH1A | 10570-61A | TIO-540-AH1A | 10773-61A |
| TIO-540-AE2A | 11167-61A | TIO-540-AH1A | 10573-61A | TIO-540-AH1A | 10776-61A |
| TIO-540-AE2A | 11184-61A | TIO-540-AH1A | 10583-61A | TIO-540-AH1A | 10778-61A |
| TIO-540-AE2A | 11188-61A | TIO-540-AH1A | 10587-61A | TIO-540-AH1A | 10790-61A |
| TIO-540-AE2A | 11190-61A | TIO-540-AH1A | 10588-61A | TIO-540-AH1A | 10797-61A |
| TIO-540-AE2A | 11191-61A | TIO-540-AH1A | 10600-61A | TIO-540-AH1A | 10798-61A |
| TIO-540-AE2A | 11194-61A | TIO-540-AH1A | 10607-61A | TIO-540-AH1A | 10799-61A |
| TIO-540-AE2A | 11195-61A | TIO-540-AH1A | 10619-61A | TIO-540-AH1A | 10800-61A |
| TIO-540-AE2A | 11196-61A | TIO-540-AH1A | 10629-61A | TIO-540-AH1A | 10801-61A |
| TIO-540-AE2A | 11197-61A | TIO-540-AH1A | 10632-61A | TIO-540-AH1A | 10802-61A |
| TIO-540-AE2A | 11231-61A | TIO-540-AH1A | 10633-61A | TIO-540-AH1A | 10814-61A |
| TIO-540-AE2A | 11259-61A | TIO-540-AH1A | 10634-61A | TIO-540-AH1A | 10818-61A |
| TIO-540-AH1A | 671-61A | TIO-540-AH1A | 10635-61A | TIO-540-AH1A | 10822-61A |
| TIO-540-AH1A | 2346-61A | TIO-540-AH1A | 10640-61A | TIO-540-AH1A | 10833-61A |
| TIO-540-AH1A | 3545-61A | TIO-540-AH1A | 10652-61A | TIO-540-AH1A | 10836-61A |
| TIO-540-AH1A | 3948-61A | TIO-540-AH1A | 10653-61A | TIO-540-AH1A | 10840-61A |
| TIO-540-AH1A | 8268-61A | TIO-540-AH1A | 10657-61A | TIO-540-AH1A | 10843-61A |
| TIO-540-AH1A | 10138-61A | TIO-540-AH1A | 10658-61A | TIO-540-AH1A | 10849-61A |
| TIO-540-AH1A | 10343-61A | TIO-540-AH1A | 10659-61A | TIO-540-AH1A | 10852-61A |
| TIO-540-AH1A | 10352-61A | TIO-540-AH1A | 10664-61A | TIO-540-AH1A | 10853-61A |
| TIO-540-AH1A | 10378-61A | TIO-540-AH1A | 10666-61A | TIO-540-AH1A | 10854-61A |
| TIO-540-AH1A | 10382-61A | TIO-540-AH1A | 10672-61A | TIO-540-AH1A | 10861-61A |
| TIO-540-AH1A | 10398-61A | TIO-540-AH1A | 10678-61A | TIO-540-AH1A | 10867-61A |
| TIO-540-AH1A | 10406-61A | TIO-540-AH1A | 10679-61A | TIO-540-AH1A | 10872-61A |
| TIO-540-AH1A | 10434-61A | TIO-540-AH1A | 10680-61A | TIO-540-AH1A | 10873-61A |
| TIO-540-AH1A | 10450-61A | TIO-540-AH1A | 10688-61A | TIO-540-AH1A | 10878-61A |
| TIO-540-AH1A | 10456-61A | TIO-540-AH1A | 10700-61A | TIO-540-AH1A | 10879-61A |
| TIO-540-AH1A | 10457-61A | TIO-540-AH1A | 10701-61A | TIO-540-AH1A | 10881-61A |
| TIO-540-AH1A | 10897-61A | TIO-540-AH1A | 11122-61A | TIO-540-AJ1A | 10114-61A |
| TIO-540-AH1A | 10952-61A | TIO-540-AH1A | 11124-61A | TIO-540-AJ1A | 10243-61A |
| TIO-540-AH1A | 10953-61A | TIO-540-AH1A | 11129-61A | TIO-540-AJ1A | 10341-61A |
| TIO-540-AH1A | 10954-61A | TIO-540-AH1A | 11134-61A | TIO-540-AJ1A | 10354-61A |
| TIO-540-AH1A | 10955-61A | TIO-540-AH1A | 11138-61A | TIO-540-AJ1A | 10355-61A |

| TIO-540-AH1A | 10957-61A | TIO-540-AH1A | 11139-61A | TIO-540-AJ1A | 10356-61A |
| --- | --- | --- | --- | --- | --- |
| TIO-540-AH1A | 10958-61A | TIO-540-AH1A | 11140-61A | TIO-540-AJ1A | 10357-61A |
| TIO-540-AH1A | 10965-61A | TIO-540-AH1A | 11141-61A | TIO-540-AJ1A | 10362-61A |
| TIO-540-AH1A | 10966-61A | TIO-540-AH1A | 11157-61A | TIO-540-AJ1A | 10367-61A |
| TIO-540-AH1A | 10968-61A | TIO-540-AH1A | 11158-61A | TIO-540-AJ1A | 10369-61A |
| TIO-540-AH1A | 10973-61A | TIO-540-AH1A | 11165-61A | TIO-540-AJ1A | 10371-61A |
| TIO-540-AH1A | 10984-61A | TIO-540-AH1A | 11183-61A | TIO-540-AJ1A | 10372-61A |
| TIO-540-AH1A | 10985-61A | TIO-540-AH1A | 11238-61A | TIO-540-AJ1A | 10373-61A |
| TIO-540-AH1A | 10986-61A | TIO-540-AH1A | 11243-61A | TIO-540-AJ1A | 10377-61A |
| TIO-540-AH1A | 10987-61A | TIO-540-AH1A | 11246-61A | TIO-540-AJ1A | 10384-61A |
| TIO-540-AH1A | 10988-61A | TIO-540-AH1A | 11247-61A | TIO-540-AJ1A | 10385-61A |
| TIO-540-AH1A | 10997-61A | TIO-540-AH1A | 11250-61A | TIO-540-AJ1A | 10388-61A |
| TIO-540-AH1A | 10998-61A | TIO-540-AH1A | 11251-61A | TIO-540-AJ1A | 10389-61A |
| TIO-540-AH1A | 10999-61A | TIO-540-AH1A | 11258-61A | TIO-540-AJ1A | 10390-61A |
| TIO-540-AH1A | 11019-61A | TIO-540-AH1A | 11260-61A | TIO-540-AJ1A | 10391-61A |
| TIO-540-AH1A | 11020-61A | TIO-540-AH1A | 11261-61A | TIO-540-AJ1A | 10400-61A |
| TIO-540-AH1A | 11022-61A | TIO-540-AH1A | 11263-61A | TIO-540-AJ1A | 10404-61A |
| TIO-540-AH1A | 11026-61A | TIO-540-AH1A | 11270-61A | TIO-540-AJ1A | 10416-61A |
| TIO-540-AH1A | 11038-61A | TIO-540-AH1A | 11271-61A | TIO-540-AJ1A | 10428-61A |
| TIO-540-AH1A | 11042-61A | TIO-540-AH1A | 11272-61A | TIO-540-AJ1A | 10437-61A |
| TIO-540-AH1A | 11047-61A | TIO-540-AH1A | 11273-61A | TIO-540-AJ1A | 10440-61A |
| TIO-540-AH1A | 11059-61A | TIO-540-AH1A | 11274-61A | TIO-540-AJ1A | 10444-61A |
| TIO-540-AH1A | 11060-61A | TIO-540-AH1A | 11275-61A | TIO-540-AJ1A | 10445-61A |
| TIO-540-AH1A | 11079-61A | TIO-540-AH1A | 11277-61A | TIO-540-AJ1A | 10446-61A |
| TIO-540-AH1A | 11080-61A | TIO-540-AH1A | 11278-61A | TIO-540-AJ1A | 10454-61A |
| TIO-540-AH1A | 11081-61A | TIO-540-AH1A | 11282-61A | TIO-540-AJ1A | 10469-61A |
| TIO-540-AH1A | 11082-61A | TIO-540-AH1A | 11293-61A | TIO-540-AJ1A | 10470-61A |
| TIO-540-AH1A | 11083-61A | TIO-540-AH1A | 11299-61A | TIO-540-AJ1A | 10477-61A |
| TIO-540-AH1A | 11097-61A | TIO-540-AH1A | 11300-61A | TIO-540-AJ1A | 10478-61A |
| TIO-540-AH1A | 11098-61A | TIO-540-AH1A | 11309-61A | TIO-540-AJ1A | 10483-61A |
| TIO-540-AH1A | 11099-61A | TIO-540-AJ1A | 4377-61A | TIO-540-AJ1A | 10484-61A |
| TIO-540-AH1A | 11104-61A | TIO-540-AJ1A | 8171-61A | TIO-540-AJ1A | 10490-61A |
| TIO-540-AH1A | 11109-61A | TIO-540-AJ1A | 8627-61A | TIO-540-AJ1A | 10491-61A |
| TIO-540-AH1A | 11118-61A | TIO-540-AJ1A | 9442-61A | TIO-540-AJ1A | 10497-61A |
| TIO-540-AH1A | 11120-61A | TIO-540-AJ1A | 9634-61A | TIO-540-AJ1A | 10503-61A |
| TIO-540-AH1A | 11121-61A | TIO-540-AJ1A | 10059-61A | TIO-540-AJ1A | 10504-61A |
| TIO-540-AJ1A | 10506-61A | TIO-540-AJ1A | 10674-61A | TIO-540-AJ1A | 10807-61A |
| TIO-540-AJ1A | 10512-61A | TIO-540-AJ1A | 10675-61A | TIO-540-AJ1A | 10809-61A |

| TIO-540-AJ1A | 10518-61A | TIO-540-AJ1A | 10676-61A | TIO-540-AJ1A | 10812-61A |
| --- | --- | --- | --- | --- | --- |
| TIO-540-AJ1A | 10520-61A | TIO-540-AJ1A | 10686-61A | TIO-540-AJ1A | 10815-61A |
| TIO-540-AJ1A | 10521-61A | TIO-540-AJ1A | 10689-61A | TIO-540-AJ1A | 10816-61A |
| TIO-540-AJ1A | 10525-61A | TIO-540-AJ1A | 10690-61A | TIO-540-AJ1A | 10820-61A |
| TIO-540-AJ1A | 10526-61A | TIO-540-AJ1A | 10691-61A | TIO-540-AJ1A | 10821-61A |
| TIO-540-AJ1A | 10527-61A | TIO-540-AJ1A | 10693-61A | TIO-540-AJ1A | 10824-61A |
| TIO-540-AJ1A | 10542-61A | TIO-540-AJ1A | 10696-61A | TIO-540-AJ1A | 10827-61A |
| TIO-540-AJ1A | 10543-61A | TIO-540-AJ1A | 10697-61A | TIO-540-AJ1A | 10831-61A |
| TIO-540-AJ1A | 10544-61A | TIO-540-AJ1A | 10698-61A | TIO-540-AJ1A | 10832-61A |
| TIO-540-AJ1A | 10551-61A | TIO-540-AJ1A | 10699-61A | TIO-540-AJ1A | 10834-61A |
| TIO-540-AJ1A | 10555-61A | TIO-540-AJ1A | 10704-61A | TIO-540-AJ1A | 10835-61A |
| TIO-540-AJ1A | 10561-61A | TIO-540-AJ1A | 10705-61A | TIO-540-AJ1A | 10841-61A |
| TIO-540-AJ1A | 10562-61A | TIO-540-AJ1A | 10713-61A | TIO-540-AJ1A | 10842-61A |
| TIO-540-AJ1A | 10563-61A | TIO-540-AJ1A | 10717-61A | TIO-540-AJ1A | 10844-61A |
| TIO-540-AJ1A | 10564-61A | TIO-540-AJ1A | 10721-61A | TIO-540-AJ1A | 10845-61A |
| TIO-540-AJ1A | 10565-61A | TIO-540-AJ1A | 10727-61A | TIO-540-AJ1A | 10846-61A |
| TIO-540-AJ1A | 10574-61A | TIO-540-AJ1A | 10728-61A | TIO-540-AJ1A | 10848-61A |
| TIO-540-AJ1A | 10580-61A | TIO-540-AJ1A | 10729-61A | TIO-540-AJ1A | 10856-61A |
| TIO-540-AJ1A | 10582-61A | TIO-540-AJ1A | 10730-61A | TIO-540-AJ1A | 10857-61A |
| TIO-540-AJ1A | 10586-61A | TIO-540-AJ1A | 10731-61A | TIO-540-AJ1A | 10858-61A |
| TIO-540-AJ1A | 10589-61A | TIO-540-AJ1A | 10736-61A | TIO-540-AJ1A | 10860-61A |
| TIO-540-AJ1A | 10596-61A | TIO-540-AJ1A | 10737-61A | TIO-540-AJ1A | 10864-61A |
| TIO-540-AJ1A | 10601-61A | TIO-540-AJ1A | 10738-61A | TIO-540-AJ1A | 10865-61A |
| TIO-540-AJ1A | 10604-61A | TIO-540-AJ1A | 10746-61A | TIO-540-AJ1A | 10868-61A |
| TIO-540-AJ1A | 10605-61A | TIO-540-AJ1A | 10747-61A | TIO-540-AJ1A | 10874-61A |
| TIO-540-AJ1A | 10615-61A | TIO-540-AJ1A | 10752-61A | TIO-540-AJ1A | 10875-61A |
| TIO-540-AJ1A | 10617-61A | TIO-540-AJ1A | 10753-61A | TIO-540-AJ1A | 10876-61A |
| TIO-540-AJ1A | 10624-61A | TIO-540-AJ1A | 10769-61A | TIO-540-AJ1A | 10877-61A |
| TIO-540-AJ1A | 10627-61A | TIO-540-AJ1A | 10770-61A | TIO-540-AJ1A | 10895-61A |
| TIO-540-AJ1A | 10628-61A | TIO-540-AJ1A | 10771-61A | TIO-540-AJ1A | 10896-61A |
| TIO-540-AJ1A | 10631-61A | TIO-540-AJ1A | 10774-61A | TIO-540-AJ1A | 10960-61A |
| TIO-540-AJ1A | 10641-61A | TIO-540-AJ1A | 10779-61A | TIO-540-AJ1A | 10961-61A |
| TIO-540-AJ1A | 10654-61A | TIO-540-AJ1A | 10783-61A | TIO-540-AJ1A | 10962-61A |
| TIO-540-AJ1A | 10661-61A | TIO-540-AJ1A | 10784-61A | TIO-540-AJ1A | 10972-61A |
| TIO-540-AJ1A | 10662-61A | TIO-540-AJ1A | 10786-61A | TIO-540-AJ1A | 10976-61A |
| TIO-540-AJ1A | 10667-61A | TIO-540-AJ1A | 10787-61A | TIO-540-AJ1A | 10977-61A |
| TIO-540-AJ1A | 10668-61A | TIO-540-AJ1A | 10803-61A | TIO-540-AJ1A | 10980-61A |
| TIO-540-AJ1A | 10669-61A | TIO-540-AJ1A | 10804-61A | TIO-540-AJ1A | 10981-61A |

| TIO-540-AJ1A | 10673-61A | TIO-540-AJ1A | 10805-61A | TIO-540-AJ1A | 10982-61A |
| --- | --- | --- | --- | --- | --- |
| TIO-540-AJ1A | 10983-61A | TIO-540-AJ1A | 11185-61A | TIO-540-J2B | 1234-61A |
| TIO-540-AJ1A | 10991-61A | TIO-540-AJ1A | 11189-61A | TIO-540-J2B | 2315-61A |
| TIO-540-AJ1A | 10992-61A | TIO-540-AJ1A | 11193-61A | TIO-540-J2B | 2453-61A |
| TIO-540-AJ1A | 10993-61A | TIO-540-AJ1A | 11198-61A | TIO-540-J2B | 3167-61A |
| TIO-540-AJ1A | 10994-61A | TIO-540-AJ1A | 11199-61A | TIO-540-J2B | 3218-61A |
| TIO-540-AJ1A | 10995-61A | TIO-540-AJ1A | 11203-61A | TIO-540-J2B | 3590-61A |
| TIO-540-AJ1A | 10996-61A | TIO-540-AJ1A | 11205-61A | TIO-540-J2B | 3692-61A |
| TIO-540-AJ1A | 11003-61A | TIO-540-AJ1A | 11210-61A | TIO-540-J2B | 4412-61A |
| TIO-540-AJ1A | 11005-61A | TIO-540-AJ1A | 11215-61A | TIO-540-J2B | 4421-61A |
| TIO-540-AJ1A | 11009-61A | TIO-540-AJ1A | 11219-61A | TIO-540-J2B | 4457-61A |
| TIO-540-AJ1A | 11010-61A | TIO-540-AJ1A | 11221-61A | TIO-540-J2B | 4612-61A |
| TIO-540-AJ1A | 11011-61A | TIO-540-AJ1A | 11223-61A | TIO-540-J2B | 4861-61A |
| TIO-540-AJ1A | 11014-61A | TIO-540-AJ1A | 11224-61A | TIO-540-J2B | 4907-61A |
| TIO-540-AJ1A | 11030-61A | TIO-540-AJ1A | 11232-61A | TIO-540-J2B | 5402-61A |
| TIO-540-AJ1A | 11034-61A | TIO-540-AJ1A | 11233-61A | TIO-540-J2B | 5544-61A |
| TIO-540-AJ1A | 11043-61A | TIO-540-AJ1A | 11234-61A | TIO-540-J2B | 5757-61A |
| TIO-540-AJ1A | 11044-61A | TIO-540-AJ1A | 11235-61A | TIO-540-J2B | 5842-61A |
| TIO-540-AJ1A | 11045-61A | TIO-540-AJ1A | 11236-61A | TIO-540-J2B | 5955-61A |
| TIO-540-AJ1A | 11046-61A | TIO-540-AJ1A | 11237-61A | TIO-540-J2B | 5976-61A |
| TIO-540-AJ1A | 11061-61A | TIO-540-AJ1A | 11239-61A | TIO-540-J2B | 5991-61A |
| TIO-540-AJ1A | 11069-61A | TIO-540-AJ1A | 11248-61A | TIO-540-J2B | 6088-61A |
| TIO-540-AJ1A | 11089-61A | TIO-540-AJ1A | 11249-61A | TIO-540-J2B | 6256-61A |
| TIO-540-AJ1A | 11092-61A | TIO-540-AJ1A | 11252-61A | TIO-540-J2B | 6743-61A |
| TIO-540-AJ1A | 11096-61A | TIO-540-AJ1A | 11253-61A | TIO-540-J2B | 6751-61A |
| TIO-540-AJ1A | 11113-61A | TIO-540-AJ1A | 11256-61A | TIO-540-J2B | 6837-61A |
| TIO-540-AJ1A | 11123-61A | TIO-540-AJ1A | 11266-61A | TIO-540-J2B | 7639-61A |
| TIO-540-AJ1A | 11127-61A | TIO-540-AJ1A | 11267-61A | TIO-540-J2B | 7948-61A |
| TIO-540-AJ1A | 11128-61A | TIO-540-AJ1A | 11268-61A | TIO-540-J2B | 8092-61A |
| TIO-540-AJ1A | 11150-61A | TIO-540-AJ1A | 11279-61A | TIO-540-J2B | 8192-61A |
| TIO-540-AJ1A | 11151-61A | TIO-540-AJ1A | 11280-61A | TIO-540-J2B | 8246-61A |
| TIO-540-AJ1A | 11153-61A | TIO-540-AJ1A | 11285-61A | TIO-540-J2B | 8353-61A |
| TIO-540-AJ1A | 11164-61A | TIO-540-AJ1A | 11286-61A | TIO-540-J2B | 8852-61A |
| TIO-540-AJ1A | 11166-61A | TIO-540-AJ1A | 11290-61A | TIO-540-J2B | 8883-61A |
| TIO-540-AJ1A | 11168-61A | TIO-540-AJ1A | 11292-61A | TIO-540-J2B | 9071-61A |
| TIO-540-AJ1A | 11169-61A | TIO-540-AJ1A | 11296-61A | TIO-540-J2B | 9300-61A |
| TIO-540-AJ1A | 11172-61A | TIO-540-AJ1A | 11308-61A | TIO-540-J2B | 9307-61A |
| TIO-540-AJ1A | 11175-61A | TIO-540-F2BD | 7357-61A | TIO-540-J2B | 9687-61A |

| TIO-540-AJ1A | 11176-61A | TIO-540-F2BD | 7596-61A | TIO-540-J2B | 9847-61A |
| --- | --- | --- | --- | --- | --- |
| TIO-540-AJ1A | 11177-61A | TIO-540-F2BD | 8368-61A | TIO-540-J2B | 9851-61A |
| TIO-540-AJ1A | 11178-61A | TIO-540-F2BD | 9810-61A | TIO-540-J2B | 9941-61A |
| TIO-540-AJ1A | 11181-61A | TIO-540-F2BD | 9839-61A | TIO-540-J2B | 10100-61A |
| TIO-540-J2B | 10214-61A | TIO-540-J2BD | 4455-61A | TIO-540-J2BD | 9993-61A |
| TIO-540-J2B | 10301-61A | TIO-540-J2BD | 4710-61A | TIO-540-J2BD | 10175-61A |
| TIO-540-J2B | 10366-61A | TIO-540-J2BD | 4863-61A | TIO-540-J2BD | 10219-61A |
| TIO-540-J2B | 10431-61A | TIO-540-J2BD | 4945-61A | TIO-540-J2BD | 10695-61A |
| TIO-540-J2B | 10443-61A | TIO-540-J2BD | 5391-61A | TIO-540-J2BD | 10741-61A |
| TIO-540-J2B | 10515-61A | TIO-540-J2BD | 5405-61A | TIO-540-J2BD | 10828-61A |
| TIO-540-J2B | 10528-61A | TIO-540-J2BD | 5720-61A | TIO-540-J2BD | 10830-61A |
| TIO-540-J2B | 10571-61A | TIO-540-J2BD | 5750-61A | TIO-540-J2BD | 11077-61A |
| TIO-540-J2B | 10576-61A | TIO-540-J2BD | 6020-61A | TIO-540-J2BD | 11146-61A |
| TIO-540-J2B | 10577-61A | TIO-540-J2BD | 6045-61A | TIO-540-J2BD | 11148-61A |
| TIO-540-J2B | 10637-61A | TIO-540-J2BD | 6089-61A | TIO-540-J2BD | 11149-61A |
| TIO-540-J2B | 10638-61A | TIO-540-J2BD | 6422-61A | TIO-540-J2BD | 11192-61A |
| TIO-540-J2B | 10655-61A | TIO-540-J2BD | 6441-61A | TIO-540-J2BD | 11227-61A |
| TIO-540-J2B | 10743-61A | TIO-540-J2BD | 6561-61A | TIO-540-J2BD | 11255-61A |
| TIO-540-J2B | 10810-61A | TIO-540-J2BD | 6582-61A | TIO-540-S1AD | 2574-61A |
| TIO-540-J2B | 10811-61A | TIO-540-J2BD | 6646-61A | TIO-540-S1AD | 3744-61A |
| TIO-540-J2B | 10862-61A | TIO-540-J2BD | 7085-61A | TIO-540-S1AD | 7554-61A |
| TIO-540-J2B | 10863-61A | TIO-540-J2BD | 7108-61A | TIO-540-S1AD | 8149-61A |
| TIO-540-J2B | 11032-61A | TIO-540-J2BD | 7501-61A | TIO-540-S1AD | 8331-61A |
| TIO-540-J2B | 11033-61A | TIO-540-J2BD | 7502-61A | TIO-540-S1AD | 8781-61A |
| TIO-540-J2B | 11037-61A | TIO-540-J2BD | 7562-61A | TIO-540-S1AD | 9815-61A |
| TIO-540-J2B | 11070-61A | TIO-540-J2BD | 7678-61A | TIO-540-S1AD | 9982-61A |
| TIO-540-J2B | 11101-61A | TIO-540-J2BD | 7790-61A | TIO-540-S1AD | 10078-61A |
| TIO-540-J2B | 11135-61A | TIO-540-J2BD | 7892-61A | TIO-540-S1AD | 10089-61A |
| TIO-540-J2B | 11136-61A | TIO-540-J2BD | 7975-61A | TIO-540-S1AD | 10969-61A |
| TIO-540-J2B | 11187-61A | TIO-540-J2BD | 8239-61A | TIO-540-S1AD | 11055-61A |
| TIO-540-J2B | 11289-61A | TIO-540-J2BD | 8405-61A | TIO-540-U2A | 1103-61A |
| TIO-540-J2BD | 842-61A | TIO-540-J2BD | 8409-61A | TIO-540-U2A | 2505-61A |
| TIO-540-J2BD | 1679-61A | TIO-540-J2BD | 8439-61A | TIO-540-U2A | 3184-61A |
| TIO-540-J2BD | 2171-61A | TIO-540-J2BD | 8615-61A | TIO-540-U2A | 4641-61A |
| TIO-540-J2BD | 2340-61A | TIO-540-J2BD | 8617-61A | TIO-540-U2A | 4658-61A |
| TIO-540-J2BD | 2372-61A | TIO-540-J2BD | 8780-61A | TIO-540-U2A | 7269-61A |
| TIO-540-J2BD | 2543-61A | TIO-540-J2BD | 8871-61A | TIO-540-U2A | 8530-61A |
| TIO-540-J2BD | 3176-61A | TIO-540-J2BD | 8963-61A | TIO-540-U2A | 8566-61A |

| TIO-540-J2BD | 3193-61A | TIO-540-J2BD | 9025-61A | TIO-540-U2A | 9064-61A |
| --- | --- | --- | --- | --- | --- |
| TIO-540-J2BD | 3259-61A | TIO-540-J2BD | 9026-61A | TIO-540-U2A | 9517-61A |
| TIO-540-J2BD | 3370-61A | TIO-540-J2BD | 9137-61A | TIO-540-U2A | 9794-61A |
| TIO-540-J2BD | 3532-61A | TIO-540-J2BD | 9164-61A | TIO-540-U2A | 10136-61A |
| TIO-540-J2BD | 3818-61A | TIO-540-J2BD | 9343-61A | TIO-540-U2A | 10241-61A |
| TIO-540-J2BD | 3918-61A | TIO-540-J2BD | 9355-61A | TIO-540-U2A | 10553-61A |
| TIO-540-J2BD | 4138-61A | TIO-540-J2BD | 9463-61A | TIO-540-U2A | 10585-61A |
| TIO-540-J2BD | 4213-61A | TIO-540-J2BD | 9573-61A | TIO-540-U2A | 11073-61A |
| TIO-540-J2BD | 4217-61A | TIO-540-J2BD | 9662-61A | TIO-540-U2A | 11074-61A |
| TIO-540-J2BD | 4240-61A | TIO-540-J2BD | 9793-61A | TIO-540-V2AD | 8560-61A |
| TIO-540-J2BD | 4241-61A | TIO-540-J2BD | 9846-61A |  |  |
| TIO-540-J2BD | 4248-61A | TIO-540-J2BD | 9965-61A |  |  |
| TIO-540-J2BD | 4371-61A | TIO-540-J2BD | 9980-61A |  |  |

Table 2 List of Crankshaft SN’s

| CRANKSHAFT SN’s |
| --- |
| V537912175 | V537912648 | V537912901 | V537912959 | V537913227 | V537913281 |
| V537912176 | V537912649 | V537912902 | V537912961 | V537913228 | V537913282 |
| V537912185 | V537912650 | V537912903 | V537912962 | V537913229 | V537913284 |
| V537912190 | V537912657 | V537912904 | V537912965 | V537913230 | V537913285 |
| V537912195 | V537912663 | V537912906 | V537912966 | V537913231 | V537913286 |
| V537912199 | V537912859 | V537912907 | V537912967 | V537913232 | V537913288 |
| V537912201 | V537912861 | V537912908 | V537912968 | V537913233 | V537913289 |
| V537912202 | V537912862 | V537912909 | V537912971 | V537913234 | V537913292 |
| V537912203 | V537912863 | V537912910 | V537912973 | V537913235 | V537913293 |
| V537912204 | V537912865 | V537912911 | V537912974 | V537913236 | V537913294 |
| V537912207 | V537912866 | V537912912 | V537912975 | V537913237 | V537913295 |
| V537912209 | V537912867 | V537912914 | V537912976 | V537913238 | V537913297 |
| V537912210 | V537912868 | V537912915 | V537912977 | V537913239 | V537913502 |
| V537912212 | V537912869 | V537912916 | V537912978 | V537913240 | V537913503 |
| V537912213 | V537912870 | V537912917 | V537912979 | V537913241 | V537913504 |
| V537912225 | V537912871 | V537912918 | V537912980 | V537913242 | V537913506 |
| V537912226 | V537912872 | V537912919 | V537912981 | V537913243 | V537913507 |
| V537912607 | V537912873 | V537912920 | V537913197 | V537913244 | V537913508 |
| V537912608 | V537912875 | V537912921 | V537913198 | V537913245 | V537913509 |
| V537912610 | V537912876 | V537912924 | V537913199 | V537913246 | V537913512 |
| V537912611 | V537912877 | V537912925 | V537913201 | V537913249 | V537913514 |
| V537912612 | V537912878 | V537912928 | V537913202 | V537913251 | V537913516 |
| V537912613 | V537912879 | V537912930 | V537913203 | V537913252 | V537913517 |

| V537912615 | V537912880 | V537912932 | V537913204 | V537913253 | V537913520 |
| --- | --- | --- | --- | --- | --- |
| V537912616 | V537912882 | V537912938 | V537913205 | V537913255 | V537913521 |
| V537912617 | V537912883 | V537912944 | V537913208 | V537913256 | V537913523 |
| V537912619 | V537912884 | V537912945 | V537913209 | V537913257 | V537913525 |
| V537912622 | V537912885 | V537912946 | V537913210 | V537913258 | V537913526 |
| V537912623 | V537912886 | V537912947 | V537913212 | V537913259 | V537913527 |
| V537912624 | V537912887 | V537912948 | V537913213 | V537913260 | V537913528 |
| V537912625 | V537912889 | V537912949 | V537913214 | V537913262 | V537913529 |
| V537912626 | V537912890 | V537912950 | V537913215 | V537913265 | V537913530 |
| V537912627 | V537912892 | V537912951 | V537913218 | V537913267 | V537913532 |
| V537912628 | V537912893 | V537912952 | V537913219 | V537913268 | V537913533 |
| V537912635 | V537912894 | V537912953 | V537913220 | V537913271 | V537913534 |
| V537912642 | V537912896 | V537912954 | V537913221 | V537913273 | V537913535 |
| V537912643 | V537912897 | V537912955 | V537913222 | V537913274 | V537913536 |
| V537912644 | V537912898 | V537912956 | V537913223 | V537913275 | V537913537 |
| V537912645 | V537912899 | V537912957 | V537913224 | V537913276 | V537913538 |
| V537912647 | V537912900 | V537912958 | V537913226 | V537913279 | V537913541 |
| V537913542 | V537914183 | V537914312 | V537915046 | V537915480 | V537916019 |
| V537913543 | V537914214 | V537914313 | V537915049 | V537915481 | V537916112 |
| V537913544 | V537914257 | V537914314 | V537915050 | V537915485 | V537916114 |
| V537913546 | V537914258 | V537914317 | V537915051 | V537915486 | V537916115 |
| V537913548 | V537914259 | V537914318 | V537915052 | V537915487 | V537916116 |
| V537913549 | V537914260 | V537914319 | V537915053 | V537915488 | V537916117 |
| V537913550 | V537914261 | V537914322 | V537915055 | V537915490 | V537916119 |
| V537913551 | V537914262 | V537914324 | V537915056 | V537915491 | V537916120 |
| V537913552 | V537914265 | V537914326 | V537915298 | V537915492 | V537916122 |
| V537913555 | V537914266 | V537914329 | V537915299 | V537915493 | V537916123 |
| V537913556 | V537914268 | V537914330 | V537915300 | V537915495 | V537916124 |
| V537913557 | V537914271 | V537914500 | V537915301 | V537915497 | V537916126 |
| V537913559 | V537914272 | V537915012 | V537915302 | V537915498 | V537916127 |
| V537913560 | V537914273 | V537915013 | V537915304 | V537915499 | V537916128 |
| V537913561 | V537914274 | V537915014 | V537915305 | V537915500 | V537916129 |
| V537913578 | V537914275 | V537915015 | V537915306 | V537915501 | V537916130 |
| V537913676 | V537914276 | V537915016 | V537915307 | V537915699 | V537916132 |
| V537913680 | V537914277 | V537915017 | V537915308 | V537915991 | V537916134 |
| V537913683 | V537914278 | V537915018 | V537915309 | V537915992 | V537916135 |
| V537913684 | V537914282 | V537915019 | V537915311 | V537915994 | V537916137 |
| V537913687 | V537914283 | V537915020 | V537915313 | V537915995 | V537916138 |
| V537913688 | V537914286 | V537915022 | V537915314 | V537915996 | V537916139 |

| V537913691 | V537914287 | V537915023 | V537915315 | V537915997 | V537916141 |
| --- | --- | --- | --- | --- | --- |
| V537913694 | V537914288 | V537915024 | V537915316 | V537915998 | V537916142 |
| V537913697 | V537914289 | V537915026 | V537915317 | V537915999 | V537916143 |
| V537913699 | V537914290 | V537915027 | V537915318 | V537916000 | V537916144 |
| V537913700 | V537914291 | V537915028 | V537915319 | V537916001 | V537916145 |
| V537913701 | V537914292 | V537915029 | V537915320 | V537916003 | V537916146 |
| V537913702 | V537914293 | V537915030 | V537915321 | V537916004 | V537916147 |
| V537913703 | V537914294 | V537915032 | V537915322 | V537916005 | V537916148 |
| V537913704 | V537914296 | V537915033 | V537915323 | V537916006 | V537916149 |
| V537913707 | V537914297 | V537915034 | V537915324 | V537916007 | V537916151 |
| V537913709 | V537914299 | V537915035 | V537915325 | V537916008 | V537916408 |
| V537913710 | V537914300 | V537915036 | V537915326 | V537916009 | V537916409 |
| V537913711 | V537914301 | V537915038 | V537915327 | V537916010 | V537916410 |
| V537913712 | V537914304 | V537915039 | V537915473 | V537916011 | V537916411 |
| V537913714 | V537914305 | V537915040 | V537915474 | V537916012 | V537916412 |
| V537913866 | V537914306 | V537915041 | V537915475 | V537916013 | V537916413 |
| V537913995 | V537914307 | V537915042 | V537915476 | V537916015 | V537916414 |
| V537913998 | V537914308 | V537915043 | V537915477 | V537916016 | V537916415 |
| V537913999 | V537914310 | V537915044 | V537915478 | V537916017 | V537916416 |
| V537914141 | V537914311 | V537915045 | V537915479 | V537916018 | V537916417 |
| V537916418 | V537916715 | V537916974 | V537917208 | V537917258 | V537917571 |
| V537916419 | V537916717 | V537916975 | V537917209 | V537917259 | V537917698 |
| V537916420 | V537916718 | V537916976 | V537917212 | V537917260 | V537917699 |
| V537916421 | V537916719 | V537916977 | V537917214 | V537917527 | V537917745 |
| V537916422 | V537916720 | V537916978 | V537917215 | V537917528 | V537917926 |
| V537916423 | V537916721 | V537916979 | V537917217 | V537917529 | V537917927 |
| V537916424 | V537916724 | V537916980 | V537917218 | V537917530 | V537917928 |
| V537916425 | V537916725 | V537916981 | V537917219 | V537917532 | V537917929 |
| V537916426 | V537916726 | V537916982 | V537917221 | V537917533 | V537917930 |
| V537916427 | V537916727 | V537916983 | V537917222 | V537917534 | V537917931 |
| V537916428 | V537916728 | V537916985 | V537917223 | V537917535 | V537917932 |
| V537916430 | V537916729 | V537916986 | V537917224 | V537917536 | V537917933 |
| V537916431 | V537916730 | V537917029 | V537917225 | V537917537 | V537917934 |
| V537916432 | V537916732 | V537917031 | V537917226 | V537917538 | V537917935 |
| V537916433 | V537916734 | V537917032 | V537917227 | V537917539 | V537917936 |
| V537916434 | V537916735 | V537917033 | V537917228 | V537917541 | V537917937 |
| V537916435 | V537916736 | V537917034 | V537917229 | V537917542 | V537917938 |
| V537916436 | V537916737 | V537917037 | V537917230 | V537917543 | V537917939 |
| V537916437 | V537916739 | V537917039 | V537917231 | V537917545 | V537917940 |

| V537916439 | V537916740 | V537917042 | V537917232 | V537917546 | V537917941 |
| --- | --- | --- | --- | --- | --- |
| V537916531 | V537916741 | V537917043 | V537917233 | V537917547 | V537917942 |
| V537916532 | V537916742 | V537917044 | V537917234 | V537917548 | V537917944 |
| V537916533 | V537916743 | V537917045 | V537917235 | V537917550 | V537917946 |
| V537916534 | V537916745 | V537917047 | V537917236 | V537917551 | V537917947 |
| V537916535 | V537916746 | V537917049 | V537917238 | V537917552 | V537917948 |
| V537916536 | V537916747 | V537917050 | V537917239 | V537917554 | V537917949 |
| V537916537 | V537916748 | V537917051 | V537917240 | V537917555 | V537917950 |
| V537916538 | V537916749 | V537917052 | V537917241 | V537917556 | V537917952 |
| V537916539 | V537916750 | V537917123 | V537917242 | V537917557 | V537917953 |
| V537916541 | V537916957 | V537917195 | V537917243 | V537917558 | V537917954 |
| V537916543 | V537916959 | V537917196 | V537917244 | V537917559 | V537917955 |
| V537916544 | V537916960 | V537917197 | V537917245 | V537917560 | V537917956 |
| V537916614 | V537916961 | V537917198 | V537917246 | V537917561 | V537917957 |
| V537916706 | V537916962 | V537917199 | V537917247 | V537917562 | V537917958 |
| V537916707 | V537916963 | V537917200 | V537917248 | V537917563 | V537917959 |
| V537916708 | V537916967 | V537917201 | V537917251 | V537917564 | V537917960 |
| V537916709 | V537916968 | V537917202 | V537917252 | V537917565 | V537917966 |
| V537916710 | V537916969 | V537917203 | V537917253 | V537917566 | V537917967 |
| V537916711 | V537916970 | V537917204 | V537917254 | V537917567 | V537917968 |
| V537916712 | V537916971 | V537917205 | V537917255 | V537917568 | V537917969 |
| V537916713 | V537916972 | V537917206 | V537917256 | V537917569 | V537917972 |
| V537916714 | V537916973 | V537917207 | V537917257 | V537917570 | V537917973 |
| V537917974 | V537918289 | V537918495 | V537918969 | V537919297 | V537919508 |
| V537917975 | V537918290 | V537918496 | V537918970 | V537919298 | V537919509 |
| V537917976 | V537918292 | V537918497 | V537919026 | V537919299 | V537919510 |
| V537917977 | V537918293 | V537918498 | V537919027 | V537919300 | V537919511 |
| V537917978 | V537918294 | V537918499 | V537919028 | V537919301 | V537919512 |
| V537917979 | V537918295 | V537918920 | V537919029 | V537919302 | V537919513 |
| V537917980 | V537918296 | V537918922 | V537919030 | V537919303 | V537919514 |
| V537917981 | V537918297 | V537918923 | V537919031 | V537919450 | V537919515 |
| V537917982 | V537918298 | V537918925 | V537919032 | V537919460 | V537919516 |
| V537917983 | V537918299 | V537918926 | V537919033 | V537919471 | V537919518 |
| V537917984 | V537918300 | V537918927 | V537919034 | V537919472 | V537919519 |
| V537918257 | V537918301 | V537918928 | V537919035 | V537919473 | V537919520 |
| V537918258 | V537918393 | V537918929 | V537919036 | V537919474 | V537919521 |
| V537918259 | V537918461 | V537918930 | V537919037 | V537919475 | V537919522 |
| V537918260 | V537918462 | V537918931 | V537919038 | V537919476 | V537919523 |
| V537918261 | V537918463 | V537918933 | V537919039 | V537919477 | V537919524 |

| V537918262 | V537918464 | V537918934 | V537919040 | V537919478 | V537919525 |
| --- | --- | --- | --- | --- | --- |
| V537918263 | V537918465 | V537918935 | V537919042 | V537919480 | V537919526 |
| V537918264 | V537918467 | V537918936 | V537919043 | V537919482 | V537919527 |
| V537918265 | V537918468 | V537918937 | V537919044 | V537919483 | V537919528 |
| V537918266 | V537918469 | V537918938 | V537919045 | V537919484 | V537919529 |
| V537918267 | V537918470 | V537918940 | V537919091 | V537919485 | V537919803 |
| V537918268 | V537918471 | V537918941 | V537919096 | V537919486 | V537919804 |
| V537918269 | V537918472 | V537918942 | V537919147 | V537919487 | V537919805 |
| V537918270 | V537918473 | V537918946 | V537919277 | V537919488 | V537919806 |
| V537918272 | V537918474 | V537918948 | V537919278 | V537919489 | V537919807 |
| V537918273 | V537918475 | V537918950 | V537919279 | V537919490 | V537919808 |
| V537918274 | V537918476 | V537918951 | V537919281 | V537919491 | V537919809 |
| V537918275 | V537918477 | V537918952 | V537919282 | V537919492 | V537919810 |
| V537918276 | V537918478 | V537918953 | V537919283 | V537919493 | V537919811 |
| V537918277 | V537918479 | V537918954 | V537919284 | V537919494 | V537919813 |
| V537918278 | V537918480 | V537918956 | V537919285 | V537919495 | V537919818 |
| V537918279 | V537918481 | V537918958 | V537919286 | V537919496 | V537919819 |
| V537918280 | V537918482 | V537918959 | V537919287 | V537919497 | V537919820 |
| V537918281 | V537918483 | V537918960 | V537919288 | V537919498 | V537919821 |
| V537918282 | V537918486 | V537918961 | V537919289 | V537919499 | V537919822 |
| V537918283 | V537918487 | V537918962 | V537919290 | V537919500 | V537919823 |
| V537918284 | V537918488 | V537918963 | V537919291 | V537919501 | V537919824 |
| V537918285 | V537918489 | V537918964 | V537919293 | V537919503 | V537919825 |
| V537918286 | V537918491 | V537918966 | V537919294 | V537919505 | V537919826 |
| V537918287 | V537918492 | V537918967 | V537919295 | V537919506 | V537919828 |
| V537918288 | V537918493 | V537918968 | V537919296 | V537919507 | V537919830 |
| V537919831 | V537920371 | V537920937 | V537920983 | V537921420 | V537921586 |
| V537919832 | V537920372 | V537920938 | V537920984 | V537921421 | V537921587 |
| V537919833 | V537920373 | V537920939 | V537920986 | V537921422 | V537921588 |
| V537919834 | V537920374 | V537920940 | V537920987 | V537921423 | V537921589 |
| V537919835 | V537920375 | V537920941 | V537920988 | V537921424 | V537921590 |
| V537919836 | V537920376 | V537920942 | V537920989 | V537921425 | V537921591 |
| V537919837 | V537920377 | V537920943 | V537921296 | V537921426 | V537921592 |
| V537919838 | V537920378 | V537920944 | V537921297 | V537921427 | V537921593 |
| V537919839 | V537920379 | V537920945 | V537921299 | V537921428 | V537921594 |
| V537919840 | V537920382 | V537920946 | V537921300 | V537921429 | V537921595 |
| V537919841 | V537920383 | V537920947 | V537921302 | V537921430 | V537921596 |
| V537919843 | V537920384 | V537920948 | V537921303 | V537921431 | V537921597 |
| V537919850 | V537920385 | V537920949 | V537921304 | V537921432 | V537921598 |

| V537919853 | V537920387 | V537920950 | V537921306 | V537921433 | V537921599 |
| --- | --- | --- | --- | --- | --- |
| V537919855 | V537920388 | V537920951 | V537921308 | V537921434 | V537921600 |
| V537919856 | V537920390 | V537920952 | V537921309 | V537921435 | V537921601 |
| V537919858 | V537920392 | V537920953 | V537921310 | V537921437 | V537921764 |
| V537920345 | V537920393 | V537920954 | V537921311 | V537921438 | V537921765 |
| V537920346 | V537920394 | V537920956 | V537921312 | V537921439 | V537921766 |
| V537920347 | V537920909 | V537920957 | V537921313 | V537921561 | V537921767 |
| V537920348 | V537920910 | V537920958 | V537921314 | V537921562 | V537921768 |
| V537920349 | V537920911 | V537920959 | V537921315 | V537921563 | V537921769 |
| V537920350 | V537920913 | V537920960 | V537921316 | V537921565 | V537921770 |
| V537920351 | V537920915 | V537920962 | V537921317 | V537921566 | V537921771 |
| V537920352 | V537920916 | V537920963 | V537921398 | V537921567 | V537921773 |
| V537920353 | V537920918 | V537920964 | V537921399 | V537921568 | V537921775 |
| V537920354 | V537920919 | V537920966 | V537921400 | V537921569 | V537921776 |
| V537920355 | V537920920 | V537920967 | V537921401 | V537921570 | V537921777 |
| V537920356 | V537920921 | V537920968 | V537921402 | V537921571 | V537921778 |
| V537920357 | V537920922 | V537920969 | V537921403 | V537921572 | V537921779 |
| V537920358 | V537920923 | V537920970 | V537921404 | V537921573 | V537921780 |
| V537920359 | V537920925 | V537920971 | V537921406 | V537921574 | V537921781 |
| V537920360 | V537920926 | V537920973 | V537921407 | V537921575 | V537921782 |
| V537920361 | V537920927 | V537920974 | V537921408 | V537921576 | V537921783 |
| V537920362 | V537920928 | V537920975 | V537921409 | V537921577 | V537921784 |
| V537920363 | V537920929 | V537920976 | V537921410 | V537921578 | V537921786 |
| V537920364 | V537920930 | V537920977 | V537921412 | V537921579 | V537921787 |
| V537920365 | V537920931 | V537920978 | V537921413 | V537921580 | V537921789 |
| V537920367 | V537920932 | V537920979 | V537921414 | V537921582 | V537921790 |
| V537920368 | V537920933 | V537920980 | V537921417 | V537921583 | V537921791 |
| V537920369 | V537920934 | V537920981 | V537921418 | V537921584 | V537921792 |
| V537920370 | V537920935 | V537920982 | V537921419 | V537921585 | V537921793 |
| V537921794 | V537922089 | V537922576 | V537922621 | V537923013 | V537924078 |
| V537921795 | V537922090 | V537922577 | V537922622 | V537923014 | V537924079 |
| V537921796 | V537922092 | V537922578 | V537922623 | V537923015 | V537924080 |
| V537921797 | V537922093 | V537922579 | V537922624 | V537923016 | V537924081 |
| V537921798 | V537922094 | V537922580 | V537922625 | V537923017 | V537924082 |
| V537921799 | V537922095 | V537922581 | V537922626 | V537923018 | V537924083 |
| V537921800 | V537922096 | V537922582 | V537922627 | V537923019 | V537924084 |
| V537921801 | V537922097 | V537922583 | V537922628 | V537923020 | V537924086 |
| V537921802 | V537922098 | V537922584 | V537922629 | V537923021 | V537924089 |
| V537922053 | V537922099 | V537922585 | V537922630 | V537923022 | V537924090 |

| V537922054 | V537922100 | V537922587 | V537922631 | V537923023 | V537924091 |
| --- | --- | --- | --- | --- | --- |
| V537922055 | V537922101 | V537922588 | V537922632 | V537923025 | V537924092 |
| V537922056 | V537922102 | V537922589 | V537922979 | V537923026 | V537924093 |
| V537922057 | V537922103 | V537922590 | V537922980 | V537923027 | V537924094 |
| V537922058 | V537922104 | V537922591 | V537922983 | V537923028 | V537924095 |
| V537922060 | V537922105 | V537922592 | V537922984 | V537923029 | V537924096 |
| V537922061 | V537922548 | V537922593 | V537922985 | V537923859 | V537924098 |
| V537922062 | V537922549 | V537922594 | V537922986 | V537923861 | V537924099 |
| V537922064 | V537922550 | V537922595 | V537922987 | V537923862 | V537924100 |
| V537922065 | V537922551 | V537922596 | V537922988 | V537923863 | V537924101 |
| V537922066 | V537922552 | V537922597 | V537922989 | V537923864 | V537924102 |
| V537922067 | V537922554 | V537922598 | V537922990 | V537923865 | V537924103 |
| V537922068 | V537922555 | V537922599 | V537922991 | V537923866 | V537924387 |
| V537922069 | V537922556 | V537922600 | V537922992 | V537923867 | V537924388 |
| V537922070 | V537922557 | V537922601 | V537922993 | V537923868 | V537924389 |
| V537922071 | V537922558 | V537922602 | V537922994 | V537923869 | V537924390 |
| V537922072 | V537922559 | V537922603 | V537922995 | V537923870 | V537924391 |
| V537922074 | V537922560 | V537922604 | V537922996 | V537923871 | V537924392 |
| V537922075 | V537922561 | V537922605 | V537922997 | V537923872 | V537924393 |
| V537922076 | V537922563 | V537922606 | V537922998 | V537923873 | V537924394 |
| V537922077 | V537922564 | V537922607 | V537922999 | V537923874 | V537924395 |
| V537922078 | V537922565 | V537922609 | V537923000 | V537923875 | V537924396 |
| V537922079 | V537922566 | V537922610 | V537923002 | V537923876 | V537924397 |
| V537922080 | V537922567 | V537922611 | V537923003 | V537923878 | V537924398 |
| V537922081 | V537922568 | V537922612 | V537923004 | V537923880 | V537924400 |
| V537922082 | V537922569 | V537922613 | V537923005 | V537923882 | V537924401 |
| V537922083 | V537922570 | V537922614 | V537923006 | V537923883 | V537924402 |
| V537922084 | V537922571 | V537922615 | V537923007 | V537923885 | V537924403 |
| V537922085 | V537922572 | V537922616 | V537923008 | V537923887 | V537924406 |
| V537922086 | V537922573 | V537922618 | V537923009 | V537923888 | V537924407 |
| V537922087 | V537922574 | V537922619 | V537923010 | V537924075 | V537924408 |
| V537922088 | V537922575 | V537922620 | V537923012 | V537924076 | V537924409 |
| V537924410 | V537924585 | V537924736 | V537924872 | V537924917 | V537925015 |
| V537924411 | V537924586 | V537924738 | V537924873 | V537924918 | V537925016 |
| V537924412 | V537924693 | V537924739 | V537924874 | V537924919 | V537925017 |
| V537924413 | V537924694 | V537924740 | V537924875 | V537924920 | V537925018 |
| V537924414 | V537924695 | V537924742 | V537924876 | V537924921 | V537925020 |
| V537924415 | V537924696 | V537924833 | V537924877 | V537924922 | V537925021 |
| V537924417 | V537924697 | V537924834 | V537924878 | V537924923 | V537925023 |

| V537924418 | V537924698 | V537924835 | V537924879 | V537924924 | V537925024 |
| --- | --- | --- | --- | --- | --- |
| V537924419 | V537924699 | V537924836 | V537924880 | V537924925 | V537925025 |
| V537924420 | V537924700 | V537924837 | V537924881 | V537924926 | V537925026 |
| V537924421 | V537924701 | V537924838 | V537924882 | V537924927 | V537925027 |
| V537924422 | V537924702 | V537924839 | V537924884 | V537924928 | V537925028 |
| V537924423 | V537924703 | V537924840 | V537924885 | V537924930 | V537925029 |
| V537924424 | V537924704 | V537924841 | V537924886 | V537924931 | V537925030 |
| V537924425 | V537924705 | V537924842 | V537924887 | V537924932 | V537925031 |
| V537924426 | V537924706 | V537924843 | V537924888 | V537924933 | V537925032 |
| V537924427 | V537924707 | V537924844 | V537924889 | V537924934 | V537925033 |
| V537924428 | V537924708 | V537924845 | V537924890 | V537924935 | V537925034 |
| V537924429 | V537924709 | V537924846 | V537924891 | V537924937 | V537925035 |
| V537924430 | V537924710 | V537924847 | V537924892 | V537924938 | V537925036 |
| V537924431 | V537924711 | V537924848 | V537924893 | V537924939 | V537925037 |
| V537924432 | V537924712 | V537924849 | V537924894 | V537924941 | V537925038 |
| V537924433 | V537924713 | V537924850 | V537924895 | V537924942 | V537925039 |
| V537924434 | V537924714 | V537924851 | V537924896 | V537924943 | V537925040 |
| V537924435 | V537924715 | V537924852 | V537924897 | V537924944 | V537925041 |
| V537924436 | V537924716 | V537924853 | V537924899 | V537924945 | V537925042 |
| V537924567 | V537924717 | V537924854 | V537924900 | V537924947 | V537925044 |
| V537924568 | V537924718 | V537924855 | V537924901 | V537924948 | V537925045 |
| V537924569 | V537924719 | V537924856 | V537924902 | V537925001 | V537925047 |
| V537924570 | V537924720 | V537924857 | V537924903 | V537925002 | V537925048 |
| V537924571 | V537924721 | V537924859 | V537924904 | V537925003 | V537925049 |
| V537924572 | V537924722 | V537924860 | V537924905 | V537925004 | V537925050 |
| V537924573 | V537924723 | V537924861 | V537924906 | V537925005 | V537925051 |
| V537924574 | V537924724 | V537924862 | V537924908 | V537925006 | V537925052 |
| V537924576 | V537924725 | V537924863 | V537924909 | V537925007 | V537925054 |
| V537924577 | V537924726 | V537924864 | V537924910 | V537925008 | V537925055 |
| V537924578 | V537924727 | V537924865 | V537924911 | V537925009 | V537925056 |
| V537924580 | V537924729 | V537924866 | V537924912 | V537925010 | V537925057 |
| V537924581 | V537924731 | V537924868 | V537924913 | V537925011 | V537925058 |
| V537924582 | V537924732 | V537924869 | V537924914 | V537925012 | V537925059 |
| V537924583 | V537924733 | V537924870 | V537924915 | V537925013 | V537925060 |
| V537924584 | V537924734 | V537924871 | V537924916 | V537925014 | V537925061 |
| V537925062 | V537925096 | V537925129 | V537925164 | V537925272 | V537925305 |
| V537925063 | V537925097 | V537925130 | V537925165 | V537925273 | V537925306 |
| V537925064 | V537925098 | V537925131 | V537925166 | V537925274 | V537925307 |
| V537925065 | V537925099 | V537925132 | V537925167 | V537925275 | V537925308 |

| V537925066 | V537925100 | V537925133 | V537925168 | V537925276 | V537925309 |
| --- | --- | --- | --- | --- | --- |
| V537925067 | V537925101 | V537925134 | V537925169 | V537925277 | V537925310 |
| V537925068 | V537925102 | V537925135 | V537925170 | V537925278 | V537925311 |
| V537925069 | V537925103 | V537925138 | V537925244 | V537925279 | V537925312 |
| V537925070 | V537925104 | V537925139 | V537925245 | V537925280 | V537925313 |
| V537925071 | V537925105 | V537925140 | V537925246 | V537925281 | V537925314 |
| V537925072 | V537925106 | V537925141 | V537925247 | V537925282 | V537925315 |
| V537925073 | V537925107 | V537925142 | V537925248 | V537925283 | V537925316 |
| V537925074 | V537925108 | V537925143 | V537925249 | V537925284 | V537925317 |
| V537925076 | V537925109 | V537925144 | V537925250 | V537925285 | V537925318 |
| V537925078 | V537925110 | V537925145 | V537925251 | V537925286 | V537925319 |
| V537925079 | V537925111 | V537925146 | V537925252 | V537925287 | V537925320 |
| V537925080 | V537925112 | V537925147 | V537925253 | V537925288 | V537925321 |
| V537925081 | V537925113 | V537925148 | V537925254 | V537925289 | V537925322 |
| V537925082 | V537925114 | V537925149 | V537925255 | V537925290 | V537925576 |
| V537925083 | V537925115 | V537925150 | V537925256 | V537925291 | V537925578 |
| V537925084 | V537925116 | V537925151 | V537925257 | V537925293 | V537925579 |
| V537925085 | V537925117 | V537925152 | V537925258 | V537925294 | V537925580 |
| V537925086 | V537925118 | V537925153 | V537925259 | V537925295 | V537925582 |
| V537925087 | V537925119 | V537925155 | V537925260 | V537925296 | V537925583 |
| V537925088 | V537925120 | V537925156 | V537925262 | V537925297 | V537925584 |
| V537925089 | V537925121 | V537925157 | V537925264 | V537925298 | V537925585 |
| V537925090 | V537925122 | V537925158 | V537925265 | V537925299 | V537925586 |
| V537925091 | V537925123 | V537925159 | V537925267 | V537925300 | V537925587 |
| V537925092 | V537925125 | V537925160 | V537925268 | V537925301 | V537925722 |
| V537925093 | V537925126 | V537925161 | V537925269 | V537925302 |  |
| V537925094 | V537925127 | V537925162 | V537925270 | V537925303 |  |
| V537925095 | V537925128 | V537925163 | V537925271 | V537925304 |  |

(b) For engines that have had a crankshaft replaced after September 30, 1999, replace any crankshaft that has a SN listed in Table 2 of this AD.

(c) After receipt of this AD, do not install any crankshaft removed in accordance with paragraph (a) or (b) of this AD into any engine.

(d) After receipt of this AD, do not install any crankshaft that has a SN listed in Table 2 of this AD on an LTIO-540 or TIO-540 model engine.

(e) An alternative method of compliance or adjustment of the compliance time that provides an acceptable level of safety may be used if approved by the Manager, New York Aircraft Certification Office (NYACO). Operators must submit their requests through an appropriate FAA Principal Maintenance Inspector, who may add comments and then send it to the Manager, NYACO.

Note 2: Information concerning the existence of approved alternative methods of compliance with this airworthiness directive, if any, may be obtained from the NYACO.

(f) Special flight permits may be issued in accordance with sections 21.197 and 21.199 of the Federal Aviation Regulations (14 CFR 21.197 and 21.199) to operate the airplane to a location where the requirements of this AD can be done.

(g) Emergency AD 2002-17-53, issued August 16, 2002, supersedes Emergency AD 2002-04-51 and becomes effective upon receipt.

FOR FURTHER INFORMATION CONTACT: Norman Perenson, Aerospace Engineer, New York Aircraft Certification Office, FAA, Engine and Propeller Directorate, 10 Fifth Street, 3rd floor, Valley Stream, NY 11581-1200; telephone (516) 256-7537; fax (516) 568-2716.

Issued in Burlington, Massachusetts on August 16, 2002.

Jay J. Pardee,

Manager, Engine and Propeller Directorate,

Aircraft Certification Service.