MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A09600 | In-Flight Anomaly Number -- | Contractor Report Number P-052 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title HELIUM FLEX HOSE - "B" NUT LEAKAGE |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 3 |
| HCRIT -- | Sys_Lvl N | Misc Codes A (6) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE EXTERNAL TANK | PART# 82601000000 | SER/LOT# LWT-24 | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE HELIUM INJECT INSTL | PART# 80921011930 | SER/LOT# N/A | MANUFACTURER MMC |
| HARDWARE NCA | NOMENCLATURE FLEX HOSE | PART# 32L2060133 | SER/LOT# N/A | MANUFACTURER MMC |
| Test/Operation L - FLD | Prevailing Condtion F - FUNCTIONAL | F / U UC | Fail Mode MR - TORQUE HI/LO | Cause DH - DES-HDW |
| System PROPULSION | Defect DB - BENT | Material S - STRUCT | Work Contact -- | Fail Date 06/21/1985 |
| Received at MSFC 10/21/1985 | Date Isolated -- | FMEA Reference 2.4.9.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom MV - EXT LEAK | Time Cycle -- |
| Effectivity Text -- |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 11/04/1991 | CN RSLV SBMT 09/18/1987 | Defer Date -- | Add Date -- | R/C Codes 5 - TRNG -- -- |
| Assignee |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| Approval |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 11/04/1987 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description REF: MARS T-81499, T-76279 DURING LEAK TESTING OF THE HELIUM INJECT SYSTEM ON LWT-24, A LEAK WAS DETECTED AT THE "B" NUT OF A FLEX HOSE ASSEMBLY. REPEATED RETORQUE AND CRUSHWASHER INSTALLATIONS DID NOT CORRECT THE PROBLEM. REMOVAL AND REPLACEMENT OF THE HOSE ASSEMBLY WAS REQUIRED TO ACHIEVE A NO LEAKAGE CONDITION. FLARED FITTING LEAKAGE HAS BEEN A RECURRING PROBLEM. THEREFORE, THIS PROBLEM ADDRESSES FLARED FITTINGS IN GENERAL |
| Contractor Investigation/Resolution R/C - 1) ACTION WAS TAKEN TO IMPLEMENT HANDLING CONTROLS, PREASSEMBLY INSPECTION OF SEALING SUR- FACES AND INCREASE PERSONNEL AWARENESS OF HARDWARE DAMAGE SENSITIVITY. 2) NEW TORQUE WRENCHES WERE REQUIRED TO REPLACE OLDER EXISTING TOOLS. A PRODUCTION TIP WAS ISSUED TO RE-EMPHASIZE CORRECT USE OF CLICK TYPE WRENCHES. 1/16/86 PRB STATUS - AN ECP IS BEING WRITTEN AND WILL PROPOSE USING KC FITTINGS ON THE HAZARDOUS GAS DETECTION SYSTEM LINES AND ON THE HELIUM INJECTION SYSTEM UP TO THE FILTERS AND CHECK VALVES. THE ECP WILL ALSO PROPOSE THAT THE B-NUTS ON THE LH2 AND LO2 VENT VALVE SYSTEM BE TORQUED AND TORQUE STRIPED. ADDITIONALLY, A TORQUE ANALYZER WILL BE USED TO VALIDATE THE TORQUE WRENCHES IMMEDIATELY AFTER USED. OLD TORQUE WRENCHES TO BE REPLACED WITH NEW ONES. 3/20/86 PRB STATUS - NO CHANGE FROM 1-16-86 STATUS EXCEPT OLD TORQUE WRENCHES ARE TO BE REPLACED BY 4-1-86. ECP IS BEING HELD UP DUE TO 51L INVESTIGATION ACTIVITY. NEW ECD FOR THIS CAPS CLOSURE IS 6-30-86. 4/17/86 PRB STATUS - OLD TORQUE WRENCHES HAVE BEEN REPLACED. CHANGE SUMMARY IS IN WORK FOR USAGE OF INTEGRAL TEFLON SEAL UNIONS. ECD REMAINS 6-30-86. 5/15/86 PRB STATUS - STILL GATHERING DATA FROM KSC. EXPECT ECD TO CHANGE. 6/19/86 PRB STATUS - DEFERRED UNTIL NEXT PRB. MEETING RAN OUT OF TIME. 7/15/86 PRB STATUS - REVIEWING KSC DATA CONCERNING CAPS USE. PARTS WILL BE SEPARATED AND PACKAGED INDIVIDUALLY. 5/28/87 STATUS UPDATE - ENGINEERING TEST PROGRAM TO DETERMINE EFFECTS OF FLARE SPRING-BACK AND TORQUE RELAXATION ENGINEERING EVALUATION OF SYSTEMS REQUIREMENT FOR "O" LEAKAGE. ECD 7/15/87 9/18/87 - GENERAL/HISTORY DURING THE ET PROGRAM, THE NUMBER OF TUBING LEAKS PER EFFECTIVITY HAS BEEN INCREASING. THESE LEAKS CAUSE PRODUCTION DELAYS AS A RESULT OF REWORK REQUIRED TO CORRECT THE PROBLEM. FORMAL FAILURE ANALYSIS OF EACH LEAK WAS NOT CONDUCTED HOWEVER, THE REWORK PROCEDURE DOES GIVE SOME INDICATION AS TO THE CAUSE OF EACH LEAK. THIS ACTIVITY VERIFIES/RETORQUES THE UNION AND CHECKS FOR LEAKAGE. IF RETORQUE FAILS TO CORRECT THE LEAKAGE, A CRUSHWASHER IS INSTALLED AND A RETEST OF THE UNION IS CONDUCTED. THIS PROCEDURE HAS BEEN EFFECTIVE IN ELIMINATING LEAKS AND IDENTIFIES AN UNDER TORQUE CONDITION OR DAMAGE SEALING SURFACES, DEPENDING ON WHAT PORTION OF THE PROCEDURE WAS SUCCESSFUL IN CORRECTING THE LEAKAGE. DATA COMPILED THUS FAR REVEALED THE FOLLOWING TRENDS: O 87% OF ALL 3/8" JOINTS WHICH LEAKED WERE BELOW TORQUE O 69% OF ALL 1/2" JOINTS WHICH LEAKED WERE BELOW TORQUE O 53% OF ALL 3/8" JOINTS WHICH LEAKED REQUIRED CRUSHWASHERS O 77% OF ALL 1/4" JOINTS WHICH LEAKED REQUIRED CRUSHWASHERS SUBSEQUENT TASKS OF THIS CAPS WILL EVALUATE EXISTING CONDITIONS AND IMPLEMENT CORRECTIVE ACTIONS, AS REQUIRED. TASK CLOSED TASK I FAILURE/INVESTIGATION THE FAILURE WAS REVERIFIED ON A TEST BENCH. EXAMINATION OF THE HOSE REMOVED FROM LWT-24 REVEALED A SCRATCH/DENTED SEALING SURFACE. THE MAGNITUDE OF THE DAMAGE WOULD EXPLAIN WHY CRUSHWASHERS WERE INEFFECTIVE IN STOPPING THE LEAKING. THE CAUSE FOR THE DAMAGE IS UNKNOWN. THE FOLLOWING ACTIONS WILL BE ACCOMPLISHED. A. DUE TO THE NUMBER OF LEAKS ATTRIBUTED TO SEALING SURFACE DAMAGE, A REVIEW OF CLEANING/TESTING FACILITIES IS REQUIRED THIS WILL IDENTIFY AREAS WHERE TUBING COMPONENTS MAY BE SUBJECTED TO INADVERTENT DAMAGE. CLOSURE STATEMENT INVESTIGATIONS REVEALED A POTENTIAL FOR SEALING SURFACE DAMAGE BY CLEANING CONTAINERS USED IN THE CLEAN ROOM (REFERENCE R. LANDRY MEMORANDUM TO C. CAMPBELL OF NOVEMBER 7, 1985). B. A REVIEW OF INSPECTION REQUIREMENTS WILL BE CONDUCTED TO DETERMINE THE ADEQUACY FOR DETECTING SEALING SURFACE DAMAGE AFTER CLEANING/TESTING AND PRIOR TO ET INSTALLATION. CLOSURE STATEMENT IN-PROCESS INSPECTION WERE INADVERTENTLY DELETED FROM THE MPPS WHEN REVISED TO THE STAND-ALONE FORMAT. MPPS WERE REVISED TO ADD INSPECTION REQUIREMENT ON LWTS 33 AND UP (REFERENCE INTER- OFFICE MEMORANDUMS 3743-85-235 AND 3743-87-070). C. CONDUCT AN INVESTIGATION INTO POSSIBLE UNDER TORQUE OF UNIONS. CLOSURE STATEMENT AN INVESTIGATION WAS CONDUCTED CONCERNING THE DATA WHICH INDICATES A SIGNIFICANT NUMBER OF LEAKS ARE ATTRIBUTABLE TO UNDER TORQUED UNIONS. THREE TORQUE WRENCHES (JO-LINE), USED EXCLU- SIVELY ON TUBING CONNECTIONS, WERE FOUND OUT OF TOLERANCE. A RISK DEFECT WAS ISSUED BY METROLOGY AND DC&R P-84-008 WAS RELEASED TO REVERIFY TORQUE AT THE UNIONS WHERE THE SUBJECT WRENCHES WERE USED DURING THE CALIBRATION CYCLE. FURTHER EVALUATION OF THIS PARTICULAR STYLE OF WRENCH REVEALED CERTAIN DEFICIENCIES IN OPERATION WHICH RESULTED IN INSUFFICIENT TORQUE (REFERENCE INTEROFFICE MEMORANDUM 3741-85-065). D. AN INVESTIGATION WAS CONDUCTED REGARDING RELAXATION OF UNIONS AFTER TORQUE. THE FERRULES USED UNDER THE "B" NUTS ARE EXPERIENCING YIELD WHEN PLACED UNDER TENSION. THE RESULT IS AN INCREASE IN FERRULE CIRCUMFERENCE WHICH MAY ALLOW A RELAXATION OF TENSION APPLIED TO THE SEALING SURFACES. TYPICAL ENLARGEMENT OF THE FERRULE IS 0.014" DIAMETER ON 3/8" TUBING. CURRENTLY, THE FERRULES ARE MADE FROM 304 STAINLESS. MATERIALS ENGINEERING IS TASKED TO INVESTIGATE THIS CONDITION AND MAKE SPECIFIC RECOMMENDATIONS. CLOSURE STATEMENT TASK IS COMPLETE (REFERENCE INTEROFFICE MEMORANDUMS 3573-86-004, 3510-87-035, AND TEST REPORT ETTR-287). ENGINEERING EVALUATION FOUND NO PERFORMANCE CONCERN. E. ENGINEERING IS TASKED TO INVESTIGATE THE FEASIBILITY OF USING KC FITTINGS WITH INTEGRAL TEFLON SEALS OR FLARES WITH CIRCULAR LAY IN LIEU OF HIGHLY POLISHED SURFACE. ANALYSIS WILL ALSO BE CONDUCTED TO DETERMINE SYSTEM ALLOWABLES AS RELATED TO JOINT LEAKAGE. CLOSURE STATEMENT TASK IS COMPLETE (REFERENCE INTEROFFICE MEMORANDUMS 3515-86-027, 3510-87-035, AND MMC 3522/P- 87-041). COST OF IMPLEMENTATION WAS NOT FEASIBLE. TASK CLOSED TASK II CORRECTIVE ACTIONS A. AMT WAS INFORMED OF THE FINDINGS IN TASK I.C AND COMMITTED TO FIND SUITABLE REPLACEMENT TOOLS (REFERENCE INTEROFFICE MEMORANDUM 3693-85-SC-382). CLOSURE STATEMENT REPLACEMENT TOOLS HAVE BEEN ACQUIRED AND ARE IN SERVICE (REFERENCE INTEROFFICE MEMORANDUM 3693- 86-SC-365) B. NEW TOOLING IS REQUIRED TO PREVENT DAMAGE TO FITTINGS DURING CLEANING. AMT IS TASKED TO ACCOMPLISH THIS ACTION. CLOSURE STATEMENT A NEW CLEANING CONTAINER (SA3611-1137) HAS BEEN FABRICATED WHICH SHOULD PRECLUDE FURTHER DAMAGE.C. IN-PROCESS INSPECTIONS OF SEALING SURFACES ARE REQUIRED TO REDUCE THE FREQUENCY OF LEAKAGE. CLOSURE STATEMENT REFERENCE INTEROFFICE MEMORANDUM 3743-87-070. D. PRODUCTION TIPS WILL BE ISSUED TO IDENTIFY TO PERSONNEL THE DAMAGE SENSITIVITY OF SEALING SUR- FACES ON PNEUMATIC TUBING AND EMPHASIZE THE CORRECT USE OF CLICK TYPE TORQUE WRENCHES. CLOSURE STATEMENT PRODUCTION TIPS 078 AND 085 HAVE BEEN ISSUED. E. REJECTION OF TUBE FITTINGS FOR DAMAGE HAS INCREASED WITH IMPLEMENTATION OF INSPECTIONS PER TASK II.C. A STOCK CHECK IS REQUIRED TO PURGE INVENTORY OF DAMAGED FITTINGS. CLOSURE STATEMENT TWO THOUSAND NINE HUNDRED TWENTY-FOUR COMPONENTS WERE INSPECTED AND REJECTED FOR SEALING SURFACE DAMAGE ON MARS T-94996, T-94994, T-94993, T-94991, AND T-94989. TASK CLOSED TASK III CLEARANCE OF EFFECTIVITIES EACH JOINT IS REQUIRED TO PASS TM04 LEAKAGE REQUIREMENTS. THERE ARE NO CONSTRAINTS. TASK CLOSED TASK IV CAPS CLOSEOUT SUMMARY DAMAGE: ACTION WAS TAKEN TO IMPLEMENT HANDLING CONTROLS, PREASSEMBLY INSPECTION OF SEALING SURFACES, AND INCREASE PERSONNEL AWARENESS OF HARDWARE DAMAGE SENSITIVITY. UNDER TORQUE: NEW TORQUE WRENCHES WERE ACQUIRED TO REPLACE OLDER EXISTING TOOLS. A PRODUCTION TIP WAS ISSUED TO RE-EMPHASIZE CORRECT USE OF CLICK TYPE WRENCHES. PRELOAD RELAXATION: A TEST PROGRAM WAS CONDUCTED BY ENGINEERING WHICH DETERMINED THAT JOINT PRELOAD RELAXATION DOES OCCUR OVER TIME AND THAT SIGNIFICANT SEALING SURFACE DISTORTION OCCURS ON MALE FITTINGS. ENGINEER- ING EVALUATION DETERMINED THAT THIS PHENOMENA WAS NOT DETRIMENTAL TO PERFORMANCE AND THAT THE EXISTING DESIGN WAS ACCEPTABLE. GENERAL: OTHER ALTERNATIVES, WHICH WOULD REDUCE OR ELIMINATE BUBBLE LEAKS, WERE INVESTIGATED. THESE INCLUDED THE FOLLOWING: O CHANGE OF FERRULE MATERIAL. O PRODUCING FLARES WITH PRONOUNCED CIRCULAR LAY FINISH. O LEAK TESTING BASED UPON SYSTEM ALLOWABLES. O USE OF "KC" FITTING WITH INTEGRAL TEFLON SEALS. THESE ACTIONS WOULD REQUIRE A DESIGN CHANGE. BASED UPON ENGINEERING'S ASSESSMENT, IT IS LESS EXPENSIVE FROM A TOTAL PROGRAM STANDPOINT TO REPAIR LEAKING JOINTS THAN TO INITIATE A DESIGN CHANGE. THIS CAPS WAS INITIATED WHEN THE NUMBER OF B-NUT LEAKS PER ET INCREASED TO 28 FOLLOWING IMPLEMENTATION OF CORRECTIVE ACTION, THE NUMBER OF B-NUT LEAKS PER ET IS AVERAGING 14, WHICH IS ACCEPTABLE |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A09600 | IFA# -- | Contractor RPT# P-052 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 32L2060133 | Asmnt Part Name HELIUM FLEX HOSE | Asmnt Serial/Lot# N/A |
| HCRIT CD -- | FCRIT CD 1 | CAUSE CD DH - DES-HDW | FAIL MODE MR - TORQUE HI/LO |
| Asmnt FMEA 2.4.9.1 | Asmnt FM 1 | FMEA CSE B | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |