Guidelines for submission of Shotgun Libraries to the DOE Joint Genome Institute

Library quality is the most critical component in the success of sequencing projects.  Users may send libraries constructed in their lab in the following formats by order of preference: transformation stock, 384-well nunc plates, or ligation. The JGI only sequences in both directions. We cannot sequence fewer than 20 plates for libraries not in standard JGI vectors (pUC18, pMCL200 and pCC1Fos).

If you cannot meet the JGI specifications for whole genome shotgun libraries or have questions or concerns, please contact jgi_project_management@lanl.gov and your project manager.

JGI User Supplied Library Specifications: Transformation Stock

- Must by accompanied by vector information. (please see required vector information at the bottom of this document)

- Must by accompanied by a completely filled out RI_Shotgun_Libraries.xls document detailing construction & QC protocols for the library.

- Must be test transformed by the user, and the number of colony forming units/ul reported, as well as the total volume provided.

- Must have < 10% insertless rate as measured by QC’ing at least 24 clones.

- Must have an efficiency of 1.7xs the desired number of clones to be end sequenced. QPixes only pick ~60% of white colonies.

- A representative gel image used to verify insert must be submitted.

- Inserts must be contained in white colonies. (we do not pick blue colonies)

- Must be shipped on dry ice.

JGI User Supplied Library Specifications: 384 well Nunc Plates

- Must be 384-well Nunc plate with lid (Tissue Culture Treated, Sterile) is P/N Beckman: #164688 for the plates and 538619 for the seals. CIC sells the same seals, the part number is FS-100.

- Must by accompanied by vector information. (please see required vector information at the bottom of this document)

- Must by accompanied by a completely filled out RI_Shotgun_Libraries.xls document detailing construction & QC protocols for the library.

- Must provide the OD of each well in separate document and identify blank wells.

- We will not copy or rearray plates. We will ship plates back to user.

- Must be shipped on dry ice. We recommend sealing the plates and using lids, and if shipping more than one plate, securing them with a rubber band.

JGI User Supplied Library Specifications: Ligation Stock

- Must by accompanied by vector information. (please see required vector information at the bottom of this document)

- Must by accompanied by a completely filled out RI_Shotgun_Libraries.xls document detailing construction & QC protocols for the library.

- Must be test transformed by the user, and the number of colony forming units/ul reported, as well as the total volume provided.

- Must have < 10% insertless rate as measured by QC’ing at least 24 clones.

- Must have an efficiency of 1.7xs the desired number of clones to be end sequenced. QPixes only pick ~60% of white colonies.

- A representative gel image used to verify insert must be submitted.

- Inserts must be contained in white colonies. (we do not pick blue colonies)

- Must be shipped on wet or dry ice.

JGI User Supplied Library Specifications: Vector Information

- The following information must be provided for all vectors:

  - Vector name

  - Vector sequence

  - Vector source

  - Vector Accession Number

  - Complete sequence of any adaptors

  - Sequencing Primer Names

  - Sequencing Primer Sequences

  - Antibiotic

  - Antibiotic concentration

  - Cloning site (cut site)

  - Other CDS/features.

- The JGI does not stock and cannot process libraries requiring growth or selection on gentamycin or tetracycline.

JGI User Supplied Library Specifications: Shipping

Prior to shipping samples to the JGI, the library prep must first be reviewed & approved. Complete the appropriate RI (http://my.jgi.doe.gov/general/gettingstarted.html and email it along with a well-labeled gel image of your library QC to your project manager.

Transformation and Ligation Stocks should be shipped to the JGI in one tube per library.

The tube should be legibly labeled with

- Short description of sample or genus, species, strain,

- Name of PI on Proposal,

- Number of colonies per microliter (cfu),

- prepped date, and

- Name or initials of primary contact (primary contact indicated in “JGI Required Information” form).

If the DNA prepared in multiple preps, each prep should be QC’ed separately, and good preps pooled into one tube for shipping to the JGI.

Plates must be shipped on dry ice. We recommend sealing the plates and using lids, and if shipping more than one plate, securing them with a rubber band.

You are ready for the next step: http://my.jgi.doe.gov/general/gettingstarted.html

Step 3: Required Information Spreadsheets.