STATEMENT OF WORK

usda, Natural Resources Conservation Service

Wisconsin

Riparian Forest Buffer (391)

DESIGN (911)

Deliverables:

1.	Design documents that demonstrate criteria in NRCS practice standard have been met and are compatible with planned and applied practices.

a.	Practice standard criteria-related computations and analyses to develop plans and specifications including but not limited to:

i.	Determination of buffer zone widths and lengths and adapted species of woody plants to be planted, retained, and/or naturally reestablished in applicable zones.

ii.	Supporting conservation practices necessary to protect the buffer zone including Use Exclusion.

iii.	Additional provisions, as required, for reducing excess amounts of pollutants in surface runoff and shallow ground water flow (creation of a zone 2 and a zone 3); providing habitat for aquatic organisms and terrestrial wildlife and increasing carbon storage in biomass and soils.

iv.	Estimated quantities of trees/shrubs and grass/forb seed required to establish buffers according to design.

v.	Estimated quantities of materials needed for Use Exclusion or other supporting practices.

2.	Written plans and specifications including location map, sketches and drawings shall be provided to the client that adequately describes the requirements to install the practice and obtain necessary permits.

3.	Documentation of needed operation and maintenance.

4.	Certification that the design meets practice standard criteria and complies with applicable laws and regulations.

5.	Required documentation of design modifications during practice installation.

6.	Itemized cost estimate.

CERTIFICATION OF COMPLETION

Riparian Forest Buffer (391)

Design (911)

Program Participant Information

Name (print):

Contract Number: _______________________________     Contract Item #(s):

Technical Service Provider Information

Name (print):

TSP ID Number: _______________________________________     Expiration Date:

I hereby certify that the technical services I provided as a Technical Service Provider for this component(s) checked above: (1) comply with all applicable Federal, State, Tribal, and Local laws and requirements, (2) meet applicable USDA NRCS conservation practice standards, specifications, and program requirements, (3) are consistent with and meet the particular conservation program goals and objectives, (4) that I have provided the above named Program Participant the Deliverables in this Statement of Work for this component, and (5) comply with all “Certification Terms” as identified in the Technical Service Provider Certification Agreement.

________________________________________________________	__________________

Technical Service Provider Signature	Date

________________________________________________________	__________________

Received By (NRCS staff)	Date

STATEMENT OF WORK

usda, Natural Resources Conservation Service

Wisconsin

Riparian Forest Buffer (391)

INSTALLATION (912)

Deliverables

1.	Documentation of pre-application conference with client.

2.	`Verification that client has obtained required permits.

3.	Staking and layout according to plans and specifications including applicable layout notes.

4.	Application guidance as needed.

5.	Facilitate, implement and document required design modifications with client, original designer permitting and funding agencies.

6.	Advise client/NRCS on compliance issues with all federal, state, tribal, and local laws, regulations and NRCS policies during installation.

7.	Certification that the application process and materials meet design and permit requirements.

CERTIFICATION OF COMPLETION

Riparian Forest Buffer (391)

Installation (912

Program Participant Information

Name (print):

Contract Number: _______________________________     Contract Item #(s):

Technical Service Provider Information

Name (print):

TSP ID Number: _______________________________________     Expiration Date:

I hereby certify that the technical services I provided as a Technical Service Provider for this component(s) checked above: (1) comply with all applicable Federal, State, Tribal, and Local laws and requirements, (2) meet applicable USDA NRCS conservation practice standards, specifications, and program requirements, (3) are consistent with and meet the particular conservation program goals and objectives, (4) that I have provided the above named Program Participant the Deliverables in this Statement of Work for this component, and (5) comply with all “Certification Terms” as identified in the Technical Service Provider Certification Agreement.

________________________________________________________	__________________

Technical Service Provider Signature	Date

________________________________________________________	__________________

Received By (NRCS staff)	Date

STATEMENT OF WORK

usda, Natural Resources Conservation Service

Wisconsin

Riparian Forest Buffer (391)

CHECKOUT (913)

Deliverables

1.	Records of application.

a.	Extent of practice units applied and location identified on a map.

b.	Width and extent of buffer zones.

c.	Actual quantities of plant materials used by species and quantities of materials used for construction of supporting conservation practices.

2.	Certification that the application meets NRCS standards and specifications and is in compliance with permits.

3.	Provide the following information to the NRCS field office servicing the relevant land unit for entry into the Performance Results System (PRS):

a.	Technical Service Provider Name

b.	Customer name

c.	USDA program funding the practice (if known)

d.	Location of work (state, county, conservation district, land tract identifier)

e.	Land use of field where the practice was installed (cropland, etc.)

f.	NRCS practice name and quantity of practice installed in appropriate units

4.	Documentation of exit conference with client and contractor.

CERTIFICATION OF COMPLETION

Riparian Forest Buffer (391)

Checkout (913)

Program Participant Information

Name (print):

Contract Number: _______________________________     Contract Item #(s):

Technical Service Provider Information

Name (print):

TSP ID Number: _______________________________________     Expiration Date:

I hereby certify that the technical services I provided as a Technical Service Provider for this component(s) checked above: (1) comply with all applicable Federal, State, Tribal, and Local laws and requirements, (2) meet applicable USDA NRCS conservation practice standards, specifications, and program requirements, (3) are consistent with and meet the particular conservation program goals and objectives, (4) that I have provided the above named Program Participant the Deliverables in this Statement of Work for this component, and (5) comply with all “Certification Terms” as identified in the Technical Service Provider Certification Agreement.

________________________________________________________	__________________

Technical Service Provider Signature	Date

________________________________________________________	__________________

Received By (NRCS staff)	Date

STATEMENT OF WORK

usda, Natural Resources Conservation Service

Wisconsin

Riparian Forest Buffer (391)

REFERENCES

- WI NRCS Field Office Technical Guide (eFOTG), Section IV, Conservation Practice Standard 391, Riparian Forest Buffer

- NRCS National Forestry Handbook (NFH), Part 636.4

- NRCS National Environmental Compliance Handbook

- NRCS Cultural Resources Handbook