WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A10659 | In-Flight Anomaly Number -- | Contractor Report Number E-93-1 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LOX LEVEL SENSOR (S/N 391) FAILED ELECT ISOLATION TEST |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl N | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE EXTERNAL TANK | PART# 82601000000 | SER/LOT# LWT 28 | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE LOX LEVEL SENSOR | PART# 74L4-1 | SER/LOT# 391 | MANUFACTURER SIMMONDS |
| Test/Operation L - FLD | Prevailing Condtion E - ENVIRONMENT | F / U F | Fail Mode EE - RANDOM | Cause ETP - EI-TEST-INST |
| System ELECTRICAL | Defect CN - CONTAM | Material C - EEE | Work Contact J. ADAMS | Fail Date 08/23/1985 |
| Received at MSFC 04/01/1987 | Date Isolated -- | FMEA Reference 3.1.1.4 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom EVM - CON/MEG FAIL | Time Cycle -- |
| Effectivity Text LWTS 15 AND SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 01/10/1995 | CN RSLV SBMT 04/01/1987 | Defer Date -- | Add Date -- | R/C Codes 4 - TEST -- -- |
| Assignee |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| Approval |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete -- | MSFC Closure Date 08/06/1987 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description LOX LEVEL SENSOR (S/N 391) ON FORWARD MAST OF LWT-28 FAILED THE ELECTRICAL ISOLATION RESISTANCE TEST PERFORMED IN THE MAF FINAL ASSY AREA. THE MEASURED VALUE OF RESISTANCE WAS LESS THAN 5 MEGOHMS. MINIMUM ACCEPTABLE ISOLATION RESISTANCE VALVE IS 5 MEGOHMS. REF: MARS T-83880, T-83884, T-83888, CAPS E-093, E-092, AND E-093-3 |
| Contractor Investigation/Resolution R/A - PROCESS INSTRUCTION 5008 WAS REVISED TO PROVIDE FORCED, HEATED, NITROGEN DRYING OF BOTH THE LOX AND LH2 INTERNAL WIRE HARNESSES/MASTS THIS L02 LEVEL SENSOR FAILURE DOES NOT CONSTRAIN FUTURE LAUNCHES FOR THE FOLLOWING REASONS: IN ADDITION TO THE ACCEPTANCE TEST AT THE VENDOR'S FACILITY, ALL L02 LEVEL SENSORS MUST PASS AN ELEC- TRICAL ISOLATION RESISTANCE TEST DURING FINAL ASSEMBLY CHECKOUT AT MAF EXPERIENCE HAS DEMONSTRA- TED THAT THE CHECKOUT PROCEDURES AT MAF IS ADEQUATE TO IDENTIFY ANY DEFECTIVE SENSOR INSTALLED INTO THE SYSTEM THIS STATEMENT HAS BEEN APPROVED BY ET PROJECT MANAGER, G. P. BRIDWELL, REF. PROBLEM A09653. GENERAL A. BACKGROUND INFORMATION THE LOX AND LH2 LIQUID LEVEL SENSORS ARE IDENTICAL EXCEPT FOR THE TYPE OF FLUOROCARBON INSULATION USED ON THE WIRE LEADS. EACH SENSOR IS CONNECTED TO A SIGNAL CONDITIONER IN THE ORBITER. EACH SENSOR CIRCUIT IS CAPABLE OF GENERATING ONLY A "WET" OR "DRY" OUTPUT SIGNAL. AN ARRAY OF THESE POINT LEVEL SENSORS IS INSTALLED IN BOTH THE LOX AND LH2 TANKS TO MONITOR THE FLUID LEVELS. EACH SENSOR CONTAINS A FINE WIRE RESISTIVE ELEMENT. THE ORBITER SIGNAL CONDITIONER PROVIDES CURRENTTO HEAT THE ELEMENT. WHEN A SENSOR IS IMMERSED IN THE CRYOGENIC LIQUID PROPELLENT, THE COOLING OF THE ELEMENT IS DETECTED BY THE SIGNAL CONDITIONER WHICH PROVIDES A "WET" OUTPUT SIGNAL TO THE ORBITER. IN THE ET LOX TANK THERE IS ONE SENSOR AT THE 5% LEVEL AND SEVEN SENSORS BETWEEN THE 98% AND 3 LEVELS. ALL SEVEN OF THE SENSORS AT THE TOP/FORWARD END OF THE LOX TANK ARE MOUNTED ON A ALUMINUM TUBE KNOWN AS THE "FORWARD LOX MAST" THE MAST IS INSTALLED AS A COMPLETED SUBASSEMBLY DURING WORK PERFORMED IN THE MAF FINAL ASSEMBLY AREA. TASK I FAILURE INVESTIGATION A. 1 DURING IN-PROCESS ELECTRICAL TESTING OF THE FORWARD LOX LEVEL SENSOR MAST ON LWT-27, THE "100% MINUS LIQUID LEVEL" CIRCUIT HAD AN ISOLATION RESISTANCE OF LESS THAN THE REQUIRED FIVE MEGOHMS. FAILURE ANALYSIS FOUND THE PROBABLE CAUSE TO BE COLD FLOW OF THE TEFLON HEAT SHRINK TUBING INTERNAL TO THE SENSOR. THE INTERNAL STEEL TERMINALS HAD BEEN IMPROPERLY FORMED DURING ASSEMBLY AT THE VENDOR. THE TERMINALS FORCED THE OUTPUT LEAD WIRES AGAINST AN INTER- NAL LIP IN THE SENSOR HOUSING AND DAMAGED THE SHRINK TUBING INSULATION (REFERENCE MARS T-85671 AND T-82975). B. 1. THE LOX LEVEL SENSOR MAST WHICH HAD BEEN REMOVED FROM LWT-27, DUE TO FAILURE LISTED IN TASK I.A.1, WAS REPAIRED AND INSTALLED IN LWT-28. AFTER INSTALLATION, A LEVEL SENSOR MEASUREMENT CIRCUIT FAILED TO MEET THE FIVE MEGOHM ISOLATION RESISTANCE REQUIREMENT. THE MAST WAS RE- MOVED, THE FAILURE TRACED TO A LEVEL SENSOR, THE SENSOR WAS REPLACED AND THE MAST WAS REIN- STALLED IN LWT-28. THE CYCLE WAS REPEATED TWICE FOR A TOTAL OF THREE FAILED LEVEL SENSORS. FAILURE ANALYSES T-83880, T-83884, AND T-83888 FOUND THE PROBABLE CAUSE OF THE FAILURES TO BE THAT MOISTURE CONDENSED ON THE SENSORS DURING CLEANING THE LEVEL SENSOR MAST ASSEMBLY IS CLEANED WITH FREON TMC AND FREON PCA IN ORDER TO MEET THE CLEANLINESS REQUIREMENTS FOR USE IN A LOX ENVIRONMENT. EVAPORATION OF THE CLEANING SOLVENT CHILLS THE MAST BELOW THE DEW POINT AND MOISTURE CONDENSES ON IT. THE FIBERGLASS BRAID USED ON LOX TANK WIRE HARNESSES ACTS AS A WICK. THE BRAID CAN BECOME WET WITH WATER CONDENSED FROM THE AIR. 2. LWT-28 MET THE ISOLATION RESISTANCE REQUIREMENTS AFTER REPAIRS TO THE MAST, LISTED IN TASK I.B.1, WERE COMPLETED AND THE ET WAS MOVED TO BUILDING 420 FOR FINAL ACCEPTANCE TESTING. TWO LOX LEVEL SENSOR CIRCUITS FAILED TO MEET THE FIVE MEGOHMS ISOLATION RESISTANCE DURING ACCEP- TANCE TESTING. THE LOX TANK WAS CONNECTED TO A HEATED VENTILATION AIR PACK FOR FOUR DAYS. AT THE END OF THIS TIME, THE TWO DEFECTIVE ISOLATION RESISTANCE READINGS HAD INCREASED FROM APPROXIMATELY TWO MEGOHMS TO APPROXIMATELY EIGHTY MEGOHMS (REFERENCE MARS T-76354). 3. A LOX LEVEL SENSOR MAST FAILED AN IN-PROCESS ISOLATION RESISTANCE TEST IN FINAL ASSEMBLY PRIOR TO INSTALLATION IN LWT-30. FIVE OF THE SEVEN CIRCUITS HAD ISOLATION RESISTANCE VALUES BELOW FIVE MEGOHMS. AFTER FORCED AIR, HEATED TO APPROXIMATELY 100 DEGREES-F, WAS BLOWN OVER THE MAST FOR FOUR HOURS, ALL CIRCUITS WERE ABOVE 100 MEGOHMS (REFERENCE MARS T-86702). 4. A REVEIW OF PREVIOUS MOISTURE CAUSED ISOLATION RESISTANCE FAILURES OF LEVEL SENSOR CIRCUITS FOUND A SINGLE PREVIOUS OCCURRENCE THAT WAS SIMILAR TO THE FAILURES OF LWTS 27, 28, AND 30. AN AFT LOX LEVEL SENSOR MAST FAILED AN ISOLATION RESISTANCE TEST WHEN BEING INSTALLED ON LWT-11. WHEN TESTED AFTER EIGHT HOURS IN THE OPEN AIR, THE ISOLATION RESISTANCE WAS ACCEP- TABLE. THE ENGINEERING ANALYSIS FOUND THAT THE PROBABLE CAUSE WAS MOISTURE ON THE WIRING/ CONNECTOR FROM THE CLEANING PROCESS (REFERENCE MARS T-49783). 5. A REVIEW OF THE PROCEDURES AND EQUIPMENT USED TO PROVIDE DRY AIR TO THE INTERIOR OF THE PRO- PELLANT TANKS DURING ASSEMBLY OF THE ET FOUND NO DEFICIENCIES. THE "PURGE CARTS" ARE CERTI- FIED FOR HUMIDITY AND PARTICULATES. WHEN THE PURGE CARTS ARE NOT IN USE, DESICCANT BREATHERS ARE INSTALLED. THE BREATHERS HAVE HUMIDITY INDICATORS WHICH ARE CHECKED REGULARLY (REFERENCE INTEROFFICE MEMORANDUM 3743-85-231). TASK II CORRECTIVE ACTION 1 PROCESS INSTRUCTION 5008 WAS REVISED TO PROVIDE FORCED, HEATED, NITROGEN DRYING OF BOTH THE LOX AND LH2 INTERNAL WIRE HARNESSES/MASTS (REFERENCE INTEROFFICE MEMORANDUM 3693-87-HP-080). 2. THE CHANGES TO PI-5008 FOR THE LOX WIRE HARNESSES/MASTS WERE INCORPORATED INTO THE MANUFACTURING PROCESS PLANS (REFERENCE MPP 80932003709-029, PLANNING CHANGE LEVEL: NEW, 3/25/87; AND MPP 80931003769-059, PLANNING CHANGE LEVEL; NEW, 3/25/87. TASK III CLEARANCE OF EFFECTIVITIES THERE ARE NO CONSTRAINTS. THE FAILURES WERE DETECTED DURING TESTING AT MAF. THERE HAVE BEEN NO FAILURES AT KSC. ALL ETS ARE PURGED WITH DRY NITROGEN PRIOR TO SHIPMENT, WHICH PREVENTS MOISTURE RELATED FAILURES WITH THE PROPELLANT TANKS AT KSC. TASK IV CAPS CLOSURE SUMMARY SEVERAL LOX LEVEL SENSORS IN USE ON ETS AT MAF HAD A LOWER ISOLATION RESISTANCE THAN ACCEPTABLE. THE SECOND PROBLEM WAS THE RESULT OF INADEQUATE DRYING OF THE MAST/HARNESS ASSEMBLIES FOLLOWING CLEANING WITH FREON SOLVENTS. THE PROCESS INSTRUCTION FOR DRYING THE ASSEMBLIES WAS IMPROVED. 7/31/87 UPDATE STATUS - THE SENSOR S/N 361 WAS BUILT USING THE OLD TOOLING WHICH IN SOME ISOLATED CASES COULD ALLOW IMPROPERLY FORMED TERMINALS RESULTING IN THE LOW 1R READINGS AS NOTED IN CAPS E-093. PER TELECON WITH MR. ADAMS OF MMC, CN 5/27/87, HE STATED THE SENSOR S/N 391 WAS NOT IN- SPECTED FOR IMPROPERLY FORMED TERMINALS TO THE STANDARDS NOW IN USE SINCE THE FAILURE WAS CAUSED BY MOISTURE (REF FAILURE ANALYSIS T83888) THE SENSOR S/N 391 WILL BE SCRAPPED/REFURBISHED. ALL NEW SENSORS WILL BE MANUFACTURED UTILIZING THE NEW TOOL. ALL SENSORS ARE TESTED AT LEAST TWICE AFTER INSTALLATION AT MAF WHICH PROVIDES PROOF OF INSTALLATION RESISTANCE. MSFC STATEMENT: 8/7/87 - THE SENSORS NOW ON LWT-28 AND LWT-30 WERE FABRICATED WITHOUT A SPECIAL TOOL TO CONTROL THE FORMING OF THE TERMINALS AS DONE ON CURRENT BUILDS. THEREFORE, THE EXACT CAUSE OF THE FAILURES NOTED AFTER INSTALLATION IS NOT KNOWN AND COULD HAVE BEEN DUE TO MOISTURE, AS ASSESSED ABOVE, OR A COMBINATION OF TEFLON COLD FLOW AND MOISTURE. THE ADDITIONAL TESTS REQUIRED AT KSC, ALONG WITH THE BUILT-IN SYSTEM REDUNDANCY, SHOULD PREVENT ANY LAUNCH PROBLEMS. 8/17/87 - MMC CLOSURE SUMMARY SEVERL LOX LEVEL SENSORS IN USE ON ETS AT MAF HAD A LOWER ISOLATION RESISTANCE THAN IS ACCEPTABLE. THE PROBLEMS WERE THE RESULT OF TWO SEPARATE DEFICIENCIES. THE FIRST PROBLEM WAS CAUSED BY COLD FLOWING OF THE TEFLON SHRINK TUBING INSULATION ON THE INTERNAL WIRES OF THE SENSOR DUE TO IMPROPER ASSEMBLY AT THE VENDOR. THE VENDOR DEVELOPED A TOOL TO CORRECT THE ASSEMBLY OPERATION WHICH HAD CAUSED THE FAILURE. ALL SENSORS BUILT BEFORE THE USE OF THE FORMING TOOL FOR THE SENSOR INTERNAL TERMINALS PASSED ACCEPTANCE TESTS. THE CONDITION OF THE TEFLON TUBING IN THESE SENSORS, WHILE NOT KNOWN, IS ADEQUATE TO ASSURE OPERATION. THE SECOND PROBLEM WAS THE RESULT OF INADEQUATE DRYING OF THE MAST/HARNESS ASSEMBLIES FOLLOWING CLEANING WITH FREON SOLVENTS. THE PROCESS INSTRUCTION FOR DRYING THE ASSEMBLIES WAS IMPROVED. THERE ARE SUFFICIENT TESTS AT THE VENDOR, MAF, AND THE LAUNCH SITES TO DETECT SENSOR FAILURES. WHILE THE CAUSE OF THE ORIGINAL SENSOR FAILURES ON LWT-28 WAS CLEARLY IDENTIFIED AS MOISTURE AND THE LATER FAILURES ON LWTS 28 AND 30 INDICATED MOISTURE RELATED PROBLEMS, NO RESEARCH WAS PERFORMED TO CHARACTERIZE THE CONDITION OF THE SENSOR INTERNAL COMPONENTS, INCLUDING THE TERMINALS, AS THEY HAD NOT AFFECTED SENSOR ACCEPTABILITY. THE CAUSE OF FAILURES WERE IDENTIFIED AS (1) IMPROPERLY FORMED TERMINALS AND (2) MOISTURE IN THE MAST/HARNESS DUE TO CLEANING PROCESS. THE FIRST CAUSE IS ADDRESSED IN PROBLEM A09653. THE ABOVE IS A VERBATIM OF MMC CAPS E-093 A |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A10659 | IFA# -- | Contractor RPT# E-93-1 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 74L4-1 | Asmnt Part Name LOX LEVEL SENSOR | Asmnt Serial/Lot# 391 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD ETP - EI-TEST-INST | FAIL MODE UC - UNSAT |
| Asmnt FMEA 3.1.2.2 | Asmnt FM 2 | FMEA CSE A | FMEA SCSE 4 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |