# FISH PASSAGE

## PRACTICE INTRODUCTION

USDA, Natural Resources Conservation Service―Practice Code 396

### FISH PASSAGE

Fish passage is the modification or removal of barriers that restrict or prevent movement or migration of fish. A fish passage allows fish to move upstream and downstream.

### PRACTICE INFORMATION

The purpose of this practice is to allow upstream and downstream movement of fish past barriers where feasible or desirable.

This practice applies to all rivers, streams, and outlets of ponds or lakes where barriers impede desired fish passage. Modification or removal of barriers, particularly on large river systems, may significantly affect hydrology, for example, by creating impoundments or increasing seasonal inundation in the flood plain.
The context and intensity of these impacts must be considered when planning any project involving a fish passage.

### COMMON ASSOCIATED PRACTICES

Fish Passage is commonly used in a Conservation Management System with the following practices:

- Obstruction Removal (500)

- Riparian Forest Buffer (391)

- Streambank and Shoreline Protection (580)

- Stream Habitat Improvement Management (395)

Refer to the practice standard in the local Field Office Technical Guide and associated Job Sheets
for further information.

# Text boxes

Note:  Effects are qualified with a plus (+) or minus (-). These symbols indicate only an increase (+) or a decrease (-) in the effect upon the resource, not whether the effect is beneficial or adverse.

The scope of the practice implementation and resulting effects are limited to those described in the “initial setting.” Projects involving larger river systems, impoundment of waters, increased seasonal inundation of flood plains, or any other changes to the hydrologic system may need to be evaluated in a site-specific EA.

(-)

Start

Associated practice

I.11 (+/-) Availability of water for other uses

I.10 (+/-)

Ground water table

D.9 (-) Sedimentation

D.3 (+) Cost for installation and maintenance

I.1 (+) Upstream and downstream movement of fish and other aquatic species

(+)

C.1 (+) Biodiversity

I.12 (-) Net return

C.4 (+/-) Water quality

I.7 (+/-) Water supply

I.3 (+) Population/recovery of target species

Streambank and Shoreline Protection (580)

I.8 (+/-) Channel/shoreline/ streambank erosion

Mitigating practice

(+) increase; (-) decrease

Pathway

C.  Cumulative effect

I.  Indirect effect

D.  Direct effect

#.  Created by practice

LEGEND

I.6 (+/-) Flows in water course

Fish Passage

4/2007

D.1 (+) Habitat connectivity; (-) fragmentation

Initial setting: Small rivers, streams, and outlets of ponds or lakes where barriers impede desired fish passage.  Removal of barriers or replacement of small structures will result in improved fish passage without significant changes to the hydrology of the system, such as impoundment of waters or increased seasonal inundation of flood plains

I.2 (+) Use of habitat by target species

C.3 (+/-) Income and income stability (individuals and community)

I.4 (+) Use of habitat by nontarget species

D.2 (+/-) Water quantity

I.5 (+) Population of nontarget species

C.2 (+/-) Recreational opportunities

1. Unrestricted pathway for migratory fish

Fish Passage (396)