423-44-01

Interface Control Document

between the Goddard Earth Sciences Data and Information Services Center (GES DISC) Simple, Scalable Script-based Science Processor Archive (S4PA) and the Science

System Element (SSE)

Interface Mechanisms

February 2007

Expires: February 2012

This page intentionally left blank.

Interface Control Document between the Goddard Earth Sciences Data and Information Services Center (GES DISC) Simple, Scalable Script-based Science Processor Archive (S4PA) and the Science System Element (SSE)

Interface Mechanisms

February 2007

Reviewed by:

| Karen Michael EOSDIS Project System Manager GSFC Code 586 |  | Date |
| --- | --- | --- |

| Steve Kempler GES DISC Manager GSFC Code 610 |  | Date |
| --- | --- | --- |

Approved by:

| Hampapuram K. Ramapriyan ESDIS Assistant Project Manager GSFC Code 423 |  | Date |
| --- | --- | --- |
| Mary Ann Esfandiari ESDIS Project Manager GSFC Code 423 |  | Date |

Goddard Space Flight Center

Greenbelt, Maryland

This page intentionally left blank.

# Preface

This document is under ESDIS Project configuration control. Once this document is approved, ESDIS approved changes are handled in accordance with Class I and Class II change control requirements described in the ESDIS Configuration Management Procedures, and changes to this document shall be made by document change notice (DCN) or by complete revision.

Any questions should be addressed to:

ESDIS Configuration Management Office
NASA/GSFC

Code 423

Greenbelt, Md. 20771

This page intentionally left blank.

# Abstract

This document provides the implementation specifications for the S4PA-SSE interface requirements maintained and controlled in ESDIS document 423-42-03, Interface Responsibilities for Standard Product Generation Using Science Investigator-Led Processing Systems.

This document specifies interface mechanisms, filenaming conventions and handshaking message formats for data exchange between the Goddard Earth Sciences Data and Information Services (GES DISC) Simple, Scalable Script-based Science Processor Archive (S4PA) and the Science System Element (SSE) interfaces. The term SSE is a generic term that includes any element that provides or receives data which is used in science data processing or distribution. The SSE's include the Science Investigator-led Processing Systems (SIPS), Distributed Active Archive Centers (DAACs), MODIS Data Processing System (MODAPS), the OMI Dutch Processing System (ODPS), the Global Modeling and Assimilation Office (GMAO) as well as other systems to be added as appropriate to this document. These data exchanges include transfer of data files from GES DISC S4PA to the SSE for standard product generation, transfer of metadata configuration files from GES DISC S4PA to the SSE to support standard product metadata generation, and transfer of the SSE standard products, algorithm packages, metadata, ancillary data, and QA data to GES DISC S4PA. The SSE may also produce EOS special products and pass them to the GES DISC S4PA for archiving and distribution using these same mechanisms.

Information specific to each SSE is also published in this ICD. At a minimum, the ICD will include brief descriptions of the SSE and its mission, context information for the GES DISC S4PA-SSE interface, lists of data types with volume and frequency specifications, and any SSE-unique GES DISC S4PA-SSE requirements.

Keywords: checksum, metadata, secure, distribution, gateway, ingest, interface, polling, standard products, reprocessing, subscription, SSE, XML

This page intentionally left blank.

Change Record Page

| ISSUE | RELEASE DATE | PAGES AFFECTED | DESCRIPTION |
| --- | --- | --- | --- |
| Baseline | TBD | All | CCR 423-44-01-001 |

This page intentionally left blank.

List of Affected Pages

| Page No. | Revision | Page No. | Revision | Page No. | Revision | Page No. | Revision |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Title | Original | 4-10 | Original | 5-12 | Original |  |  |
| i | Original | 4-11 | Original | 5-13 | Original |  |  |
| ii | Original | 4-12 | Original | 5-14 | Original |  |  |
| iii | Original | 4-13 | Original | 5-15 | Original |  |  |
| iv | Original | 4-14 | Original | 5-16 | Original |  |  |
| v | Original | 4-15 | Original | 5-17 | Original |  |  |
| vi | Original | 4-16 | Original | 5-18 | Original |  |  |
| vii | Original | 4-17 | Original | 5-19 | Original |  |  |
| viii | Original | 4-18 | Original | 5-20 | Original |  |  |
| ix | Original | 4-19 | Original | 5-21 | Original |  |  |
| x | Original | 4-20 | Original | 5-22 | Original |  |  |
| xi | Original | 4-21 | Original | 5-23 | Original |  |  |
| xii | Original | 4-22 | Original | 5-24 | Original |  |  |
| xiii | Original | 4-23 | Original | 5-25 | Original |  |  |
| xiv | Original | 4-24 | Original | 5-26 | Original |  |  |
| 1-1 | Original | 4-25 | Original | 5-27 | Original |  |  |
| 1-2 | Original | 4-26 | Original | 5-28 | Original |  |  |
| 1-3 | Original | 4-27 | Original | 5-29 | Original |  |  |
| 1-4 | Original | 4-28 | Original | 5-30 | Original |  |  |
| 2-1 | Original | 4-29 | Original | 5-31 | Original |  |  |
| 2-2 | Original | 4-30 | Original | 5-32 | Original |  |  |
| 2-3 | Original | 4-31 | Original | AB-1 | Original |  |  |
| 2-4 | Original | 4-32 | Original | AB-2 | Original |  |  |
| 3-1 | Original | 5-1 | Original | AB-3 | Original |  |  |
| 3-2 | Original | 5-2 | Original | AB-4 | Original |  |  |
| 4-1 | Original | 5-3 | Original | AB-5 | Original |  |  |
| 4-2 | Original | 5-4 | Original | AB-6 | Original |  |  |
| 4-3 | Original | 5-5 | Original | AB-7 | Original |  |  |
| 4-4 | Original | 5-6 | Original | AB-8 | Original |  |  |
| 4-5 | Original | 5-7 | Original |  |  |  |  |
| 4-6 | Original | 5-8 | Original |  |  |  |  |
| 4-7 | Original | 5-9 | Original |  |  |  |  |
| 4-8 | Original | 5-10 | Original |  |  |  |  |
| 4-9 | Original | 5-11 | Original |  |  |  |  |

This page intentionally left blank.

# Contents

Preface

Abstract

1.  Introduction

1.1	Identification	1-1

1.2	Scope	1-1

1.3	Purpose	1-2

1.4	Change Control	1-2

1.5	Organization	1-2

2.  Related Documentation

2.1	Parent Documents	2-1

2.2	Applicable Documents	2-1

2.3	Information Documents	2-2

2.3.1	Information Documents Referenced	2-2

2.3.2	Information Documents Not Referenced	2-3

3.  Interface Overview

3.1	Summary of Data Flows	3-1

4.  Data Exchange Framework

4.1	Internetworking Protocols and Network Topology	4-11

4.1.1	Transport Layer Protocol	4-11

4.1.2	Network Layer Protocols	4-11

4.1.3	Physical/Datalink Protocols	4-22

4.2	Communications Protocols	4-22

4.2.1	Simple Mail Transport Protocol	4-22

4.2.2	File Transfer Protocol	4-22

4.2.3	Secure File Transfer Protocol	4-22

4.2.4	HyperText Transfer Protocol	4-2

4.3	Subscriptions for Requesting Level 0 and Ancillary Data	4-33

4.3.1	Subscription Request	4-33

4.3.2	Subscription Request Acknowledgment	4-55

4.3.3	Subscription Update	4-55

4.3.4	Subscription Cancellation	4-66

4.3.5	Data Distribution	4-77

4.4	Metadata Associated with SSE-Produced Collections	4-1144

4.5	Transfer of Higher-Level Products to S4PA	4-1155

4.5.1	Overview of Polling Ingest Methodology	4-1155

4.5.2	PDR File Naming Convention	4-1717

4.5.3	Product Delivery Record (PDR)	4-1818

4.5.4	Product Delivery Record Discrepancy (PDRD)	4-23

4.5.5	Production Acceptance Notification (PAN)	4-2626

4.5.6	SSE-S4PA Electronic Data Exchange Error Handling/Back-up Methods	4-2929

4.6	Accessing Archived Data for Reprocessing	4-3030

4.7	Data Exchange Security	4-3030

4.7.1	Encryption	4-3030

4.7.2	Secure Ingest	4-3131

4.7.3	Secure Distribution	4-3131

5.  SSE Data and Metadata

5.1	S4PA Datatypes	5-1

5.2	Metadata	5-1

5.2.1	Metadata Files for S4PA Ingest	5-1

5.2.2	Checksums in Distributed Metadata	5-2

5.3	Unique Granule Identification	5-2

5.3.1	LocalGranuleID Format	5-2

5.3.2	S4PA Use of LocalGranuleID	5-3

5.4	Granule Cross References	5-3

5.4.1	InputPointer Format	5-3

5.5	File Transfer Quick Reference Summary  ……………………………………………...5-5

5.6	XML Schema for S4PA Granule Level Metadata………………………………………5-5

Abbreviations and Acronyms

Appendix A.  Microwave Limb Sounder (MLS) Data Flows (TBS)

Appendix B.  High  Resolution Dynamics Limb Sounder (HIRDLS) Data Flows (TBS)

Appendix C.  Ozone Monitoring Instrument (OMI) Data Flows (TBS)

Appendix D.  OMI Dutch Processing System (ODPS) Data Flows (TBS)

Appendix E.  Atmospheric InfraRed Sounder (AIRS) Data Flows (TBS)

Appendix F.  SOlar Radiation and Climate Experiment (SORCE) Data Flows (TBS)

Appendix G.  Atmospheric Sciences Data Center (ASDC) Data Flows (TBS)

Appendix H.  Global Modeling Assimilation Office (GMAO) Data Flows (TBS)

Appendix I.  MODIS Data Processing System (MODAPS) Data Flows (TBS)

Appendix J.  Land Processing DAAC (LP DAAC) Data Flows (TBS)

Appendix K. National Snow and Ice Data Center (NSIDC) Data Flows (TBS)

Figures

Figure 4.3.5-1.  Example Distribution Notice for a Subscription FTP or SFTP Request	4-12

Figure 4.3.5-2.  Example Distribution Notice for a List orURLs	4-12

Figure 4.3.5-3.  Example Distribution Notice for HTTP Request	4-13

Figure 4.5-1.  Polling with Delivery Record File Transfer Mechanism	4-17

Figure 4.5-2.  Example PDR File Naming Convention	4-18

Figure 4.5-3.  Example PDR PVL File	4-23

Figure 4.5-4.  Example Short PDRD PVL	4-24

Figure 4.5-5.  Example Long PDRD PVL	4-26

Figure 4.5-6.  ExampleShort PAN PVL	4-27

Figure 4.5-7.  Example Long PAN PVL	4-29

Figure 5-1.  Example InputPointer LGID Reference Format	5-4

Figure 5-2.  S4PA Granule Level Metadata	5-30

Figure 5-3.  Example S4PA ODL Metadata File	5-32

Tables

Table 3-1.  S4PA and SSE Interface Overview	3-2

Table 4.3.1-1.  E-Mail Subscription Request Format	4-4

Table 4.3.2-1.  Format of Subscription Request Acknowledgement 	4-5

Table 4.3.3-1.  Subscription Update Format 	4-6

Table 4.3.4-1.  Subscription Cancellation Format 	4-6

Table 4.3.5-1.  Distribution Notice Contents (1 of 3) 	4-8

Table 4.3.5-1.  Distribution Notice Contents (2 of 3) 	4-9

Table 4.3.5-1.  Distribution Notice Contents (3 of 3)	4-10

Table 4.5-1.  Example File Naming Convention forSSE Product Delivery Record	4-18

Table 4.5-2.  Product Delivery Record PVL Parameters (1 of 3)	4-20

Table 4.5-2.  Product Delivery Record PVL Parameters (2 of 3)	4-21

Table 4.5-2.  Product Delivery Record PVL Parameters (3 of 3)	4-22

Table 4.5-3.  Short Product Delivery Record Discrepancy PVL Parameters	4-24

Table 4.5-4.  Long Product Delivery Record Discrepancy PVL Parameters	4-25

Table 4.5-5.  Short Production Acceptance Notification PVL Parameters	4-27

Table 4.5-6.  Long Production Acceptance Notification PVL Parameters (1 of 2)	4-27

Table 4.5-6.  Long Production Acceptance Notification PVL Parameters (2 of 2)	4-28

# 1.  Introduction

## 1.1	Identification

This Interface Control Document (ICD) is based on the ICD between EOSDIS Core System (ECS) and the SIPS, Volume 0, Interface Mechanisms and is intended as a replacement of that document for the interfaces to the GES DISC S4PA. The goal is to make the transition from ECS to S4PA at the GES DISC transparent to all data providers.

## 1.2	Scope

This document specifies the interface design between S4PA and the SSE interfaces. It includes specifications for data exchange between the GES DISC S4PA and the Science System Elements that fall under the following topics:

1.	Internetworking

2.	Interface mechanisms

3.	Filenaming conventions

4.	Handshaking message formats

5.	Error handling and fallback procedures

6.	Security

Data exchanges addressed include --

a. 	Transfer of data from S4PA to the SSE for standard product generation, and

b.	Transfer to S4PA of the SSE standard products and other files resulting from or associated with the SSE standard product generation.

Also addressed are special services to ensure that data granules received from the SSE are associated with defined collections in the archives.

The SSE may also produce EOS special products and use these same mechanisms to pass them to the S4PA for archiving and distribution.

The SSE may employ the S4PA Machine Request Interface (MRI) to search and retrieve data from the S4PA archives for use in reprocessing by the SSE. Specifications and instructions for the MRI are found at http://discapps.gsfc.nasa.gov/wiki/Machine_Request_Interface.

Certain implementation details are not suitable for, or specified in, this document.  Such items as contact address, telephone or fax numbers, internet host id's, values for operator tunable parameters such as number of retries on failure or timeouts should be documented in an Operations Agreement or Operations Procedures document under the control of the DISC and with concurrence of the SSE.  The term "Operations Agreement(s)" in this document refers to such a document.

The Earth Science Data and Information System (ESDIS) Project has responsibility for the development and maintenance of this ICD. Any changes in the interface requirements must be agreed to, and assessed at the ESDIS Project Level. This ICD is approved under the signature of the ESDIS Project Manager.

## 1.3	Purpose

This document is written to formalize the interpretation and general understanding of the interfaces between S4PA and the SSE. This volume provides clarification and elaboration of those interfaces to the extent necessary to assure hardware, software, and operational service compatibility within the end-to-end system. The SSE-unique interface specifications may be found in the SSE-specific appendix of this ICD. This document provides a point of mutual control of external interface definitions via the ESDIS Configuration Control Board (CCB).

## 1.4	Change Control

Changes to this ICD may be submitted for consideration by the DISC, SSE and ESDIS CCB under the normal change process at any time. Changes to the main volume of this ICD will need to be reviewed and approved by all SSEs. Changes to an SSE-unique appendix will only need to be reviewed and approved by that SSE.

## 1.5	Organization

Section 1 provides information regarding the identification, scope, purpose, and organization of this document.

Section 2 lists related non-SSE-unique documents that were used as sources of information for this document or that provide additional background information to aid understanding of the interface implementations. The SSE-unique documents are identified in the SSE appendix of this ICD.

Section 3 is an overview of the interfaces for data exchange between S4PA and the SSE.

Section 4 is a detailed presentation of the data exchange framework for S4PA-SSE interfaces. Again, this is limited to implementation information applicable to any SSE. Specifically, the following topics are discussed: applicable internetworking protocols, data transfer methodologies, error conditions and error handling, backup methods, and data exchange security.

Section 5 explains some critical requirements for providing data and metadata to the S4PA. It contains guidelines that must be followed to ensure the interfaces function and is not intended to be a comprehensive discussion of S4PA data and metadata. Additionally, a quick reference summary of the characteristics of the polling with delivery record mechanism for the SSE interface and information on the S4PA metadata model are provided. A list of abbreviations and acronyms is also provided.

Appendix A contains the Microwave Limb Sounder (MLS) Data Flows (TBS).

Appendix B contains the High Resolution Dynamics Limb Sounder (HIRDLS) Data Flows (TBS).

Appendix C contains the Ozone Monitoring Instrument (OMI) Data Flows (TBS).

Appendix D contains the OMI Dutch Processing System (ODPS) Data Flows (TBS).

Appendix E contains the Atmospheric InfraRed Sounder (AIRS) Data Flows (TBS).

Appendix F contains the SOlar Radiation and Climate Experiment (SORCE) Data Flows (TBS).

Appendix G contains the Atmospheric Sciences Data Center (ASDC) Data Flows (TBS).

Appendix H contains the Global Modeling Assimilation Office (GMAO) Data Flows (TBS).

Appendix I contains MODIS Data Processing System (MODAPS) Data Flows (TBS).

Appendix J contains Land Processing DAAC (LP DAAC) Data Flows (TBS).

Appendix K contains National Snow and Ice Data Center (NSIDC) Data Flows (TBS).

This page intentionally left blank.

# 2.  Related Documentation

The latest versions of all documents below should be used. The latest ESDIS Project documents can be obtained from URL: https://romulus.gsfc.nasa.gov/htbin/cm/emdshome.cgi. ESDIS documents have a document number starting with either 423 or 505. The latest EOSDIS Core System (ECS) documents can be obtained from URL: http//edhs1.gsfc.nasa.gov/.

## 2.1	Parent Documents

The parent document is the document from which this interface control document’s scope and content are derived.

423-10-69	Requirements for Archiving, Distribution and User Services in EOS Data and Information System (EOSDIS)

423-42-03	Goddard Space Flight Center, Interface Responsibilities for Standard Product Generation Using Science Investigator-led Processing Systems (SIPS)

## 2.2	Applicable Documents

The following documents are referenced within this interface control document, or are directly applicable, or contain policies or other directive matters that are binding upon the content of this volume.

| 160-TP-013 | The Role of Metadata in EOSDIS |
| --- | --- |
| 170-TP-510-001 | EOSDIS Core System Project, HDF-EOS Library User’s Guide for the ECS Project, Volume 1: Overview and Examples |
| 170-TP-511-001 | EOSDIS Core System Project, HDF-EOS Library Users Guide for the ECS Project, Volume 2: Function Reference Guide. |
| 333-CD-510-001 | EOSDIS Core System Project, Release (1) SDP Toolkit Users Guide for the ECS Project. |
| 423-41-64 | ESDIS Project Requirements for EOS Instrument Team Science Data Processing Systems |
| 423-41-67 | Data Format Control Document for NCEP Stratosphere Analysis Combined Product |
| 423-41-56 | Interface Control Document between EOSDIS Core System (ECS) and the Data Assimilation System (DAS) |
| 423-35-10 | Interface Control Document (ICD) Between the Earth Observing System (EOS) Networks and the Science Investigator-led Processing Systems (SIPS) for Aura Instruments |
| 505-10-20 | System Interface Control Plan for the Earth Science Data and Information System (ESDIS) Project |

## 2.3	Information Documents

### 2.3.1	Information Documents Referenced

The following documents are referenced herein and, amplify or clarify the information presented in this document. These documents are not binding on the content of this document.

420-TP-016-003	Backus-Naur Format (BNF) Representation of the B.0 Earth Science Data Model

ISO 7498	International Organization for Standardization, Basic Reference Model for Systems Interconnection

RFC 791	Postel, J. Internet Protocol, Sep-01-1981, (Status: STANDARD)

RFC 793	Postel, J. Transmission Control Protocol, Sep-01-1981, (Status: STANDARD)

RFC 821	Postel, J. Simple Mail Transfer Protocol, Aug-01-1982, (Status: STANDARD)

RFC 0959	Postel, J. & J.K. Reynolds, File Transfer Protocol, Oct-01-1985, (Status: STANDARD)

RFC 1321	Rivest, R., The MD5 Message-Digest Algorithm, April 1992

RFC 2616 	Fielding, R. et al Hypertext Transfer Protocol, Jun-01-1999, (Status: STANDARD)

CCSDS 641.0-B-l	Consultative Committee for Space Data Systems (CCSDS), Recommendation for Space Data System Standards: PVLSPEC - Parameter Value Language Specification, 5/92 (http://www.ccsds.org/blue_books.html)

JPL D-7669, Part-2.	Planetary Data System Standards Reference, Version 3.2, Chapter 12: Object Description Language (ODL) Specification and Usage, July 24, 1995 (http://pds.jpl.nasa.gov/stdref/stdref.htm)

### 2.3.2	Information Documents Not Referenced

The following documents, although not referenced herein and/or not directly applicable, do amplify or clarify the information presented in this document. These documents are not binding on the content of this document.

170-TP-005	HDF-EOS Library User’s Guide, Volume 1, Overview & Examples

170-TP-006	HDF-EOS Library User’s Guide, Volume 2, Function and Reference Guide

420-TD-069	ODL Restrictions, ECS Specific and ODL Library Specific

| 505-41-33 | Interface Control Document Between EOSDIS Core System (ECS) and Science Computing Facilities (SCF). |
| --- | --- |
| 423-ICD-EDOS/EGS | Interface Control Document between EDOS and EOS Ground System (EGS). |

This page intentionally left blank.

# 3.  Interface Overview

## 3.1	Summary of Data Flows

Table 3-1 summarizes the data flows between S4PA and the SSE that are specified in Section 4. The table shows three categories of data exchange interfaces.

1.  In response to standing requests (subscriptions) from an SSE, S4PA sends Distribution Notices (DNs) and data files, including Level 0 data, ancillary data and orbit and attitude data.

2.  Nominally the SSE provides metadata and standard product data granules to the S4PA via a standardized electronic polling with delivery record mechanism. The SSE may elect to send browse data, ancillary data, QA granules, algorithm package TAR files as appropriate to the S4PA. Each delivered granule is accompanied by metadata that conforms to the minimal metadata requirements of S4PA. (See Section 5.2)

3.  The SSE searches for and retrieves data for reprocessing from the S4PA via the MRI, FTP or HTTP. Specifications and instructions for the MRI are found at http://discapps.gsfc.nasa.gov/wiki/Machine_Request_Interface.

In the table below, the Destination "SSE" is a location designated by the SSE. The methods or procedures that the SSE uses to interact with this staging location are not under the control of this document.

Also, the table assumes an electronic interface for delivery of products from the SSE. The transfer mechanisms utilized by the S4PA are email, File Transfer Protocol (FTP), Secure File Transfer Protocol (SFTP), and HyperText Transfer Protocol (HTTP).

Table 3-1.  S4PA and SSE Interface Overview

| Item No. | Source | Destination | Message | Data | Transfer Mechanism |
| --- | --- | --- | --- | --- | --- |
| Subscription transfer of Products from S4PA to SSE |
| 1 | SSE | S4PA | Data Subscription Request | N/A | e-mail |
| 1a | SSE | S4PA | Subscription Update | N/A | e-mail |
| 1b | SSE | S4PA | Subscription Cancellation | N/A | e-mail |
| 2 | S4PA | SSE | Subscription Acknowledgment | N/A | e-mail |
| 3 | S4PA | SSE | N/A | Newly ingested data from S4PA archive needed for Higher Level Standard Product generation. | S4PA standard distribution options (FTP or SFTP push, FTP pull) as supported by the DISC |
| 4 | S4PA | SSE | Distribution Notice | N/A | e-mail, FTP or SFTP push |
| Polling with Delivery Record Ingest |
| 5 | SSE | S4PA | Product Delivery Record (PDR) | N/A | Polling interface. FTP or SFTP Pull initiated by S4PA |
| 6 | SSE | S4PA | N/A | S4PA-compatible Metadata File for each granule transferred | FTP or SFTP Pull initiated by S4PA |
| 7 | SSE | S4PA | N/A | Higher Level Standard Products | FTP or SFTP Pull initiated by S4PA |
| 8 | SSE | S4PA | N/A | Browse Data files | FTP or SFTP Pull initiated by S4PA |
| 9 | SSE | S4PA | N/A | Ancillary Data | FTP or SFTP Pull initiated by S4PA |
| 10 | SSE | S4PA | N/A | QA Granules | FTP or SFTP Pull initiated by S4PA |
| 11 | SSE | S4PA | N/A | Algorithm Package TAR files | FTP or SFTP Pull initiated by S4PA |
| 12 | SSE | S4PA | Product Delivery Record Discrepancy (PDRD) (Short/Long) | N/A | FTP Push or e-mail initiated by S4PA |
| 13 | S4PA | SSE | Production Acceptance Notification (PAN) (Short/Long) | N/A | FTP Push or e-mail initiated by S4PA |
| SSE Reprocessing "Gateway" |
| 14 | SSE | S4PA | Searches for and Pulls archived data | N/A | MRI, FTP or HTTP |
| 15 | S4PA | SSE | N/A | Data from S4PA archive needed for reprocessing | MRI, FTP Pull or HTTP Pull |

# 4.  Data Exchange Framework

## 4.1	Internetworking Protocols and Network Topology

GES DISC S4PA provides internetworking services that are based on protocols and standards corresponding to layers 1 through 4 of the Open Systems Interconnection (OSI) Reference Model. These include, respectively, the physical, datalink, network, and transport layers. The transport layer protocol provides data consistency functions. The network, datalink and physical layers play significant roles in defining external interfaces (i.e., between S4PA and non-S4PA networks/systems). In particular, GES DISC S4PA routers provide the physical demarcation points between S4PA networks and external networks/systems. The routing software resident on the routers provides network layer services, while the interfaces on the router make up the datalink/physical layers.

### 4.1.1	Transport Layer Protocol

The transport layer protocol used for communications between GES DISC S4PA processes and non-S4PA processes is the Transmission Control Protocol (TCP) specified in RFC 793. TCP is a reliable connection-oriented, end-to-end protocol designed to fit into a layered hierarchy of protocols that support multi-network applications. It provides for reliable inter-process communication between pairs of processes in host computers attached to networks within and outside of GES DISC S4PA.

The interface between TCP and an application process consists of a set of calls much like the calls an operating system provides to an application process for manipulating files. For example, there are calls to open and close connections and to send and receive data on established connections.

### 4.1.2	Network Layer Protocols

The network layer provides the functional and procedural means to exchange network data units (i.e., packets) between devices over network connections, both for connection-mode and connectionless-mode communications. It relieves the transport layer of any concern regarding routing and relay operations associated with network connection. The basic function of the network layer is to provide the transparent transfer of data between devices. It should be noted that the network layer delivers packets only to a device, not an individual process. It remains up to the transport layer protocol to include, beforehand, the additional information needed to permit addressing to an individual process. Network layer protocols supported by GES DISC S4PA networks include Internet Protocol (IP) plus various routing protocols.

4.1.2.1	Internet Protocol (IP)

The Internet Protocol (IP), specified in RFC 791 is the network protocol that GES DISC S4PA supports, based on its dominance in industry usage and wide-community support. As part of IP support, Internet Control Message Protocol (ICMP) and Address Resolution Protocol (ARP) are also supported. As the Internet Engineering Task Force (IETF) specified new generation IP becomes available for deployment, it will be supported by GES DISC S4PA networks.

4.1.2.2	Routing

GES DISC S4PA generally uses Routing Information Protocol (RIP) for route exchanges with external networks. Other more robust routing protocols such as Border Gateway Protocol (BGP-4) can also be used depending on the need and center routing policies.

### 4.1.3	Physical/Datalink Protocols

Physical and Datalink protocols may differ among the various GES DISC S4PA-SSE interfaces, so detailed information may be found in the SSE-unique appendix for each SSE.

## 4.2	Communications Protocols

GES DISC S4PA provides various communications services that are based on protocols and standards corresponding to the applications level of the Open Systems Interconnection (OSI) Reference Model. Four of these services are the Simple Mail Transport Protocol (SMTP), File Transfer Protocol (FTP), Secure File Transfer Protocol (SFTP), and HyperText Transfer Protocol (HTTP).

### 4.2.1 	Simple Mail Transport Protocol

All electronic mail (e-mail) message exchange is achieved through the use of Internet e-mail messages. The protocol for Internet e-mail transfer is the Simple Mail Transfer Protocol (SMTP) defined in RFC 821.

### 4.2.2 	File Transfer Protocol

File transfers between GES DISC S4PA and the external provider host computers are accomplished through the use of standard File Transfer Protocol (FTP). FTP, as described in RFC 959, is an Internet standard for file transfers that support downloading of files by a user (acting as a client) from a remote server.

### Secure File Transfer Protocol

The GES DISC S4PA supports secure file transfer via the Secure FTP (SFTP) application in the Secure SHell (SSH) suite. Secure SHell is a suite of TCP/IP-based applications supporting secure remote access, file transfer and data tunneling. It uses public key authentication and passwords are encrypted. It provides strong encryption in a client-server architecture.

### 4.2.4	HyperText Transfer Protocol

Outbound file transfers from the GES DISC S4PA to external data customers are also accomplished through the use of HyperText Transfer Protocol (HTTP). HTTP, as described in RFC 2616, is an Internet standard that allows access to resources (data) by a user (acting as a client) from distributed applications on the World Wide Web. S4PA uses HTTP primarily for access to restricted data that requires user authentication (username and password) through a web browser.

## 4.3	Subscriptions for Requesting Level 0 and Ancillary Data

GES DISC S4PA receives Level 0 data from EDOS or another participating Mission Operations Center and archives it in S4PA. S4PA also receives and archives ancillary and orbit and attitude data needed by the SSE for producing higher-level products. Each SSE obtains these data or any other data routinely ingested by the S4PA that is required for EOS standard product generation through the S4PA Subscription Service. A subscription is a standing request to the S4PA subscription service for data expected to be archived. A subscription for Level 0 or Ancillary data, for example, may be triggered by the insert of a new granule of the given data type into the S4PA archive. However, a mechanism will be provided for requesting shipment of missed or lost subscription data.

### 4.3.1	Subscription Request

Typically, the SSE operator e-mails a subscription request for each data type to the GES DISC operator, who registers each subscription on behalf of the SSE. Table 4.3.1-1 is a suggested format for the SSE to use for supplying e-mail subscription requests to the DISC operator. The format of the notice and the distribution method should be agreed-on with the DISC. The DISC operator may respond with a subscription request acknowledgment (see Section 4.3.2).

How the User ID and password for FTP Push deliveries are furnished to the DISC should be agreed on with DISC User Services. Accounts for secure distribution (SFTP; see Section 4.7.3) must be arranged with the DISC in advance.

Table 4.3.1-1.  E-Mail Subscription Request Format

| Message Field | Description | Type | Format/ Size1 (bytes) | Value or Content with Value |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Subject of email message | Subject of message identifies the purpose of the message | Variable String | ASCII (255 B) | e.g., ‘L0 Data Subscription Request’ |  |  |
| Note: the following rows define the body of the email message. |  |  |
| USERSTRING | SSE-provided text uniquely describing the event for which a subscription is requested. If the request includes a distribution option this text will be included in the distribution notice for the delivery. | Variable String | ASCII (255 B including 237 B of free text) 1 | ‘USERSTRING: <free text>’ 2 |  |  |
| Datatype Shortname | S4PA defined Short Name of the S4PA Dataset. | Fixed String | ASCII (18 B including 12 B for <Datatype> and <version>)1 | ‘Datatype’ 2 |  |  |
| Datatype Version (optional) | S4PA defined version of the S4PA dataset | Fixed String | ASCII | “Version” |  |  |
| FTP Push (optional) | Include to request that the associated granule be pushed to the SSE automatically when the event is triggered. | Fixed String | ASCII (16 B) | ‘FTP Push: Enable’ |  |  |
| sftp (optional) | Granules and distribution notice are both pushed to a designated SSE host using Secure FTP. See Section 4.7 for conditions for using this distribution type. | Fixed String | ASCII (11 B) | ‘sftp: Enable’ |  |  |
| FTP Host (required only with FTP Push or sftp) | Host Name to which the granule is to be pushed. | Variable String | ASCII (89 B) | e.g., ‘FTP Host: cloud.jpl.nasa.gov’ |  |  |
| FTP Destination (required only with FTP Push or sftp) | Directory Location to which the granule (and, for sftp, distribution notice) should be pushed. | Variable String | ASCII (1040 B)3 | e.g., ‘FTP Destination: /usr/xx/yy/’ |  |  |
| start date | Instruction for subscription to begin on and include the specified start date. | Fixed String | ASCII (28 B) | ‘start date: MM/DD/YYYY-HH:MM’ |  |  |
| expiration date | Instruction for subscription to include and end on the specified expiration date. | Fixed String | ASCII (33 B) | ‘expiration date: MM/DD/YYYY-HH:MM’ |  |  |
| Qualifier Statement (optional) | A freeform text string containing a set of one or more logical comparison statements ANDed together. Temporal qualifiers are currently supported. Additional qualifications will be implemented at request of the SSE, given at least one month's notice. | Variable String | ASCII (1024 B) |  |  |  |

1Field length includes a content category, a colon, 1 blank, and a value string.

2Angle brackets (“<” and “>”) enclose user-provided information (userid, Datatype, and free text).

3FTP Destination consists of path name and file name, in which the path cannot exceed 254B and total cannot exceed 1040B.

### 4.3.2	Subscription Request Acknowledgment

The DISC operators use the subscription acknowledgment email to confirm receipt of a new subscription request or update or cancellation of an existing subscription. The format and content of the Subscription Request Acknowledgment are defined in Table 4.3.2-1.  The original request message is retained for possible future reference. These email messages are created manually by a DISC operator.

Table 4.3.2-1.  Format of Subscription Request Acknowledgment1

| Message Field | Description | Type | Format/ Max Size (Bytes) | Content with Value |
| --- | --- | --- | --- | --- |
| Email Subject | Describes purpose of message. | Variable String | ASCII (256 B) | ‘Data Subscription Request Acknowledgment’ |
| All fields as in primary message | The original Subscription Request/Update/Cancel Email message fields are included for reference | Variable String | ASCII (2812 B) | N/A |
| Status | DISC operator provided text indicating the results of the attempt to insert, update, or cancel a subscription. | Variable String | ASCII (256 B) 2 | ‘status: accepted’ OR ‘status: failed; <free text>’ example of <free text>: matching subscribable event description could not be found |
| SubscriptionID | The ID generated by the S4PA when the subscription is successfully entered. Used for subscription cancellations or updates via Email to the DISC Operator. | Fixed String | ASCII (24 B) 2 | ‘SubscriptionID: NNNNNNNN’, where NNNNNNNN is an integer |

1This table defines contents in addition to the contents of the preceding request message.

2This field length includes a content category, a colon, 1 blank, and a value string.

### 4.3.3	Subscription Update

Update of an existing subscription is accomplished by supplying the Subscription ID to the DISC operator and supplying the parameters to be changed. The format and content of the Subscription Update email message are defined in Table 4.3.3-1.  Content of this message should be supplied in the request defined in the table, for consistency and to allow for automation. Each message field begins on a new line.

Table 4.3.3-1.  Subscription Update Format

| Message Field | Description | Type | Format/ Max Size (bytes) | Value or Content with Value |
| --- | --- | --- | --- | --- |
| Subject of email message | Subject of message identifies the purpose of the message | Fixed String | ASCII (32 B) | ‘QA Data Subscription Update’ |
| Note: the following rows define the body of the email message. |  |  |
| Subscription ID | The Subscription ID returned by the DISC in the Subscription Request Acknowledgment. | Variable String | ASCII (16 B ) | ‘Update: NNNNNNNN’, where NNNNNNNN is the Subscription ID (integer) |
| Dataset Identification | Dataset short name and version ID | Variable String | ASCII (32 B ) | Example: AIRX2RET.005 |
| Update <field> From1 | Current value of field to be changed in the existing subscription. | Variable String | ASCII | e.g., ‘Update Expiration Date From: MM/DD/YYYY-HH:MM’ |
| Update <field> To1 | New value of field to be used when updating the subscription. | Variable String | ASCII | e.g., ‘Update Expiration Date To: MM/DD/YYYY-HH:MM’ |

1More than one set of update to/from fields may be included in the request.

### 4.3.4	Subscription Cancellation

Cancellation of an existing subscription is accomplished by supplying the Subscription ID to the operator and requesting cancellation. The format and content of the Subscription Cancellation email message are defined in Table 4.3.4-1.  Content of this message should be supplied in the request defined in the table, for consistency and to allow for automation. Each message field begins on a new line.

Table 4.3.4-1.  Subscription Cancellation Format

| Message Field | Description | Type | Format/ Max Size (bytes) | Value or Content with Value |
| --- | --- | --- | --- | --- |
| Subject of email message | Subject of message identifies the purpose of the message | Fixed String | ASCII (32 B) | ‘QA Data Subscription Cancellation’ |
| Note: the following rows define the body of the email message. |  |  |
| Subscription ID | The Subscription ID returned by the DISC in the Subscription Request Acknowledgment. It is suggested that the original subscription be included as the body of the message with the Cancel option specified. | Variable String | ASCII (16 B) | ‘Cancel: NNNNNNNN’, where NNNNNNNN is the Subscription ID (integer) |

### 4.3.5	Data Distribution

#### 4.3.5.1	Introduction

The triggering granule can be pushed (via FTP, SFTP or HTTP) to an SSE-specified host address and directory or is available for pickup from the online archive within S4PA. S4PA then automatically sends a notification that includes the information needed for locating the file (FTP push) or retrieving (FTP pull or HTTP Pull) the data. The notification (Distribution Notification [DN]) may be sent via email, FTP or SFTP. The DN may be a formatted message, PDR or merely a list of URLs for the granule(s) available for pickup. An SSE-unique appendix of this ICD describes the particular implementation for each SSE.

### 4.3.5.2	Metadata Distribution

A metadata file is available for distribution for each data granule. The metadata may be furnished in either of two formats: (1) an eXtensible Markup Language (XML) file with filename extension .xml or (2) an Object Definition Language (ODL) file with filename extension .met. The default format for distributed metadata is XML. Note: metadata in ODL is available only if the metadata were provided to S4PA as ODL. The XML schema for the S4PA granule level metadata is described in Section 5.6.

#### 4.3.5.3	Checksums

The S4PA supports two checksum types: POSIX Cyclic Redundancy Check (CRC), commonly know as Unix CKSUM and MD5. The default checksum type is the Unix CKSUM. CKSUM is expressed as a decimal integer, corresponding to a 32-bit unsigned value. The MD5 checksum is used if it is specified in the data provider Product Delivery record (PDR).  Checksums are applied to all non metadata files.

A checksum is computed on ingest into S4PA. If a checksum is included in a data provider PDR then it is compared with the computed checksum for verification. If a checksum verification does not succeed, the ingest fails.

The checksum type furnished on distribution will be the type that is in the S4PA metadata. Checksum information (checksum type, checksum origin, and checksum value) will be included in the metadata file that is distributed as well as in the Distribution Notice (DN).

If data compression is desired, it is the responsibility of the SSE. Compression of files must be performed internally on the data provider’s side. S4PA will distribute the files in the format provided.

#### 4.3.5.4	Distribution Notice for Data Deliveries

The DN for FTP, SFTP, or HTTP deliveries includes file names and locations for retrieving the data.

The file names are the names of the files as inserted into the S4PA archive, or the LocalGranuleID if provided in the granule’s metadata. The LocalGranuleID overrides the native file name. If there is more than one file in a granule, a sequence number is added to the end of the LocalGranuleID for each file upon distribution. For multi-file production data sets (PDS), the filenames are the original filenames supplied by EDOS.

The DN for FTP, HTTP, or SFTP deliveries is defined in Table 4.3.5-1. The DN is preceded by a delimited, DISC-configurable preamble. Thereafter, each row of the table represents a single PARAMETER = VALUE statement in the DN. Figure 4.3.5-1 is an example of the standard DN. Figure 4.3.5-2 is a DN example that lists the URLS of the distributed data. Figure 4.3.5-3 is an example of a DN for HTTP data distribution of restricted data.

For the FTP or HTTP data deliveries, the e-mail subject of a system-generated DN is “GES DISC Order Notification Order ID: DN”NNNNNNNNNN-NNNN, where NNNNNNNNNN-NNNN is system-generated for uniqueness.

The email address to which S4PA sends the DN is documented in an Operations Agreement(s) between the GES DISC and the SSE. The DISC operator uses this information from the Operations Agreement when entering the subscription request.

For a SFTP data delivery, the DN file is secure-ftp’d to the same directory as the data, as specified in the subscription request. The DN file name is <requestID>.notifysftp, where <requestID> is a unique alphanumeric string of maximum 50 characters.

In support of cross-DAAC ingest, the format of the DN is a Product Delivery Record (PDR). This capability supports S4PA to ECS data transfers with some configuration required within the ECS ingest subsystem.

Table 4.3.5-1.  Distribution Notice Contents (1 of 3)

| Keyword | Description | Type | Format/ Size1 (bytes) | Keyword: Value2 |
| --- | --- | --- | --- | --- |
| (None, optional customized preamble) | Each distribution notice message begins with an explanatory preamble. The preamble file is specific to the DAAC, to the delivery media type and to success or failure of the delivery. The preamble ends with a special character sequence: a blank line followed by a line of 10 "+" characters followed by another blank line. To parse the message, the parser can be written either to skip the delimiter portion or to search for KEYWORD: (distribution notice keyword as defined in this table followed by a colon). | Free text | NA | The preamble ends with a special character sequence: a blank line followed by a line of 10 "+" characters followed by another blank line. The preamble shall not contain keyword plus colon sequences or "+" signs. |
| USERSTRING | USERSTRING as documented in Operations Agreements between GES DISC and SSE. | Variable String | ASCII (255 B) | ‘USERSTRING: <value>' |

Table 4.3.5-1.  Distribution Notice Contents (2 of 3)

| Keywords | Description | Type | Format/ Size1 (bytes) | Keyword: Value2 |
| --- | --- | --- | --- | --- |
| FINISHED | Time at which S4PA stages data for pull by the SSE or FTP’s to the SSE’s host directory. | Fixed String | ASCII (29 B including 19 B for date and time) | ‘FINISHED: MM/DD/YYYY <blank>HH:MM:SS’ |
| [Blank line] | ASCII line feed code 010 |  |  |  |
| MEDIATYPE | This type indicates data transmission via FTP pull, FTP push, HTTP pull, or SFTP. | Variable String | ASCII (18 B including 7 B for <type>) | ’MEDIATYPE: <type>’ where <type> is FtpPush, FtpPull, HTTPPull or sftp |
| FTPHOST | Name or IP address of workstation where data were made available for FTP pull by the SSE. | Variable String | ASCII (73 B including 64 B for host name or IP address) | e.g., ‘FTPHOST: shark’ |
| FTPDIR | File directory location without filename. If the DN contains reference to a single granule then the directory will be listed in this field. If multiple granules are listed in the DN then this field will be populated with MULTIPLE (even if the granules reside in the same directory). | Variable String | ASCII (263 B max including 8 B for FTPDIR:) | ‘FTPDIR: <directory> or MULTIPLE’ |
| MEDIA | Media number within request | Fixed String | ASCII (12 B) | ‘MEDIA 1 of 1’ |
| MEDIAID | No value provided. | Fixed String | ASCII (8 B) | ‘MEDIAID:’ |
| [Blank line] | ASCII line feed code 010 |  |  |  |  |  |
| GRANULE | Indicates start of a data granule. Value is the UR for that data granule. (Repeat for each granule.) (Indent by 1 tab.) | Variable String | ASCII (98 B including 89 B for UR) | ‘GRANULE: <UR>’ |  |  |
| ESDT | Specifies the short name and Version ID (001 through 255) of the datatype. (Repeat for each granule.) (Indent by 1 tab.) | Fixed String | ASCII (18 B including 8 B for the ESDT name and 3 B for the version) | ‘ESDT: <Datatype ShortName.VersionID>’ |  |  |
| [Blank line] | ASCII line feed code 010 |  |  |  |
| FILENAME | The filename for a file in the present granule. Set to the LocalGranuleID metadata parameter (plus sequence number if more than one file in a granule), if available. Otherwise, set to the file name as inserted into the S4PA archive. (Repeat for each file in present granule.) (Indent by 2 tabs.) Note: Filename extensions for metadata files may be either .met or .xml. | Variable String | ASCII. 255 bytes max if LocalGranuleID is not used. For LocalGranuleID, 80 B max (plus sequential identifier for multi-file granules). | ‘FILENAME: <name>’ or 'N/A' |
| FILESIZE | The file’s size in Bytes. (Repeat for each file in present granule.) (Indent by 2 tabs.) | Variable String | ASCII (22 B including 12 B for file size) | ‘FILESIZE: <size>’ where size is a decimal value |

Table 4.3.5-1.  Distribution Notice Contents (3 of 3)

| Keyword | Description | Type | Format/ Size1 (bytes) | Keyword: Value2 |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| FILECKSUMTYPE | The checksum type of the FILECKSUMVALUE parameter for the file. Checksums are provided only if the SSE is on the DAAC’s checksum distribution list. | Variable String | ASCII (up to 79 B including up to 64 B for checksum type) | ‘FILECKSUMTYPE: <checksum type>’ where checksum type is ‘CKSUM’ or ‘MD5’ |  |  |
| FILECKSUMVALUE | The value of the checksum recorded with the file in the S4PA. Present only if a FILECKSUMTYPE is provided. The checksum is verified before distribution if required by the DAAC’s Checksum Verification Percentage parameter. If the file is delivered compressed, the checksum value furnished will be for the uncompressed file. | Variable string representing signed or unsigned integer or hexadecimal string (with alpha characters all lower case) | ASCII (up to 271 B including up to 255 for checksum) | ‘FILECKSUMVALUE: <numeric value, signed or unsigned>’ or, for MD5, ‘FILECKSUMVALUE: <32-character hexadecimal string>’ |  |  |
| [blank line] | ASCII line feed code 010 Follows each FILENAME / FILESIZE / FILECKSUMTYPE / FILECKSUMVALUE entry |  |  |  |  |  |

1This field length includes a keyword, a colon, 1 blank, and a value string.

2Angle brackets (“<” and “>”) enclose information to be supplied by S4PA at distribution time.

EXAMPLE ONLY 																																												EXAMPLE ONLY

++++++++++

ORDERID: DN1158690302-16442

REQUESTID: DN1158690302-16442

USERSTRING: FTP-Pull

FINISHED: 09/19/2006 18:25:02

MEDIATYPE: FtpPull

FTPHOST: acdisc.sci.gsfc.nasa.gov

FTPDIR: MULTIPLE

MEDIA 1 of 1

MEDIAID:

GRANULE:ftp://acdisc.sci.gsfc.nasa.gov/data/s4pa/Aura_OMI_Level2G/OMTO3G/2006/OMI-Aura_L2G-OMTO3G_2006m0914_v002-2006m0915t173309.he5

ESDT: OMTO3G.000

FILENAME: OMI-Aura_L2G-OMTO3G_2006m0914_v002-2006m0915t173309.he5

FILESIZE: 157487881

FILECKSUMTYPE: CKSUM

FILECKSUMVALUE: 1355870891

FILENAME: OMI-Aura_L2G-OMTO3G_2006m0914_v002-2006m0915t173309.he5.xml

FILESIZE: 28490

GRANULE:ftp://acdisc.sci.gsfc.nasa.gov/data/s4pa/Aura_OMI_Level2G/OMTO3G/2006/OMI-Aura_L2G-OMTO3G_2006m0913_v002-2006m0915t212633.he5

ESDT: OMTO3G.000

FILENAME: OMI-Aura_L2G-OMTO3G_2006m0913_v002-2006m0915t212633.he5

FILESIZE: 158908439

FILECKSUMTYPE: CKSUM

FILECKSUMVALUE: 671749716

FILENAME: OMI-Aura_L2G-OMTO3G_2006m0913_v002-2006m0915t212633.he5.xml

FILESIZE: 27478

GRANULE:ftp://acdisc.sci.gsfc.nasa.gov/data/s4pa/Aura_OMI_Level2G/OMTO3G/2006/OMI-Aura_L2G-OMTO3G_2006m0915_v002-2006m0916t200747.he5

ESDT: OMTO3G.000

FILENAME: OMI-Aura_L2G-OMTO3G_2006m0915_v002-2006m0916t200747.he5

FILESIZE: 156607722

FILECKSUMTYPE: CKSUM

FILECKSUMVALUE: 1802961641

FILENAME: OMI-Aura_L2G-OMTO3G_2006m0915_v002-2006m0916t200747.he5.xml

FILESIZE: 28494

GRANULE:ftp://acdisc.sci.gsfc.nasa.gov/data/s4pa/Aura_OMI_Level2G/OMTO3G/2006/OMI-Aura_L2G-OMTO3G_2006m0916_v002-2006m0917t165033.he5

ESDT: OMTO3G.000

FILENAME: OMI-Aura_L2G-OMTO3G_2006m0916_v002-2006m0917t165033.he5

FILESIZE: 148616910

FILECKSUMTYPE: CKSUM

FILECKSUMVALUE: 1484135560

FILENAME: OMI-Aura_L2G-OMTO3G_2006m0916_v002-2006m0917t165033.he5.xml

FILESIZE: 27479

Figure 4.3.5-1.  Example Distribution Notice for a Subscription FTP or SFTP Request

EXAMPLE ONLY 																																						EXAMPLE ONLY

ftp://acdisc.sci.gsfc.nasa.gov/data/s4pats1/Aura_OMI_Level2/OMTO3.002/2006/262/OMI-Aura_L2-OMTO3_2006m0919t0654-o11592_v002-2006m0919t195853.he5

ftp://acdisc.sci.gsfc.nasa.gov/data/s4pats1/Aura_OMI_Level2/OMTO3.002/2006/262/OMI-Aura_L2-OMTO3_2006m0919t0654-o11592_v002-2006m0919t195853.he5.xml

ftp://acdisc.sci.gsfc.nasa.gov/data/s4pats1/Aura_OMI_Level2/OMTO3.002/2006/261/OMI-Aura_L2-OMTO3_2006m0918t0929-o11579_v002-2006m0919t195902.he5

ftp://acdisc.sci.gsfc.nasa.gov/data/s4pats1/Aura_OMI_Level2/OMTO3.002/2006/261/OMI-Aura_L2-OMTO3_2006m0918t0929-o11579_v002-2006m0919t195902.he5.xml

### Figure 4.3.5-2.  Example Distribution Notice for a List of URLs

EXAMPLE ONLY 																																						EXAMPLE ONLY

ORDERID: DN1158696652-20707

REQUESTID: DN1158696652-20707

USERSTRING: XYZ123

FINISHED: 09/19/2006 20:10:52

MEDIATYPE: HTTPPull

FTPHOST: acdisc.sci.gsfc.nasa.gov

FTPDIR: /data/s4pats1/Aura_OMI_Level2/OMAERO.002/2006/261

MEDIA 1 of 1

MEDIAID:

GRANULE: http://acdisc.sci.gsfc.nasa.gov/data/s4pats1/Aura_OMI_Level2/OMAERO.002/2006/261/OMI-Aura_L2-OMAERO_2006m0918t1426-o11582_v002-2006m0919t194004.he5

ESDT: OMAERO.002

FILENAME: OMI-Aura_L2-OMAERO_2006m0918t1426-o11582_v002-2006m0919t194004.he5

FILESIZE: 28925630

FILECKSUMTYPE: CKSUM

FILECKSUMVALUE: 1370276651

FILENAME: OMI-Aura_L2-OMAERO_2006m0918t1426-o11582_v002-2006m0919t194004.he5.xml

FILESIZE: 17079

Figure 4.3.5-3.  Example Distribution Notice for HTTP Request

### 4.3.5.5	Electronic Distribution Failure Recovery

An FTP or SFTP Push of data from the S4PA may fail, leaving a partial file in the designated SSE directory. The SSE’s server should allow overwrite of the partial file. File sizes provided in the S4PA Distribution Notice can be checked against those on the SSE server. Failure procedures should be covered in the Operations Agreement between the SSE and the DISC.

It is suggested that the SSE have procedures in place for verifying that all files required for a standard product processing run have been received. This should cover the possibility that the files have been pushed to the specified directory but the DN hasn’t been received, or that the subscription process itself has failed at some point because of internal problems.

The SSE operator can then acquire the file(s) by using FTP pull or request a re-shipment from S4PA. The operator uses the collection name and other attributes (such as data date and time) provided in the electronic notification to search for the required data.

The SSE may employ the S4PA Machine Request Interface (MRI) to search and retrieve data from the S4PA archives. Specifications and instructions for the MRI are found at http://discapps.gsfc.nasa.gov/wiki/Machine_Request_Interface.

Non-fatal errors in the SFTP push of DNs to the SSE are retried. The SSE should discuss subsequent recovery procedures with the DISC and the procedures should be documented in the Operations Agreement.

## 4.4	Metadata Associated with SSE-Produced Collections

The correct transfer of metadata information for population of the S4PA inventory is essential to the S4PA/SSE interface. The key mechanism for ensuring correct transfer is a metadata template that contains the metadata specification for files archived in S4PA. Each SSE may require Metadata Configuration Files (MCFs) as templates for producing metadata for data collections that are to be archived in S4PA (see Section 5.2). Upon ingest, the metadata structures provided by the SSE will be compared against an XML template for the given datatype.  If the metadata structure and content provided by the SSE is not consistent with the XML template then the ingest will fail.  The metadata file may be Object Definition Language (ODL) text or eXtensible Markup Language (XML) and may be produced by the SSE using any method the SSE deems appropriate.  Given the history and amount of effort put into metadata specifications for existing collections, it is recommended that if the SSE uses MCFs and the metadata population tools developed by ECS and distributed with the SDP Toolkit that they continue to do so. If metadata modifications are necessary for future collections (e.g., reprocessing) the SSE is responsible for updating the MCFs or identifying an alternate means of generating appropriate metadata within the production system.

The procedures by which an SSE obtains metadata templates from the GES DISC must be agreed on and should be documented in Operations Agreement(s) between the DISC and the particular SSE.

## 4.5	Transfer of Higher-Level Products to S4PA

The SSE makes available products for ingest by the S4PA. For each SSE, these products are specified in the SSE-unique appendix of this ICD. Data is transferred from the SSE to the S4PA by a Polling with Delivery Record (PDR) mechanism. This section (Section 4.5) of this ICD provides detailed specifications for this interface methodology.

The PDR interface is used to transfer the SSE’s science data granule products, metadata, and other appropriate products to S4PA. All products supplied for ingest by S4PA must be compliant with EOSDIS format and standards and be accompanied by S4PA conformant metadata. The transfer protocol documented in this section must be used to ensure that S4PA can associate files to the correct granules during ingest.

### 4.5.1	Overview of Polling Ingest Methodology

The purpose of the S4PA-SSE electronic interface is to support the delivery of data files from the SSE to S4PA. To accommodate the polling with delivery record interface, a single PDR server directory will be identified for each SSE to S4PA interface. The data files and the Product Delivery Records (PDRs) are placed on this server directory by the SSE. At the end of the data exchange process, the SSE removes the PDR, the PAN or PDRD file and where necessary the data from the server directory.

The SSE makes the directory sub-tree available to S4PA with the allowable privileges. The S4PA uses either of two file transfer methods to retrieve the PDR and data from the SSE server directory. The standard method is FTP.  Secure transfer, using SFTP, is also available by prior agreement between the SSE and the DISC (see Section 4.7 for a description of available data exchange security options).

Implementation of the Polling with Delivery Record Ingest consists of the following steps (Figure 4.5-1 shows the standard transfer method using FTP):

(1) 	The SSE places data files in specified locations on the PDR Server.

(2) 	The SSE generates a PDR and places it on the PDR Server in a previously specified directory.

(3) 	S4PA polls the PDR Server directory at operator-tunable intervals, detects a PDR, and acquires the PDR file via FTP or SFTP.

(4) 	Once a PDR has been detected and acquired by S4PA, the PDR is validated. In the event that the PDR is invalid, S4PA automatically returns a Product Delivery Record Discrepancy (PDRD), via FTP (not SFTP), to an operator-configurable address provided by the SSE. If an error is detected in the PDR, processing is terminated and none of the specified files are transferred to the S4PA server for processing until a corrected PDR is received and successfully processed. If the PDR is valid, S4PA schedules to pull the files specified in the PDR using FTP or SFTP.

(5) 	S4PA pulls the specified files from the PDR Server to be ingested or otherwise processed. The files are then archived.

(6) 	S4PA sends a Production Acceptance Notification (PAN) to the SSE via FTP, SFTP, or email to an operator-configurable address provided by the SSE. The PAN reports either success or error found for each data type in the PDR.

(7) 	Upon determining that no further action can or should be taken with respect to the PDR, the SSE deletes the PAN or PDRD, the PDR and if necessary the associated data from the PDR server.

Address information and operator tunable parameters for the transfer of the PDR, PDRD and PAN are documented for each individual SSE in an Operations Agreement(s) between the DISC(s) and the SSE. Associated procedures should be included in the appropriate DISC documentation of procedures (e.g., on line). Examples include the SSE’s unique identifier, PDR server address and directory, e-mail addresses, contact telephone numbers, and the time between S4PA Ingest receiving a failure and sending a new PDRD/LONGPAN.

The Polling Ingest with PDR transfer mechanism is fully automated. In the context of this transfer mechanism, the following sections address the PDR, PDRD and PAN. Error conditions and error handling/backup methods are then discussed.

Sections 4.5.2 through 4.5.5 give details of this interface methodology specific to the S4PA-SSE interface. A quick reference summary is provided in Section 5.5.

Figure 4.5-1.  Polling with Delivery Record File Transfer Mechanism

(standard method using FTP or SFTP available by prior agreement)

    - PDR File Naming Convention

The PDR file name must be unique within the PDR Server directory and have a ".PDR" file extension. The file name with path must be no longer than 255 characters.  For the purpose of error tracking, S4PA recommends that the file name contain the file creation date as part of the file name.  PDRD and PAN messages returned by S4PA will use the same name as the reference PDR except that the file name extension will be changed to “.PDRD” or ".PAN" respectively. PDR File Naming Convention examples are depicted in Table 4.5-1 and Figure 4.5-2. Note that the SSE designation is free text that may consist of any identifier that has meaning to the SSE operators. The ".PDR" as a filename extension is the only requirement for the S4PA ingest processing (except that there must be some part of the file name preceding the extension).

Table 4.5-1.  Example File Naming Convention for SSE Product Delivery Record

| Field | Description | Format/ Type Max Size (Bytes) | Value |
| --- | --- | --- | --- |
| SSE Designation | Identifier meaningful for the SSE (DataProvider) | ASCII String (21) | Free text |
| PDR Creation Date | Date when PDR was created (optional) | ASCII (15) | .yyyymmddhhmmss |
| Filename extension | Extension for PDR filename (required) | ASCII String (4) | ‘.PDR’ |

EXAMPLE ONLY	EXAMPLE ONLY

FILENAME = MLS123.20010719123845.PDR

Figure 4.5-2.  Example PDR File Naming Convention

### 4.5.3	Product Delivery Record (PDR)

4.5.3.1	SSE PDR Server Directory

The purpose of the PDR is to announce the availability of data and associated files for transfer to S4PA. It contains file names, file size, data types, data type versions, and location. While a PDR may contain references to multiple datatypes, all datatypes referenced in a single PDR must be of the same data processing level (e.g., Level 1, Level 2, or Level 3). The PDR is generated by the SSE and placed in a pre-specified directory on the PDR Server after the files referenced in the PDR have been placed in their respective directories. The address of the SSE's PDR Server and the directory name are operator-configurable items that are documented in an Operations Agreement(s) between the DISC and the SSE. S4PA regularly polls the PDR Server, detects/acquires/validates the PDR, and pulls the data.

4.5.3.2	PDR Format

The PDR is comprised of Parameter-Value Language (PVL) Statements. The required PDR PVL parameters are depicted in Table 4.5-2. The PDR PVL statements are ASCII strings, having at most 256 characters, in the form: "Parameter = Value." Each statement ends with a semicolon.  Comments can be included if preceded by /* and closed with */. The Value strings shown in Table 4.5-2 include pre-defined values shown by single quote marks and the SSE determined values which include ASCII strings, International Standards Organization (ISO) times, and integers to be filled in with appropriate values by the SSE processor during PDR creation.

An example PDR PVL file is provided in Figure 4.5-3. PDRs are validated to check that all required fields contain valid values and that the format of the PDR is correct and consistent with the standards. PDRs that adhere to the defined message standards shown in Table 4.5-2 are accepted and processed. Additional information on PVL valid characters can be found in Parameter Value Language Specification (document referenced in Section 2.3.1).

#### 4.5.3.3	Checksums

The SSE may include a checksum for any science, HDF or HDF-EOS file in the PDR. Two checksum types are supported. Type CKSUM is a 32-bit unsigned value produced by the Unix cksum command. The CKSUM type is the POSIX-CRC checksum. Type MD5 is the 128-bit Message Digest output of the RFC 1321 algorithm, represented as a 32-character hexadecimal string (with alpha characters all lower case).

(For details of the algorithm see RFC 1321 at http://www.faqs.org/rfcs/rfc1321.html.)

If a checksum is included in the data provider PDR then S4PA will verify checksums upon ingest. If checksum verification does not succeed, data ingest fails.

If the SSE does not provide checksums in the PDR, the S4PA computes and record checksums for the SSE science files using a UNIX algorithm.

Table 4.5-2.  Product Delivery Record PVL Parameters (1 of 3)

| Parameter | Description | Type | Format/ Max Size (Bytes) | Value |
| --- | --- | --- | --- | --- |
| ORIGINATING_SYSTEM | Originator of delivery record. Identifier for the SSE | Variable String | ASCII (20 Bytes) | Free text ,e.g MLS123 (not an IP address) |
| TOTAL_FILE_COUNT | Total number of files to transfer | Integer | ASCII (4 Bytes) | 1 to 9999 |
| EXPIRATION_TIME | SSE designated ISO time for deletion of data from originating system. This parameter is specified in the Operations Agreement(s) between the DISC and the SSE | Fixed String | ASCII (20 Bytes)2 | GMT in the format:yyyy-mm-ddThh:mm:ssZ, where T indicates the start of time information and Z indicates "Zulu" time |
| OBJECT | Start of file group parameters (repeat for each DATA_TYPE/group of files). Note that associated browse granule, quality assessment, and metadata files must be in the same FILE_GROUP as the data file(s) to ensure that they will be linked to the data when they are ingested into S4PA | Fixed String | ASCII (10 Bytes) | 'FILE_GROUP' |
| DATA_TYPE | S4PA implemented data type for science data granule. There can be only one DATA_TYPE in a FILE_GROUP | Variable String | ASCII (8 Bytes) | ESDT for science data granule or a generic data type |
| DATA_VERSION | Data type version number (if this is omitted, system will default to the last version installed in S4PA) | Integer | ASCII (3 Bytes) | 3-digit version number |
| NODE_NAME | Name of network node on which the files in the FILE_GROUP are staged for pickup | Variable String | ASCII (64 Bytes) | Name or IP address |
| OBJECT | Start of file parameters for science data file (repeat for all files in the granule) | Fixed String | ASCII (9 Bytes) | 'FILE_SPEC' |
| FILE_TYPE | File type of the data | Variable String | ASCII (20 Bytes) | 'HDF-EOS', or 'HDF', or 'SCIENCE', or 'ALGORITHM' |
| FILE_SIZE | Length of file in bytes | Unsigned 32 bit Integer | ASCII (10 Bytes) | < 2 GB |

Table 4.5-2.  Product Delivery Record PVL Parameters (2 of 3)

| Parameter | Description | Type | Format/ Max Size (Bytes) | Value |
| --- | --- | --- | --- | --- |
| DIRECTORY_ID | File directory location (i.e., a path name) | Variable String | ASCII1 | Directory |
| FILE_ID | File name of granule as defined by the SSE. Used by S4PA for distribution if there is no LocalGranuleID in the metadata | Variable String | ASCII1 | Science data file name |
| FILE_CKSUM_TYPE | Type of checksum, presently either 32-bit unsigned value (type CKSUM) or MD5. Optional and allowed only for science files (e.g., FILE_TYPE = SCIENCE, HDF, or HDF-EOS, but not .met, .xml, DAP, BROWSE | Variable String | ASCII (max 64 Bytes) | 'CKSUM' or 'MD5' |
| FILE_CKSUM_VALUE | Checksum value. Required if the optional FILE_CKSUM_TYPE parameter is present | Variable String | ASCII (max 255 Bytes) | '<signed or unsigned numeric string>' or, for MD5, '<32 character hexadecimal string>' (with alpha characters all lower case) |
| END_OBJECT | End of parameters for data file | Fixed string | ASCII (9 Bytes) | 'FILE_SPEC' |
| OBJECT | Start of file parameters for a metadata file. There can be multiple metadata files in a FILE_GROUP, but only one per FILE_SPEC. Repeat FILE_SPEC for each metadata file type needed in the file group | Fixed string | ASCII (9 Bytes) | 'FILE_SPEC' |
| FILE_TYPE | Metadata file type | Variable String | ASCII (20 Bytes) | 'METADATA' or 'BROWSE_METADATA' or 'QA_METADATA' |
| FILE_SIZE | Length of file in bytes | Unsigned 32 bit Integer | ASCII (10 Bytes) | < 2 GB |
| DIRECTORY_ID | File directory location (i.e., a path name) | Variable String | ASCII1 | Directory |
| FILE_ID | Metadata file name | Variable String | ASCII1 | Metadata file name (ends in .met or .xml) |
| END_OBJECT | End of file parameters for metadata file | Variable String | ASCII (9 Bytes) | 'FILE_SPEC' |

Table 4.5-2.  Product Delivery Record PVL Parameters (3 of 3)

| Parameter | Description | Type | Format/ Max Size (Bytes) | Value |
| --- | --- | --- | --- | --- |
| OBJECT | Start of file parameters for browse data or quality assessment file. Repeat as needed | Fixed string | ASCII (9 Bytes) | 'FILE_SPEC' |
| FILE_TYPE | File type for browse or quality assessment | Variable String | ASCII (20 Bytes) | 'BROWSE' or 'QA' |
| FILE_SIZE | Length of file in bytes | Unsigned 32 bit Integer | ASCII (10 Bytes) | < 2 GB |
| DIRECTORY_ID | File directory location (i.e., a path name) | Variable String | ASCII1 | Directory |
| FILE_ID | File name of browse data file or quality assessment file as defined by the SSE. Used by S4PA for distribution if there is no LocalGranuleID in the metadata | Variable String | ASCII1 | Browse data or quality assessment file name |
| END_OBJECT | End of parameters for browse data, quality assessment file | Fixed string | ASCII (9 Bytes) | 'FILE_SPEC' |
| OBJECT | Start of file parameters for optional metadata file for browse or quality assessment | Fixed string | ASCII (9 Bytes) | 'FILE_SPEC' |
| FILE_TYPE | File type for browse or QA metadata file | Variable String | ASCII (20 Bytes) | 'BROWSE_METADATA' or 'QA_METADATA' |
| FILE_SIZE | Length of file in bytes | Unsigned 32 bit Integer | ASCII (10 Bytes) | < 2 GB |
| DIRECTORY_ID | File directory location (i.e., a path name) | Variable String | ASCII1 | Directory |
| FILE_ID | File name of metadata file for browse data or quality assessment file as defined by the SSE. Used by S4PA for distribution if there is no LocalGranuleID in the metadata | Variable String | ASCII1 | Browse data or quality assessment file name |
| END_OBJECT | End of parameters for browse or QA metadata file | Fixed string | ASCII (9 Bytes) | 'FILE_SPEC' |
| END_OBJECT | End of FILE_GROUP parameters. Repeat for each DATA_TYPE/group of files | Fixed string | ASCII (10 Bytes) | 'FILE_GROUP' |

1Size does not exceed a total of 256 bytes when DIRECTORY_ID and FILE_ID are combined.

2Only used when PDR server is not under S4PA control.

EXAMPLE ONLY 																																						EXAMPLE ONLY

ORIGINATING_SYSTEM=S4PA_acdisc;

TOTAL_FILE_COUNT=2;

EXPIRATION_TIME=2007-09-01T00:00:00Z;

OBJECT=FILE_GROUP;

DATA_TYPE=OMAERO;

DATA_VERSION=002;

NODE_NAME=acdisc.sci.gsfc.nasa.gov;

OBJECT=FILE_SPEC;

FILE_TYPE=SCIENCE;

FILE_SIZE=28925630;

DIRECTORY_ID=/data/s4pats1/Aura_OMI_Level2/OMAERO.002/2006/261/.hidden;

FILE_ID=OMI-Aura_L2-OMAERO_2006m0918t1426-o11582_v002-2006m0919t194004.he5;

END_OBJECT=FILE_SPEC;

OBJECT=FILE_SPEC;

FILE_TYPE=METADATA;

FILE_SIZE=17079;

DIRECTORY_ID=/data/s4pats1/Aura_OMI_Level2/OMAERO.002/2006/261/.hidden;

FILE_ID=OMI-Aura_L2-OMAERO_2006m0918t1426-o11582_v002-2006m0919t194004.he5.xml;

END_OBJECT=FILE_SPEC;

END_OBJECT=FILE_GROUP;

Figure 4.5-3.  Example PDR PVL File

### 4.5.4	Product Delivery Record Discrepancy (PDRD)

The Product Delivery Record Discrepancy (PDRD) is sent by S4PA to the SSE via ftp or e-mail, only in the event that the PDR cannot be successfully validated. The subject of the e-mail message is the PDRD file name. The e-mail address (or ftp address) is an operator-tunable parameter documented for each SSE in an Operations Agreement(s) between the GES DISC and the SSE. The PDRD identifies the error/success dispositions for file groups in the PDR resulting from S4PA’s attempt to validate the PDR.  The same file-naming convention is used for the PDRD as for the PDR, except that the file name extension is ‘.PDRD’ instead of the ‘.PDR’. There are two forms of PDRD, a short form (Table 4.5-3) and long form (Table 4.5-4). The short form is used when the first error encountered in each file group within the PDR is the same or the first error found applies to each group. The long form is used when one or more file groups in the PDR have invalid parameters; some file groups may be error-free. For each file group, if an error is encountered when the PDR is processed, S4PA halts processing and reports the error that it just encountered for that file group. None of the remaining conditions in that file group are validated. S4PA processing then continues on with the next file group in the PDR. The dispositions in the Long PDRD will be reported for all file groups in the order listed in the PDR. In the event that a PDRD is returned to the SSE, none of the files are transferred to the S4PA for processing, and the SSE must correct the errors and resubmit the entire PDR for processing.

The PDRD consists of PVL Statements. Short and Long PDRD PVL examples are provided, respectively, in Figure 4.5-4 and Figure 4.5-5.

Table 4.5-3.  Short Product Delivery Record Discrepancy PVL Parameters

| Parameter1 | Description | Type/Format (Length in Bytes) | Value1 | Explanation |
| --- | --- | --- | --- | --- |
| MESSAGE_TYPE | Short Product Delivery Record Discrepancy | Fixed String/ASCII (9) | SHORTPDRD |  |
| DISPOSITION | Disposition of Ingest Request | Variable String/ASCII (64) | One of the following: |  |
|  |  |  | “invalid or unreadable file” | PDR could not be validated. Not retryable. |
|  |  |  | “invalid file count” | TOTAL_FILE_COUNT parameter is either missing or <= 0 - not retryable |
|  |  |  | “invalid file group” | One or more FILE_GROUP within PDR contained incorrect syntax or invalid parameters - not retryable |

1Each parameter/value is followed by an EOL mark.

EXAMPLE ONLY		EXAMPLE ONLY

MESSAGE TYPE = SHORTPDRD;
DISPOSITION = “INVALID FILE COUNT”;

Figure 4.5-4.  Example Short PDRD PVL

Table 4.5-4.  Long Product Delivery Record Discrepancy PVL Parameters

| Parameter2 | Description | Type/Format (Length in Bytes) | Value2 | Explanation |
| --- | --- | --- | --- | --- |
| MESSAGE_TYPE | Long Product Delivery Record Discrepancy | Fixed String/ASCII (8) | LONGPDRD |  |
| NO_FILE_GRPS (to follow) | Number of File Groups in the PDR | Integer/ASCII (4) | Number of File Groups in the PDR |  |

For each file group in the PDR

| Parameter | Description | Type/Format (Length in Bytes) | Value2 | Explanation |
| --- | --- | --- | --- | --- |
| DATA_TYPE | S4PA Data Type | ASCII String ( 20) | DATA_TYPE in PDR |  |
| DISPOSITION | Disposition of Ingest Request1 | Variable String/ASCII (64) | One of the following: |  |
|  |  |  | “SUCCESSFUL” | No error |
|  |  |  | “INVALID DATA TYPE” | The DATA_TYPE parameter is missing from the file group or the value along with its associated Version ID is not configured in S4PA - not retryable |
|  |  |  | “INVALID DIRECTORY” 3 | The DIRECTORY_ID parameter is missing or empty for a file - not retryable |
|  |  |  | “INVALID FILE SIZE” | The FILE_SIZE parameter is missing, empty or 0 for a file - not retryable |
|  |  |  | “INVALID FILE ID” 3 | The FILE_ID parameter is missing or empty for a file - not retryable |
|  |  |  | “INVALID NODE NAME” 3 | The NODE_NAME parameter is missing or empty for the file group - not retryable |
|  |  |  | “INVALID FILE TYPE” | The FILE_TYPE parameter is missing or empty for a file or the value is not configured in S4PA for the given data type - not retryable |
|  |  |  | “UNSUPPORTED CHECKSUM TYPE” | The checksum type given on the PDR is not supported by S4PA – not retryable |
|  |  |  | “MISSING FILE_CKSUM_VALUE PARAMETER” | The FILE_CKSUM_TYPE parameter is present in the PDR but the FILE_CKSUM_VALUE is not – not retryable |
|  |  |  | “MISSING FILE_CKSUM_TYPE PARAMETER” | The FILE_CKSUM_VALUE is present but FILE_CKSUM_TYPE is not – not retryable |
|  |  |  | “INVALID FILE_CKSUM_VALUE” | The FILE_CKSUM_VALUE is present but syntactically incorrect – not retryable |

1For each file group, only one disposition value may be provided. In cases where multiple errors may exist, the disposition value corresponding to the first error encountered will be provided.

2Each parameter/value statement is followed by an EOL mark.

3Null string check only

EXAMPLE ONLY								EXAMPLE ONLY

MESSAGE_TYPE = LONGPDRD; 
NO_FILE_GRPS = 3;
DATA_TYPE = MLS_DATA1; 
DISPOSITION = “INVALID DATA TYPE”;
DATA_TYPE = MLS_DATA2;
DISPOSITION = “INVALID FILE ID”; 
DATA_TYPE = MLS_DATA3; 
DISPOSITION = “SUCCESSFUL”;

Figure 4.5-5.  Example Long PDRD PVL

### 4.5.5	Production Acceptance Notification (PAN)

After S4PA has attempted to ingest and archive the data, S4PA automatically sends a “Production Acceptance Notification” (PAN) via e-mail or FTP to the SSE. The PAN file announces the completion of data transfer and archival, and identifies any errors or problems that have been encountered. The e-mail or FTP address and actions to be taken in case of data or archival failure are specified for each SSE, in an Operations Agreement(s) between the DISC and the SSE.

The naming convention for the PAN is the same as that used for the PDR, except that the file name extension is PAN instead of PDR. The subject of an e-mail PAN is the PAN file name. There are two forms of the PAN, a short form (Table 4.5-5) and a long form (Table 4.5-6) form. The short form of the PAN (SHORTPAN) is sent to acknowledge that all files in the PDR, regardless of the number of file groups in the PDR, have been successfully transferred. Individual file names are not referenced in a SHORTPAN since the only disposition for every file in the corresponding PDR is always “successful”.

If any of the files in the PDR fails ingest, the long form of the PAN (LONGPAN) is generated and returned to the SSE. In the LONGPAN, each file in the PDR is referenced with an appropriate disposition based on the following conditions:

- If a PDR contains references for a single data granule (data and metadata) and the granule fails ingest then S4PA generates a LONGPAN with the single granule referenced with appropriate dispositions (data and metadata).

- If a PDR contains references for multiple granules and all granules fail for the same reason, S4PA will generate a LONGPAN with references to all granules in the PDR with the same disposition given for all granules.

- If a PDR references multiple granules and if some granules ingest successfully while others fail, S4PA generates a LONGPAN with references to all granules in the PDR with appropriate dispositions for granules that either succeeded or failed ingest.

The PAN consists of PVL Statements. Short and Long PAN PVL examples are provided, respectively, in Figure 4.5-6 and Figure 4.5-7.

Table 4.5-5.  Short Production Acceptance Notification PVL Parameters

| Parameter1 | Description | Type/Format (Length in Bytes) | Value1 | Explanation |
| --- | --- | --- | --- | --- |
| MESSAGE_TYPE | Short Production Acceptance Notification Definition | Fixed String/ASCII (8) | SHORTPAN |  |
| DISPOSITION | Disposition of Ingest Request | Variable String/ASCII (64) | “successful” | No error |
| TIME_STAMP | ISO Time when the S4PA completed transfer of the file. | ASCII (20) | GMT in the format: yyyy-mm-ddThh:mm:ssZ, where T indicates the start of time information and Z indicates “Zulu” time |  |

1Each parameter/value statement is followed by an EOL mark.

EXAMPLE ONLY	EXAMPLE ONLY

MESSAGE_TYPE=SHORTPAN;

DISPOSITION="SUCCESSFUL";

TIME_STAMP=2006-09-19T23:16:01Z;

Figure 4.5-6.  Example Short PAN PVL

Table 4.5-6.  Long Production Acceptance Notification PVL Parameters (1 of 2)

| Parameter2 | Description | Type/Format (Length in Bytes) | Value2 | Explanation |  |
| --- | --- | --- | --- | --- | --- |
| MESSAGE_TYPE | Long Production Acceptance Notification | Fixed String/ASCII (7) | LONGPAN |  |  |
| NO_OF_FILES | Number of Files in PDR | ASCII (4) | TOTAL_FILE_COUNT parameter in PDR |  |  |

For each File in the PDR

| FILE_DIRECTORY | ASCII string specifying file directory location | ASCII (<256) Equivalent to PDR length | DIRECTORY_ID parameter in PDR |  |  |
| --- | --- | --- | --- | --- | --- |
| FILE_NAME | File names on system creating PDR | ASCII (<256) Equivalent to PDR length | FILE_ID parameter in PDR |  |  |
| DISPOSITION1 | Disposition of Ingest Request | Variable String/ASCII (64) | One of the following: |  |  |
|  |  |  | “successful” | No error |  |
|  |  |  | “transfer failure” 4 | FTP service not available - retryable |  |

Table 4.5-6.  Long Production Acceptance Notification PVL Parameters (2 of 2)

| Parameter2 | Description | Type/Format (Length in Bytes) | Value2 | Explanation |  |
| --- | --- | --- | --- | --- | --- |
|  |  |  | “ALL FILE GROUPS/FILES NOT FOUND” | Data file not available when trying to FTP it or data file not found or has a size of 0 after it has been FTP'd - may or may not be retryable5 |  |
|  |  |  | “POST-TRANSFER FILE SIZE CHECK FAILURE” | Size of data file in the PDR is incorrect or the entire data file did not get FTP'd - first case is not retryable, the second case is retryable |  |
|  |  |  | “METADATA PREPROCESSING ERROR” | Error in generating metadata file - may or may not be retryable5 |  |
|  |  |  | “FAILURE-DISK SPACE NOT AVAILABLE” | Unable to create or extend the staging disk - may or may not be retryable5 |  |
|  |  |  | “DATA CONVERSION FAILURE” | Error in preprocessing science files, validating metadata or adding file to appropriate group in the insert command - not retryable |  |
|  |  |  | “INVALID OR MISSING FILE TYPE” | If the input file type has a null or invalid internal file type - not retryable |  |
|  |  |  | “DATA ARCHIVE ERROR” | Archive error - may or may not be retryable5 |  |
|  |  |  | “CHECKSUM VERIFICATION FAILURE” | If checksum on ingest is required but the checksum in the PDR could not be verified when recomputed by S4PA – not retryable |  |
|  |  |  | “ASSOCIATED FILE FAILURE” | File OK for ingest, associated data/metadata file contained error on ingest – not retryable |  |
| TIME_STAMP | ISO Time when the S4PA completed transfer of the file. Does not necessarily indicate successful ingest. | ASCII (20) | GMT in the format: yyyy-mm-ddThh:mm:ssZ, where T indicates the start of time information and Z indicates “Zulu” time. |  |  |

1In any given instance, only one disposition value may be provided. In cases where multiple errors have occurred, the disposition value corresponding to the first error encountered will be provided.

2Each parameter/value statement is followed by an EOL mark.

3Dispositions will include a time stamp.

4It is recommended that these be automatically retried but retries should be limited to 2 attempts at 10-minute intervals for 3 hours.

5It is recommended that these errors not be retried without prior agreement with the DISC.

EXAMPLE ONLY 							EXAMPLE ONLY

MESSAGE_TYPE=LONGPAN;

NO_OF_FILES=6;

FILE_DIRECTORY=private/s4pa/pull/TRMM_3A12;

FILE_NAME=3A12t.060301.6.HDF.Z;

DISPOSITION="SUCCESSFUL";

TIME_STAMP=2007-02-02T10:34:09Z;

FILE_DIRECTORY=private/s4pa/pull/TRMM_3A12;

FILE_NAME=3A12t.060301.6.HDF.xml;

DISPOSITION="SUCCESSFUL";

TIME_STAMP=2007-02-02T10:34:09Z;

FILE_DIRECTORY=private/s4pa/pull/TRMM_3A12;

FILE_NAME=3A12t.060101.6.HDF.Z;

DISPOSITION="ASSOCIATED FILE FAILURE";

TIME_STAMP=2007-02-02T10:34:09Z;

FILE_DIRECTORY=private/s4pa/pull/TRMM_3A12;

FILE_NAME=3A12t.060101.6.HDF.xml;

DISPOSITION="POST-TRANSFER FILE SIZE CHECK FAILURE";

TIME_STAMP=2007-02-02T10:34:09Z;

FILE_DIRECTORY=private/s4pa/pull/TRMM_3A12;

FILE_NAME=3A12t.060201.6.HDF.Z;

DISPOSITION="SUCCESSFUL";

TIME_STAMP=2007-02-02T10:34:09Z;

FILE_DIRECTORY=private/s4pa/pull/TRMM_3A12;

FILE_NAME=3A12t.060201.6.HDF.xml;

DISPOSITION="SUCCESSFUL";

TIME_STAMP=2007-02-02T10:34:09Z;

Figure 4.5-7.  Example Long PAN PVL

### 4.5.6	SSE-S4PA Electronic Data Exchange Error Handling/Back-up Methods

During the course of data exchange via FTP, the following typical error conditions may arise:

•	Failure to establish TCP/IP connection

•	Erroneous FTP command

•	File not found (listed in PDR, but not found on disk)

•	File not readable due to permissions

Should a problem develop during an FTP file transfer due to any of the above error conditions, an operator-tunable number of attempts are made to pull the data. In the event that problems cannot be resolved within this operator-tunable number of attempts, the DISC and SSE operations personnel should coordinate recovery efforts.

## 4.6	Accessing Archived Data for Reprocessing

The S4PA provides a Machine Request Interface (MRI) that provides the capability for the SSE to directly search and retrieve archived data for reprocessing. The MRI allows an SSE to request distribution of files via subscription for user-specified data type and time range. Specifics of the MRI are provided at http://discapps.gsfc.nasa.gov/wiki/Machine_Request_Interface.

## 4.7	Data Exchange Security

S4PA implements EOSDIS security policy by supporting the following standard file transfer methods:

If S4PA is using FTP to poll the SSE’s disk, standard FTP login procedures including the use of a password for the purposes of security are used.

For FTP connections to the S4PA, anonymous FTP is used.  For HTTP connections to the S4PA, username and password would be required. Improved security may be obtained by implementing Secure Shell, which is a drop-in replacement for the Berkeley r- commands in a Unix environment. The S4PA uses OpenSSH. Use of Secure Shell services is by advance agreement with the DISC; procedures, responsibilities and configurations must be documented in an Operations Agreement with the DISC.

### 4.7.1	Encryption

The S4PA supports encrypted data ingest and data distribution with the limitations described in Sections 4.7.2 and 4.7.3, respectively. The S4PA itself uses only secure FTP for secure ingest and secure distribution.

The DISC operations and the SSE will work together to make sure that the versions of SSH used by each system are compatible.

The DISC will provide support for software which allows the username and passwords to be encrypted without the encryption of the data.

Three ciphers are supported:

(1)	aes128 (advanced encryption standard) forces data encryption but is faster than triple Digital Encryption Standard (DES).

(2)	Cipher None with pass phrase authentication supports an interface without data encryption.

(3)	triple DES is an older standard that is still supported but file transfer is slow and it is not recommended.

By using a ssh public/private key pair, connection between machines can be established automatically. This makes it easier to automate the ingest and distribution process and eliminates the burden of managing passwords. A configuration file must reside on the machine that acts as ssh server (~/.ssh/authorized_keys2 under OpenSSH). The public key is useless without the private key because the connections can only be established when both keys are in place, and it is not possible to derive one key from the other. Therefore, if the public key is lost or stolen, there is no effect on security. Several other options are also possible in this configuration file.

### 4.7.2	Secure Ingest

The S4PA supports encryption of the SSE data ingest interface using SSH (Secure SHell). Data encryption will be supported provided that performance is not significantly impacted. The SSE should contact DISC operations to set up the account. The DISC will provide guidance with configuration issues in coordination with the SSE.

The SSH server software must be installed on the same SSE host where SSE PDRs and data are staged and which is polled by the S4PA ingest software. If the SSE has selected FTP for transfer of PDRDs and PANs from the S4PA, they must be transferred to the same host.

The SSE may elect to use pass phrase authentication but the procedure for configuring this must be coordinated with the DISC and documented in the Operations Agreement with the DISC.

### 4.7.3	Secure Distribution

This option encrypts the destination host’s authentication information.

Secure distribution of S4PA data is available for subscription requests only. Prior arrangements must be made with the DISC to set up the secure account. SSH must be installed on the destination host. The DISC needs to know the destination host name, destination directory name and password. If the SSE elects to use pass phrase authentication, configuration procedures must be coordinated with the DISC and documented in the Operations Agreement with the DISC.

The SSE chooses secure distribution of a request by including the sftp (secure ftp) option in its e-mail Subscription Request to the DISC (see Table 4.3.1-1). The requested granules and the distribution notice are pushed by the DISC to the designated SSE destination. If the destination host has not been correctly configured with ssh, an error condition will result. Recovery procedures should be agreed on with the DISC and included in the Operations Agreement.

This page intentionally left blank.

# 5.  SSE Data and Metadata

This section addresses only those aspects of the subject that are critical for ensuring S4PA-SSE data exchange interface functionality. For more information about S4PA metadata requirements, see “The Role of Metadata in EOSDIS” (Doc. # 160-TP-013) and “Backus-Naur Format (BNF) Representation of the B.0 Earth Science Data Model” (Doc. # 420-TP-016-003).

## 5.1	S4PA Datatypes

A versioned datatype must be configured in the S4PA before granules of that datatype and version can be ingested. The SSE coordinates with the DISC to ensure there is adequate metadata for each SSE datatype and version. As part of the transition from ECS to S4PA, all datatypes that are operationally ingested into ECS are configured for ingest into S4PA.

All data granules stored in S4PA are members of Datatype Collections. These collections and the granules themselves are described in the S4PA online inventory catalog using metadata, that is, “data about data”. The metadata is organized according to a data schema described in the S4PA data model. The core of the S4PA model contains many parameters which may be used to describe the data; additionally, the S4PA data model is extensible through the use of Product Specific Attributes (PSAs) to describe aspects of a particular collection or granule which are not covered by the core model. Thus each collection is described by a set of metadata attributes with defined values on the collection level; and on the granule level, a defined set of metadata attributes with defined valid domains. The mechanism used within S4PA to define the collection level attributes is the Global Change Master Directory (GCMD) Data Interchange Format (DIF). The collection level metadata will be delivered to the GCMD by the DISC in the DIF. The collection level metadata will be available from the GCMD and the DISC. The collection level metadata is stored only once in the top level directory within a single data type. The collection level metadata can be accessed via the attribute URL linking in the granule level metadata. The mechanism used within S4PA to define granule level attributes is described in the metadata template file. Section 5.6 describes the XML schema for the S4PA granule level metadata. The graphical representation of the schema is presented in Figure 5-2.

## Metadata

### Metadata Files for S4PA Ingest

The SSE should continue to provide an ECS compliant metadata file for each granule that is to be inserted into the S4PA. Metadata that is ECS compliant is automatically S4PA compliant so no changes are necessary at the SSE. Minimally, to support search and retrieval of data, the metadata needs to contain the following: Data Type name (ShortName), Version ID (VersionID), and Start Time (RangeDateTime).

Once the S4PA metadata template is established, all granules of the associated collection must conform to the template by providing values for the attributes defined in the template. For data production, the ECS Science Data Processing (SDP) Toolkit provides metadata tools that make this task easier. The SDP Toolkit requires as input a Metadata Configuration File (MCF). For datatypes migrated from ECS to S4PA the metadata templates were derived from existing MCFs.

Both the MCF and the metadata produced using the SDP Toolkit (either as a stand alone file or as metadata encapsulated within HDF-EOS) are written in Object Description Language (ODL). ODL is described in “Object Description Language (ODL) Specification and Usage” referenced in Section 2.3.1 of this document. The particular characteristics of ODL are not important for metadata produced using the SDP Toolkit metadata tools because the tools will produce correct ODL. In the case where the metadata delivered within a FILE_GROUP is not produced using the SDP Toolkit metadata tools, the metadata must conform to the ODL structures found in the associated MCF file regardless of whether the metadata file is provided in ODL or XML.

### Checksums in Distributed Metadata

When the S4PA distributes the metadata file for a granule being distributed, it includes checksum information. The checksum type and checksum value are included in the metadata file.

## 5.3	Unique Granule Identification

Each SSE provides granules for ingest by S4PA at the DISC specified for the S4PA-SSE interface in the relevant SSE-unique appendix. Each granule must have a unique identifier, which the SSE provides in the metadata file for the granule as LocalGranuleID (LGID). Each SSE should review its existing LocalGranuleID formats against the uniqueness requirement specified in Section 5.3.1.

### 5.3.1	LocalGranuleID Format

When the SSE supplies a granule to S4PA, for archival and distribution, it must assign a unique identifier to that granule and provide the identifier in the metadata as LocalGranuleID. The SSE may use any convention for the LocalGranuleID that meets the following criteria:

- The LocalGranuleID for each granule is unique within its collection.

- The LocalGranuleID is a valid filename (with no directory path component) for use under both Unix and Windows-NT.

- The length of LocalGranuleID is variable, but no more than 80 characters.

An SSE may choose to use the production system product filename as the value of LocalGranuleID if it conforms to these LocalGranuleID criteria. If an SSE uses ancillary data received from sources other than S4PA in production of its standard products, the SSE may provide that ancillary data to S4PA for archive. It is likely that filenames from such external sources would not follow the LocalGranuleID conventions. The SSE may either change to local filename to conform, or else use a conforming LocalGranuleID that is not the local filename.

### 5.3.2	S4PA Use of LocalGranuleID

When the SSE granule is ingested by S4PA the LocalGranuleID is stored in online metadata. Regardless of the SSE file names originally used for ingesting the granule, S4PA uses the LocalGranuleID to construct the Unix filename (s) when it distributes an archived granule.

## 5.4	Granule Cross References

InputPointer is an attribute in the granule metadata in the metadata file supplied to S4PA with each granule. It contains pointer(s) to the granule(s) used as input in the production of the granule, including ancillary data granules and orbit parameter granules. The InputPointer attribute is optional for granules that are not EOS Standard Products because the inputs to those granules are not stored in the S4PA archive.  For all EOS Standard Products, the EOS data policy requires that precursor products be made known and available to the general end user. For these products, the InputPointer is a required attribute.

### 5.4.1	InputPointer Format

S4PA and its users need InputPointers to determine which input products were heritage products in the generation of granules. In order for InputPointers to be of value to users and data providers for searching and requesting EOS data, they should conform to the format specified below.

The format of the InputPointer references for input products depends upon the source of the input product. For input products that are distributed from or archived in the S4PA, the InputPointer should be a LGID pointer. For input products that are not archived by S4PA (such as SSE intermediate products) the External Granule ID Pointer (EGID) standard for reference pointers should be used. Failure to conform to the recommended format for InputPointers will not cause the Ingest or Insert of the SSE produced granules into S4PA to fail and no present S4PA services depend upon the format. There are two defined granule pointer reference formats.

1.	The preferred format of InputPointer is a reference based upon the value of the LocalGranuleID of the input product. This method is valid only for collections where the LocalGranuleId conforms to the criteria described in Section 5.3.1 above.  This includes collections produced by the SSE for ingest by S4PA, and other granules in the S4PA archive that are known by the SSE to follow the LocalGranuleId criteria. The following LGID Reference format should be used:

LGID:ShortName:VersionID:Identifier

Where

":" is a colon - a separator for the components of the pointer.

"LGID" is a literal string indicating that this pointer is a LocalGranuleID .

"ShortName" is the S4PA Datatype ShortName (up to 20 characters) of the referenced input granule.

"VersionID" is the S4PA Datatype version (up to 10 characters) of the referenced input granule. To be consistent with the ECS Data Model, the use of 3-character version ID will be supported.

"Identifier" is the value of the 80-character (max) LocalGranuleID for the referenced input granule.

Figure 5-1 is an example of an LGID Reference format. In this example, “mls0120010119.122357001.dat” is the value the SSE assigned for the LocalGranuleID of a granule of the MLS01 version 002 collection when it delivered the granule to S4PA.

Example																																																	 Example

LGID:MLS01:002:mls0120010119.122357001.dat

Figure 5-1.  Example InputPointer LGID Reference Format

2.	If the referenced input granule is not a member of an S4PA collection then the LGID can not be defined. Such a case may occur if an input product is an intermediate product that is not archived in S4PA.  The SSE should provide a pointer reference that a science user can use to obtain the input data directly from the data provider. The following standard format indicates that the referenced granule is not a member of an S4PA collection.

EGID:DATAPROVIDER:FILEIDENTIFIER

where

Maximum total number of characters for InputPointer is 255

":" is a colon - a separator for components of the pointer

"EGID" indicates that this is an External Granule pointer that does not point to the S4PA archive

"DATAPROVIDER" is a 4-character code assigned by the DISC or ESDIS for the source of the data (might be an SSE or some other data provider)

"FILEIDENTIFIER" uniquely identifies the data to the data provider. (Data provider could include a handle of some sort within this component separated by a colon.)

Note: Within S4PA, an EGID pointer is not a valid reference and S4PA will not use such pointers for any purpose.

## 5.5	File Transfer Quick Reference Summary

1.	Granule. There can be only one data granule (Datatype) in a FILE_GROUP on a PDR. The data granule may consist of multiple files, however. Each individual file in a multi-file granule is called a granulit. While a PDR may contain references to multiple datatypes, all datatypes referenced in a single PDR must be of the same data processing level (e.g., Level 1, Level 2, or Level 3).

2.	Metadata File. Every data granule must be accompanied by a metadata file (.met or .xml) in the same FILE_GROUP (only one per file group).

3.	Browse, QA. A data granule may also be accompanied by a browse file and/or a quality assurance file in the same FILE_GROUP, provided that none of these files has multiple granule associations.

4.	LocalGranuleID.

a.	Must be unique for each Granule in a given collection (Datatype).

b.	Must be a valid filename for Unix or Windows-NT with a maximum length 80 characters.

c.	S4PA uses for constructing filename for the granule when it is distributed.

d.	LocalGranuleId is a required metadata field for all products delivered from an SSE.

5.	InputPointer.

a.	The convention is, InputPointer is in the format LGID:ShortName:VersionID:Identifier, where Identifier is a LocalGranuleID and is unique within the given collection.

b.	Non-standard InputPointer references will not affect Ingest by S4PA, but may be confusing to end users and may not be compatible with any future services that might use the standard.

c. 	For all EOS standard products, the InputPointer is a required attribute.

## 5.6	XML Schema for S4PA Granule Level Metadata

<?xml version="1.0" encoding="UTF-8"?>

<!-- This schema is a placeholder for Granule level, S4PA -->

<!-- meta-data elements  -->

<xs:schema xmlns:xs="http://www.w3.org/2001/XMLSchema" elementFormDefault="qualified" attributeFormDefault="unqualified">

<xs:include schemaLocation="S4paCommonTypes.xsd"/>

<xs:element name="CollectionMetaData">

<xs:annotation>

<xs:documentation xml:lang="en">

Collection Meta-Data Information. This contains the product ShortName

and LongName as well as the VersionID. These elements are associated

with the Collection (S4paCollection.xsd) level schema.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element ref="Description" minOccurs="0"/>

<xs:element ref="LongName" minOccurs="0"/>

<xs:element ref="ShortName"/>

<xs:element ref="VersionID"/>

<xs:element ref="URL" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="DataGranule">

<xs:annotation>

<xs:documentation xml:lang="en">

Meta-data specific to the granule. This currently includes ten

elements, including granulID (ID for the granule, which is usually

the filename), Format (format of data e.g., HDF-EOS), CheckSum,

SizeBytesDataGranule (size of the granule in bytes), InsertDateTime

(date and time granule was inserted into S4PA), ProductionDateTime

(date and time the granule was produced).

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:all>

<xs:element ref="GranuleID"/>

<xs:element ref="LocalGranuleID" minOccurs="0"/>

<xs:element ref="Format" minOccurs="0"/>

<xs:element ref="CheckSum" minOccurs="0"/>

<xs:element name="SizeBytesDataGranule"/>

<xs:element ref="InsertDateTime" minOccurs="0"/>

<xs:element ref="ProductionDateTime" minOccurs="0"/>

<xs:element ref="PGEVersionClass" minOccurs="0"/>

<xs:element ref="Granulits" minOccurs="0"/>

<xs:element ref="DayNightFlag" minOccurs="0"/>

</xs:all>

</xs:complexType>

</xs:element>

<xs:element name="PGEVersionClass">

<xs:annotation>

<xs:documentation xml:lang="en">

Lists the PGE version that was used to process the data

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element ref="PGEVersion" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="PGEVersion">

<xs:annotation>

<xs:documentation xml:lang="en">

</xs:documentation>

</xs:annotation>

<xs:simpleType>

<xs:restriction base="xs:string"/>

</xs:simpleType>

</xs:element>

<xs:element name="SizeBytesDataGranule">

<xs:simpleType>

<xs:list>

<xs:simpleType>

<xs:union memberTypes="xs:unsignedLong"/>

</xs:simpleType>

</xs:list>

</xs:simpleType>

</xs:element>

<xs:element name="InsertDateTime">

<xs:simpleType>

<xs:list>

<xs:simpleType>

<xs:union memberTypes="xs:date xs:time"/>

</xs:simpleType>

</xs:list>

</xs:simpleType>

</xs:element>

<xs:element name="ProductionDateTime">

<xs:simpleType>

<xs:list>

<xs:simpleType>

<xs:union memberTypes="xs:string"/>

</xs:simpleType>

</xs:list>

</xs:simpleType>

</xs:element>

<xs:element name="GranuleID">

<xs:annotation>

<xs:documentation>

The unique identifier for each granule. In most cases this is the

file name.

</xs:documentation>

</xs:annotation>

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="180"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="LocalGranuleID">

<xs:annotation>

<xs:documentation>

The unique identifier for each granule. In most cases this is the

file name.

</xs:documentation>

</xs:annotation>

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="180"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="Format">

<xs:annotation>

<xs:documentation>

The format of the data. This type is unique to S4PA.

</xs:documentation>

</xs:annotation>

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="32"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="CheckSum">

<xs:annotation>

<xs:documentation xml:lang="en">

Checksum, which is a unique number, based on the content of the file.

There are two elements, CheckSumValue (value of the checksum) and

CheckSumType (the type of checksum e.g., 64bit long).

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element ref="CheckSumType" minOccurs="0"/>

<xs:element name="CheckSumValue" type="xs:string" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="CheckSumType">

<xs:annotation>

<xs:documentation xml:lang="en">

</xs:documentation>

</xs:annotation>

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="12"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="Granulits">

<xs:annotation>

<xs:documentation xml:lang="en">

This container is for multi-file granules or granulits.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:all>

<xs:element name="Granulit" minOccurs="0"/>

</xs:all>

</xs:complexType>

</xs:element>

<xs:element name="Granulit">

<xs:annotation>

<xs:documentation xml:lang="en">

The container is for individual files, or granulit, in

multi-file granules or granulits.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:all>

<xs:element ref="GranulitID"/>

<xs:element ref="FileName"/>

<xs:element ref="CheckSum"/>

<xs:element name="FileSize" type="xs:unsignedLong" minOccurs="0"/>

</xs:all>

</xs:complexType>

</xs:element>

<xs:element name="GranulitID">

<xs:annotation>

<xs:documentation>

The unique identifier for each granule. In most cases this is the

file name.

</xs:documentation>

</xs:annotation>

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="8"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="FileName">

<xs:annotation>

<xs:documentation>

The unique identifier for each granule. In most cases this is the

file name.

</xs:documentation>

</xs:annotation>

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="180"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="FileSize">

<xs:annotation>

<xs:documentation>

Size of each file

</xs:documentation>

</xs:annotation>

<xs:simpleType>

<xs:restriction base="xs:unsignedLong">

<xs:maxLength value="10"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="DayNightFlag">

<xs:simpleType>

<xs:list>

<xs:simpleType>

<xs:union memberTypes="xs:string"/>

</xs:simpleType>

</xs:list>

</xs:simpleType>

</xs:element>

<xs:element name="RangeDateTime">

<xs:annotation>

<xs:documentation xml:lang="en">

The date and time range of the granule. This includes four

elements, RangeEndingTime, RangeEndingDate, RangeBeginningTime

and RangeBeginningDate.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:all>

<xs:element name="RangeEndingDate" type="xs:date"/>

<xs:element name="RangeEndingTime" type="xs:time"/>

<xs:element name="RangeBeginningDate" type="xs:date"/>

<xs:element name="RangeBeginningTime" type="xs:time"/>

</xs:all>

</xs:complexType>

</xs:element>

<xs:element name="SpatialDomainContainer">

<xs:annotation>

<xs:documentation xml:lang="en">

Spatial information on granule. Currently contains two element,

VerticalSpatialDomain and HorizontalSpatialDomainContainer, which

provide information on Vertical fields, and the following horizontal

fields: GPolygon and BoundingRectangle lat/lon coordinates for the

granule.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element name="LocalityValue" minOccurs="0"/>

<xs:element name="ZoneIdentifier" minOccurs="0"/>

<xs:element ref="VerticalSpatialDomain" minOccurs="0"/>

<xs:element ref="HorizontalSpatialDomainContainer" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="VerticalSpatialDomain">

<xs:annotation>

<xs:documentation xml:lang="en">

Contains vertical spatial fields.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element ref="VerticalSpatialDomainContainer" minOccurs="0" maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="VerticalSpatialDomainContainer" >

<xs:annotation>

<xs:documentation xml:lang="en">

Vertical spatial information on the granule. Contains two elements,

a specific vertical spatial type and value.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:all>

<xs:element ref="VerticalSpatialDomainType"/>

<xs:element ref="VerticalSpatialDomainValue"/>

</xs:all>

</xs:complexType>

</xs:element>

<xs:element name="VerticalSpatialDomainType">

<xs:annotation>

<xs:documentation>

Contains specific vertical spatial type.

</xs:documentation>

</xs:annotation>

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="80"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="VerticalSpatialDomainValue">

<xs:annotation>

<xs:documentation>

Contains specific vertical spatial value.

</xs:documentation>

</xs:annotation>

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="80"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="HorizontalSpatialDomainContainer">

<xs:annotation>

<xs:documentation xml:lang="en">

Horizontal spatial information on the granule. Currently contains two

elements, GPolygon and BoundingRectangle.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:all>

<xs:element ref="GPolygon" minOccurs="0"/>

<xs:element ref="BoundingRectangle" minOccurs="0"/>

</xs:all>

</xs:complexType>

</xs:element>

<xs:element name="GPolygon">

<xs:annotation>

<xs:documentation xml:lang="en">

Horizontal spatial information, on the granule, in the GPolygon form.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:all>

<xs:element ref="Boundary"/>

</xs:all>

</xs:complexType>

</xs:element>

<xs:element name="Boundary">

<xs:annotation>

<xs:documentation xml:lang="en">

Boundary of the GPloygon, consisting of a series of points.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element ref="Point" minOccurs="0" maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="Point">

<xs:annotation>

<xs:documentation xml:lang="en">

A GPolygon pint, consisting of a longitude and latitude coordinate.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element ref="ExclusionFlag" minOccurs="0" maxOccurs="1"/>

<xs:element ref="PointLongitude"/>

<xs:element ref="PointLatitude"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="ExclusionFlag">

<xs:annotation>

<xs:documentation>

Indicates whether the polygon should be included or excluded

</xs:documentation>

</xs:annotation>

<xs:simpleType>

<xs:restriction base="xs:string" />

</xs:simpleType>

</xs:element>

<xs:element name="PointLatitude">

<xs:annotation>

<xs:documentation>

decimal degrees (+ = north (default), - = south)

</xs:documentation>

</xs:annotation>

<xs:simpleType>

<xs:restriction base="xs:float">

<xs:minInclusive value="-90.0000"/>

<xs:maxInclusive value="+90.0000"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="PointLongitude">

<xs:annotation>

<xs:documentation>

decimal degrees (+ = east (default), - = west)

</xs:documentation>

</xs:annotation>

<xs:simpleType>

<xs:restriction base="xs:float">

<xs:minInclusive value="-180.0000"/>

<xs:maxInclusive value="+180.0000"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="BoundingRectangle">

<xs:annotation>

<xs:documentation xml:lang="en">

Horizontal spatial information, on the granule, in the

BoundingRectangle form.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element ref="WestBoundingCoordinate"/>

<xs:element ref="NorthBoundingCoordinate"/>

<xs:element ref="EastBoundingCoordinate"/>

<xs:element ref="SouthBoundingCoordinate"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="OrbitCalculatedSpatialDomain">

<xs:annotation>

<xs:documentation xml:lang="en">

Orbit spatial temporal information on the granule.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element ref="OrbitCalculatedSpatialDomainContainer" minOccurs="0" maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="OrbitCalculatedSpatialDomainContainer">

<xs:annotation>

<xs:documentation xml:lang="en">

Orbital Information on the granule. Includes, OrbitNumber,

EquatorCrossingLongitude, EquatorCrossingDate and

EquatorCrossingTime.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element name="OrbitNumber" type="xs:unsignedLong" minOccurs="0"/>

<xs:element name="StartOrbitNumber" minOccurs="0"/>

<xs:element name="StopOrbitNumber" minOccurs="0"/>

<xs:element ref="EquatorCrossingLongitude"/>

<xs:element name="EquatorCrossingDate" type="xs:date" minOccurs="0"/>

<xs:element name="EquatorCrossingTime" type="xs:time"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="EquatorCrossingLongitude">

<xs:annotation>

<xs:documentation>

decimal degrees (+ = east (default), - = west)

</xs:documentation>

</xs:annotation>

<xs:simpleType>

<xs:restriction base="xs:float">

<xs:minInclusive value="-180.0000"/>

<xs:maxInclusive value="+180.0000"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="Platform">

<xs:annotation>

<xs:documentation xml:lang="en">

The platform (short name) the instrument was mounted on. Includes

reference to the instrument container element. The platform

container structure is the same in ECHOs schema. The S4PA Collection

level meta-data uses a platform container, which has the same

structure in GCMD-DIF schema.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element ref="PlatformShortName"/>

<xs:element ref="Instrument" minOccurs="0" maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="Instrument">

<xs:annotation>

<xs:documentation xml:lang="en">

The instrument associated with the sensor. Includes an InstrumentShortName

and reference to sensor container element.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element name="InstrumentShortName">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="20"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element ref="Sensor"  minOccurs="0" maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="Sensor">

<xs:annotation>

<xs:documentation xml:lang="en">

Sensor (short name) used to measure data.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:all>

<xs:element ref="SensorShortName"/>

</xs:all>

</xs:complexType>

</xs:element>

<xs:element name="PSAs">

<xs:annotation>

<xs:documentation xml:lang="en">

PI specific attributes.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element ref="PSA" minOccurs="0" maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="PSA">

<xs:annotation>

<xs:documentation xml:lang="en">

PI specific attribute. Includes, PSAName and PSAValue.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element ref="PSAName"/>

<xs:element ref="PSAValue"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="PSAName">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="50"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="PSAValue">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="500"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="MeasuredParameters">

<xs:annotation>

<xs:documentation xml:lang="en">

PI specific attributes.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element ref="MeasuredParameter" minOccurs="0" maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="MeasuredParameter">

<xs:annotation>

<xs:documentation xml:lang="en">

PI specific attribute. Includes, ParameterName, QAPercentMissing, QAPercentOutofBounds, QAInterpolatedData, AutomaticQualityFlag, AutomaticQualityFlagExplanation, OperationalQualityFlag, OperationalQualityFlagExplanation, ScienceQualityFlag, ScienceQualityFlagExplanation.

</xs:documentation>

</xs:annotation>

<xs:complexType>

<xs:sequence>

<xs:element ref="ParameterName" minOccurs="0"/>

<xs:element ref="QAPercentMissing" minOccurs="0"/>

<xs:element ref="QAPercentOutofBounds" minOccurs="0"/>

<xs:element ref="QAPercentInterpolatedData" minOccurs="0"/>

<xs:element ref="QAPercentCloudCover" minOccurs="0"/>

<xs:element ref="AutomaticQualityFlag" minOccurs="0"/>

<xs:element ref="AutomaticQualityFlagExplanation" minOccurs="0"/>

<xs:element ref="OperationalQualityFlag" minOccurs="0"/>

<xs:element ref="OperationalQualityFlagExplanation" minOccurs="0"/>

<xs:element ref="ScienceQualityFlag" minOccurs="0"/>

<xs:element ref="ScienceQualityFlagExplanation" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

</xs:element>

<xs:element name="ParameterName">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="50"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="QAPercentMissing">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="50"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="QAPercentOutofBounds">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="50"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="QAPercentInterpolatedData">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="50"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="QAPercentCloudCover">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="50"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="AutomaticQualityFlag">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="50"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="AutomaticQualityFlagExplanation">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="500"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="OperationalQualityFlag">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="50"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="OperationalQualityFlagExplanation">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="500"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="ScienceQualityFlag">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="50"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="ScienceQualityFlagExplanation">

<xs:simpleType>

<xs:restriction base="xs:string">

<xs:maxLength value="500"/>

</xs:restriction>

</xs:simpleType>

</xs:element>

<xs:element name="ProducersMetaData">

<xs:annotation>

<xs:documentation xml:lang="en">

This section will contain a copy of the ODL file in a text output format.

</xs:documentation>

</xs:annotation>

</xs:element>

</xs:schema>

Figure 5-2.  S4PA Granule Level Metadata

EXAMPLE ONLY 								EXAMPLE ONLY

GROUP = INVENTORYMETADATA

GROUPTYPE = MASTERGROUP

GROUP = ECSDATAGRANULE

OBJECT = LOCALGRANULEID

NUM_VAL = 1

VALUE = "SORCE_L3_TSI_6M_V0007_20030225_20070126.txt"

END_OBJECT = LOCALGRANULEID

OBJECT = PRODUCTIONDATETIME

NUM_VAL = 1

VALUE = "2007-02-01T03:51:24.000Z"

END_OBJECT = PRODUCTIONDATETIME

OBJECT = LOCALVERSIONID

NUM_VAL = 1

VALUE = "7"

END_OBJECT = LOCALVERSIONID

END_GROUP = ECSDATAGRANULE

GROUP = MEASUREDPARAMETER

OBJECT = MEASUREDPARAMETERCONTAINER

CLASS = "1"

GROUP = QAFLAGS

CLASS = "1"

OBJECT = SCIENCEQUALITYFLAG

NUM_VAL = 1

VALUE = "Not Investigated"

CLASS = "1"

END_OBJECT = SCIENCEQUALITYFLAG

OBJECT = AUTOMATICQUALITYFLAGEXPLANATION

NUM_VAL = 1

CLASS = "1"

VALUE = "The data passed all automatic quality tests"

END_OBJECT = AUTOMATICQUALITYFLAGEXPLANATION

OBJECT = AUTOMATICQUALITYFLAG

NUM_VAL = 1

CLASS = "1"

VALUE = "Passed"

END_OBJECT = AUTOMATICQUALITYFLAG

OBJECT = OPERATIONALQUALITYFLAGEXPLANATION

NUM_VAL = 1

CLASS = "1"

VALUE = "Operational quality not investigated"

END_OBJECT = OPERATIONALQUALITYFLAGEXPLANATION

OBJECT = OPERATIONALQUALITYFLAG

NUM_VAL = 1

CLASS = "1"

VALUE = "Not Investigated"

END_OBJECT = OPERATIONALQUALITYFLAG

END_GROUP = QAFLAGS

GROUP = QASTATS

CLASS = "1"

OBJECT = QAPERCENTMISSINGDATA

NUM_VAL = 1

CLASS = "1"

VALUE = 0

END_OBJECT = QAPERCENTMISSINGDATA

OBJECT = QAPERCENTINTERPOLATEDDATA

NUM_VAL = 1

CLASS = "1"

VALUE = 0

END_OBJECT = QAPERCENTINTERPOLATEDDATA

END_GROUP = QASTATS

OBJECT = PARAMETERNAME

CLASS = "1"

NUM_VAL = 1

VALUE = "GranuleParameters"

END_OBJECT = PARAMETERNAME

END_OBJECT = MEASUREDPARAMETERCONTAINER

END_GROUP = MEASUREDPARAMETER

GROUP = COLLECTIONDESCRIPTIONCLASS

OBJECT = VERSIONID

NUM_VAL = 1

VALUE = 2

END_OBJECT = VERSIONID

OBJECT = SHORTNAME

NUM_VAL = 1

VALUE = "SOR3TSI6"

END_OBJECT = SHORTNAME

END_GROUP = COLLECTIONDESCRIPTIONCLASS

GROUP = SPATIALDOMAINCONTAINER

GROUP = GRANULELOCALITY

OBJECT = LOCALITYVALUE

NUM_VAL = 1

VALUE = "Global"

END_OBJECT = LOCALITYVALUE

END_GROUP = GRANULELOCALITY

END_GROUP = SPATIALDOMAINCONTAINER

GROUP = RANGEDATETIME

OBJECT = RANGEENDINGDATE

NUM_VAL = 1

VALUE = "2007-01-26"

END_OBJECT = RANGEENDINGDATE

OBJECT = RANGEENDINGTIME

NUM_VAL = 1

VALUE = "21:00:00.0"

END_OBJECT = RANGEENDINGTIME

OBJECT = RANGEBEGINNINGDATE

NUM_VAL = 1

VALUE = "2003-02-25"

END_OBJECT = RANGEBEGINNINGDATE

OBJECT = RANGEBEGINNINGTIME

NUM_VAL = 1

VALUE = "03:00:00.0"

END_OBJECT = RANGEBEGINNINGTIME

END_GROUP = RANGEDATETIME

GROUP = PGEVERSIONCLASS

OBJECT = PGEVERSION

NUM_VAL = 1

VALUE = "1.0"

END_OBJECT = PGEVERSION

END_GROUP = PGEVERSIONCLASS

END_GROUP = INVENTORYMETADATA

Figure 5-3.  Example S4PA ODL Metadata File

# Abbreviations and Acronyms

AIRS	Atmospheric Infrared Sounder

AMSU-A	Advanced Microwave Sounding Unit - Version A (AMSU-A1 and AMSU-A2)

APID	Application Processor Identifier

ANGe	Archive Next Generation

ARP	Address Resolution Protocol

ASCII	American Standard Code for Information Interchange

ASDC	Atmospheric Sciences Data Center

BGP	Border Gateway Protocol

BNF	Backus-Naur Form

BRTEMP	Brightness Temperature

BUV	Backscatter Ultraviolet

CCB	Configuration Control Board

CCR	Configuration Change Request

CCSDS	Consultative Committee for Space Data Systems

CERES	Clouds and Earth's Radiant Energy System

DAAC	Distributed Active Archive Center

DAO	Data Assimilation Office (now part of the GMAO)

DAP	Delivered Algorithm Package

DAS	Data Assimilation System

DASCE	Data Assimilation System Computing Environment

DES	Digital Encryption Standard

DEM	Digital Elevation Model

DCN	Document Change Notice

DIF	Data Interchange Format

DISC	Data and Information Services Center

DLT	Digital Linear Tape

DN	Distribution Notice

DOAS	Differential Optical Absorption Spectroscopy

DPREP	Data Pre-Processing

DPS	DAAC Processing System

DTD	(XML) Document Type Definition

EASE	Equal-Area Scalable Earth (grid)

EDS	Expedited Data Set

EBnet	EOSDIS Backbone Network

ECHO  	EOS ClearingHOuse

EDG	EOS Data Gateway

ECS	EOSDIS Core System

EDOS	EOS Data and Operations System

EGID	External Granule ID

EGS	EOS Ground System

EMSn	EOS Mission Support Network

EOS	Earth Observing System

EOSDIS	EOS Data and Information System

ESDIS	Earth Science Data and Information System

ESDT	Earth Science Data Type

ESE	Earth Science Enterprise

ESSn	EOS Science Support network

ESSP	Earth System Science Pathfinder Project

FMI	Finnish Meteorological Institute

FNL	Final Analysis and Forecast System, Global Analysis

FTP	File Transfer Protocol

GB	Giga Byte

GCMD	Global Change Master Directory

GES	GSFC Earth Sciences

GogE	Gigabit Ethernet

GMAO	Global Modeling and Assimilation Office

GOES	Geostationary Operational Environmental Satellite

GPCC	Global Precipitation Climatology Centre

GPI	GOES Precipitation Index

GRIB	GRid In Binary

GSFC	Goddard Space Flight Center

GUI	Graphical User Interface

HIRDLS	High Resolution Dynamics Limb Sounder

HDF	Hierarchical Data Format

HDF-EOS	Hierarchical Data Format – Earth Observing System

HSB	Humidity Sounder for Brazil

ICD	Interface Control Document

ICMP	Internet Control Message Protocol

IETF	Internet Engineering Task Force

IP	Internet Protocol

ISO	International Standards Organization

JPL	Jet Propulsion Laboratory

JPIP	Joint Project Implementation Plan

KNMI	Royal Netherlands Meteorological Institute

L0	Level 0

L1A	Level 1A

L1B	Level 1B

L2	Level 2

LaRC	Langley Research Center

LASP	Laboratory for Atmospheric and Space Physics

LAN	Local Area Network

LATIS	Langley TRMM Information System

LGID	Local Granule Identifier

LID	Logical ID

LP DAAC	Land Processes (DAAC)

MB	Mega Byte

MCF	Metadata Configuration File

MD5	Message Digest

MLS	Microwave Limb Sounder

MODAPS	MODIS Data Processing System

MODIS	Moderate Resolution Imaging Spectroradiometer

MO&IS	Mission Operations and Information Systems

MOU	Memoranda of Understanding

MRF	Medium Range Forecast System

MW	Microwave

NASA	National Aeronautics and Space Administration

NCDC	National Climatic Data Center (NOAA)

NCEP		National Center for Environmental Prediction

NESDIS	National Environmental Satellite Data and Information Service

NIR	Near-Infrared

NIVR	Netherlands Agency for Aerospace Programmes

NMC	National Meteorological Center (NOAA)

NOAA	National Oceanic and Atmospheric Administration

NRT	Near Real Time

NSI	NASA Science Internet

NSIDC	National Snow and Ice Data Center (DAAC)

OA	Operations Agreement

ODL	Object Description Language

ODPS 	OMI Dutch Processing System

OMI	Ozone Monitoring Instrument

OSF	Observation Schedule File

OSI	Open Systems Interconnection

OSIPA	OMI SIPS

PAN	Production Acceptance Notification

PDR	Product Delivery Record

PDRD	Product Delivery Record Discrepancy

PI	Principal Investigator

PSA	Product Specific Attribute

PVL	Parameter Value Language

QA	Quality Assurance

RFC	Request For Comments

RIP	Routing Information Protocol

S4PA	Simple, Scalable Script-based Science Processor Archive

SCF	Science Computing Facility

scp	Secure Copy

SDP	Science Data Processing

SDPS	Science Data Processing Segment

SFTP	Secure FTP

SIPS	Science Investigator-led Processing System

S-MOC	SORCE Mission Operations Center

S-SOC	SORCE Science Operations Center

SMOBA	Stratosphere Monitoring Group Ozone Blended Analysis

SMTP	Simple Mail Transport Protocol

SORCE	Solar Radiation and Climate Experiment

SSE	Science System Element

SSH	Secure Shell

SSIT	Science Software Integration and Test

SSM/I	Special Sensor Microwave/Imager

TAI	Universal Atomic Time

TAR	Tape Archive

TBD	To Be Determined

TBR	To Be Resolved

TBS	To Be Supplied

TCP	Transmission Control Protocol

TCP/IP	Transmission Control Protocol/Internet Protocol

TL	Team Leader

TLCF	Team Leader Computing Facility

TMI	TRMM Microwave Imager

TOMS	Total Ozone Mapping Spectrometer

TRMM	Tropical Rainfall Measuring Mission

UARS	Upper Atmosphere Research Satellite

UE	University of Edinburgh

UR	Universal Reference (an ECS construct)

URL	Universal Resource Locator

UV	Ultraviolet

UV-B	Ultraviolet-B

VIRS	Visible and Infrared Scanner

VIS	Visible

WIST	Warehouse Inventory Search Tool

XML	eXtensible Markup Language

This page intentionally left blank.