# IRRIGATION SYSTEM, SPRINKLER

## PRACTICE INTRODUCTION

USDA, Natural Resources Conservation Service―Practice Code 442

### IRRIGATION SYSTEM, SPRINKLER

An irrigation system is a system in which all necessary equipment and facilities are installed for efficiently applying water by means of nozzles operated under pressure.

### PRACTICE INFORMATION

Sprinkler irrigation systems are used to achieve one or more of the following purposes:

Efficient and uniform application of irrigation water to maintain adequate soil water for plant growth and production without causing excessive water loss, erosion, or water quality impairment

Control of and/or modification of climate

Application of chemicals, nutrients, and/or wastewater

Reduction of particulate matter emissions to improve air quality

Common sprinkler systems on agricultural lands include fixed solid-set, big gun, periodic move

and traveling sprinkler systems. Application rate and depth of application are based on the specific soils and crops. Runoff, translocation, and deep percolation are minimized. Distribution patterns, spacing, and operating pressure control the application rate. Systems used for chemigation or fertigation must meet industry-accepted wash-off and total rinse-out times.

### COMMON ASSOCIATED PRACTICES

Irrigation System, Sprinkler is commonly used in a Conservation Management System with practices such as:

Water Well (642)

Pumping Plant (533)

Irrigation Water Conveyance (428 series)

Irrigation Water Management (449)

For further information, refer to the practice standard in the local Field Office Technical Guide and associated practice specifications and job sheets.

# Text boxes

I.7 (+/-) Net return

I.6 (+) Potential income

D.4 (+) Cost of installation, operation, and maintenance

I.1 (-) Water for other downstream uses

Irrigation Water Management (449)

Mulching (484)

Residue management practices

Pest Management (595)

Nutrient management (590)

C.3 (+/-) Quality of receiving waters

C.1 (+/-) Fish and wildlife habitat and biodiversity

I.8 (+) Agri-chemical use efficiency

I.11 (+) Potential income

D.6 (+) Erosion potential; (+) potential for deep percolation

D.3 (+) Frost protection of crop

D.1 (+) Water use

D.4 (+) Cost of installation, operation, and maintenance

I.5 (-) Withdrawals from aquifers or streams

D.2 (+) Water delivery to crop

Irrigation Water Management (449)

Note: Effects are qualified with a plus (+) or minus (-).  These symbols indicate only an increase (+) or a decrease (-) in the effect upon the resource, not whether the effect is beneficial or adverse.

Mitigating practice

(+) increase; (-) decrease

Pathway

C.  Cumulative effect

I.  Indirect effect

D.  Direct effect

#.  Created by practice

LEGEND

I.9 (+) Biomass

D.5 (+) Agri-chemicals delivery to crop

1. Pipeline with sprinkler heads

Start

Irrigation System, Sprinkler

10/2008

I.3 (+) Crop vigor and production

I.12 (+/-)    Net return

Initial setting: Agricultural land where irrigation is needed to enhance plant growth; new irrigation/chemigation system to be installed where none previously existed

C.2 (+/-) Income and income stability (individuals and community)

Irrigation System, Sprinkler (442)

(New System)

I.10 (+) Soil quality

I.4 (+) Biomass

Pest Management (595)

Nutrient management (590)

C.3 (+) Quality of receiving waters

C.1 (+) Fish and wildlife habitat and biodiversity

I.1 (+) Agri-chemical use efficiency

I.6 (+) Water for other downstream uses

D.3 (+) Frost protection of crop

D.1 (+) Water use efficiency

D.2 (+) Water delivery to crop

Irrigation Water Management (449)

Note: Effects are qualified with a plus (+) or minus (-). These symbols indicate only an increase (+) or a decrease (-) in the effect upon the resource, not whether the effect is beneficial or adverse.

Associated practice

Mitigating practice

(+) increase; (-) decrease

Pathway

C.  Cumulative effect

I.  Indirect effect

D.  Direct effect

#.  Created by practice

LEGEND

D.5 (+) Agri-chemicals delivery to crop

1. Pipeline with sprinkler heads (improved efficiency)

Start

Irrigation System, Sprinkler                                                   10/2008

I.8 (+) Crop vigor and production

Initial setting: Agricultural land where irrigation is needed to enhance plant growth, and the existing irrigation/chemigation system is determined to be inefficient (will be replaced with a more efficient system)

C.2 (+/-) Income and income stability (individuals and community)

Irrigation System, Sprinkler (442)

(Replacement of Existing System)

I.3 (-) Transport of pesticides, nutrients and organics to surface waters

I.2 (-) Potential for runoff

I.4 (-) Irrigation-induced erosion, sedimentation

I.5 (+) Soil quality

I.2 (+) Energy use

I.9 (-) Energy use

I.7 (-) Energy use

I.1 (-) Potential for deep percolation