Land Clearing

Vermont Conservation Practice Job Sheet	460

Definition

Removing trees, stumps, and other vegetation from wooded areas.

Purpose

To achieve needed land use adjustments and improvements in the interest of soil and water conservation and in keeping with the capabilities of the land.

Where used

This practice applies to wooded areas where the removal of trees, stumps, brush, and other vegetation is needed in carrying out a soil and water conservation plan, and the land to be cleared will be used according to its capabilities.

Considerations

The method, intensity and timing of land clearing will match the limitations of the site, equipment, and the purpose for removing the vegetation.

An appropriate land clearing method will be chosen to protect any desirable vegetation, wetlands, wildlife habitat and cultural resources.

Remaining debris shall not create habitat for or harbor harmful levels of pests.

Remaining debris shall not hinder needed access, drainage or create an undue fire hazard.

Erosion and/or runoff will be controlled by appropriate erosion control practices.

Soil compaction and displacement will be minimized.

Comply with applicable federal, state and local laws and regulations during the installation, operation and maintenance of this practice including “Vermont’s Acceptable Management Practices for Maintaining Water Quality on Logging Jobs in Vermont” (AMP’s).

The land clearing method should be cost effective and protect cultural resources, wildlife habitat, threatened and endangered species, water resources, and identified unique areas.

Visual quality objectives should be considered when selecting land clearing methods.

Anticipate possible off-site effects and modify the land clearing design accordingly.

Consider personnel safety during land clearing activities.

Operation and maintenance

An Operation and Maintenance Plan shall be prepared and implemented by the landowner or operator responsible for the land clearing.  The plan shall be effective from the time the land clearing operation is started to the time the intended land use is established.  The plan includes at a minimum a method to establish and maintain desired vegetative cover to prevent erosion, measures to protect watercourses from sedimentation and contaminants, and use of mechanical treatments and chemical applications to control undesired species.

Specifications

Site-specific requirements are listed on the specifications sheet. Additional provisions are entered on the job sketch sheet. Specifications are prepared in accordance with the VT NRCS Field Office Technical Guide. See practice standard for Land Clearing, code 460 for specific requirements.

Land Clearing – Job Sheet

If needed, an aerial view or a side view of the practice can be shown below. Other relevant information, complementary practices and measures, and additional specifications may be included.

Scale 1"=________ ft. (NA indicates sketch not to scale: grid size=1/2" by 1/2")                                                    ↑N

Additional Specifications and Notes: (Indicate from methods table field and acres corresponding to additional notes)

The United States Department of Agriculture (USDA) prohibits discrimination in its programs on the basis of race, color, national origin, sex, religion, age, disability, political beliefs and marital or familial status.  (Not all prohibited bases apply to all programs.) Persons with disabilities who require alternative means for communication program information (Braille, large print, audiotape, etc.) should contact the USDA Office of Communications (202) 720-2791.

To file a complaint of discrimination write USDA, Director, Office of Civil Rights, Room 326-W, Whitten Building, 14th and Independence Avenue, SW, Washington, DC 20250-9410 or call (202) 720-5964 (voice or TDD). USDA is an equal opportunity provider and employer.

Land Clearing – Job Sheet

| For: | Farm #: |
| --- | --- |
| Field(s): | Tract #: |
| Designed By: Drawing No(s).: | Approved By: Signature: |
| Date: | Date: |

| Purpose (check all that apply) |
| --- |
| Adjusting land use in interest of soil & water conservation | Improvement to existing land use for soil & water conservation |

| Adjusting land use for fish and wildlife habitat | Improvement to existing land use for fish and wildlife habitat |
| --- | --- |

| Land Clearing Layout and Methods (Refer to VT Standard & Specification Land Clearing, 460 for specific requirements) |
| --- |
| Field | Acres | Vegetation Removal Method, including equipment types | Date | Number of access roads, skid trails, log landings | Debris Removal Method1 |

Note: For clearcut harvesting refer to VT Heavy Cutting Rules for specific requirements and notifications.

NEPA requirements met, including cultural resource assessment?_____  Permits required?______Permit No._______ (if Yes)

1Specify debris removal method – Options are:

Contour windrows - Usually vegetation is pushed into contour windrows, especially if the area is to be planted by machine. These piles should be high, narrow, and compact. See standard 460 for appropriate berm pile length, width, height and distance between piles. Width_____________, Length__________________, Height___________, Distance between piles_______________.

Burn – all burns must be conducted by personnel certified for prescribed burning and in accordance with all federal, state and local laws and regulations.

Bury –Select areas that are deep to bedrock and where remaining fill can be spread without increasing erosion and sedimentation.

Limits of Area to be cleared:

Location of disposal areas:

Locations of areas off limits to disposal:

Location of trees and woody materials to be left undisturbed:

Operation and Maintenance: Measures to control erosion, sedimentation and contamination during and after the land clearing until the intended land use is established : Measures to avoid and protect wildlife habitat, wetlands, cultural resources, and other environmental sensitive areas: Weed (especially non-native, invasive species) control measures during and after the land clearing until the intended land use is established:

Installation shall be in accordance with the specified drawings, specifications, and special requirements.  No changes are to be made in the drawings or specifications without prior approval of {name of technical specialist} at {phone number}.

Questions regarding the planting or maintenance of the tree/shrub establishment should be directed to [name of technical specialist], at [phone number].