| NRCS Natural Resources Conservation Service | LAND SMOOTHING Conservation Practice Job Sheet 466 |
| --- | --- |
| April 2003 |
| Client: |  | Tract: |  | Farm No. |  | Field No.: |  |
| Farm/Ranch Location: |  | County: |  | Acre(s): |  | Date: | 4/8/03 |
| Program: |  | Contract Item #: |  | Planned Installation Date: |  |
| Drawing No.:NM-E- |  |
| Definition: |

Removing irregularities on the land surface by use of special equipment.

Purpose:

To improve surface drainage, provide for more effective use of precipitation, obtsin more uniform planting depths, provide for more uniform cultivation, improve equipment operation and efficiency, improve terrace alignment, and facilitate contour cultivation.

Requirements:

- It shall be the responsibility of the owner / leasee to obtain all necessary permits and/or rights, and to comply with all ordinances and laws pertaining to this installation.

- On Federal, State, or Tribal lands, or when Federal funding is involved on private land, the landowner / leasee must have archaeological clearance and approval / permit from the responsible permitting agency prior to any earth moving.  If during installation, any cultural resources, historical resources, threatened or endangered species are found, the landowner / leasee must cease operations and obtain archaeological clearance and approval / permit from the responsible permitting agency prior to continuing construction.

- NRCS assumes no responsibility for interference with private or public utilities or facilities.

- Supporting data for this practice are to include a record of planning, design, installation, checking, and maintenance necessary to ensure an effective practice.  Location identification is required.

- Installation shall be in accordance with the drawings, specifications, and special requirements.

- The following additional data is required: Area treated, equipment used, and number of passes made.

Practice Classification and Approval (NEM Section 501):

Job Class is based upon the following limiting element from Conservation Specification 466:

| Area Benefited | __________Acres |
| --- | --- |
| Job Class | __________ |

Design Approved By: ___________________________________ Date: ____________________________

NRCS Representative

Landowner/Operator Acknowledgement and Acceptance:

The landowner/operator acknowledges that:

- They have received a copy of the approved construction drawings and specifications, and understand the contents and requirements.

- Maintenance of the installed work is necessary for proper performance for the life of the practice.  All federal cost shared practices must be maintained to these specifications for the expected life of the practice.

Accepted by: ____________________________________; Date: _____________________

Landowner/Operator

Practice Completion:

I have made an on-site inspection (or I am accepting owner/contractor documentation located in the case file).       I have determined that the job, as installed, conforms to the drawings and specifications and that ______ Acres of Land Smoothing was performed according to Conservation Specification 466.

Accepted by: _____________________________; Job Title: ___________________; Date: ____________

Authorized NRCS Representative