Tree/Shrub Site Preparation

Conservation Practice Job Sheet	VT-490

Definition

Treatment of areas to improve site conditions for establishing trees and shrubs.

Purpose

•	Encourage natural regeneration of desirable woody plants.

•	Permit artificial establishment of woody plants.

Where used

On all lands where establishment of woody plants is desired and practical.

NOTE: The Tree/Shrub Establishment (Code 612) Job Sheet should always be used in conjunction with this job sheet.

Considerations

The method, intensity and timing of site preparation will match the limitations of the site, equipment, and the requirements of the desired woody species.

An appropriate site preparation method will be chosen to achieve the intended purpose and to protect any desirable vegetation, site and soil conditions.  Other complementary practices and measures will be used as necessary to control erosion, runoff, compaction and displacement to acceptable levels.

Slash and debris shall be removed, treated or eliminated as appropriate.  Refer to the standard Forest Slash Treatment, 384.

Remaining slash and debris shall not create habitat for or harbor harmful levels of pests.

Remaining slash and debris shall not hinder needed equipment operations or create an undue fire hazard.  Refer to the standard Prescribed Burning, 338, for slash and debris that will be burned.

Measures, including the use of equipment, will be implemented to control or protect against locally invasive and noxious species that may arise from site preparation activities.  If pesticides are used, refer to the standard Pest Management, 595.

Comply with applicable federal, state and local laws and regulations during the installation, operation and maintenance of this practice including “Vermont’s Acceptable Management Practices for Maintaining Water Quality on Logging Jobs in Vermont” (AMP’s) and “Wetlands Rules and Regulations: What they mean to your logging operation in Vermont”.

Impacts on wildlife species, habitat and aesthetics should be considered when selecting site preparation methods.

Particulates, smoke, and other air pollutants generated by site preparation may have on-site and off-site effects on air quality.

Operation and maintenance

Maintain erosion control measures as necessary.

Control locally invasive and noxious plants as necessary.  If pesticides are used, refer to the standard Pest Management, 595.

Access by vehicles or equipment during or after site preparation shall be controlled to minimize erosion, compaction and other site impacts.  Refer to the standard Use Exclusion, 472.

Specifications

Site-specific requirements are listed on the specifications sheet. Additional provisions are entered on the job sketch sheet. Specifications are prepared in accordance with the VT NRCS Field Office Technical Guide. See practice standard and Supplemental Specifications for Tree/Shrub Site Preparation, code 490 for specific requirements.

Tree/Shrub Site Preparation – Job Sheet

| For: | Farm #: |
| --- | --- |
| Field(s): | Tract #: |
| Designed By: | Approved By: Signature: |
| Date: | Date: |

| Purpose (check all that apply) |
| --- |
| Encourage natural regeneration of desirable woody plants | Permit artificial establishment of woody plants |

| Site Preparation for: (check all that apply) (Refer to VT Standard & Specification Tree/Shrub Site Preparation, 490 for specific requirements) |
| --- |
| Natural Regeneration after harvest | Artificial Regeneration in undesirable forest or brush |
| Natural Regeneration for forested wetland restoration | Artificial Regeneration in field |
| Other | Other |

| Site Preparation Method (Refer to VT Standard & Specification Tree/Shrub Site Preparation, 490 for specific requirements) |
| --- |
| Field | Acres | Method1 | Date | Remarks |

1Specify method, - Options are:

Chemical - provide product name, strength and amount used, and purpose in remarks column (For recommendations refer to the most recent New England Guide to Chemical Weed and Brush Control in Christmas Trees)

Mechanical-hand (girdling or removing the outer bark of vegetation)

Mechanical-machine in Fields-mowing (used for abandoned pasture and cropland)/harrowing, disking or plowing (used for cleared areas, sodded areas and on areas lightly covered with brush)/subsoiling (mainly for white pine regeneration in fields with a plow-caused hardpan soil layer)/bedding (for high water tables, that are not wetlands)

Mechanical-machine in Brush and Woods-logging (disturbs soil)/chopping (used on brush and small tree diameter ≤ 5 inches)/shearing (used on vegetation diameter ≥ 8 inches)/blading (removal of all vegetation using a straight-blade dozer).  Usually vegetation is pushed into contour windrows, especially if the area is to be planted by machine.  Windrowing is usually an added expense and should be noted in the remarks column.

Prescribed burning – all burns must be conducted by personnel certified for prescribed burning and in accordance with all federal, state and local laws and regulations.

Shelterwood, Seed-tree or Clearcut harvesting systems Refer to VT Standard and Specification 490 for specific requirements.

NEPA requirements met, including cultural resource assessment?_____  Permits required?______Permit No._______ (if Yes)

Questions regarding the planting or maintenance of the tree/shrub establishment should be directed to State Resource Specialist, at (802)951-6796.

Tree/Shrub Site Preparation – Job Sheet

If needed, an aerial view or a side view of the practice can be shown below. Other relevant information, complementary practices and measures, and additional specifications may be included.

Scale 1"=________ ft. (NA indicates sketch not to scale: grid size=1/2" by 1/2")

Additional Specifications and Notes: (Indicate from methods table field and acres corresponding to additional notes)

The United States Department of Agriculture (USDA) prohibits discrimination in its programs on the basis of race, color, national origin, sex, religion, age, disability, political beliefs and marital or familial status.  (Not all prohibited bases apply to all programs.) Persons with disabilities who require alternative means for communication program information (Braille, large print, audiotape, etc.) should contact the USDA Office of Communications (202) 720-2791.

To file a complaint of discrimination write USDA, Director, Office of Civil Rights, Room 326-W, Whitten Building, 14th and Independence Avenue, SW, Washington, DC 20250-9410 or call (202) 720-5964 (voice or TDD). USDA is an equal opportunity provider and employer.