MSFC PRACA : 2003-02-12 07:54

MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A02499 | In-Flight Anomaly Number -- | Contractor Report Number E-047 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LO2 ULLAGE PRESSURE TRANSDUCER INDICATES OPEN CIRCUIT |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl N | Misc Codes A B (X) C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE LO2 ULL PRES TRNSDCR | PART# PD7400098-029 | SER/LOT# 123 & 490 | MANUFACTURER GULTON |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE LO2 ULL PRES TRNSDCR | PART# PD7400098-029 | SER/LOT# 123 & 490 | MANUFACTURER GULTON |
| Test/Operation A - ATP | Prevailing Condtion -- | F / U F | Fail Mode -- | Cause -- |
| System ELECTRICAL | Defect -- | Material -- | Work Contact S. BRAGG | Fail Date 12/17/1980 |
| Received at MSFC 01/28/1981 | Date Isolated -- | FMEA Reference 3.1.1.9 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location NSTL/CSC | Symptom -- | Time Cycle -- |
| Effectivity Text NONE |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 05/03/1989 | CN RSLV SBMT 02/17/1981 | Defer Date -- | Add Date -- | R/C Codes 4 - TEST -- -- |
| Assignee |
| Design L. GUZINSKY | Chief Engineer -- | S & MA D. NEWMAN | Project R. ABRAHAM | Project MGR -- |
| Approval |
| Design L. GUZINSKY | Chief Engineer -- | S & MA D. NEWMAN | Project R. ABRAHAM | Project MGR -- |
| PAC Assignee C. NEWTON | PAC Review Complete CN | MSFC Closure Date 03/20/1981 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description 1) REF: MARS T38785 2) TRANSDUCER S/N 123 FAILED CALIBRATION TESTING AT NSTL/CSC. TRANSDUCER INDICATED SHORTED TURNS AT HIGH END OF RANGE. 3) TRANSDUCER S/N 490 FAILED CALIBRATION TESTING AT NSTL/CSC. TRANSDUCER INDICATED AN OPEN CIRCUIT AT THE LOW END |
| Contractor Investigation/Resolution 1) CAUSE: A) FAILURE ANALY WAS PERFORMED ON S/N 123 AT GULTON, SCD RESULTS INDICATED THAT RESISTIVE ELEMENT WAS SHORTED AT THE HIGH END (22-30 PSID) DUE TO HIGH CURRENT. B) FAILURE ANALY WAS PERFORMED ON S/N 490 AT GULTON, SCD. RESULTS INDICATED THAT RESISTIVE ELEMENT WAS OPEN AT THE LOW END (0-2 PSID) DUE TO HIGH CURRENT. 2) INVESTIGATION: FAILURE ANALY HAS SHOWN THAT EXCESSIVE CURRENT THROUGH THE ELEMENT WINDINGS OF THESE TRANSDUCERS RESULTED IN FAILURE. A COMPLETE REVIEW OF EACH UNIT'S ACCEPTANCE TEST RECORD. SHOWS THEM TO HAVE BEEN GOOD AT THE TIME OF ACCEPTANCE. THESE FACTS, ALONG WITH A REVIEW OF THE UNITS' HISTORICAL RECORDS WHICH VERIFY THAT THEY HAVE NEVER BEEN INSTALLED OR ELECTRICALLY/ PRESSURE TESTED OTHER THAN AT NSTL/CSC SINCE DELIVERY, IDENTIFY THE CAUSE OF THESE FAILURES TO HAVE BEEN OPERATOR ERRORS DURING CALIBRATION OPERATION. THEREFORE, THIS PROBLEM IS NOT CONSIDERED A CONSTRAINT TO STS-1. CAPS E-041A CLOSURE REC'D 2-17-81, BACKUP DATA MAILED. INVESTIGATION: CORRECTIVE ACTION DIRECTIVE (CAD) 3741-81-002 HAS BEEN GENERATED TO ESTABLISH & IM APPROPRIATE CORRECTION ACTIONS. A COPY IS ATTACHED TO THIS CAPS. COORDINATION WITH KSC REVEALS THAT BENCH CALIBRATION OF THESE UNITS IS NOT PERFORMED AT KSC. UNITS REQUIRING CALIBRATION ARE SENT TO NSTL/CSC. FURTHERMORE, MAF DOES NOT PERFORM BENCH CALIBRATION; THEY ALSO, RETURN UNITS TO NSTL/CSC. 3) RESOLUTION: THE TEST CALIBRATION PROCEDURE AT NSTL/CSC HAS BEEN CHANGED TO REFLECT A CAUTION FOR STEP (2)C WHICH ENERGIZES THE CURRENT LIMITER TO 1.0 MA ON THE TEST EQUIPMENT. IN ADDITION, TECHNICIANS HAVE BEEN VERBALLY INSTRUCTED TO USE THE CURRENT LIMITING MODE (REF REPLY TO CAD 3741-81-002). EFFECTIVITY: NONE. 3/3/81 - CLOSURE DISTRIBUTED |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A02499 | IFA# -- | Contractor RPT# E-047 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# -- | Asmnt Part Name -- | Asmnt Serial/Lot# -- |
| HCRIT CD -- | FCRIT CD -- | CAUSE CD -- | FAIL MODE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |