4910.1

TABLE OF CONTENTS

Page

CHAPTER 5      MATERIALS

500       GENERAL ------------------------------------------  5-3

500-1     Materials ----------------------------------------  5-3

507       THERMAL AND MOISTURE PROTECTION ------------------  5-3

507-1     Building Insulation ------------------------------  5-3

507-2     Caulking and Joint Sealants ----------------------  5-3

508       DOORS, WINDOWS, GLAZING PANELS -------------------  5-3

508-1     Performance Testing ------------------------------  5-3

508-2     Metal Doors and Frames ---------------------------  5-4

508-3     Wood Doors ---------------------------------------  5-4

508-4     Metal Windows ------------------------------------  5-4

508-5     Wood Windows -------------------------------------  5-5

508-6     Hardware -----------------------------------------  5-5

509       FINISH MATERIALS ---------------------------------  5-6

509-1     Exterior Wall Finishes ---------------------------  5-6

509-2     Finish Flooring, Rigid ---------------------------  5-6

509-3     Finish Flooring, Resilient -----------------------  5-7

509-4     Carpets and Mats ---------------------------------  5-9

509-5     Painting -----------------------------------------  5-9

513       SPECIAL CONSTRUCTION MATERIALS -------------------  5-9

513-1     Definition ---------------------------------------  5-9

513-2     Usage --------------------------------------------  5-9

513-3     Requirements for Acceptance ----------------------  5-9

5-1

1994

_____________________________________________________________________

4910.1

CHAPTER 5

MATERIALS

500       GENERAL

500-1     MATERIALS

Materials installed shall be of such kind and quality to

ensure that the dwelling will provide acceptable

durability, economy of maintenance and adequate

resistance to weather, moisture, corrosion and fire.  The

local HUD Field Office may request evidence of a

material's compliance with the requirements of the

structure's plans and specifications and these MPS.

Product labels are considered acceptable evidence.

507       THERMAL AND MOISTURE PROTECTION

507-1     BUILDING INSULATION

Materials used for insulation shall be of proven

effectiveness and adequate durability so as to ensure

that required design specifications concerning heat

transmission, sound control and fire rating are attained.

Insulation in contact with the ground shall be installed

so as not to be adversely affected by soil, vermin and

water.

507-2     CAULKING AND JOINT SEALANTS

Materials used for caulking and sealants shall be

suitable for the use intended, and shall be compatible

with the materials to which they are applied and with any

finish that may be applied over them.

508       DOORS, WINDOWS, GLAZING PANELS

508-1     PERFORMANCE TESTING

All windows and sliding glass doors shall be tested for

air infiltration, water penetration and physical loading

as set forth in Appendix D.  The test unit shall be

either the largest size marketed by the manufacturer or

the size designated in the referenced standard.  All

windows and sliding glass doors shall meet or exceed the

minimum performance levels set forth in Appendix D.

5-3

1994

_____________________________________________________________________

4910.1

508-2     METAL DOORS AND FRAMES

508-2.1   Steel Doors

a.   Each interior and exterior steel door shall bear

the manufacturer's certification that the product

complies with the applicable standard.

b.   Each steel sliding glass door unit shall bear a

label that identifies the manufacturer, certifies

compliance with the tests required in Appendix D,

identifies the certifying organization, and states

the maximum size of the unit tested.

508-2.2   Aluminum Doors

Each aluminum sliding glass door and aluminum storm door

shall bear the label of an independent inspection agency.

The label shall identify the manufacturer by name or

symbol, and shall certify compliance with the applicable

standard.

508-3     WOOD DOORS

508-3.1   Materials

a.   Doors may be complete manufactured units or stock

doors and frames.  Job-built wood frames may be

used.

b.   Entrance doors shall be of exterior type as defined

in the applicable referenced standard and not less

than 1-3/4 in. thick.  Service doors (where

temperature is near the same on both sides) may be

1-3/8 in. thick.  Exterior door frames shall be

treated against decay.

c.   Interior hinged doors shall be not less than 1-3/8

in. thick.  Closet doors may be 1-1/8 in thick,

provided that warp does not exceed 1/4 in.

508-4     METAL WINDOWS

508-4.1   General

Where metal windows or sliding glass doors are used in

areas subject to a winter design temperature of 100 degree F or

lower, insulating frames shall be provided.  These

5-4

1994

_____________________________________________________________________

4910.1

windows or doors shall comply with AAMA 1503.1-88,

Condensation Resistance of Windows, Doors and Glazed Wall

Sections.  Where wood is to be used as the insulator, it

shall be treated with a water repellent preservative.

Storm sash are acceptable to serve this purpose if a

thermal separation is provided between the prime and the

storm window, where both window frames are metal.

508-4.2   Steel Windows

Steel windows shall bear a label that identifies the

manufacturer, certifies compliance with the tests

required in Section 508-1, identifies the certifying

organization, and states the maximum size of the unit

tested.

508-4.3   Aluminum Windows

Aluminum windows shall bear the label of an independent

inspection agency.  The label shall identify the

manufacturer by name or symbol, and shall certify

compliance with the applicable standard.

508-5     WOOD WINDOWS

508-5.1   Operating Wood Windows

Operating windows shall be manufactured units consisting

of the frame, sill, sash, weatherstripping and operating

hardware.  Job site assembled windows composed of frames

and sashes made by different manufacturers are not

acceptable.

Each operating wood window unit shall bear the label of

an independent inspection agency.  The label shall

identify the manufacturer by name or symbol and shall

certify compliance with the applicable standard.

508-5.2   Fixed Sash Windows

Fixed sash windows such as picture windows and bay

windows, may be manufactured, job-built or job assembled

units.

508-6     HARDWARE

508-6.1   Hardware shall comply with Section 402-1.2.  Locks shall

meet or exceed the performance criteria of ANSI A156.2-89

for the series and grades as follows:

5-5

1994

_____________________________________________________________________

4910.1

a.   Building entrance doors serving more than two

families, series 4000, grade 1.

b.   Living unit entrance doors and building entrance

doors serving one or two families, series 4000,

grade 2.

c.   Doors within living units, series 4000, grade 3.

The performance criteria are contained in Sections 7, 8,

and 9 of ANSI A156.2-89.  Evidence of conformance shall

be provided to the HUD Field Office upon request.

Three butt hinges shall be used on all exterior doors.

508-6.2   Labeling

Locks shall be labeled as complying with the performance

criteria of the applicable series and grade of ANSI

A156.2-89.  This information shall appear on the lock, in

the installation instructions or on the packing box.

509       FINISH MATERIALS

509-1     EXTERIOR WALL FINISHES

a.   Each bundle of shingles or shakes shall bear a

label identifying its grade and species, and

certifying compliance with the applicable

commercial standard.

b.   Each panel or package of hardboard shall bear a

label identifying the specific type of hardboard

and the manufacturer, and certifying compliance

with the applicable standard.

c.   Hardboard products shall be manufactured in

accordance with the standards listed in Appendix C.

Other hardboard products are considered special

products and may be used in accordance with the

procedures set forth in Paragraph 513.

509-2     FINISH FLOORING, RIGID

a.   Each bundle or package of wood flooring shall bear

a label identifying grade and species.

b.   Ceramic tile shall be identified as required by the

applicable referenced standard.

5-6

1994

_____________________________________________________________________

4910.1

509-3     FINISHED FLOORING, RESILIENT

The thickness of resilient flooring may be less than

required by the referenced standards in Appendix C, but

no less than the thickness shown in Table 5-9.1.

5-7

1994

_____________________________________________________________________

4910.1

___________________________________________________________________________

TABLE 5-9.1

MINIMUM RESILIENT FLOORING THICKNESS (Links to 49101c05.pdf)

___________________________________________________________________________

5-8

1994

_____________________________________________________________________

4910.1

509-4     CARPETS AND MATS

Carpet cushions shall comply with the requirements of

UM 72-80.  Carpets shall comply with the requirements of

UM 44C-78.

509-5     PAINTING

509-5.1   Lead Content

No paint shall contain more than 0.06 percent lead by

weight calculated as lead metal in the total nonvolatile

content of liquid paints or in the dried film of paint

already applied.

509-5.2   Suitability

If a paint to be used on exterior surfaces is not

inherently mold resistant, a suitable fungicide shall be

included in the formulation.

513       SPECIAL CONSTRUCTION MATERIALS

513-1     DEFINITION

Special or alternate construction materials and products

are those which are new or are not covered by specific

requirements in these standards or in the referenced

standards in Appendices C, E & F.

513-2     USAGE

Special or alternate materials and products may be used

as prescribed in Section 101-1 and in HUD Handbook 4950.1

Technical Suitability of Products Program, Technical and

Processing Procedures.

513-3     REQUIREMENTS FOR ACCEPTANCE

Special or alternate materials and products will be

accepted for use in multifamily structures in accordance

with the procedures set forth in HUD Handbook 4950.1.

5-9

1994