|  | INTERNATIONAL TELECOMMUNICATION UNION |  |
| --- | --- | --- |
|  | RADIOCOMMUNICATION STUDY GROUPS | Document 3K/ |
|  |  | 15 September 2006 |
|  |  | English only |

China(People’s Republic of)

A PATH SPECIFIC PREDICTION METHOD FOR POINT-TO-AREA PROPAGATION

# 1 Introduction

In this document a path specific prediction method is presented for point-to area propagation, based on Recommendations ITU-R P. 452, 526 and 1546. The field strength can be expressed as

(1)

Where is the field strength for  of time and  of locations ,  the median field strength,  the variation for  of time, and  the variation for  of locations. It is suggested that the median field strength be predicted based on Recommendations ITU-R P. 452 and 526, and the variation with time and locations predicted based on Recommendation ITU-R P. 1546.

# 2 Prediction of median field strength

The median field strength, (dB(μV)/m), can be expressed in terms of the median basic transmission loss, (dB), as follows:

(2)

Where  is the effective radiated power(dBW) and f the frequency(MHz). Before prediction of median basic transmission loss, input data should be clarified and followed by path profile analysis.

# 2.1 Input data

The basic input data includes the following:

: frequency(MHz)

: antenna heights(m) above ground level

: radio-refractivity lapse-rate(N-units/km) through the lowest 1 km of the atmosphere

: sea level surface refractivity(N-units)

: terrain point number on the path profile

: distance(km) of the ith terrain point from the 0th point

: terrain height(m) of the ith point amsl

: ground-cover type of the ith point

: ground-cover height(m) of the ith point

# 2.2 Path profile analysis

Path profile is analysed based on the effective earth radius, :

where

(3)

is the true earth radius(6371km).

- whether the path is LOS(Line-Of-Sight) or NLOS(trans-horizon)

It is adjudged by comparison between (mrad) and (mrad) where

(4)

(5)

(6)

(7)

(8)

(9)

If , the path is NLOS. Otherwise it is LOS.

- Whether a LOS path has first Fresnel zone clearance or sub-path diffraction

It is adjudged by comparison between (mrad) and  where

(10)

(11)

(12)

If , the LOS path has first Fresnel zone clearance. Otherwise it has sub-path diffraction.

- Whether the sub-path surface is spherical or irregular

It is adjudged by (m) and (m) where

(13)

(14)

(15)

If  and , the sub-path surface is spherical. Otherwise it is irregular. Where

(16)

- Whether the surface between two ends’ horizons is spherical or irregular

It is adjudged by (m) and (m) where

(17)

(18)

for                                                          (19)

for                                                      (20)

(21)

If  and , the surface between two ends’ horizons is spherical. Otherwise it is irregular.

# 2.3 Prediction of median basic transmission loss

The median basic transmission loss can be expressed by

(22)

where  is the free-space basic transmission loss(dB),

(23)

is the median attenuation(dB) relative to free-space. It is predicted for different path types.

- LOS path with first Fresnel zone clearance

(24)

where  is the additional clutter loss (dB) due to diffraction.

- LOS path with sub-path diffraction

(25)

where  is the median sub-path diffraction loss(dB).

If the sub-path surface is spherical,  is predicted according to Recommendation ITU-R P. 526-8, §3.2.

If the sub-path surface is irregular,  is predicted according to Recommendation ITU-R P. 526-8, §4.1.

- Trans-horizon path

(26)

where  and  are the median basic transmission loss(dB) due to trans-horizon diffraction and troposcatter, respectively,  and  the clutter loss(dB) due to diffraction and scatter.

The median basic transmission loss due to trans-horizon diffraction can be expressed by

(27)

where is the median trans-horizon diffraction loss(dB) relative to free-space.

If the surface between two ends’ horizons is spherical,  is predicted according to Recommendation ITU-R P. 526-8, §3.1.1.2.

If the surface between two ends’ horizons is irregular,  is predicted according to Recommendation ITU-R P. 526-8, §4.4.2.

The median basic transmission loss due to troposcatter is predicted according to Recommendation ITU-R P. 452-12, Equation(15), taking angular distance(mrad) as

(28)

where

(29)

(30)

- Additional clutter loss

There are two basic parameters for clutter loss prediction, i.e.

: clutter height(m) above local ground level

: distance(km) from the clutter to the antenna.

The typical clutter data can be summarized in the following table.

Typical clutter data

| code | clutter category |  | min()(km) |
| --- | --- | --- | --- |
| 0 | unknown | 10.0 | 0.05 |
| 1 | open/rural | 0.0~5.0 | 0.1 |
| 2 | water | 0.0 |  |
| 3 | trees/forest | 10.0~30.0 | 0.05 |
| 4 | suburban | 5.0~15.0 | 0.025 |
| 5 | urban | 15.0~25.0 | 0.02 |
| 6 | dense urban | 20.0~40.0 | 0.02 |

Concrete data might be obtained from path profile data. If the ratio of the clutter height to the distance from the antenna attains to the maximum at a terrain point, the relevant clutter height and distance are taken to be  and , respectively.

The clutter loss due to diffraction,  is predicted as for a knife-edge diffraction, taking the diffraction parameter as

(31)

where

(32)

is a reference elevation angle.

For a LOS path with or without first Fresnel zone clearance,

(33)

For a trans-horizon path,

(34)

The clutter loss due to troposcatter can be predicted by

(35)

where  is the angular distance.

# 3 Prediction of the variation with time and locations

The variation of field strength with time can be expressed by

(36)

where  is the field strength for  of time.

The variation of field strength with locations is considered for land. According to Recommendation ITU-R P. 1546-1, Annex 5, §12, It can be predicted by

(37)

Where  is the inverse complementary cumulative normal distribution and  the standard deviation.

The prediction of  is briefed in the following.

# 3.1 Basic data files

The prediction of variation with time is based on Recommendation ITU-R P. 1546 tabulated field strengths and relevant Recommendation ITU-R P. 453 climatic data files. Therefore the basic field strength data files should be built first, and the climatic data files should be cited. There are 24 basic field strength data files, corresponding to 24 figures in Recommendation ITU-R P. 1546, each applying a specific set of frequency, zone and time percentage, and containing 702 basic field strength values for 8 different effective transmitting/base antenna height values and maximums at 78 specific distances. There are three relevant climatic data files, i.e. DNDZ-50.TXT, DNDZ-10.TXT and DNDZ-01.TXT, each corresponding to one of three time percentage 50, 10 and 1, and containing  values at specific grid points. The latitude grid is from +90ºN to -90ºS in 1.5º steps; the longitude grid is from 0º to 360º in 1.5º steps.

# 3.2 Input data

The basic input data includes the following:

: latitude and longitude of transmitting/base station

: latitude and longitude of receiving/mobile station

: frequency

: percentage of time

: path length

: transmitting/base antenna height above ground level

: fraction of path over sea

: terrain point number on a path section

: distance of the ith terrain point from the transmitting/base station

: terrain height of the ith point

where  and

If full information of path profile is available, data ,, and  can be replaced by , and (Ground cover) for the whole path.

# 3.3 Rough path analysis

- Zone analysis

If , the path is over land.

If , the path is over sea.

If  and , the path is over warm sea.

If  and , the path is over cold sea.

If  and , the path is mixed with land and warm sea.

If  and , the path is mixed with land and cold sea.

- Analysis of transmitting/base station antenna height,

It is determined according to Recommendation ITU-R P. 1546-1, Annex 5, §1.

# 3.4 Prediction of the variation with time

In time variation consideration, field strength is predicted based on Recommendation ITU-R P. 1546-1 in a simplified form.

- For any one of three frequencies 100MHz, 600MHz and 2000MHz, any one of three zones land, cold sea and warm sea, any one of three time percentages 50, 10 and 1, and any distance, , between 1 km and 1000km, open the right basic field strength data file by the set of frequency, zone and time percentage, and draw 9 pairs of field strengths at two specific distances closest to the desired distance. The 9 pairs of field strengths correspond to 8 specific effective transmitting/base antenna heights and a maximum field strength.

- Through distance interpolation according to Recommendation ITU-R P. 1546-1, Annex 5, §5, obtain 9 field strengths for the desired distance, .

- Open the climatic data file for desired time percentage, draw the data by the latitude and longitude of the mid-path, and use it to adjust the 9 field strengths according to Recommendation ITU-R P. 1546-1 Annex 8.

- For any effective transmitting/base antenna height, , between 10m and 3000m, through interpolation according to Recommendation ITU-R P. 1546-1, Annex 5, §4.1, obtain the desired field strength for the desired  from the 9 field strenghts.

- If the effective transmitting/base antenna height is less than 10m, correct the field strength according to Recommendation ITU-R P. 1546-1, Annex 5, §4.2 for m, and  §4.3 for m.

- For any frequency between 30MHz and 3000MHz and any time percentage between 50 and 1, take interpolations according to Recommendation ITU-R P. 1546-1, Annex 5, §6 for frequency and §7 for time percentage.

- For mixed paths, take the method in Recommendation ITU-R P. 1546-1, Annex 5, §8.

- Considering what is concerned is field strength difference of two time percentages, other corrections independent of time, such as those for different receiving/mobile antenna herghts and terrain clearance angle, are not needed.

# 4 Software

A software for the above method has been compiled and is executable, which can be names temporarily PSPROGCN. Its input data includes the following:

: frequency

: effective radiated power

: polarization

: antenna heights above ground level

: sea level surface refractivity

: radio-refractivity lapse-rate through the lowest 1km of the atmosphere

: distance from transmitting/base station, terrain height amsl, ground cover type and its height at the ith terrain point on the path profile

: latitude and longitude of transmitting/base station

: latitude and longitude of receiving/mobile station

: percentage of time

: Percentage of locations

PSPROGCN mainly consists of three functions: ALB, DETT and EVSLB.

The input data of the functions includes the following:

ALB(median basic transmission loss):

: frequency

: polarization

: antenna heights above ground level

: sea level surface refractivity

: radio-refractivity lapse-rate through the lowest 1km of the atmosphere

: distance from transmitting/base station, terrain height amsl, ground cover type and its height at the ith terrain point on the path profile

DETT(variation with time and locations):

: frequency

: percentage of time

: Percentage of locations

: transmitting/base antenna height above ground level

: fraction of path over sea

: latitude and longitude of transmitting/base station

: latitude and longitude of receiving/mobile station

EVSLB(transformation from  to field strength):

: frequency

: effective radiated power

: basic transmission loss

PSPROGCN has been tested by the measurement data files from ITU-R WP3K-1. The prediction errors are summarized in Tables 1 and 2.

Table 1. Prediction errors for different data sources

| data source | path amount | data amount | mean error(dB) | r.m.s error(dB) |
| --- | --- | --- | --- | --- |
| BBC | 38 | 70 | 7.0 | 12.5 |
| BBCL | 68 | 68 | 9.8 | 16.2 |
| BBCn | 274 | 274 | 5.9 | 12.5 |
| ERT | 37 | 37 | 6.4 | 13.1 |
| HOL | 72 | 73 | 3.5 | 11.3 |
| IRT | 600 | 600 | 3.0 | 9.3 |
| IRTL | 156 | 156 | -6.2 | 18.7 |
| IRTs | 11 | 63 | 2.0 | 9.2 |
| ORF | 77 | 497 | -15.5 | 19.0 |
| RAI | 87 | 87 | 0.7 | 7.4 |
| S | 107 | 107 | 13.3 | 17.2 |
| SUI | 1083 | 1247 | 3.4 | 12.3 |
| TDF | 68 | 72 | -7.9 | 15.8 |
| YLE | 100 | 100 | -6.3 | 13.4 |
| YLEs | 17 | 68 | 5.6 | 12.5 |
| TOTAL | 2795 | 3519 | 0.4 | 13.6 |

Table 2 Prediction errors for different frequency bands

| Frequency bands | path amount | data amount | mean error(dB) | r.m.s error(dB) |
| --- | --- | --- | --- | --- |
| below 300MHz | 1670 | 2365 | -1.3 | 13.4 |
| 300~1000MHz | 913 | 913 | 5.6 | 12.4 |
| 1000~3000MHz | 241 | 241 | -1.9 | 18.7 |
| TOTAL | 2824 | 3519 | 0.4 | 13.6 |

Software PSPROGCN and its detailed output data files of the test against ITU-R WP3K-1 input data are submitted to ITU-R WP3K-1.