Title:

Influence of desulphurization of thermal power stations on pH of precipitation

Authors: Hana Smilková (15), Markéta Ambrožová (13)

Základní škola Brumov – Bylnice

Czech republic

Abstrakt:

When the electric energy is produced in thermal power stations non-renewable resource of energy is used – brown coal with a high content of sulphur. During the incineration  of coal sulphur acid and carbon dioxide CO2 are released into the atmosphere. Sulphur dioxide SO2 is oxidized in the atmosphere and on the surface of vegetation and sulphure acid H2SO4 arises. The presence of this acid in rainfall water lowers pH of precipitation. This leads to the rise of “acid rain“.

The influence of acid rains on:

-agriculture and forests  - the process of breathing and photosynthesis is worsen, it causes slower

growth, smaller hectare crops, falling down of leaves and needles, bark beetles

-water sources – acid water causes dying out of fish, insect and water plants

- historical monuments and cultural sights – eroding of plaster, statues and sculptures, corrosion of

steel constructions /railway tracks, buildings.../

- human population –insult of respiratory system /asthma, allergy, skin diseases, emphysema of

lungs/, smog /psyche, the length of a human life/

Hypothesis:

Does desulphurization of thermal power stations influence the value of pH precipitation?

We think that it does.

Research metod:

The aim of this project is to verify the hypothesis, if the  desulphurization of thermal power stations influences the rising of value of pH precipitation.

To could verify this hypothesis, we needed to know the placement of thermal power stations in the Czech republic (2), the amount of produced sulphur dioxide during the incineration of brown coal before and after their desulphurization(1), the year of desulphurization and mainly measured data of pH of precipitation of single schools participating in the project GLOBE in the Czech republic.

In the database of every of 102 schools registrated in GLOBE we were finding out the year since which they have measured and if they have recorded pH of precipitation. We used data of 35 schools in total (3, 3.1). First the average of pH precipitation in every year was counted (4) and then the whole year of all schools was averaged (5).

Data summary:

1. The amount of produced SO2  in 1994 – 2001 in the Czech republic

The sources emitting  pollutants into the atmosphere are nationwide monitored within the framework of so called Register of emissions and sources of pollution of the atmosphere /REZZO/

REZZO 1 – great sources of pollution, thermal performance is higher than 5 MW /power stations/

REZZO 2 – middle sources of pollution, thermal performance from 0,2 to 5 MW

REZZO 3 – small sources of pollution, thermal performance under 0,2 MW

2. Placement of thermal power stations in the Czech republic

3.  Placement of schools whose data was used

3.1 List of the schools:

1.ZŠ Žďár nad Sázavou				19.ZŠ T.G. Masaryka, Lomnice nad Popelkou

2.ZŠ Most						20.ZŠ Vrané nad Vltavou

3.ZŠ-Ekolog. praktikum Jičín			21.ZŠ Horní Maršov

4.ČAG České Budějovice				22.ZŠ Vítkov

5.DDM na Vápenci+ZŠ Rejsková,Prostějov 	23.ZŠ Telč

6.DDM-Středisko ekologické, Valašské Meziříčí	24.ZŠ Havlíčkův Brod

7.Rozšířená výuka jazyků, Zlín			25.ZŠ Pomezí

8.Gymnázium Česká Třebová			26.ZŠ Buchlovice

9.Gynázium Liberec					27.ZŠ Trutnov

10.Gymnázium Dačice				28.ZŠ Bánov

11.Gymnázium Dr. A. Hrdličky, Humpolec	            29.ZŠ Horáčkova, Praha 4

12.Gymnázium Líšeň s.r.o, Brno			30.ZŠ Habrmanova, Česká Třebová

13.Gymnázium Voděradská, Praha 10		31.ZŠ Brumov - Bylnice

14.Masarykova stř. škola chemická, Praha		32.ZŠ Lysice

15.SPŠ Textilní, Dvůr Králové			33.ZŠ Mohelnice

16.Stř. zeměděl. ekol. škola, Humpolec		34.ZŠ Smržovka

17.ZŠ Borovského, Karviná				35.ZŠ Velké Opatovice

18.ZŠ Velký Beranov

4.  Values of pH precipitation which were found out

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1995 |  |  | 4.50 |  |  |  |  |  |  |  |  |  |  |  |
| 1996 |  |  | 4.37 |  |  |  |  |  |  |  |  |  |  |  |
| 1997 |  |  | 4.70 |  |  |  |  |  |  |  | 6.86 |  |  |  |
| 1998 |  |  | 4.60 |  | 5.80 | 4.63 |  | 5.25 | 5.24 |  | 7.14 |  | 5.56 |  |
| 1999 |  |  | 4.57 |  | 5.41 | 5.04 | 7.31 | 5.46 | 5.00 | 6.68 | 6.64 | 6.13 | 7.80 | 7.04 |
| 2000 |  | 6.40 | 4.47 | 4.96 | 5.30 | 6.02 | 7.94 | 5.33 | 5.54 | 6.11 | 6.57 | 6.91 | 7.24 | 7.83 |
| 2001 | 5.58 | 5.69 | 4.93 | 4.84 | 5.14 | 4.94 |  | 5.35 |  | 5.85 | 6.73 |  | 6.75 | 6.69 |
| 2002 |  | 5.72 | 4.50 | 4.34 | 5.00 |  |  | 5.37 |  | 5.97 | 6.66 |  | 6.92 | 6.94 |

|  | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1995 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1996 |  |  |  |  |  |  |  |  |  |  | 5.07 |  |  |  |
| 1997 |  |  |  |  |  |  |  |  |  |  | 5.30 |  |  |  |
| 1998 | 6.09 |  |  |  |  |  |  | 6.00 | 5.42 |  | 5.32 | 5.67 |  | 5.29 |
| 1999 | 5.56 |  |  | 5.84 |  |  | 4.82 | 4.86 | 6.31 |  | 5.45 | 5.31 |  | 5.05 |
| 2000 | 5.32 | 6.59 | 5.40 |  | 4.85 |  |  | 5.69 | 5.67 | 5.98 | 5.71 |  | 6.53 | 4.69 |
| 2001 | 5.11 |  | 5.18 |  | 4.69 | 5.18 |  | 5.73 | 5.28 |  | 4.95 |  | 6.57 | 5.04 |
| 2002 |  |  | 5.91 |  |  | 5.16 |  | 5.79 |  |  | 6.16 |  | 5.82 | 5.15 |

|  | 29 | 30 | 31 | 32 | 33 | 34 | 35 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1995 |  |  |  |  |  |  |  |
| 1996 |  |  |  |  |  |  |  |
| 1997 | 5.17 | 4.84 |  |  |  |  |  |
| 1998 | 4.83 | 5.05 |  |  | 5.71 |  |  |
| 1999 |  | 5.24 |  |  | 5.41 | 5.36 | 5.50 |
| 2000 |  | 5.31 |  | 5.14 | 5.76 |  | 4.70 |
| 2001 |  | 5.58 |  | 5.23 | 5.74 |  | 5.15 |
| 2002 |  | 5.12 | 6.83 |  | 6.01 |  | 5.42 |

5. Average pH

| 1995 | 4.500 |
| --- | --- |
| 1996 | 4.719 |
| 1997 | 5.373 |
| 1998 | 5.474 |
| 1999 | 5.731 |
| 2000 | 5.851 |
| 2001 | 5.496 |
| 2002 | 5.726 |

Analysis of data:

When we use the data, it is necessary to take account of a certain divergence, because  in the beginning of GLOBE pH papers were used for measuring of pH precipitation and their resolution is 0,5 pH. Only in last years more accurate pH meter has been used. In spite of it, we can find out from the results that after the desulphurization of the most of thermal power stations, pH precipitations rose and pH of rainfalls was higher in 1997 than in 1996 /the difference was 0,5/. In another years there is a slow rising of the average of pH. The exception is the year 2001, because the value returned to the year 1998. This fact could be probably caused by longer and more freezing winter.

This data results in the fact that thermal power stations greatly influence the pollution of the atmosphere. Of course we have to take into consideration also smaller local sources of pollution – heating plants, stokeholds, factories etc.

The highest amount of SO2 was produced in the area of  the North Bohemia, Mělník and Ostrava.

We could solve it by cancelling of thermal power stations and by using water, solar, wind or nuclear power stations. Regrattably unemployment would rise in these local areas and in the branches which are dependent on them.

The hypothesis about the positive influence of desulphurization of thermal power stations on the rising of pH or precipitation was confirmed.

Literature and the sources of data:

The Globe Data Archive

www.chmi.cz

www.cez.cz

www.zoner.cz