$$551.00A

Section 551.—DRIVEN PILES

Revised 25 January 2005

INCLUDE THE FOLLOWING IF REQUIRED BY GEOTECH (ASK GEOTECH)

$$551.05A

551.05.  Add the following:

After completing the static load test, install instruments on the pile.  Strike the pile 50 to 100 blows with the driving hammer while the dynamic measurement is made.  Operate the pile hammer at normal operating temperature before it is used to restrike the pile.  After the dynamic measurement of pile capacity, the CO will remove the instruments from the pile.

$$551.08A

551.08.  Add the following:

Drive permanent piles a minimum of 40 calendar days after completion of the approach fills at the following locations:

1.	________________________________

2.	________________________________

3.	________________________________

$$551.11A

551.11. Delete the first paragraph and substitute the following:

Pile Load Tests.  Dynamic load testing is required.