| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 16 to Document 41-E |
|  | 22 August 2007 |
|  | Original: English |
| Asia-Pacific Telecommunity Administrations |
| COMMON proposals for the work of the conference |
| Agenda item 1.16 |

1.16	to consider the regulatory and operational provisions for Maritime Mobile Service Identities (MMSIs) for equipment other than shipborne mobile equipment, taking into account Resolutions 344 (Rev.WRC-03) and 353 (WRC-03)

Introduction

Agenda item 1.16 considers the expansion of MMSIs to Search and Rescue (SAR) aircraft and Aids to Navigation. This agenda item is comprised of two issues:

1)	Management of the MMSIs numbering resource (Resolution 344 (Rev.WRC-03)); and

2)	MMSIs for equipment other than shipborne mobile equipment (Resolution 353 (WRC-03)).

With regard to Issue B, the CPM Report sets out two Methods and associated revised regulatory provisions to satisfy this agenda item.

Taking the above into consideration, APT members support Method B in the CPM Report and propose modifications to Article 19 of the Radio Regulations as shown below.

# Proposed texts are the same as the text in the CPM Report (5/1.16/4.2)

ARTICLE  19

Identification of stations

Section II  –  Allocation of international series and assignment of call signs

MOD	ASP/41A16/303

19.30		2)	As the need arises, ship stations and ship earth stations to which the provisions of Chapter IX apply, and coast stations or coast earth stations, or other non-shipborne stations capable of communicating with such ship stations, shall have assigned to them maritime mobile service identities in accordance with Section VI of this Article.

Reasons:	Modified Recommendation ITU-R M.585-3 extends the assignment of MMSIs to aircraft stations and aids to navigation.

MOD	ASP/41A16/304

Section VI  –  Maritime mobile service identities

MOD	ASP/41A16/305

19.99	§ 39	When a station5 operating in the maritime mobile service or the maritime mobile-satellite service is required to use maritime mobile service identities, the responsible administration shall assign the identity to the station in accordance with the provisions described in  Recommendation ITU-R M.585-4; in so doing, it should take into account any other relevant ITU-R and ITU-T Recommendations. In accordance with No. 20.16, administrations shall notify the Bureau immediately when assigning maritime mobile service identities.

Reasons:	Provision is modified to establish the incorporation by reference of Recommendation ITU-R M.585-4.

MOD	ASP/41A16/306

19.100	§ 40	1)	Maritime mobile service identities are formed of a series of nine digits which are transmitted over the radio path in order to uniquely identify ship stations, ship earth stations, coast stations, coast earth stations group calls, and other non-shipborne stations operating in the maritime mobile service or the maritime mobile-satellite service.

Reasons:	Consequential change of the extension of the assignments of MMSIs.

MOD	ASP/41A16/307

# 19.102		3)	The types of maritime mobile service identities shall be as described in Recommendation ITU-R M.585-4.

Reasons:	Provision indicates that the assignments of MMSIs are based on Recommendation ITU-R M.585.

SUP	ASP/41A16/308

# 19.103 to 19.107

Reasons:	Consequential change of the incorporation by reference of Recommendation ITU-R M.585-4.

MOD	ASP/41A16/309

19.108A	§ 41	The maritime identification digits M1I2D3 are an integral part of the maritime mobile service identity and denote the geographical area of the administration responsible for the station so identified.     (WRC-07)

Reasons:	Consequential change of the suppression of Nos. 19.102 to 19.106.

MOD	ASP/41A16/310

19.110	C  –  Maritime mobile service  identities

Reasons:	Consequential change of the extension of the assignments of MMSIs.

MOD	ASP/41A16/311

19.111	§ 43	1)	Administrations shall follow the provisions contained in Recommendation ITU-R M.585-4 concerning the assignment and use of maritime mobile service identities.

Reasons:	Consequential change of the incorporation by reference of Recommendation ITU-R M.585-4.

MOD	ASP/41A16/312

19.112		2)	Administrations should:Reasons:	Consequential change of the incorporation by reference of Recommendation ITU-R M.585-4. Provision is reflected in No. 19.111.

(MOD)	ASP/41A16/313

19.113	a)	make optimum use of the possibilities of forming identities from the single MID allocated to them;

Reasons:	This is an editorial modification.

(MOD)	ASP/41A16/314

19.114	b)	take particular care in assigning ship station identities with six significant digits (i.e. having three-trailing-zero identities), which should be assigned only to ship stations which can reasonably be expected to require such an identity for automatic access on a worldwide basis to public switched networks, in particular for mobile-satellite systems accepted for use in the GMDSS on or before 1 February 2002, as long as those systems maintain the MMSI as part of their numbering scheme.     (WRC-07)

Reasons:	This is an editorial modification.

SUP	ASP/41A16/315

19.115 to 19.126

Reasons:	Similar contents of these provisions are described in Recommendation ITU-R M.585-4.

______________