| User Request Form For a NESDIS Satellite Product or Service |
| --- |
| NESDIS INPUT |
| 1. Tracking Number: 0507-05 2. Date Received: 28 July 2005 3. Amendments Date(s): 4. Significant Notes: |
| USER INPUT |
| 5. Request Title: Polar/Geostationary Volcanic Ash Detection and Height on CLAVR-X |
| 6. User Project Leader (Agency or office, Name, Phone, Fax & email): OSDPD/SSD/SAB (VAAC), Greg Gallina, phone: 301-763-8444, fax: 301-763-8333; email: greg.gallina@noaa.gov |
| 7. Operational Points of Contact (Agency or office, Name, Phone, Fax & email): Greg Gallina; phone: 301-763-8444; email: Greg.Gallina@noaa.gov and other Washington VAAC analysts |
| 8. Technical Points of Contact (Agency or office, Name, Phone, Fax & email): Andrew Heidinger, NOAA/NESDIS: 608-263-6757; fax: 608-262-5974; email: Andrew.Heidinger@noaa.gov and Michael Pavolonis, CIMSS/SSEC/UW; phone: 608-263-9597; fax: 608-262-5974; email: mpav@ssec.wisc.edu |
| 9. General Description of Need: Volcanic ash poses a large threat to aviation. The VAAC would benefit from automatic and real-time ash detection and height estimates. Current detection methods are typically qualitative and require manual analysis. Current estimates of ash height are often limited to surface observation and to inaccurate window-channel based satellite methods. The automated products would greatly complement the qualitative techniques. |
| 10. Product specifications / needs: Environmental parameter: Volcanic Ash Detection and Height Satellite sources (e.g., satellite, sensor, etc.): AVHRR, MODIS, GOES 10-11, MTSAT, SEVIRI Geographical coverage (e.g., orbital, global, regional): Global Vertical range: Troposphere Vertical resolution: 100 hPa Horizontal resolution: 1 – 4 km (nadir) Mapping accuracy: 2 km Measurement range: Ash Detection (n/a): Ash Height – 1000 to 100 hPa Measurement accuracy: 100 hPa Measurement precision: 20 hPa Frequency (e.g, Daily, weekly, orbital, delivery times, granularity): All data will be processed. From AVHRR alone we expect global coverage every 4 hours. With additional GEO and polar orbiters, we expect coverage every 2 hours. Data Latency: Data will be processed at each VAAC. We expect production will require 5 minutes after each HRPT reception Refresh: Timeliness (e.g., how soon after observation is product needed?): As soon as possible Projection view: Unmapped Format (eg., BUFR, GRIB, FF, GIF, GeoTIF, McIDAS/HDF, SARAD, SATEM, AWIPS’ NetCDF): HDF and McIDAS Grid spacing: NA Units: Heights in hPa,, K, and km Compression (e.g., JPEG, MPEG, RICE, GZIP, ZIP, GIP): none Long term stability: N/A Archive requirements: none Others: |
| 11. Benefits: This product will assist the VAAC’s in detecting ash and estimating its height. The ash cloud height and coverage are critical to forecast the movement of the ash plume since they are used to initialize trajectory models. Since upper wind data are now used to help determine ash cloud height, the CIMSS method will reduce dependence on wind data, which is poor in many parts of the world. The CIMSS method produced significantly better ash cloud heights from the March 2005 Mt. St. Helens eruption when compared to heights derived from the GOES sounder (30K ft. vs. 18K ft.). The result of this improved flight safety. The avoidance of only one aircraft encounter with an ash cloud can lead to a savings of $1M or more in damage. |
| Value Range (check): |  | Less than $100K |  | $100K to $1 Million | X | Greater than $1 Million |
| 12. Shortcomings of Existing Capabilities: Existing ash detection capabilities are qualitative and require human interpretation. The methods proposed here will allow for quantitative classification of ash into two classes depending on the amount of ice present with the ash. Currently, most satellite estimates of ash height are based on infrared window brightness temperatures. For optically thin plumes, these satellite-derived estimates of ash height are not accurate. |
| 13. Need Date: As soon as possible User Program Implementation Details: Is the user willing to cost share on developing this capability? |
| 14. Termination Date: None, we expect this product to exist during NPOESS and GOES-R |
| 15. User Priority: | Check Appropriate Box Below |  |
|  |  | Mission Critical: Cannot meet operational mission objectives without this requirement |
|  | X | Mission Optimal: Requirement not critical but would provide significant improvement to operational capability |
|  |  | Mission Enhancing: Requirement needed to enhance state of knowledge or assess potential for operational capability |
| 16. For NOAA Users only Please place an "X" in the appropriate block identifying which NOAA mission goal(s) and program(s) this request supports (goal is the 1st item and programs found under that goal are the second column) |
| NOAA Mission Goals | NOAA Programs |
|  | Ecosystems |  |
|  |  | Habitat |
|  |  | Corals |
|  |  | Coastal and Marine Resources |
|  |  | Aquaculture |
|  |  | Ecosystem Research |
|  |  | Ecosystem Observations |
|  |  | Protected Species |
|  |  | Fisheries Management |
|  |  | Enforcement |
|  | Climate |  |
|  |  | Climate Observations & Analysis |
|  |  | Climate Forcing |
|  |  | Climate & Ecosystems |
|  |  | Climate Predictions & Projections |
|  |  | Regional Decision Support |
|  | Weather and Water |  |
|  | X | Local Forecast & Warnings |
|  |  | Space Weather |
|  |  | Hydrology-Rivers, Lakes & Floods |
|  | X | Air Quality |
|  | X | Environmental Modeling |
|  |  | Coasts, Estuaries & Oceans |
|  |  | Weather Water Science, Technology, & Infusion Program |
|  | Commerce & Transportation |  |
|  |  | Marine Transportation Systems |
|  | X | Aviation Weather |
|  |  | Marine Weather |
|  |  | Geodesy |
|  |  | Surface Weather |
|  | X | NOAA Emergency Response |
|  |  | Commercial & Remote Sensing Licensing |
|  | Satellite Sub-goal |  |
|  |  | Geostationary Satellite Acquisition |
|  |  | Polar Satellite Acquisition |
|  |  | Satellite Services |
|  | Fleet Services Sub-goal |  |
|  |  | Aircraft Replacement |
|  |  | Fleet Replacement |
|  |  | Marine Operations & Maintenance |
|  |  | Aircraft Services |
|  | Leadership Sub-goal |  |
|  |  | Homeland Security |
|  |  | Line Office Headquarters |
|  |  | NOAA Headquarters |
|  | Mission Support Sub-goal |  |
|  |  | Information Technology Services |
|  |  | Administrative Services |
|  |  | Financial Services |
|  |  | Workforce Management |
|  |  | Acquisition & Grants |
|  |  | Facilities |
| Suggested Solutions (Optional): |
| Concept Of Operations (Optional): The Clouds from AVHRR (CLAVR-x) system will serve as the vehicle for the volcanic ash detection and height algorithms. Our concept of operations is that ORA/CIMSS develops a version of CLAVR-x that processes AVHRR data and makes products in the format needed by the VAAC. This code is then implemented at each participating VAAC. In addition, a version of CLAVR-x run with NESDIS (ORA/CIMSS and/or OSDPD/IPD) is used to process all relevant AVHRR data and make it publicly accessible to other customers. This would also serve as backup to processing done locally at the VAAC. Processing capabilities for additional satellite platforms (e.g. GOES, SEVIRI, MTSAT, MODIS) will follow once CLAVR-x is implemented. |
| 19. Additional Remarks (Optional): |
| 20. Approval Authority (Agency or office, Name, Phone, Fax & email) (mandatory entry): Development is being funded by NCAR, implementation resources have not been identified. Dave Benner is the approval authority on this request. |
| 21. National Weather Service user requests must be sent James.Heil@noaa.gov and he will forward them to NESDIS. All other requests should be sent by Email, fax, or mail to: Email: Selina.Nauman@noaa.gov Phone: 301-763-8081 ext 134 Fax: 301-763-8131 Mail: NESDIS/OSDPD/Satellite Services Division (Attn: Selina Nauman) ESP/23 5200 Auth Road, Building 607 Camp Springs, MD. 20747 |
| Triage Board Member Initial Technical Assessment |
| 22. Triage Board member: OSD - Tom Schott ORA - Hank Drahos OSDPD- David Benner Current capabilities: OSD: There are currently several volcanic ash products generated from GOES Imager, AVHRR, and MODIS data, which are used to detect and monitor ash plumes. - Infrared products are generated from AVHRR data in the 10-12 micron range (channels 4 and 5). MODIS data and individual GOES channel data are also used. - Experimental three channel infrared products are generated from GOES Imager channels 2 (3.9 microns), 4 (10.7 microns), and 5 (12 microns) on GOES -10 and from channels 2, 4, and 6 (13.3 microns) on GOES-12. - Another experimental GOES product is the channel 2-4 image difference. - Operational visible products are generated from the GOES Imager channel 1 (0.6 microns). - Operational Significant Event Imagery (OSEI) products are generated from AVHRR GAC, LAC, and HRPT data, MODIS, and GOES Imager. ORA: Comments incorporated in user request OSDPD: Currently, analysts at the Volcanic Ash Advisory Center detect and estimate the extent and movement of airborne volcanic ash using visible band satellite imagery from several sources, and on multi-spectral imagery derived from GOES imager data. Ash cloud height determinations are primarily derived from analysis of upper level wind data and satellite derived cloud temperatures. Near term improvement plans related to this capability request: OSD: Polar-PSDI is currently funding the CLAVR-X project. However, the project plan does not mention the development of a CLAVR-X ash product. ORA and OSDPD: Implementation of this request will enable automated detection of ash clouds and more accurate ash cloud height determinations from several platforms, including GOES, POES and MODIS, and will be extensible to future satellite sensors, especially VIIRS. In addition, the CIMSS method should greatly enhance products from GOES-M through P series that do not have the 12 micron band. It is not dependent on the presence of the discontinued GOES-12 micron band, as has been the case with past multi-spectral techniques. Technical solution options to meet user request: OSD: N/A ORA: Most of the work has already been done by the ASPT/CIMSS group to meet this request, except for documenting the science a little more. The legacy science is of course the CLAVR-x algorithm which is already well documented. OSDPD: It is reported this technique was developed by the ASPT/CIMSS group as an adjunct to the CLAVR-X program, which runs operationally in OSDPD and very well documented. The developer, Michael Pavolonis, has been hired by NESDIS and it is anticipated he will be available to implement the algorithm operationally. Recommended course of action: OSD: N/A ORA: I would recommend approval of this request, which will fall under the oversight of ICAPOP. OSDPD: Strongly recommend accepting this request to support the safety and financial attributes of the aviation industry. Other comments: OSD: Need John Sapper and/or Andy Heidenger to provide a technical assessment whether CLAVR-X can produce this product. If it is technically feasible and it makes sense to pursue this course of action, then they would put together a proposal for product development to be approved by the SPSRB. |
| NESDIS TRIAGE BOARD INPUT |
| 23. The Triage Board supports this user request and asks that Andy Heidinger lead an Integrated Product Team (IPT) and provides a product development brief on utilizing CLAVR-X for volcanic ash detection at an upcoming SPSRB meeting. The Triage Board has identified the following as the IPT members: John Sapper and Greg Gallina (OSDPD) Hank Drahos, Mike Pavolonis (ORA) Tom Schott (OSD) The ICAPOP co-chairs (Gary.Ellrod@noaa.gov/George.Serafino@noaa.gov) are also be kept informed of progress on this request. Finally, 2 weeks prior to the presentation of this brief at an SPSRB review your briefing is to be reviewed by the SPSRB Management Team. |
| NESDIS SPSRB INPUT |
| 24. |
| NESDIS Resource Updates |
| 25. |