MonProc USOpr.doc										15 Mar 05

RVSM Monitoring Procedures for U.S. Operators

*Document Updates.   This document was updated on March10, 2005.   Paragraphs containing clarifications or updates are marked in the left margin.

*Basic Guidance on RVSM Monitoring.  (See page 2-3 for additional guidance).

*1.  Monitoring requirements do NOT have to be completed prior to the operator receiving RVSM authority (Letter of Authorization (LOA) or Operations Specifications).

*2.  Operators have up to six months after they receive RVSM authority or until six months after the start of RVSM operations in an airspace, whichever occurs later, to complete RVSM monitoring requirements.

*3.  With only limited exceptions, operators must have FAA authorization to cruise in RVSM airspace.  This provision applies to flights conducted for monitoring.   FAA Notice GEN04009, paragraph j discusses the exceptions for Non-RVSM aircraft.  See page 2-3 for additional detail.

*4.  The provision for ATC to accommodate operators/aircraft that do not have RVSM authority in RVSM airspace for "aircraft certification and development" purposes is NOT intended to apply to flights conducted for the specific purpose of accomplishing RVSM monitoring.   Guidance for monitoring conducted by Aircraft Service Centers and Airplane Manufacturers is posted under “Guidance For Conducting Monitoring Flights” on page 2.

*5.  Operators are required to participate in the RVSM Monitoring Program.

Contacts and Responsibilities.   The Separation Standards Group at the FAA Wm. J. Hughes Technical Center in Atlantic City, New Jersey serves as the U.S. Operator/Aircraft RVSM Approvals Database and Monitoring Coordinator.   The group also provides staffing and funding for the North American Approvals Registry and Monitoring Organization (NAARMO) and the Asia/Pacific Approvals Registry and Monitoring Organization (APARMO).    The group coordinates monitoring results and U.S. aircraft/operator RVSM approval information with Regional Monitoring Agencies (RMA) in other regions such as the North Atlantic and Europe.

Contacts in the Separation Standards Group are shown below.  (+1 indicates the U.S. country code).

U.S. Operator/Aircraft RVSM Approvals Database and Monitoring Coordinator

Phone:				+1 609-485-5475

Fax:				+1 609-485-5078

Email:				wayne.smoot@faa.gov

RVSM Program Manager for Regulation & Certification (AVR)

Phone:				+1 202-385-4576

Fax:				+1 202-385-4653

Email:				robert.swain@faa.gov

NAARMO/APARMO Operations Coordinator at FAA Technical Center

Phone:				+1 609-485-5678

Fax:				+1 609-485-5078

Email:				naarmo@faa.gov

*Additional Guidance For Conducting Monitoring Flights

*1.  Aircraft Status For Monitoring.   Aircraft must be RVSM-compliant for monitoring to be conducted.  For in-service aircraft, aircraft modification and/or inspection required by RVSM Service Bulletin, STC or other approved RVSM document must be completed prior to the aircraft being monitored.  For aircraft manufactured RVSM-compliant, the Airplane Flight Manual and/or Type Certificate Data Sheet will show a statement of RVSM compliance.    Any exception to this rule must be coordinated with AFS-400.

*2.  LOA's are issued to operators intending to conduct operations in a Special Area of Operation (e.g., RVSM airspace).  RVSM monitoring can be conducted after the operator receives the LOA.

*3.  Airplane manufacturers have authorization to fly RVSM-compliant "production" airplanes in RVSM airspace as RVSM-compliant flights.  Monitoring can be accomplished on these flights when the aircraft is in an RVSM-compliant configuration.

*4.  Monitoring By Aircraft Service Centers, Repair Stations and Designated Airworthiness Stations.   Monitoring flights are often completed on behalf of operators by Aircraft Service Centers, Certificated Repair Stations or Designated Airworthiness Stations.   (There are established provisions for these organizations to obtain FAA RVSM authorization).  STC or Service Bulletin work is completed to bring an aircraft into RVSM-compliance and then, as part of the service, monitoring is conducted.  In these circumstances, monitoring can be conducted prior to the operator submitting aircraft RVSM documents to the Flight Standards field office (FSDO or CMO).  Normally, however, it is good practice to submit RVSM documents to the FSDO or CMO prior to conducting monitoring.

*5.  Monitoring During RVSM STC or Service Bulletin (SB) Test Flights.  Aircraft test flights flown for final STC or SB sign off can be monitored as long as the aircraft is in an RVSM-compliant condition and the FAA Tech Center is notified of the circumstances on the “US Operator Application for RVSM Monitoring” form.  (See Appendix 1).

*6.  Instructions on use of trailing cone data to fulfill monitoring requirements are posted on the minimum monitoring requirements charts.

Monitoring Requirements Charts.   Monitoring requirements charts are published on the RVSM Documentation Webpage under “Monitoring Requirements and Procedures”.  They are used to determine the number of airframes that operators are required to have monitored.  Instructions for using the monitoring requirements charts for various regions are also posted on the Webpage. The first page of the charts contains guidelines for monitoring and for using the charts.

Monitoring Not Required Prior to the Issue of Operational Approval.   The “Minimum Monitoring Requirements” charts are the source documents for monitoring requirements and deadlines.   The North American Minimum Monitoring Requirements Chart states that monitoring requirements are not required to be completed until “6 months after the issue of operational approval or not later than 6 months after the start of North American RVSM operations, whichever occurs later.”   The Minimum Monitoring Requirements Charts for other regions state that monitoring requirements are not required to be completed until “6 months after the issue of operational approval.”  .

Required Participation.   Operators are required to participate in the RVSM Monitoring Program.  As stated in FAA Guidance 91-RVSM paragraph 11d (8), in its application for RVSM authority, the operator should show its plan for completion of monitoring requirements.   Monitoring requirements are published on the FAA “RVSM Documentation” page.   This page can be accessed through the FAA RVSM Website homepage:

- http://www.faa.gov/ats/ato/rvsm1.htm

Application of Monitoring Results To and From Different Regional Programs.   Monitoring data obtained to fulfill the monitoring requirements for one region can be used to fulfill the monitoring requirements for another region.  Regional Monitoring Agencies coordinate with each other to exchange database information on monitoring results.

Options for Participation in Monitoring Programs.   The following options for operator participation in RVSM monitoring programs are discussed in this paper:

- Operators can fly a portable GPS-based Monitoring Unit (GMU) on their aircraft. See Appendix 2.

- *Operators can overfly the ground-based Height Monitoring Units (HMU) near  Strumble in the U.K.  The HMU near Gander in Canada has been decommissioned.   See Appendix 3.

- Operators can overfly one of the three HMU’s deployed in Europe.   See Appendix 4.

- *Domestic U.S. RVSM Monitoring System.   The first Aircraft Geometric Height Measurement Element (AGHME) constellation was operational in January 2005.  See Appendix 5 for details.

Procedures for successfully completing a monitoring flight using one of these systems are discussed in detail in the Appendices.

Application for Monitoring.   All operators must complete an “Application For Monitoring” form and fax it to the organizations shown at the top of the form.   This information will help track and process operator monitoring efforts.   See Appendix 1.

Appendices

Appendix 1	Form:   U.S Operator Application for RVSM Monitoring…………………….Page 4

Appendix 2	GPS-based Monitoring System (GMS) Procedures………………...................Page 6

Appendix 3	Procedures for North Atlantic (Strumble) Height Monitoring Unit…..……….Page 10

(NAT HMU)

Appendix 4	Basic Monitoring Procedures for Europe:  HMUs and GMUs……...................Page 12

Appendix 5	*Domestic U.S. AGHME GMS (Aircraft Geometric Height……………….....Page 15

Measurement Element Ground-based Monitoring System)

## Appendix 1

## U.S. OPERATOR APPLICATION FOR RVSM MONITORING

Instructions

1.  	All operators:  fax completed form to +1 609-485-5078.

2.  	Operators planning GMS monitoring, also fax copy to the appropriate GMS Support Contractor.

CSSI:  +1 202-863-2398;   ARINC:   +1 410-573-3007

Operator Name:_____________________________________________________________________________________________

Operator’s 3-letter  ICAO Identifier ___________________________________________________________________

(For IGA operator, enter IGA.   If no ICAO identifier assigned, enter “None”.

Address:___________________________________________________________________________________________

___________________________________________________________________________________________________

Operator Primary Point of Contact

Name:_________________________________________________________Title:________________________________

Telephone Number:_________________________ Fax Number: ______________________

Email Address:_________________

# Operator Secondary Point of Contact

Name:_______________________________________________________Title:__________________________________

Telephone Number:________________________ Fax Number: ______________________

Email Address:__________________

# Responsible Flight Standards Office (FSDO or CMO) Point of Contact

Name:_______________________________________________________Title:__________________________________

Address: ___________________________________________________________________________________________

Telephone Number:________________________ Fax Number: ______________________

Email Address:__________________

REGION WHERE RVSM OPERATIONS WILL BE CONDUCTED:

(Check all that apply)

|  | North America |  | Pacific |  | West PAC/ SCS |  | Bay Of Bengal |  | North Atlantic |  | Caribbean/ South American |  | European |  | Asia |  | Other (Please Specify) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Information on HMU Flights

Approximate date(s) of HMU flight: __________________

HMU(s) planned to be overflown: __________________

(Requested Aircraft Information on next page)

AIRCRAFT INFORMATION

(Please be sure to include data for the ENTIRE fleet)

| Aircraft Model | Registration Number | Serial Number | Mode S Address |
| --- | --- | --- | --- |

Appendix 2

GPS-based Monitoring System (GMS) Procedures

The NAARMO is responsible for all aircraft height monitoring activity for North American RVSM operations (Domestic U.S., Southern Canadian Domestic, and Mexico) and administers the GMU height-monitoring program.  CSSI Incorporated and ARINC, as GMS support contractors, will assist the NAARMO with the monitoring program.

GMS Description

The GMS is composed of the equipment and procedures to collect and process three required data elements:  1) GPS data;  2) pressure altitude or Mode C data; and 3) meteorological data.  The GPS-based Monitoring Unit (GMU) is used to collect the GPS data during the monitoring flight.  The NAARMO will use information on the attached Flight Information Form (FIF) to coordinate the collection of pressure altitude or Mode C data from ATC facilities.  Late transmittal of the FIF or illegible or blank entries will delay post-flight processing of data and the dissemination of results.  Meteorological data will be obtained by the NAARMO without operator involvement.

GMS Contacts:

U.S. GMS Coordinator at FAA Technical Center,

Atlantic City, N.J.

Phone:				+1 609-485-5102

Fax:				+1 609-485-5078

Email:				rvsm@faa.gov

CSSI Inc. GMS Support Contractor:

*Phone:			+1 866-468-8111 or +1 202-554-1051

Fax:				+1 202-863-2398

Email:				monitor@cssiinc.com

ARINC GMS Support Contractor:

Phone:				+1 410-266-4707

Fax:				+1 410-573-3007

Email:				rvsmops@arinc.com

Forms

The following forms are required to be completed:

- Application for Monitoring shown in Appendix 1

- Flight Information Form attached to Appendix 2 (this appendix)

GMU Monitoring Flights

Height monitoring can be conducted on scheduled flights, ferry flights, or monitoring-specific flights.  To ensure collection of sufficient position data the aircraft must fly straight and level at any altitude from FL290 to FL 410 for at least thirty minutes in duration. Monitoring flights do not need to be conducted in North American airspace; however, monitoring should be conducted in areas where Mode-C radar data can be retrieved by the FAA Technical Center staff in a timely manner.

GMU Description

The GMU is a portable unit composed of a Global Positioning System (GPS) receiver, two GPS antennas (temporarily mounted on interior windows with suction cups), and a laptop computer to record the GPS performance data. The GMU requires plug-in power from the aircraft (draws 2.0 to 4.0 amperes maximum) and accepts multiple types of power standard to most aircraft.  The GMU can be installed in the aircraft cockpit or cabin, depending upon aircraft type.  Installation time is approximately 15 minutes. For most transport aircraft, the GMU is best installed using the aft cockpit windows.  The GMS Support Contractor typically occupies a jump seat to monitor GMU performance.  GMU installation and operation will not interfere with crew operations.

GMU Monitoring Process

The monitoring sequence for the operator is illustrated in Figure 1 below.  The operator will be kept informed as the FIF, GPS data file, and pressure altitude data file move through the

post-flight processing steps.

*Aircraft Status For Monitoring.   Aircraft must be RVSM-compliant for monitoring to be conducted.  For in-service aircraft, aircraft modification and/or inspection required by RVSM Service Bulletin, STC or other approved RVSM document must be completed prior to the aircraft being monitored.

Any exception to this rule must be coordinated with AFS-400.

The operator should contact a GMS Support Contractor to discuss monitoring options, such as time, date, origin and destination airport and routing for the GMU flight.  The operator should submit the Monitoring Application to the U.S. GMS Coordinator and the GMS Support Contractor by facsimile.  The operator should list on the Monitoring Application each aircraft that will be operated in RVSM airspace or attach a list to the application.   The collection of GPS data with the GMU can be accomplished by a GMS Support Contractor or by an operator representative that has received GMU training.  Operator representatives should coordinate directly with the GMS Support Contractor to develop a monitoring plan as described above.

To conduct the monitoring flight, the GMS Support Contractor or a trained operator representative will perform the following tasks:

1.   Submit pre-flight FIF to the U.S. GMS Coordinator and the GMS Support Contractor

2.   Conduct the height monitoring flight with the GMU

3.   Submit post-flight FIF to the U.S. GMS  Coordinator and the GMS Support Contractor

4.   Submit GPS data files to GMS Support Contractor

FSDO OR CMO Action.  After determining that aircraft are RVSM-compliant, the FSDO or CMO will forward operator and airframe information to the U.S. Operator/Aircraft RVSM Approvals Database using the Flight Standards Program Tracking and Reporting Subsystem (PTRS).

Post-Flight Processing and Operator Notification

After completion of the monitoring flight, the GPS data from the monitoring flight will be processed by the GMS Support Contractor (CSSI or ARINC) and forwarded to the U.S. GMS Coordinator for further processing. The NAARMO will collect and merge Meteorological and Mode C data with the GPS file to determine the aircraft’s Altimetry System Error (ASE).  Final ASE results should be available from the NAARMO within three weeks of the flight.  The results will be sent to the responsible FAA FSDO or CMO.

The operator can obtain a copy of the results from the FSDO or CMO.

Flight Information Form (FIF)

Please Fax to the U.S. GMS Coordinator at +1 609 485 5078and the appropriate GMS Operations Coordinator

CSSI:  +1 202-863-2398;   ARINC:   +1 410-573-3007

Fax 24 hours prior to flight and within 6 hours of landing.

| INFORMATION TO BE RECORDED PRIOR TO FLIGHT |
| --- |
| Airline/Operator: | GMU Container Number: |  |
| Point of Contact for Operator: Name: Phone: Fax: |
| Aircraft Type/Series: | Aircraft Registration Number: |
| Call Sign: | Airframe Serial Number: |
| Planned: Origin: Departure Date (UTC): Departure Time (UTC): |
| Planned: Destination: Arrival Date (UTC): Arrival Time (UTC): |
| Installer (Name/Org.): | Retriever (Name/Org.): |
| Mode S Equipped (Yes/No): Separation Between Mounted Antennas (ft.): |
| Installer/Operator Comments: |
| INFORMATION TO BE RECORDED BY FLIGHT CREW/GMU OPERATOR |
| Data Collection: | Start Date (UTC): | Start Time (UTC): |
| GMU File Name: |
| Departure Time (UTC): | Origin (ICAO ID): |  |
| Please record the requested information as soon as practical when: Aircraft is first established in level flight at or above FL 290, or The ATC assigned transponder code is changed at or above FL 290, or There is a flight level change and aircraft remains at or above FL 290, or An autopilot change is initiated at or above FL 290, or The ARTCC or FIR changes. |
| Time | Assigned | Mach/Air | Xpndr | Altimeter Reading | Autopilot (L, R, C) | FMS/PMS | ARTCC/FIR |
| (UTC) | FL | Speed | Code/Source | Pilot | Co-pilot | Pilot | Co-pilot | (Y/N) | (ICAO ID) |
| Data Collection: | End Date (UTC): | End Time (UTC): |
| Arrival Time (UTC): | Destination ICAO (ID): |  |
| Comments on flight conditions affecting height keeping performance, i.e. turb, and location |

Appendix 3

Procedures for North Atlantic (Strumble) Height Monitoring Unit

1.  Options for Monitoring Flights.   In the North Atlantic Region, monitoring can be completed by overflying ground-based Height Monitoring Units (HMUs) or utilizing the portable, airborne GPS-based Monitoring System (GMS).   Procedures for using the GMS are provided in Appendix 2.

2.  Monitoring Requirements.  Monitoring requirements charts for the North/West Atlantic are posted on the FAA RVSM Documentation webpage (www.faa.gov/ats/ato/rvsm1.htm) and on the North Atlantic Programme Coordination Office website (www.nat-pco.org).   As a general rule, operators seeking RVSM approval will be required to have a number of their aircraft monitored within 6 months of receiving RVSM approval.

3.  Monitoring Using the HMU Method

a.	*An HMU is located near the Strumble (STU) VOR below the centreline of UG1. The horizontal coverage areas for the Strumble HMU is a 13.8 nm radius circle centered on position N51( 56’ 00’’ W004( 40’ 00’’.  In the vertical dimension, the coverage is from FL 290 to FL 410 inclusive.  The site is unmanned and designed to operate continuously.

b.	*The HMU near the Gander (YQX) VORTAC in Canada was decommissioned on 1/20/05.

c.	While straight and level flight through the area of coverage should normally result in successful monitoring, operators of aircraft making a flight with the specific intention of getting monitored should, where possible, plan to meet the requirements outlined in the ensuing paragraphs:

d.	Pre-Flight Procedures.

(1)  Operators complete and fax a copy of the “Application for Monitoring” form to the U.S. Operator/Aircraft RVSM Approvals Database and Monitoring Coordinator.  See Appendix 1.

(2)  *Operators proposing to divert from an optimum route in order to fly over an HMU are strongly advised to call the Strumble HMU status line on 44 (*0) 189 542-3823 (*0 not required from U.S. locations) for HMU serviceability information.  Every effort will be made to ensure that the promulgated information is accurate; however, operators should note that the equipment may become unserviceable at short notice.

(3)  *Aircraft for monitoring by an HMU should be flight planned to route via STU.  Dispatchers should ensure that Item 18 of the flight plan (CA48) includes both aircraft registration (if it is not already included in Item 7) and “RMK/HMU FLT STU”.

d.	In Flight Procedures.  For overflights of the Strumble HMU, crews should aim to fly straight and level while within the coverage area of the respective HMU.  Failure to do so may invalidate the result.  Prior to an overflight of the Strumble HMU, crews should transmit “... for HMU Flight” to London Control on initial contact.  Operational requirements permitting, the controller will endeavor to do his/her best to allow the aircraft to route through the HMU coverage area in straight and level flight.

- The HMU is capable of tracking many aircraft simultaneously.  To that end, provided the above procedures are followed, aircraft height will be monitored and there will, therefore, be no necessity to carry out a second consecutive overflight.

e.	Post Flight Procedures.  Operators wishing to ascertain the result of the overflight may fax a request to the NAT Central Monitoring Agency (CMA) on +44 (*0) 189 542-3931. (*0 not required from U.S. locations).  Any request for information regarding the result of monitoring will be more speedily dealt with if the Mode S or Mode A codes and approximate time of overflight are included in the enquiry.

Appendix 4

Basic Monitoring Procedures for Europe:   HMU’s and GMU’s

Introduction.   The information below was adopted for U.S. operators from Monitoring Procedures on the Eurocontrol RVSM website.  The full document can be found under “Aircraft Operators” in the European RVSM website.   The address is:   http://www.eur-rvsm.com

Options for Monitoring Flights.   Operators have the option of overflying an HMU or using the GMS.   Basic GMS procedures are addressed in Appendix 2.    For operators based outside the U.S., a contact is provided below for the ARINC European Division GMS monitoring program.

HMU Procedures

Pre-Flight Coordination with U.S. Operator/RVSM Approvals Database and Monitoring Coordinator.   U.S. operators planning to complete monitoring using an HMU located in Europe should complete the following steps:

1.	Operator obtains FAA Flight Standards field office RVSM airworthiness and operational approval

for the aircraft to be monitored in European airspace.   (Airframe and operational approval information will be forwarded to the U.S. RVSM Approvals Database through the AFS Program Tracking and Reporting Subsystem (PTRS)).

2.	Operator completes the “Application for Monitoring” form shown in Appendix 1 and faxes it to		 U.S. Operator/RVSM Approvals Database and Monitoring Coordinator at +1 609-485-5078 and…

3.	If it has not already been accomplished, the U.S. Operator/RVSM Approvals Database and Monitoring Coordinator will coordinate the operator’s FAA RVSM Approvals Database information with Eurocontrol.

4.	If not previously accomplished, the operator also faxes USC Form 2 (see below) to the AMN User Support Cell.

Flight Procedures.   The HMU is a passive ground based system that measures aircraft height keeping over an approximately circular area. Each system consists of a set of ground stations arranged as a central site with four additional receivers arranged in a square. Each site receives aircraft SSR replies (Modes A, C and S) from which the 3D position of the aircraft is derived. Using meteorological information and the Mode C/S height data the altimetry system error is calculated. The HMUs are operating at the following locations:

- Linz in Austria [centre 48°12’N, 014°18’E]

Nattenheim in Germany [centre 49°57’N, 006°28’E]

Geneva in Switzerland [centre 46°22’N, 005°56’E]

HMU Range.   ATS route segments within HMU coverage can be determined by considering a circle with 45 NM radius around the center coordinates given above. Up-to-date information can be obtained from the RMA.

Level Flight.   For a successful measurement by an HMU, it is required that the aircraft is in level flight for approximately 5 minutes, between FL290 and FL410 (inclusive) within the coverage of the HMU.

Monitoring Flight Results and Eurocontrol Database Information.   Operators may consult the Eurocontrol RVSM Web Site (www.eur-rvsm.com) or contact the User Support Cell (see contact details below) to ascertain that the information stored about the aircraft is correct and to identify whether the aircraft have been monitored and acceptable performance has been demonstrated.

Contacts.

Eurocontrol (currently acting as RMA for European RVSM):

AMN User Support Cell (USC)

Tel 	+32-2-729-3785

Fax 	+32-2-729-4634

## Email 	amn.user.support@eurocontrol.int

ARINC European Division Programme/Logistics Manager

(European RVSM Programme)

Kevin Harling

Tel:  +44 1293 763 342

Mbl:  +44 7720 075 208

Fax:  +44 1293 763 212

Email:   kharling@arinc.com

Appendix 5

Domestic U.S. AGHME GMS (Aircraft Geometric Height

Measurement Element Ground-based Monitoring System)

*For information on AGHME locations and procedures, please access the AGHME Main Page at:

http://www.tc.faa.gov/act-500/niaab/rvsm/AGHME_main.asp

*On the “AGHME Locations” Webpage, in the “Flight Plan Information” column, you can click on “Location Overview” and “Optimal Coverage Area” for details on location and coverage.

# Text boxes

NAARMO USE

Operator Receives Monitoring Results from FSDO or CMO

Monitoring Flight Activity

- Submit Pre-Flight Flight Information Form

- Operate GMU

- Submit Post-Flight Flight Information Form

- Submit GPS Data File

FSDO or CMO Receives Monitoring Results from the NAARMO

Receive Status Updates

Conduct GMU Monitoring Flight

Operator Receives Training on GMU Process

Operator Schedules GMU Flight with GMS Support

NAARMO Coordinates Collection of Pressure Altitude Data for the GMU Flight

Operator Completes Monitoring Application and faxes it to the U.S. GMS Coordinator and the GMS Support Contractor

Operator Contacts GMS Support Contractor to Plan Monitoring Flight

FSDO/ CMO Determination of Aircraft RVSM-compliance and PTRS Action May Occur Before or After Monitoring Is Completed

For Example, an Aircraft Service Center May Complete Monitoring When RVSM-compliance Work is Completed Before the Operator

Re-takes Possession of the Aircraft

The Aircraft Is Determined to be RVSM-compliant.  (RVSM Modifications/ Inspections Completed, As Required)

Figure 1. GMU Monitoring Process For U.S. Operators